AER Benchmark Specification Sheet

1. Test ID:	AER-BCR-001

- Short Description:	Criticality calculations of simple VVER440 pin cell  array

with fresh and spent fuel of 30 and 40 GWd/tU burnup and 1 and 5 years cooling time

3. Submitted by: (name) (Company)	L. Markova, NRI Rez plc., Czech Republic

Date:					February 17, 1999

4. Reviewed by: M. Makai (AEKI) and P. Dařilek (VUJE)

Date: November 1999

5. Accepted by: M. Makai (AEKI) and P. Dařilek (VUJE)

Date: February 2000

6. Objective:	To evaluate an ability to describe the spent fuel from the reactivity point of view using selected groups of major isotopes representing the spent fuel inventory.

To intercompare reactor-away criticality codes and libraries for VVER spent fuel system criticality calculations.

7. Rationale for Test Setup: A part of the burnup credit calculational methodology is verified, namely that simple models using established away-from-reactor codes (e.g. KENO, MCNP) can be used to evaluate the criticality safety margins for spent fuel systems. The benchmark was designed to study the effects of various fission products and actinides on safety margins taking the fuel burnup and cooling time as parameters. The present benchmark works with given isotopic compositions.

8. Input:			see Appendix 1

a, Geometry

b, Material Compositions

c, Other

- Hardware and Software Requirements:

It strongly depends on the methodology used by the

individual analyst

10. Output:

a, Expected Results (primary, secondary)

Data		Contents of the data file

1		* General Data *

2		Date

3		Institute

4		Participants

5		Computer Code

6		Data library identification, origin, description

7		No. of Energy Groups (NEG), supply 1 for continuous energy

8		Upper Energy Limit, High -( Low of each energy group (i=1,NEG)

9		* Result of Case 1*

10		Multiplication Factor (For Monte Carlo: No. of histories, Std Deviation)

11		Neutron Spectrum in water (i=1,NEG)

12		Neutron Spectrum in fuel    (i=1,NEG)

13		- Reaction rates - (Total of all energy ranges)

14		U-235		Production,	Absorption,	Neutrons per fission

15		U-236		Production,	Absorption,	Neutrons per fission

16		U-238		Production,	Absorption,	Neutrons per fission

17		Pu-238 		Production,	Absorption,	Neutrons per fission

18		Pu-239		Production,	Absorption,	Neutrons per fission

19		Pu-240		Production,	Absorption,	Neutrons per fission

20		Pu-241		Production,	Absorption,	Neutrons per fission

21		Pu-242 		Production,	Absorption,	Neutrons per fission

22		Am-241 	Production,	Absorption,	Neutrons per fission

23		Am-243 	Production,	Absorption,	Neutrons per fission

24		Np-237 		Production,	Absorption,	Neutrons per fission

25		Mo-95				Absorption

26		Tc-99 				Absorption

27		Ru-101 				Absorption

28		Rh-103 				Absorption

29		Ag-109 				Absorption

30		Cs-133	 			Absorption

31		Sm-147 				Absorption

32		Sm-149 				Absorption

33		Sm-150 				Absorption

34		Sm-151 				Absorption

35		Sm-152 				Absorption

36		Nd-143 				Absorption

37		Nd-145 				Absorption

38		Eu-153 				Absorption

39		Gd-155 				Absorption

40		O-16  				Absorption

Repeat Data 9 to 40 for the other benchmark Cases, see Appendix 1.

In each Case, two sets of results are required. The results differ only in the normalisation. In the first set, the total of all the production rate, in the second the absorption rate should be unity. The absorption reaction rate (Ai), the production reaction rate (Pi) and the neutrons per fission (Fi) of nuclide i are defined as follows:

where

where

b, Files, Format	ASCII

11. References:

See Appendix 1  (which is an appendix originally included into ‘Continuation of the VVER Burnup Credit Benchmark: Evaluation of CB1 Results, Overview of CB2 Results to Date, and Specification of CB3’ presented on  the 8th AER SYMPOSIUM on VVER Reactor Physics and Reactor Safety, September 21-25, 1998 Bystrice nad Pernštejnem, Czech Republic ) :

/1/	M. Takano: OECD/NEA Burnup Credit Criticality Benchmark, Result of Phase-I A, Jan 1994, JAERI - M, 94-003, NEA/NSC/DOC(93)22

/2/ L. Markova: Calculational Burnup Credit Benchmark Proposal ( 6th AER Symposium on VVER Reactor Physics and Reactor Safety,  Kirkkonummi, Finland, Sept. 23-26, 1996)

/3/ SCALE: A Modular Code System for Performing Standardized Computer Analyses for Licensing Evaluation, NUREG/CR-0200, Rev.4 (ORNL/NUREG/CSD-2R4), Vols. I,II, and III (April 1995). Version 4.2 , RSIC code package CCC-545.

/4/ Preliminary Safety Report for Dukovany Power Plant, Unit 1, part 4.3.1 Neutron Physics Characteristics of the core and 4.3.2.4.8 Thermomechanical Characteristics of the Fuel Pins (SKODA Nuclear Machinery, Pilsen, Czech Republic, Ae 8281/Dok, 1994

/5/ Castor Licensing Documentation, Personal Communication with Mr. V. Fajman, The State Office of Nuclear Safety, Prague, Czech Republic

12. Recommended Solution:

a, Method				established away-from-reactor codes

b, Data, Estimated Error		validated libraries

13. Summary of Available Solutions:

See Appendix 1 for the results, the list of CB1 participants follows:

| Name of Participant | Institute | E-Mail | Code | Library |
| --- | --- | --- | --- | --- |
| A. Tanskanen | VTT Energy, Finland | aapo.tanskanen@vtt.fi | SCALE 4.3, CSAS26 | 27BURNUPLIB and 44GROUPNDF5 |
| A. Tanskanen | VTT Energy, Finland |  | MCNP4B | endf60+kidman,rmccsa,endf5u |
| M.Anttila, S.Luhtala | VTT Energy, Finland | markku.anttila@vtt.fi | CASMO-4, V1.22C | E4LBL40 based on ENDF/B-IV |
| V.Barshevtzev, A.Tsiboulia | IPPE Obninsk, Russia | abbn@indigo. ippe.rssi.ru | TWODANT | ABBN-93 |
| G. M. Jerdev, S.V. Zabrodskaia | IPPE Obninsk, Russia | abbn@indigo. ippe.rssi.ru | WIMS/ABBN | WIMS/ABBN |
| V. Chrapciak | VUJE Trnava, Slovakia | chrapc_v@inst.vujett.sk | SCALE 4.3 | 44GROUPNDF5 |
| R L Bowden | British Nuclear Fuels plc, Risley, Warrington, UK | russ_bowden@hotmail.com | MONK7B | MONK7B based on JEF2.2 |
| E. Tinkova | ENERGOPROJEKT a.s. Praha, Czech Republic | tinkova@egp. cz | HELIOS version 1.4 | HELIOS based on ENDF/B-VI |
| P.Mikolas | SKODA Plzen, Czech Republic | pmikolas@jad. ln.skoda.cz | WIMS7 | based on JEF2.2 |
| L. Markova | NRI plc, Rez , Czech Republic | mar@nri.cz | MCNP4B | DLC-189/MCNPXS (‘free gas’ and S((,() aproaches ) |

APPENDIX 1

Specification of CB1

Result of CB1 - final evaluation

Introduction

When the safety of a fuel storage or a transport cask is assessed with spent fuel instead of the suggested fresh fuel, the methodology of the criticality calculation need to be checked thoroughly and the safety margins need to be studied. This VVER benchmark as well as that for PWR of the western type described in /1/ answer some questions connected with the issue if, under what conditions, and with what results a simple model using away-from-reactors codes (KENO, MCNP, MONK..) is able to be used for the criticality safety analyses of such systems. The first phase of the both benchmarks evaluates the safety margins resulted from criticality calculations by the away-from-reactors codes if selected actinides and fission products (FPs) describe the spent fuel of different burnups and after different cooling time.

In the following the final result of the CB1 (the first phase of the VVER burnup credit calculational benchmark similar to the Phase-1A of the benchmark conducted by the OECD/NEA/NSC Burnup Credit Criticality Benchmark Working Group (NEACRP-L337, Rev.1, 1992, also /1/)) is described. The VVER burnup credit (BUC) calculational benchmark was proposed /2/ on the 6th Atomic Energy Research (AER) Symposium on VVER Reactor Physics and Reactor Safety, Kirkkonummi, Finland, Sept. 23-26, 1996. The first phase of the benchmark - entitled CB1 - was specified as follows (see Appendix of /2/):

CB1 Specification

1.	General Specification of Spent Fuel Cell of Hexagonal Section

Fuel Enrichment class		3.6 % wt. 235U

Fuel Cell Pitch			1.22 cm

Fuel Radius			0.38 cm

Cladding Inner Radius		0.38 cm

Outer Radius		0.455 cm

Material			1% wt. Nb, 98.97% wt. Zr, 0.03% wt. Hf,

(eff = 6.0881 g/cm3

Moderator			Water

Fuel Length			Infinite

Axial Burnup Distribution		Uniform

Radial Burnup Distribution	Uniform

Temperature			300 K

Atomic Number Densities		see Table 1.a.

of Nuclides in Fuel

2.	Parameters

Cooling Time			1 and 5 year(s)

Fuel Burnup			0, 30 and 40 GWd/tU

Fission Products			Selected or Omitted (see Table 1)

Table 1 Reference Case Number

| Cooling | Considered | Burnup (GWd/tU) |
| --- | --- | --- |
| Time (year) | FPs | Actinides | Fresh | 30 | 40 |
|  | Selected * | All ** |  | Case 2 | Case 3 |
| 1 |  | Major *** |  | Case 10 |  |
|  | No FPs | All | Case 1 | Case 4 | Case 5 |
|  | Selected | All |  | Case 6 | Case 7 |
| 5 |  | Major |  | Case 11 |  |
|  | No FPs | All |  | Case 8 | Case 9 |

***	U .......235, 236, 238,  Pu .............239, 240, 241

**	U .......235, 236, 238,  Pu .....238, 239, 240, 241, 242,  Am .....241, 243,	 Np......237

*	Mo-95, Tc-99, Ru-101, Rh-103, Ag-109, Cs-133, Nd-143, Nd-145, Sm-147, Sm-149, Sm-150, Sm-151, Sm-152, Eu-153, Gd-155

3.	Requested Information and Results

If some part of the following set of the requested results is not available as output tallies of your code, please, note it, and omit in the result list.

Please forward the results by electronic mail to NRI (mar@nri.cz), otherwise send a diskette by mail.

Data		Contents

1		* General Data *

2		Date

3		Institute

4		Participants

5		Computer Code

6		Data library identification, origin, description

7		No. of Energy Groups (NEG), supply 1 for continuous energy

8		Upper Energy Limit, High -( Low of each energy group (i=1,NEG)

9		* Result of Case 1*

10		Multiplication Factor (For Monte Carlo: No. of histories, Std Deviation)

11		Neutron Spectrum in water (i=1,NEG)

12		Neutron Spectrum in fuel    (i=1,NEG)

13		- Reaction rates - (Total of all energy ranges)

14		U-235		Production,	Absorption,	Neutrons per fission

15		U-236		Production,	Absorption,	Neutrons per fission

16		U-238		Production,	Absorption,	Neutrons per fission

17		Pu-238 		Production,	Absorption,	Neutrons per fission

18		Pu-239		Production,	Absorption,	Neutrons per fission

19		Pu-240		Production,	Absorption,	Neutrons per fission

20		Pu-241		Production,	Absorption,	Neutrons per fission

21		Pu-242 		Production,	Absorption,	Neutrons per fission

22		Am-241 	Production,	Absorption,	Neutrons per fission

23		Am-243 	Production,	Absorption,	Neutrons per fission

24		Np-237 		Production,	Absorption,	Neutrons per fission

25		Mo-95				Absorption

26		Tc-99 				Absorption

27		Ru-101 				Absorption

28		Rh-103 				Absorption

29		Ag-109 				Absorption

30		Cs-133	 			Absorption

31		Sm-147 				Absorption

32		Sm-149 				Absorption

33		Sm-150 				Absorption

34		Sm-151 				Absorption

35		Sm-152 				Absorption

36		Nd-143 				Absorption

37		Nd-145 				Absorption

38		Eu-153 				Absorption

39		Gd-155 				Absorption

40		O-16  				Absorption

Repeat Data 9 to 40 for the other Cases.

In each Case, the total of all the production rates as well as all the absorption rates should be normalized to unity. The absorption reaction rate (Ai), the production reaction rate (Pi) and the neutrons per fission (Fi) of nuclide i are defined as follows:

where

where

Atomic Number Densities

(by NRI Rez using SCALE, SAS2H sequence /3/)

--------------------------------------------------------------------------------------------------------------------------------------

Table 1.a.

Isotopic compositions for different burnup levels and cooling times

Data were derived by ORIGEN-S/SAS2H with

VVER fuel assembly design description /4/,/5/

Parameter							Data

Assembly general data

Lattice						hexagonal, pitch 14.7cm

Water temperature, K				559

Pressure						13.7 MPa

Soluble boron cycle av., ppm (wt)			500

Number of fuel rods				126

Number of instrument tubes			1

Casing 	inner size				14.0 cm

outer size				14.4 cm

Material					2.5% wt. Nb, 97.47% wt. Zr, 									0.03% wt. Hf,

( = 6.44 g/cm3

Fuel rod data

Pellet density (effective)				10.193

Rod pitch, cm					1.22

Rod OD, cm					0.91

Pellet diameter, cm				0.76

Active fuel length, cm				242

Effective fuel temperature, K			732

Clad 	temperature, K				585

material					1% wt. Nb, 98.97% wt. Zr, 									0.03% wt. Hf,

(eff = 6.0881 g/cm3

Instrument tube data

Inner radius, cm					0.440

Outer radius, cm					0.515

Material		  				1% wt. Nb, 98.97% wt. Zr, 									0.03% wt. Hf,

( = 6.44 g/cm3

Operating History Data and Fuel Isotopic Content of VVER Cases

Specific Power						4.143 MW/assembly

Number of cycles					3, 4 (for the 30, 40 MWd/kgU 									burnup cases respectively

Cycle duration (days)

Uptime						300

Downtime (between cycles)			65

Cooling Time (year) 					0, 1, 5

Uranium Content (wt %)

U-235					3.6

U-238					96.4

--------------------------------------------------------------------------------------------------------------------------------------

Isotopics for Fresh Fuel

U-235				8.2470E-04

U-238				2.2085E-02

O				4.5819E-02

Isotopics for 30 GWd/t case

ORIGEN-S ISOTOPICS RESULTS 30 GWD/T FOR COOLING TIME  (YR) = 0.00

U-235			2.9048E-04

U-236			9.4030E-05

U-238			2.1559E-02

NP-237			1.0127E-05

PU-238			2.9796E-06

PU-239			1.5002E-04

PU-240			4.3652E-05

PU-241			3.2616E-05

PU-242			7.4607E-06

AM-241			9.5869E-07

AM-243			1.4992E-06

O			4.5819E-02

MO-95			3.3565E-05

TC-99			4.0934E-05

RU-101			3.7035E-05

RH-103			1.7058E-05

AG-109			2.9037E-06

CS-133			4.2276E-05

ND-143			3.0026E-05

ND-145			2.3103E-05

SM-147			1.3973E-06

SM-149			2.8795E-07

SM-150			1.3141E-05

SM-151			1.5091E-06

SM-152			2.5830E-06

EU-153			3.8847E-06

GD-155			2.1744E-09

ORIGEN-S ISOTOPICS RESULTS 30 GWD/T FOR COOLING TIME  (YR) = 1.00

U-235			2.9048E-04

U-236			9.4035E-05

U-238			2.1559E-02

NP-237			1.0362E-05

PU-238			3.1999E-06

PU-239			1.5195E-04

PU-240			4.3661E-05

PU-241			3.1079E-05

PU-242			7.4611E-06

AM-241			2.4931E-06

AM-243			1.5012E-06

O			4.5819E-02

MO-95			3.9371E-05

TC-99			4.1138E-05

RU-101			3.7037E-05

RH-103			1.9400E-05

AG-109			2.9118E-06

CS-133			4.2746E-05

ND-143			3.0857E-05

ND-145			2.3113E-05

SM-147			2.2267E-06

SM-149			3.5010E-07

SM-150			1.3141E-05

SM-151			1.5064E-06

SM-152			2.5831E-06

EU-153			3.9237E-06

GD-155			3.0055E-08

ORIGEN-S ISOTOPICS RESULTS 30 GWD/T FOR COOLING TIME  (YR) = 5.00

U-235			2.9050E-04

U-236			9.4053E-05

U-238			2.1559E-02

NP-237			1.0396E-05

PU-238			3.1576E-06

PU-239			1.5193E-04

PU-240			4.3690E-05

PU-241			2.5621E-05

PU-242			7.4612E-06

AM-241			7.9166E-06

AM-243			1.5007E-06

O			4.5819E-02

MO-95			3.9533E-05

TC-99			4.1137E-05

RU-101			3.7037E-05

RH-103			1.9404E-05

AG-109			2.9118E-06

CS-133			4.2746E-05

ND-143			3.0848E-05

ND-145			2.3113E-05

SM-147			4.0273E-06

SM-149			3.5010E-07

SM-150			1.3141E-05

SM-151			1.4608E-06

SM-152			2.5835E-06

EU-153			3.9237E-06

GD-155			1.0815E-07

Isotopics for 40 GWd/t case

ORIGEN-S ISOTOPICS RESULTS 40 GWD/T FOR COOLING TIME  (YR) = 0.00

U-235			1.9640E-04

U-236			1.0616E-04

U-238			2.1362E-02

NP-237			1.4287E-05

PU-238			5.8179E-06

PU-239			1.5775E-04

PU-240			5.5897E-05

PU-241			4.2060E-05

PU-242			1.3673E-05

AM-241			1.4886E-06

AM-243			3.5964E-06

O			4.5819E-02

MO-95			4.4252E-05

TC-99			5.3059E-05

RU-101			4.8791E-05

RH-103			2.0112E-05

AG-109			3.9429E-06

CS-133			5.3719E-05

ND-143			3.6112E-05

ND-145			2.8976E-05

SM-147			1.6947E-06

SM-149			2.8078E-07

SM-150			1.7485E-05

SM-151			1.8367E-06

SM-152			3.1879E-06

EU-153			5.4429E-06

GD-155			4.0958E-09

ORIGEN-S ISOTOPICS RESULTS 40 GWD/T FOR COOLING TIME  (YR) = 1.00

U-235			1.9640E-04

U-236			1.0617E-04

U-238			2.1362E-02

NP-237			1.4557E-05

PU-238			6.2225E-06

PU-239			1.5979E-04

PU-240			5.5936E-05

PU-241			4.0078E-05

PU-242			1.3673E-05

AM-241			3.4669E-06

AM-243			3.6001E-06

O			4.5819E-02

MO-95			4.9778E-05

TC-99			5.3262E-05

RU-101			4.8792E-05

RH-103			2.2606E-05

AG-109			3.9529E-06

CS-133			5.4186E-05

ND-143			3.6912E-05

ND-145			2.8985E-05

SM-147			2.5004E-06

SM-149			3.4513E-07

SM-150			1.7485E-05

SM-151			1.8320E-06

SM-152			3.1881E-06

EU-153			5.4925E-06

GD-155			4.8815E-08

ORIGEN-S ISOTOPICS RESULTS 40 GWD/T FOR COOLING TIME  (YR) = 5.00

U-235			1.9642E-04

U-236			1.0619E-04

U-238			2.1362E-02

NP-237			1.4603E-05

PU-238			6.1371E-06

PU-239			1.5978E-04

PU-240			5.6076E-05

PU-241			3.3040E-05

PU-242			1.3674E-05

AM-241			1.0459E-05

AM-243			3.5988E-06

O			4.5819E-02

MO-95			4.9933E-05

TC-99			5.3261E-05

RU-101			4.8792E-05

RH-103			2.2610E-05

AG-109			3.9529E-06

CS-133			5.4186E-05

ND-143			3.6904E-05

ND-145			2.8985E-05

SM-147			4.2502E-06

SM-149			3.4513E-07

SM-150			1.7485E-05

SM-151			1.7765E-06

SM-152			3.1885E-06

EU-153			5.4926E-06

GD-155			1.7407E-07

Results of  the CB1 Calculations

In total, 12 sets of the CB1 results were obtained from 7 institutes of 5 countries (Czech Republic, Finland, Slovakia, Russia and United Kingdom), prevalently from researchers coming from countries operating VVERs (Czech Republic, Finland, Slovakia, and Russia) and participating in AER Working Group E („Physical problems on Spent fuel, Radwaste and Decommissioning of Nuclear Power Plant“) activity.

The goal of the CB1 was to study effects of 6 major and 5 minor actinides and 15 major fission products (FPs) upon criticality resulting from criticality calculations of a simple infinite hexagonal lattice of both spent and fresh VVER 440 fuel rods for the fuel burnup of 30 and 40 GWd/tU after 1 and 5 year(s) cooling time. Calculations were performed for 11 cases (see Table 1), each having different spent fuel isotopes (major or minor actinides and major fission products) involved.

An effect of minor fission products was not investigated (otherwise, about 200 isotopes would have to be entered as data for the spent fuel zone in the calculation). The results of the calculations obtained in OECD (see /1/) for simple PWR pin cell can be used for a comparison (see Table 2, below). All tendencies found there are the same and comparable values are very similar. On the other hand, as far as multiplication factor uncertainties of the VVER results (see Table 4) are concerned, there is a visible shift to lower values because of a progress in the methodology used for the calculations (latest data libraries are mostly used in the case of CB1 calculations).

Multiplication Factors

In spite of the fact that the effect of minor fission products was not investigated in the VVER benchmark, the results from /1/ can be used as an estimation: it results from Table 4.3 in /1/ (see also Table 2) that using the major and minor actinides and major fission products (that is 6+5+15 isotopes, see Table 1) for the spent fuel description covers a little more than 90% of the reactivity loss of the spent fuel system. It is conservative and seems to be acceptable way of taking the fuel burnup into account for the burnup credit calculation by away-from-reactor (mostly 3D Monte Carlo) codes. As far as the contribution of the major actinides only is concerned, it gives about 50% of the reactivity loss. In the following Table 2, there are the reactivity losses by each set of nuclides as resulted from the calculations for PWR /1/ and VVER:

Table 2  Reactivity loss by different sets of selected nuclides

|  | PWR /1/ | VVER-440 (as a result of CB1) |
| --- | --- | --- |
|  | 30 GWd/t,1 year | 30 GWd/t,5 year | 40/1 | 40/5 | 30/1 | 30/5 | 40/1 | 40/5 |
|  | (k | ratio [%] | (k | ratio [%] | (k | (k | (k | (k | (k | (k |
| Major Actinides | 0.1746 | 53.2 | 0.1815 | 50.2 | not calculated | 0.1630 | 0.1706 | not calculated |
| Minor Actinides | 0.0176 | 5.3 | 0.0279 | 7.7 | - | - | 0.0207 | 0.0318 | - | - |
| All Actinides | 0.1922 | 58.5 | 0.2094 | 57.9 | 0.2492 | 0.2721 | 0.1837 | 0.2024 | 0.2324 | 0.2558 |
| Major Fission Products | 0.1054 | 32.0 | 0.1161 | 32.2 | 0.1248 | 0.1417 | 0.1303 | 0.1325 | 0.1462 | 0.1498 |
| All Actinides+Major FPs | 0.2976 | 90.5 | 0.3255 | 90.1 | 0.3740 | 0.4138 | 0.3140 | 0.3349 | 0.3786 | 0.4056 |
| Minor Fission Products | 0.0314 | 9.5 | 0.0357 | 9.9 | not calculated |
| Total | 0.3290 | 100.0 | 0.3612 | 100.0 | - | - | - | - | - | - |

In addition to the BUC evaluation through the averaged values of reactivity losses caused by major and minor actinides and major fission products (Table 5, Table 2) resulted from an evaluation (Table 4) of the results obtained from the participants (Table 3), all the results can be used for an intercomparison of the codes and libraries currently used in this application field.

The average values and standard deviations of the multiplication factor

, 	where 	k is number of the case, k =1,..,11  ,

and  	n  is the number of the result sets,

are listed in Table 4 (together with relative differences between the calculated and average values) and can be also seen, by the individual cases, in Fig. 1- 11. The differences shown in these figures are expressed in the standard deviation units for each case to provide relative values (related to (k for k- case) for a comparison. Three sets of the results were excluded from the evaluation due to obvious reasons: the KENO VI calculation using the (obsolete) 27-group ENDF/B-IV library within SCALE, the CASMO calculation for 2,3,6,7 Cases (because Mo-95, Tc-99 and Ru-101 could not be taken into consideration) and the MCNP calculation using (improperly) free-gas model instead of the S((,() thermal scattering treatment for H2O moderator. Excluding these sets of the results, the others were evaluated together for each of 11 cases. In addition to the results of the evaluation, in Table 4 and Fig. 1-11 there are also the differences between the average value and the calculated one for the sets (or cases as far as CASMO is concerned) which were excluded from the evaluation (the brighter bars in the figures).

The reactivity decrease due to burnup between the individual cases and the fresh fuel case calculated as

(k=(case n) - (case 1)

is shown in Table 5. The 2( deviation of the multiplication factors resulted from the evaluation of Phase 1 A of the OECD benchmark /1/ for PWR (0.0175 for fresh fuel, 0.0099 - 0.0110 for the cases with actinides, 0.0156 - 0.0170 for those with actinides and FPs) can be compared with the results of this VVER benchmark (see Table 4) : 0.0056 for fresh fuel, 0.0052 - 0.0081 for the cases with actinides and 0.0038 - 0.0081 for those with actinides and FPs.

Neutron Spectrum and Reaction Rates

Since none of the 12 benchmark participants sent the neutron spectrum (two participants sent multigroup flux and another two participants sent integral values over the energy interval for fuel and water) this item of the results was not compared.

As far as the reaction rates and ( values are concerned, they were included in 7 sets of the results obtained from the participants. The reaction rates obtained from different participants but calculated by the same methodology (the code and data library) are represented in this draft only by one set of the results (e.g. Czech and Finnish results of MCNP calculation ).

The results obtained from the participants, mean values and standard deviations as well as relative deviations are tabulated (Tables 6 -31) and particularly for the CASE 7 (as probably the most instructive case) also shown in a graphical form in Fig.13-16. Some sets of the results were excluded from the evaluation because they did not meet the all or some of the CB1 specifications, namely CASMO absorption rate results for Cases 2,3,6,7 (because Mo-95, Tc-99 and Ru-101 could not be taken into consideration), these results for O for all the cases (oxygen is not present in the code output but it was taken into consideration as for the normalization) and all the CASMO results for Cases 10 and 11 (because the choice of the major actinides for these cases did not agree with the Table 1). As for the HELIOS results, oxygen absorption rates were omitted in 1,4,5,8,9,10, and 11 cases so they could not be evaluated as well as absorption rates of the other isotopes because the normalization was made without the oxygen contributions. Both of the Russian results were renormalized according to the benchmark specifications. In Tables 21-32 and Fig. 13-16 there are also the differences between the average value and the calculated one for the subsets which were excluded from the evaluation.

References

/1/	M. Takano: OECD/NEA Burnup Credit Criticality Benchmark, Result of Phase-I A, Jan 1994, JAERI - M, 94-003, NEA/NSC/DOC(93)22

/2/ L. Markova: Calculational Burnup Credit Benchmark Proposal ( 6th AER Symposium on VVER Reactor Physics and Reactor Safety,  Kirkkonummi, Finland, Sept. 23-26, 1996)

/3/ SCALE: A Modular Code System for Performing Standardized Computer Analyses for Licensing Evaluation, NUREG/CR-0200, Rev.4 (ORNL/NUREG/CSD-2R4), Vols. I,II, and III (April 1995). Version 4.2 , RSIC code package CCC-545.

/4/ Preliminary Safety Report for Dukovany Power Plant, Unit 1, part 4.3.1 Neutron Physics Characteristics of the core and 4.3.2.4.8 Thermomechanical Characteristics of the Fuel Pins (SKODA Nuclear Machinery, Pilsen, Czech Republic, Ae 8281/Dok, 1994

/5/ Castor Licensing Documentation, Personal Communication with Mr. V. Fajman, The State Office of Nuclear Safety, Prague, Czech Republic

List of CB1 participants

| Name of Participant | Institute | E-Mail | Code | Library |
| --- | --- | --- | --- | --- |
| A. Tanskanen | VTT Energy, Finland | aapo.tanskanen@vtt.fi | SCALE 4.3, CSAS26 | 27BURNUPLIB and 44GROUPNDF5 |
| A. Tanskanen | VTT Energy, Finland |  | MCNP4B | endf60+kidman,rmccsa,endf5u |
| M.Anttila, S.Luhtala | VTT Energy, Finland | markku.anttila@vtt.fi | CASMO-4, V1.22C | E4LBL40 based on ENDF/B-IV |
| V.Barshevtzev, A.Tsiboulia | IPPE Obninsk, Russia | abbn@indigo. ippe.rssi.ru | TWODANT | ABBN-93 |
| G. M. Jerdev, S.V. Zabrodskaia | IPPE Obninsk, Russia | abbn@indigo. ippe.rssi.ru | WIMS/ABBN | WIMS/ABBN |
| V. Chrapciak | VUJE Trnava, Slovakia | chrapc_v@inst.vujett.sk | SCALE 4.3 | 44GROUPNDF5 |
| R L Bowden | British Nuclear Fuels plc, Risley, Warrington, UK | russ_bowden@hotmail.com | MONK7B | MONK7B based on JEF2.2 |
| E. Tinkova | ENERGOPROJEKT a.s. Praha, Czech Republic | tinkova@egp. cz | HELIOS version 1.4 | HELIOS based on ENDF/B-VI |
| P.Mikolas | SKODA Plzen, Czech Republic | pmikolas@jad. ln.skoda.cz | WIMS7 | based on JEF2.2 |
| L. Markova | NRI plc, Rez , Czech Republic | mar@nri.cz | MCNP4B | DLC-189/MCNPXS (‘free gas’ and S((,() aproaches ) |

Table 3 Results of  CB1 calculations: k(

| Name Affiliation Country | G.Jerdev, S.Zabrods-kaja, IPPE Russia | V. Chrapciak VUJE Trnava Slovakia | A.Tanskanen VTT Energy Finland | M.Anttila, S.Luhtala VTT Energy Finland | A.Tanskanen VTT Energy Finland | R.L. Bowden British Nuclear Fuels plc, Risley, Warrington, UK | L. Markova NRI Rez CZ | E.Tinkova EGP Praha CZ | P.Mikolas SKODA Plzen, CZ | V.Barshevtzev A.Tsiboulia IPPE Russia |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Code/ Library | WIMS/ ABBN | KENO VI 44groupndf5 | KENO VI 44groupndf5/ 27burnlib | CASMO4 E4LBL40 | MCNP4B endf60,kidman,rmccsa and endf5u, (S((,()) | MONK7B MONK7B 13193 Point Energy Library, Based on JEF2.2 Evaluations | MCNP4B DLC-189/MCNPXS (free gas / S((,()) | HELIOS 1.4 ENBF/B-VI based lib. | WIMS7 JEF2.2 based lib. | TWODANT ABBN-93 |
| Energy Groups | 69 | 44 | 44/27 | 40 | continuous energy | continuous energy | continuous energy | 190 | 69 | 299 |
|  | k( | k( | ( | k( | ( | k( | k( | ( | k( | ( | k( | ( | k( | k( | k( |
| Case 1 | 1.389093 | 1.38867 | 0.00122 | 1.3886 1.3741 | 0.0010 0.0009 | 1.39061 | 1.38878 | 0.00086 | 1.3979 | 0.0010 | 1.39250 1.39044 | 0.00081 0.00084 | 1.38850 | 1.39155 | 1.3913 |
| Case 2 | 1.077066 | 1.07678 | 0.00103 | 1.0759 1.0729 | 0.0016 0.0015 | 1.09190* | 1.07789 | 0.00128 | 1.0768 | 0.0010 | 1.08391 1.07630 | 0.00096 0.00091 | 1.07975 | 1.07283 | 1.0752 |
| Case 3 | 1.007111 | 1.01457 | 0.00097 | 1.0152 1.0071 | 0.0016 0.0014 | 1.02988* | 1.01333 | 0.00138 | 1.0142 | 0.0010 | 1.01547 1.01242 | 0.00102 0.00087 | 1.01699 | 1.00758 | 1.0053 |
| Case 4 | 1.208282 | 1.20421 | 0.00103 | 1.2060 1.1991 | 0.0017 0.0016 | 1.21068 | 1.20354 | 0.00146 | 1.2106 | 0.0010 | 1.21142 1.20456 | 0.00062 0.00092 | 1.20860 | 1.20569 | 1.2058 |
| Case 5 | 1.15476 | 1.15624 | 0.00109 | 1.1580 1.1496 | 0.0019 0.0018 | 1.16399 | 1.15589 | 0.00114 | 1.1637 | 0.0010 | 1.16590 1.15577 | 0.00099 0.00089 | 1.16299 | 1.15803 | 1.1520 |
| Case 6 | 1.051679 | 1.05875 | 0.00094 | 1.0562 1.0512 | 0.0015 0.0015 | 1.07122* | 1.05742 | 0.00127 | 1.0597 | 0.0010 | 1.06088 1.05587 | 0.00098 0.00087 | 1.05927 | 1.05215 | 1.0498 |
| Case 7 | 0.981970 | 0.98684 | 0.00098 | 0.9878 0.9808 | 0.0014 0.0016 | 1.00188* | 0.98447 | 0.00136 | 0.9869 | 0.0010 | 0.98857 0.98716 | 0.00100 0.00091 | 0.98934 | 0.97974 | 0.9802 |
| Case 8 | 1.184553 | 1.18567 | 0.00148 | 1.1863 1.1795 | 0.0018 0.0018 | 1.19280 | 1.18919 | 0.00134 | 1.1925 | 0.0010 | 1.19397 1.18926 | 0.00104 0.00087 | 1.19092 | 1.18774 | 1.1822 |
| Case 9 | 1.131456 | 1.13367 | 0.00120 | 1.1345 1.1306 | 0.0016 0.0016 | 1.14010 | 1.13317 | 0.00124 | 1.1390 | 0.0010 | 1.14238 1.13230 | 0.00099 0.00087 | 1.13929 | 1.13402 | 1.1290 |
| Case 10 | 1.228444 | 1.22726 | 0.00122 | 1.2282 1.2174 | 0.0017 0.0015 | 1.23189 | 1.22471 | 0.00145 | 1.2333 | 0.0010 | 1.23271 1.22574 | 0.00095 0.00086 | 1.22902 | 1.22684 | 1.2195 |
| Case 11 | 1.215641 | 1.22030 | 0.00122 | 1.2195 1.2119 | 0.0017 0.0017 | 1.22541 | 1.21886 | 0.00146 | 1.2248 | 0.0010 | 1.22481 1.21823 | 0.00092 0.00088 | 1.22255 | 1.22033 | 1.2131 |

* CASMO code cannot take Mo-95, Tc-99 and Ru-101 into account

Table 4 Relative Differences Between the Calculated and Average Values of  k( [%] for All Participants, Average Value and Standard Deviation for Each Case

| Name Affiliation Country | G.Jerdev, S.Zabrods-kaja, IPPE Russia | V. Chrapciak VUJE Trnava Slovakia | A.Tanskanen VTT Energy Finland | M.Anttila, S.Luhtala VTT Energy Finland | A.Tanskanen VTT Energy Finland | R.L. Bowden BNF UK | L. Markova NRI Rez CZ free gas/S((,() | E.Tinkova EGP Praha CZ | P.Mikolas SKODA Plzen CZ | V.Barshevtzev A.Tsiboulia IPPE Russia | All cases of KENO VI+27g, MCNP for free gas and 2,3,6,7 cases of CASMO were not taken into evaluation: |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Code Library | WIMS/ ABBN | KENO VI 44g | KENO VI 44g | KENO VI 27g | CASMO4 E4LBL40 | MCNP4B endf60,kidman, rmccsa, endf5u | MONK7B MONK7B JEF2.2 based library | MCNP4B DLC-189/ MCNPXS | HELIOS 1.4 ENDF/B-VI based lib. | WIMS7 JEF2.2 based lib. | TWODANT ABBN-93 | Average Value | Standard Deviation ( |  |  |  |  |
| Case 1 | -0.104 | -0.135 | -0.140 | -1.183 | 0.005 | -0.127 | 0.529 | 0.141/-0.008 | -0.147 | 0.072 | 0.054 | 1.3905 | 0.0028 |
| Case 2 | 0.056 | 0.029 | -0.081 | -0.331 | 1.434* | 0.132 | 0.031 | 0. 691/-0.016 | 0.305 | -0.338 | -0.118 | 1.0765 | 0.0019 |
| Case 3 | -0.469 | 0.268 | 0.331 | -0.470 | 1.781* | 0.146 | 0.232 | 0.357/0.056 | 0.507 | -0.423 | -0.648 | 1.0119 | 0.0041 |
| Case 4 | 0.123 | -0.214 | -0.066 | -0.638 | 0.322 | -0.270 | 0.315 | 0.383/-0.185 | 0.149 | -0.092 | -0.083 | 1.2068 | 0.0026 |
| Case 5 | -0.292 | -0.164 | -0.012 | -0.737 | 0.505 | -0.194 | 0.480 | 0.670/-0.204 | 0.419 | -0.009 | -0.530 | 1.1581 | 0.0041 |
| Case 6 | -0.376 | 0.294 | 0.052 | -0.421 | 1.475* | 0.168 | 0.384 | 0.496/0.021 | 0.343 | -0.331 | -0.554 | 1.0556 | 0.0036 |
| Case 7 | -0.301 | 0.193 | 0.291 | -0.420 | 1.720* | -0.047 | 0.199 | 0.369/0.226 | 0.447 | -0.528 | -0.481 | 0.9849 | 0.0035 |
| Case 8 | -0.300 | -0.206 | -0.153 | -0.725 | 0.394 | 0.091 | 0.369 | 0.493/0.097 | 0.236 | -0.031 | -0.498 | 1.1881 | 0.0035 |
| Case 9 | -0.282 | -0.086 | -0.013 | -0.357 | 0.480 | -0.130 | 0.383 | 0.681/-0.207 | 0.409 | -0.056 | -0.498 | 1.1347 | 0.0037 |
| Case 10 | 0.078 | -0.019 | 0.058 | -0.822 | 0.358 | -0.227 | 0.473 | 0.425/-0.143 | 0.125 | -0.053 | -0.651 | 1.2275 | 0.0038 |
| Case 11 | -0.347 | 0.035 | -0.031 | -0.654 | 0.454 | -0.083 | 0.404 | 0.405/-0.135 | 0.220 | 0.038 | -0.555 | 1.2199 | 0.0038 |

Table 5 Reactivity Decrease (k Due to Burnup

|  | CASE 2 | CASE 3 | CASE 4 | CASE 5 | CASE 6 | CASE 7 | CASE 8 | CASE 9 | CASE 10 | CASE 11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| (k=(case n)-(case 1) | -0.3140 | -0.3786 | -0.1837 | -0.2324 | -0.3349 | -0.4056 | -0.2024 | -0.2558 | -0.1630 | -0.1706 |

Table 6 Results of  CB1 calculations: reaction rates and ( averaged for CASE 1

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 9,434E-01 | 6,930E-01 | 2,434 | 9,335E-01 | 6,489E-01 | 2,421 | 9,427E-01 | 6,923E-01 | 2,439 | 9,417E-01 | 6,900E-01 | 2,434 | 9,352E-01 | 6,863E-01 | 2,436 | 9,418E-01 | 6,888E-01 | 2,434 |
| U-238 | 5,657E-02 | 3,024E-01 | 2,820 | 6,651E-02 | 2,926E-01 | 2,798 | 5,729E-02 | 3,053E-01 | 2,790 | 5,832E-02 | 3,076E-01 | 2,786 | 6,478E-02 | 3,137E-01 | 2,784 | 5,818E-02 | 3,063E-01 | 2,828 |
| O-16 |  | 4,554E-03 |  |  |  |  |  | 2,361E-03 |  |  | 2,351E-03 |  |  |  |  |  | 4,848E-03 |  |

Table 7 Results of  CB1 calculations: reaction rates and ( averaged for CASE 2

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 3,745E-01 | 2,133E-01 | 2,434 | 3,687E-01 | 2,035E-01 | 2,422 | 3,760E-01 | 2,126E-01 | 2,439 | 3,732E-01 | 2,117E-01 | 2,434 | 3,731E-01 | 2,138E-01 | 2,436 | 3,747E-01 | 2,118E-01 | 2,434 |
| U-236 | 1,575E-04 | 2,592E-03 | 2,679 | 8,487E-04 | 8,566E-03 | 2,571 | 8,485E-04 | 9,265E-03 | 2,535 | 8,592E-04 | 8,667E-03 | 2,568 | 8,045E-04 | 6,453E-03 | 2,589 | 2,980E-04 | 2,566E-03 | 2,529 |
| U-238 | 7,417E-02 | 2,857E-01 | 2,826 | 7,829E-02 | 2,727E-01 | 2,805 | 7,404E-02 | 2,879E-01 | 2,791 | 7,587E-02 | 2,921E-01 | 2,791 | 7,629E-02 | 2,911E-01 | 2,792 | 7,542E-02 | 2,908E-01 | 2,832 |
| Pu-238 | 3,066E-04 | 1,628E-03 | 2,967 | 1,172E-04 | 1,637E-03 | 2,750 | 2,874E-04 | 1,777E-03 | 3,036 | 2,882E-04 | 1,662E-03 | 2,991 | 2,892E-04 | 1,664E-03 | 2,991 | 3,050E-04 | 1,774E-03 | 2,982 |
| Pu-239 | 4,424E-01 | 2,661E-01 | 2,864 | 4,436E-01 | 2,549E-01 | 2,865 | 4,393E-01 | 2,619E-01 | 2,873 | 4,415E-01 | 2,632E-01 | 2,872 | 4,409E-01 | 2,641E-01 | 2,872 | 4,412E-01 | 2,641E-01 | 2,864 |
| Pu-240 | 9,354E-04 | 6,540E-02 | 3,188 | 9,941E-04 | 6,287E-02 | 3,051 | 9,466E-04 | 6,324E-02 | 3,011 | 9,681E-04 | 6,409E-02 | 3,100 | 9,755E-04 | 6,435E-02 | 3,100 | 9,390E-04 | 6,644E-02 | 3,154 |
| Pu-241 | 1,071E-01 | 5,597E-02 | 2,924 | 1,070E-01 | 5,356E-02 | 2,918 | 1,081E-01 | 5,611E-02 | 2,934 | 1,069E-01 | 5,498E-02 | 2,947 | 1,071E-01 | 5,537E-02 | 2,947 | 1,067E-01 | 5,493E-02 | 2,939 |
| Pu-242 | 1,168E-04 | 2,968E-03 | 3,137 | 1,261E-04 | 2,928E-03 | 3,108 | 1,352E-04 | 3,222E-03 | 3,077 | 1,262E-04 | 3,361E-03 | 3,150 | 1,273E-04 | 2,580E-03 | 3,149 | 1,190E-04 | 3,057E-03 | 3,139 |
| Am-241 | 1,020E-04 | 3,263E-03 | 3,402 | 1,163E-04 | 3,186E-03 | 3,499 | 1,386E-04 | 3,402E-03 | 3,417 | 1,065E-04 | 3,237E-03 | 3,396 | 1,079E-04 | 3,260E-03 | 3,383 | 1,010E-04 | 3,191E-03 | 3,291 |
| Am-243 | 2,823E-05 | 1,045E-03 | 3,535 | 1,955E-05 | 9,378E-04 | 3,000 | 3,381E-05 | 1,055E-03 | 3,333 | 3,163E-05 | 1,073E-03 | 3,672 | 3,190E-05 | 1,071E-03 | 3,673 | 2,900E-05 | 1,012E-03 | 3,737 |
| Np-237 | 1,960E-04 | 4,628E-03 | 3,011 | 1,711E-04 | 4,745E-03 | 2,610 | 1,386E-04 | 5,034E-03 | 2,929 | 1,959E-04 | 4,981E-03 | 2,956 | 1,976E-04 | 4,980E-03 | 2,956 | 1,970E-04 | 4,576E-03 | 3,012 |
| Mo-95 |  | 2,361E-03 |  |  |  |  |  | 2,098E-03 |  |  | 2,194E-03 |  |  | 1,840E-03 |  |  | 2,381E-03 |  |
| Tc-99 |  | 4,978E-03 |  |  |  |  |  | 4,713E-03 |  |  | 4,472E-03 |  |  | 4,270E-03 |  |  | 4,631E-03 |  |
| Ru-101 |  | 1,666E-03 |  |  |  |  |  | 1,884E-03 |  |  | 1,585E-03 |  |  | 1,830E-03 |  |  | 1,632E-03 |  |
| Rh-103 |  | 9,280E-03 |  |  | 8,630E-03 |  |  | 9,192E-03 |  |  | 9,257E-03 |  |  | 9,205E-03 |  |  | 9,120E-03 |  |
| Ag-109 |  | 1,604E-03 |  |  | 1,519E-03 |  |  | 1,666E-03 |  |  | 1,586E-03 |  |  | 1,494E-03 |  |  | 1,620E-03 |  |
| Cs-133 |  | 6,779E-03 |  |  | 6,078E-03 |  |  | 6,566E-03 |  |  | 5,995E-03 |  |  | 4,855E-03 |  |  | 6,243E-03 |  |
| Sm-147 |  | 7,772E-04 |  |  | 9,203E-03 |  |  | 7,530E-04 |  |  | 7,814E-04 |  |  | 1,026E-02 |  |  | 7,866E-04 |  |
| Sm-149 |  | 2,536E-02 |  |  | 2,982E-03 |  |  | 2,562E-02 |  |  | 2,502E-02 |  |  | 2,810E-03 |  |  | 2,505E-02 |  |
| Sm-150 |  | 2,826E-03 |  |  | 5,950E-04 |  |  | 1,972E-03 |  |  | 1,799E-03 |  |  | 7,779E-04 |  |  | 2,200E-03 |  |
| Sm-151 |  | 1,695E-02 |  |  | 2,357E-02 |  |  | 1,687E-02 |  |  | 1,548E-02 |  |  | 2,485E-02 |  |  | 1,694E-02 |  |
| Sm-152 |  | 2,776E-03 |  |  | 2,358E-03 |  |  | 3,268E-03 |  |  | 3,107E-03 |  |  | 2,411E-03 |  |  | 2,863E-03 |  |
| Nd-143 |  | 1,033E-02 |  |  | 1,567E-02 |  |  | 1,014E-02 |  |  | 1,030E-02 |  |  | 1,702E-02 |  |  | 1,033E-02 |  |
| Nd-145 |  | 2,600E-03 |  |  | 3,088E-03 |  |  | 2,863E-03 |  |  | 2,764E-03 |  |  | 2,823E-03 |  |  | 2,685E-03 |  |
| Eu-153 |  | 3,111E-03 |  |  | 3,422E-03 |  |  | 3,272E-03 |  |  | 3,104E-03 |  |  | 3,163E-03 |  |  | 3,095E-03 |  |
| Gd-155 |  | 1,133E-03 |  |  | 1,072E-03 |  |  | 1,135E-03 |  |  | 1,127E-03 |  |  | 1,129E-03 |  |  | 1,133E-03 |  |
| O-16 |  | 4,869E-03 |  |  |  |  |  | 2,530E-03 |  |  | 2,506E-03 |  |  | 2,544E-03 |  |  | 5,037E-03 |  |

Table 8 Results of  CB1 calculations: reaction rates and ( averaged for CASE 3

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 2,736E-01 | 1,456E-01 | 2,434 | 2,695E-01 | 1,403E-01 | 2,422 | 2,751E-01 | 1,459E-01 | 2,439 | 2,726E-01 | 1,457E-01 | 2,434 | 2,732E-01 | 1,476E-01 | 2,436 | 2,735E-01 | 1,445E-01 | 2,434 |
| U-236 | 7,450E-04 | 8,878E-03 | 2,679 | 9,988E-04 | 9,387E-03 | 2,573 | 8,586E-04 | 9,599E-03 | 2,549 | 1,014E-03 | 9,156E-03 | 2,575 | 9,457E-04 | 7,076E-03 | 2,591 | 1,357E-03 | 9,239E-03 | 2,536 |
| U-238 | 7,873E-02 | 2,836E-01 | 2,826 | 8,143E-02 | 2,708E-01 | 2,806 | 8,018E-02 | 2,877E-01 | 2,798 | 8,027E-02 | 2,914E-01 | 2,793 | 7,908E-02 | 2,894E-01 | 2,793 | 8,039E-02 | 2,889E-01 | 2,832 |
| Pu-238 | 6,414E-04 | 3,207E-03 | 2,965 | 2,379E-04 | 3,239E-03 | 2,750 | 5,514E-04 | 3,032E-03 | 2,980 | 5,990E-04 | 3,288E-03 | 2,991 | 5,983E-04 | 3,313E-03 | 2,990 | 6,370E-04 | 3,487E-03 | 2,982 |
| Pu-239 | 4,962E-01 | 2,785E-01 | 2,864 | 4,977E-01 | 2,694E-01 | 2,865 | 4,923E-01 | 2,766E-01 | 2,873 | 4,954E-01 | 2,776E-01 | 2,872 | 4,955E-01 | 2,794E-01 | 2,872 | 4,946E-01 | 2,763E-01 | 2,864 |
| Pu-240 | 1,278E-03 | 7,556E-02 | 3,189 | 1,328E-03 | 7,338E-02 | 3,053 | 1,428E-03 | 7,392E-02 | 3,088 | 1,318E-03 | 7,456E-02 | 3,101 | 1,300E-03 | 7,498E-02 | 3,102 | 1,287E-03 | 7,665E-02 | 3,156 |
| Pu-241 | 1,481E-01 | 7,237E-02 | 2,924 | 1,482E-01 | 6,999E-02 | 2,918 | 1,489E-01 | 7,250E-02 | 2,934 | 1,480E-01 | 7,166E-02 | 2,947 | 1,486E-01 | 7,241E-02 | 2,947 | 1,475E-01 | 7,099E-02 | 2,939 |
| Pu-242 | 2,293E-04 | 5,037E-03 | 3,141 | 2,415E-04 | 5,104E-03 | 3,109 | 1,813E-04 | 5,189E-03 | 3,267 | 2,464E-04 | 5,667E-03 | 3,150 | 2,434E-04 | 4,122E-03 | 3,151 | 2,330E-04 | 5,293E-03 | 3,140 |
| Am-241 | 1,511E-04 | 4,493E-03 | 3,403 | 1,699E-04 | 4,427E-03 | 3,499 | 1,924E-04 | 4,496E-03 | 3,467 | 1,569E-04 | 4,488E-03 | 3,397 | 1,576E-04 | 4,535E-03 | 3,383 | 1,490E-04 | 4,389E-03 | 3,293 |
| Am-243 | 7,241E-05 | 2,458E-03 | 3,556 | 4,901E-05 | 2,227E-03 | 3,000 | 8,141E-05 | 2,551E-03 | 3,667 | 8,072E-05 | 2,527E-03 | 3,674 | 7,988E-05 | 2,534E-03 | 3,674 | 7,400E-05 | 2,362E-03 | 3,738 |
| Np-237 | 2,948E-04 | 6,464E-03 | 3,010 | 2,511E-04 | 6,679E-03 | 2,610 | 2,405E-04 | 7,099E-03 | 2,955 | 2,932E-04 | 6,939E-03 | 2,957 | 2,895E-04 | 7,016E-03 | 2,957 | 2,970E-04 | 6,379E-03 | 3,013 |
| Mo-95 |  | 2,989E-03 |  |  |  |  |  | 2,532E-03 |  |  | 2,704E-03 |  |  | 2,268E-03 |  |  | 2,988E-03 |  |
| Tc-99 |  | 6,383E-03 |  |  |  |  |  | 5,973E-03 |  |  | 5,725E-03 |  |  | 5,413E-03 |  |  | 5,883E-03 |  |
| Ru-101 |  | 2,198E-03 |  |  |  |  |  | 2,173E-03 |  |  | 2,070E-03 |  |  | 2,409E-03 |  |  | 2,150E-03 |  |
| Rh-103 |  | 1,056E-02 |  |  | 9,899E-03 |  |  | 1,077E-02 |  |  | 1,055E-02 |  |  | 1,057E-02 |  |  | 1,042E-02 |  |
| Ag-109 |  | 2,152E-03 |  |  | 2,064E-03 |  |  | 2,079E-03 |  |  | 2,164E-03 |  |  | 2,008E-03 |  |  | 2,151E-03 |  |
| Cs-133 |  | 8,516E-03 |  |  | 7,721E-03 |  |  | 8,303E-03 |  |  | 7,600E-03 |  |  | 6,119E-03 |  |  | 7,747E-03 |  |
| Sm-147 |  | 8,730E-04 |  |  | 1,123E-02 |  |  | 9,449E-04 |  |  | 8,804E-04 |  |  | 1,253E-02 |  |  | 8,832E-04 |  |
| Sm-149 |  | 2,520E-02 |  |  | 3,757E-03 |  |  | 2,617E-02 |  |  | 2,503E-02 |  |  | 3,536E-03 |  |  | 2,488E-02 |  |
| Sm-150 |  | 3,781E-03 |  |  | 6,705E-04 |  |  | 2,732E-03 |  |  | 2,446E-03 |  |  | 8,781E-04 |  |  | 2,942E-03 |  |
| Sm-151 |  | 2,093E-02 |  |  | 2,372E-02 |  |  | 2,128E-02 |  |  | 1,930E-02 |  |  | 2,501E-02 |  |  | 2,090E-02 |  |
| Sm-152 |  | 3,385E-03 |  |  | 3,172E-03 |  |  | 3,854E-03 |  |  | 3,763E-03 |  |  | 3,242E-03 |  |  | 3,470E-03 |  |
| Nd-143 |  | 1,247E-02 |  |  | 1,954E-02 |  |  | 1,232E-02 |  |  | 1,254E-02 |  |  | 2,127E-02 |  |  | 1,246E-02 |  |
| Nd-145 |  | 3,255E-03 |  |  | 3,817E-03 |  |  | 3,559E-03 |  |  | 3,483E-03 |  |  | 3,488E-03 |  |  | 3,357E-03 |  |
| Eu-153 |  | 4,349E-03 |  |  | 4,829E-03 |  |  | 4,185E-03 |  |  | 4,387E-03 |  |  | 4,454E-03 |  |  | 4,327E-03 |  |
| Gd-155 |  | 1,877E-03 |  |  | 1,798E-03 |  |  | 1,886E-03 |  |  | 1,882E-03 |  |  | 1,895E-03 |  |  | 1,876E-03 |  |
| O-16 |  | 4,876E-03 |  |  |  |  |  | 2,599E-03 |  |  | 2,535E-03 |  |  | 2,531E-03 |  |  | 5,086E-03 |  |

Table 9 Results of  CB1 calculations: reaction rates and ( averaged for CASE 4

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 3,823E-01 | 2,446E-01 | 2,434 | 3,751E-01 | 2,281E-01 | 2,421 | 3,821E-01 | 2,430E-01 | 2,439 | 3,804E-01 | 2,414E-01 | 2,434 | 3,796E-01 | 2,438E-01 | 2,436 | 3,824E-01 | 2,428E-01 | 2,434 |
| U-236 | 1,410E-04 | 2,719E-03 | 2,679 | 7,941E-04 | 8,875E-03 | 2,570 | 6,489E-04 | 9,869E-03 | 2,570 | 7,789E-04 | 9,198E-03 | 2,565 | 7,484E-04 | 6,768E-03 | 2,589 | 2,790E-04 | 2,684E-03 | 2,521 |
| U-238 | 6,624E-02 | 3,005E-01 | 2,826 | 7,318E-02 | 2,855E-01 | 2,803 | 6,802E-02 | 3,025E-01 | 2,791 | 6,795E-02 | 3,047E-01 | 2,791 | 7,098E-02 | 3,078E-01 | 2,791 | 6,737E-02 | 3,046E-01 | 2,832 |
| Pu-238 | 2,912E-04 | 1,889E-03 | 2,961 | 1,098E-04 | 1,843E-03 | 2,750 | 2,399E-04 | 1,892E-03 | 2,969 | 2,748E-04 | 1,921E-03 | 2,985 | 2,801E-04 | 1,922E-03 | 2,987 | 2,910E-04 | 2,058E-03 | 2,976 |
| Pu-239 | 4,417E-01 | 2,983E-01 | 2,864 | 4,417E-01 | 2,796E-01 | 2,865 | 4,415E-01 | 2,956E-01 | 2,873 | 4,413E-01 | 2,942E-01 | 2,872 | 4,392E-01 | 2,947E-01 | 2,873 | 4,406E-01 | 2,961E-01 | 2,864 |
| Pu-240 | 8,373E-04 | 7,051E-02 | 3,187 | 9,307E-04 | 6,680E-02 | 3,051 | 9,620E-04 | 6,922E-02 | 3,073 | 8,688E-04 | 7,006E-02 | 3,099 | 9,092E-04 | 6,941E-02 | 3,099 | 8,410E-04 | 7,137E-02 | 3,153 |
| Pu-241 | 1,081E-01 | 6,375E-02 | 2,924 | 1,077E-01 | 5,963E-02 | 2,918 | 1,061E-01 | 6,232E-02 | 2,934 | 1,080E-01 | 6,239E-02 | 2,947 | 1,078E-01 | 6,274E-02 | 2,947 | 1,078E-01 | 6,261E-02 | 2,939 |
| Pu-242 | 1,044E-04 | 3,089E-03 | 3,145 | 1,182E-04 | 3,009E-03 | 3,107 | 1,263E-04 | 2,964E-03 | 3,125 | 1,129E-04 | 3,541E-03 | 3,150 | 1,187E-04 | 2,707E-03 | 3,149 | 1,060E-04 | 3,179E-03 | 3,139 |
| Am-241 | 9,535E-05 | 3,598E-03 | 3,398 | 1,112E-04 | 3,450E-03 | 3,495 | 8,838E-05 | 3,525E-03 | 3,500 | 9,963E-05 | 3,558E-03 | 3,389 | 1,030E-04 | 3,593E-03 | 3,379 | 9,400E-05 | 3,510E-03 | 3,282 |
| Am-243 | 2,533E-05 | 1,115E-03 | 3,558 | 1,833E-05 | 1,002E-03 | 3,000 | 2,525E-05 | 1,107E-03 | 3,333 | 2,845E-05 | 1,150E-03 | 3,671 | 2,975E-05 | 1,149E-03 | 3,671 | 2,600E-05 | 1,077E-03 | 3,737 |
| Np-237 | 1,751E-04 | 5,016E-03 | 3,013 | 1,605E-04 | 5,056E-03 | 2,610 | 1,237E-04 | 5,443E-03 | 2,882 | 1,754E-04 | 5,396E-03 | 2,956 | 1,842E-04 | 5,405E-03 | 2,955 | 1,760E-04 | 4,969E-03 | 3,012 |
| O-16 |  | 4,911E-03 |  |  |  |  |  | 2,525E-03 |  |  | 2,504E-03 |  |  |  |  |  | 5,080E-03 |  |

Table10 Results of  CB1 calculations: reaction rates and ( averaged for CASE 5

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 2,811E-01 | 1,719E-01 | 2,434 | 2,757E-01 | 1,611E-01 | 2,421 | 2,809E-01 | 1,718E-01 | 2,439 | 2,799E-01 | 1,711E-01 | 2,434 | 2,796E-01 | 1,731E-01 | 2,436 | 2,810E-01 | 1,706E-01 | 2,434 |
| U-236 | 6,538E-04 | 9,418E-03 | 2,678 | 9,225E-04 | 9,809E-03 | 2,572 | 9,002E-04 | 1,091E-02 | 2,519 | 9,100E-04 | 9,929E-03 | 2,570 | 8,654E-04 | 7,503E-03 | 2,591 | 1,257E-03 | 9,704E-03 | 2,526 |
| U-238 | 6,882E-02 | 3,019E-01 | 2,826 | 7,506E-02 | 2,863E-01 | 2,805 | 6,848E-02 | 3,028E-01 | 2,791 | 7,078E-02 | 3,076E-01 | 2,794 | 7,226E-02 | 3,095E-01 | 2,792 | 7,030E-02 | 3,059E-01 | 2,833 |
| Pu-238 | 6,048E-04 | 3,840E-03 | 2,960 | 2,199E-04 | 3,738E-03 | 2,750 | 7,578E-04 | 3,971E-03 | 2,968 | 5,696E-04 | 3,932E-03 | 2,984 | 5,767E-04 | 3,945E-03 | 2,985 | 6,050E-04 | 4,173E-03 | 2,975 |
| Pu-239 | 4,968E-01 | 3,201E-01 | 2,865 | 4,966E-01 | 3,015E-01 | 2,865 | 4,973E-01 | 3,208E-01 | 2,873 | 4,958E-01 | 3,176E-01 | 2,873 | 4,947E-01 | 3,194E-01 | 2,873 | 4,953E-01 | 3,174E-01 | 2,865 |
| Pu-240 | 1,120E-03 | 8,297E-02 | 3,188 | 1,227E-03 | 7,909E-02 | 3,052 | 1,279E-03 | 8,135E-02 | 3,051 | 1,162E-03 | 8,206E-02 | 3,101 | 1,192E-03 | 8,232E-02 | 3,100 | 1,128E-03 | 8,378E-02 | 3,155 |
| Pu-241 | 1,503E-01 | 8,477E-02 | 2,923 | 1,497E-01 | 7,974E-02 | 2,918 | 1,498E-01 | 8,440E-02 | 2,934 | 1,502E-01 | 8,362E-02 | 2,947 | 1,501E-01 | 8,428E-02 | 2,947 | 1,498E-01 | 8,323E-02 | 2,939 |
| Pu-242 | 2,004E-04 | 5,299E-03 | 3,143 | 2,234E-04 | 5,288E-03 | 3,108 | 1,800E-04 | 5,495E-03 | 3,045 | 2,167E-04 | 6,086E-03 | 3,151 | 2,230E-04 | 4,376E-03 | 3,150 | 2,040E-04 | 5,559E-03 | 3,140 |
| Am-241 | 1,396E-04 | 5,063E-03 | 3,392 | 1,613E-04 | 4,879E-03 | 3,494 | 1,908E-04 | 5,296E-03 | 3,381 | 1,455E-04 | 5,042E-03 | 3,389 | 1,490E-04 | 5,106E-03 | 3,377 | 1,370E-04 | 4,931E-03 | 3,282 |
| Am-243 | 6,376E-05 | 2,660E-03 | 3,556 | 4,535E-05 | 2,416E-03 | 3,000 | 4,837E-05 | 2,596E-03 | 3,600 | 7,153E-05 | 2,747E-03 | 3,672 | 7,330E-05 | 2,755E-03 | 3,672 | 6,500E-05 | 2,545E-03 | 3,738 |
| Np-237 | 2,577E-04 | 7,137E-03 | 3,011 | 2,324E-04 | 7,220E-03 | 2,610 | 2,365E-04 | 8,051E-03 | 2,839 | 2,580E-04 | 7,698E-03 | 2,958 | 2,654E-04 | 7,756E-03 | 2,956 | 2,590E-04 | 7,057E-03 | 3,013 |
| O-16 |  | 4,928E-03 |  |  |  |  |  | 2,576E-03 |  |  | 2,589E-03 |  |  |  |  |  | 5,140E-03 |  |

Table11 Results of  CB1 calculations: reaction rates and ( averaged for CASE 6

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 3,815E-01 | 2,120E-01 | 2,434 | 3,761E-01 | 2,037E-01 | 2,422 | 3,793E-01 | 2,115E-01 | 2,439 | 3,798E-01 | 2,114E-01 | 2,434 | 3,806E-01 | 2,140E-01 | 2,436 | 3,814E-01 | 2,104E-01 | 2,434 |
| U-236 | 6,305E-04 | 8,013E-03 | 2,679 | 8,607E-04 | 8,565E-03 | 2,571 | 8,144E-04 | 9,154E-03 | 2,539 | 8,770E-04 | 8,602E-03 | 2,570 | 8,160E-04 | 6,447E-03 | 2,589 | 1,148E-03 | 8,371E-03 | 2,535 |
| U-238 | 7,592E-02 | 2,847E-01 | 2,826 | 7,927E-02 | 2,723E-01 | 2,805 | 7,710E-02 | 2,863E-01 | 2,794 | 7,797E-02 | 2,911E-01 | 2,791 | 7,730E-02 | 2,906E-01 | 2,792 | 7,715E-02 | 2,896E-01 | 2,832 |
| Pu-238 | 3,091E-04 | 1,597E-03 | 2,965 | 1,170E-04 | 1,617E-03 | 2,750 | 3,135E-04 | 1,461E-03 | 3,000 | 2,894E-04 | 1,632E-03 | 2,992 | 2,902E-04 | 1,643E-03 | 2,991 | 3,070E-04 | 1,740E-03 | 2,982 |
| Pu-239 | 4,501E-01 | 2,642E-01 | 2,864 | 4,519E-01 | 2,548E-01 | 2,865 | 4,496E-01 | 2,643E-01 | 2,872 | 4,496E-01 | 2,629E-01 | 2,872 | 4,492E-01 | 2,640E-01 | 2,872 | 4,488E-01 | 2,622E-01 | 2,864 |
| Pu-240 | 9,579E-04 | 6,492E-02 | 3,188 | 1,007E-03 | 6,281E-02 | 3,051 | 1,085E-03 | 6,381E-02 | 3,135 | 9,946E-04 | 6,535E-02 | 3,099 | 9,890E-04 | 6,428E-02 | 3,100 | 9,620E-04 | 6,592E-02 | 3,154 |
| Pu-241 | 8,988E-02 | 4,586E-02 | 2,924 | 9,004E-02 | 4,420E-02 | 2,918 | 9,109E-02 | 4,640E-02 | 2,934 | 8,973E-02 | 4,525E-02 | 2,947 | 9,012E-02 | 4,570E-02 | 2,947 | 8,955E-02 | 4,499E-02 | 2,939 |
| Pu-242 | 1,197E-04 | 2,949E-03 | 3,145 | 1,277E-04 | 2,927E-03 | 3,108 | 2,090E-04 | 3,062E-03 | 3,053 | 1,292E-04 | 3,279E-03 | 3,150 | 1,290E-04 | 2,577E-03 | 3,149 | 1,210E-04 | 3,036E-03 | 3,139 |
| Am-241 | 3,303E-04 | 1,026E-02 | 3,405 | 3,746E-04 | 1,010E-02 | 3,499 | 3,351E-04 | 1,024E-02 | 3,444 | 3,453E-04 | 1,026E-02 | 3,397 | 3,476E-04 | 1,032E-02 | 3,383 | 3,250E-04 | 1,001E-02 | 3,292 |
| Am-243 | 2,891E-05 | 1,037E-03 | 3,576 | 1,977E-05 | 9,349E-04 | 3,000 | 3,604E-05 | 1,115E-03 | 3,333 | 3,239E-05 | 1,068E-03 | 3,673 | 3,231E-05 | 1,068E-03 | 3,672 | 3,000E-05 | 1,004E-03 | 3,737 |
| Np-237 | 2,013E-04 | 4,610E-03 | 3,010 | 1,738E-04 | 4,755E-03 | 2,610 | 1,874E-04 | 5,086E-03 | 2,889 | 2,014E-04 | 4,966E-03 | 2,957 | 2,008E-04 | 4,989E-03 | 2,956 | 2,020E-04 | 4,557E-03 | 3,012 |
| Mo-95 |  | 2,359E-03 |  |  |  |  |  | 2,020E-03 |  |  | 2,207E-03 |  |  | 1,845E-03 |  |  | 2,381E-03 |  |
| Tc-99 |  | 4,936E-03 |  |  |  |  |  | 4,333E-03 |  |  | 4,508E-03 |  |  | 4,270E-03 |  |  | 4,578E-03 |  |
| Ru-101 |  | 1,662E-03 |  |  |  |  |  | 1,714E-03 |  |  | 1,565E-03 |  |  | 1,827E-03 |  |  | 1,627E-03 |  |
| Rh-103 |  | 9,192E-03 |  |  | 8,602E-03 |  |  | 9,298E-03 |  |  | 9,208E-03 |  |  | 9,171E-03 |  |  | 9,044E-03 |  |
| Ag-109 |  | 1,589E-03 |  |  | 1,520E-03 |  |  | 1,448E-03 |  |  | 1,575E-03 |  |  | 1,493E-03 |  |  | 1,599E-03 |  |
| Cs-133 |  | 6,723E-03 |  |  | 6,080E-03 |  |  | 6,820E-03 |  |  | 6,051E-03 |  |  | 4,856E-03 |  |  | 6,183E-03 |  |
| Sm-147 |  | 1,399E-03 |  |  | 9,212E-03 |  |  | 1,457E-03 |  |  | 1,406E-03 |  |  | 1,027E-02 |  |  | 1,414E-03 |  |
| Sm-149 |  | 2,521E-02 |  |  | 2,982E-03 |  |  | 2,611E-02 |  |  | 2,512E-02 |  |  | 2,811E-03 |  |  | 2,490E-02 |  |
| Sm-150 |  | 2,813E-03 |  |  | 1,075E-03 |  |  | 2,040E-03 |  |  | 1,803E-03 |  |  | 1,405E-03 |  |  | 2,189E-03 |  |
| Sm-151 |  | 1,634E-02 |  |  | 2,362E-02 |  |  | 1,655E-02 |  |  | 1,493E-02 |  |  | 2,490E-02 |  |  | 1,632E-02 |  |
| Sm-152 |  | 2,749E-03 |  |  | 2,358E-03 |  |  | 3,078E-03 |  |  | 3,118E-03 |  |  | 2,411E-03 |  |  | 2,826E-03 |  |
| Nd-143 |  | 1,027E-02 |  |  | 1,522E-02 |  |  | 1,030E-02 |  |  | 1,030E-02 |  |  | 1,653E-02 |  |  | 1,026E-02 |  |
| Nd-145 |  | 2,583E-03 |  |  | 3,090E-03 |  |  | 2,740E-03 |  |  | 2,800E-03 |  |  | 2,824E-03 |  |  | 2,671E-03 |  |
| Eu-153 |  | 3,092E-03 |  |  | 3,422E-03 |  |  | 3,066E-03 |  |  | 3,128E-03 |  |  | 3,162E-03 |  |  | 3,075E-03 |  |
| Gd-155 |  | 4,053E-03 |  |  | 3,865E-03 |  |  | 4,124E-03 |  |  | 4,039E-03 |  |  | 4,071E-03 |  |  | 4,050E-03 |  |
| O-16 |  | 4,864E-03 |  |  |  |  |  | 2,507E-03 |  |  | 2,505E-03 |  |  | 2,531E-03 |  |  | 5,027E-03 |  |

Table12 Results of  CB1 calculations: reaction rates and ( averaged for CASE 7

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 2,809E-01 | 1,458E-01 | 2,434 | 2,769E-01 | 1,403E-01 | 2,422 | 2,820E-01 | 1,468E-01 | 2,439 | 2,800E-01 | 1,454E-01 | 2,434 | 2,807E-01 | 1,476E-01 | 2,436 | 2,808E-01 | 1,447E-01 | 2,434 |
| U-236 | 7,643E-04 | 8,913E-03 | 2,680 | 1,019E-03 | 9,384E-03 | 2,573 | 9,017E-04 | 1,011E-02 | 2,547 | 1,047E-03 | 9,265E-03 | 2,574 | 9,656E-04 | 7,066E-03 | 2,591 | 1,393E-03 | 9,264E-03 | 2,536 |
| U-238 | 8,075E-02 | 2,840E-01 | 2,826 | 8,292E-02 | 2,701E-01 | 2,807 | 8,288E-02 | 2,884E-01 | 2,791 | 8,254E-02 | 2,914E-01 | 2,793 | 8,066E-02 | 2,887E-01 | 2,794 | 8,241E-02 | 2,892E-01 | 2,832 |
| Pu-238 | 6,493E-04 | 3,167E-03 | 2,965 | 2,388E-04 | 3,194E-03 | 2,750 | 6,711E-04 | 3,219E-03 | 2,964 | 6,091E-04 | 3,242E-03 | 2,990 | 6,042E-04 | 3,267E-03 | 2,989 | 6,450E-04 | 3,444E-03 | 2,982 |
| Pu-239 | 5,090E-01 | 2,785E-01 | 2,864 | 5,109E-01 | 2,691E-01 | 2,865 | 5,041E-01 | 2,755E-01 | 2,873 | 5,080E-01 | 2,767E-01 | 2,872 | 5,087E-01 | 2,790E-01 | 2,872 | 5,074E-01 | 2,764E-01 | 2,864 |
| Pu-240 | 1,314E-03 | 7,565E-02 | 3,189 | 1,357E-03 | 7,335E-02 | 3,053 | 1,519E-03 | 7,342E-02 | 3,050 | 1,359E-03 | 7,473E-02 | 3,101 | 1,329E-03 | 7,494E-02 | 3,102 | 1,323E-03 | 7,671E-02 | 3,156 |
| Pu-241 | 1,255E-01 | 5,978E-02 | 2,924 | 1,256E-01 | 5,773E-02 | 2,918 | 1,268E-01 | 5,986E-02 | 2,934 | 1,253E-01 | 5,895E-02 | 2,947 | 1,259E-01 | 5,973E-02 | 2,947 | 1,250E-01 | 5,863E-02 | 2,939 |
| Pu-242 | 2,352E-04 | 5,045E-03 | 3,141 | 2,459E-04 | 5,105E-03 | 3,109 | 1,729E-04 | 5,148E-03 | 3,231 | 2,534E-04 | 5,701E-03 | 3,150 | 2,481E-04 | 4,115E-03 | 3,151 | 2,390E-04 | 5,298E-03 | 3,140 |
| Am-241 | 4,669E-04 | 1,352E-02 | 3,405 | 5,234E-04 | 1,332E-02 | 3,499 | 5,764E-04 | 1,397E-02 | 3,500 | 4,839E-04 | 1,337E-02 | 3,398 | 4,855E-04 | 1,363E-02 | 3,382 | 4,610E-04 | 1,318E-02 | 3,293 |
| Am-243 | 7,426E-05 | 2,456E-03 | 3,556 | 4,985E-05 | 2,219E-03 | 3,000 | 5,352E-05 | 2,529E-03 | 3,250 | 8,288E-05 | 2,464E-03 | 3,675 | 8,144E-05 | 2,523E-03 | 3,674 | 7,600E-05 | 2,359E-03 | 3,738 |
| Np-237 | 3,034E-04 | 6,482E-03 | 3,011 | 2,564E-04 | 6,687E-03 | 2,610 | 2,964E-04 | 6,657E-03 | 2,880 | 3,025E-04 | 7,008E-03 | 2,957 | 2,960E-04 | 7,022E-03 | 2,958 | 3,050E-04 | 6,398E-03 | 3,013 |
| Mo-95 |  | 2,999E-03 |  |  |  |  |  | 2,658E-03 |  |  | 2,685E-03 |  |  | 2,271E-03 |  |  | 2,998E-03 |  |
| Tc-99 |  | 4,244E-03 |  |  |  |  |  | 5,487E-03 |  |  | 5,821E-03 |  |  | 5,411E-03 |  |  | 3,945E-03 |  |
| Ru-101 |  | 2,199E-03 |  |  |  |  |  | 2,229E-03 |  |  | 2,059E-03 |  |  | 2,404E-03 |  |  | 2,151E-03 |  |
| Rh-103 |  | 1,053E-02 |  |  | 9,856E-03 |  |  | 1,021E-02 |  |  | 1,041E-02 |  |  | 1,052E-02 |  |  | 1,041E-02 |  |
| Ag-109 |  | 2,162E-03 |  |  | 2,066E-03 |  |  | 1,972E-03 |  |  | 2,084E-03 |  |  | 2,006E-03 |  |  | 2,167E-03 |  |
| Cs-133 |  | 8,550E-03 |  |  | 7,722E-03 |  |  | 8,706E-03 |  |  | 7,637E-03 |  |  | 6,118E-03 |  |  | 7,770E-03 |  |
| Sm-147 |  | 1,485E-03 |  |  | 1,123E-02 |  |  | 1,470E-03 |  |  | 1,482E-03 |  |  | 1,252E-02 |  |  | 1,501E-03 |  |
| Sm-149 |  | 2,526E-02 |  |  | 3,755E-03 |  |  | 2,595E-02 |  |  | 2,506E-02 |  |  | 3,535E-03 |  |  | 2,493E-02 |  |
| Sm-150 |  | 3,784E-03 |  |  | 1,139E-03 |  |  | 2,491E-03 |  |  | 2,418E-03 |  |  | 1,489E-03 |  |  | 2,946E-03 |  |
| Sm-151 |  | 2,033E-02 |  |  | 2,375E-02 |  |  | 2,037E-02 |  |  | 1,865E-02 |  |  | 2,505E-02 |  |  | 2,029E-02 |  |
| Sm-152 |  | 3,402E-03 |  |  | 3,169E-03 |  |  | 3,665E-03 |  |  | 3,800E-03 |  |  | 3,240E-03 |  |  | 3,473E-03 |  |
| Nd-143 |  | 1,248E-02 |  |  | 1,895E-02 |  |  | 1,229E-02 |  |  | 1,252E-02 |  |  | 2,063E-02 |  |  | 1,247E-02 |  |
| Nd-145 |  | 3,262E-03 |  |  | 3,820E-03 |  |  | 3,211E-03 |  |  | 3,440E-03 |  |  | 3,488E-03 |  |  | 3,365E-03 |  |
| Eu-153 |  | 4,355E-03 |  |  | 4,827E-03 |  |  | 4,261E-03 |  |  | 4,382E-03 |  |  | 4,450E-03 |  |  | 4,331E-03 |  |
| Gd-155 |  | 6,704E-03 |  |  | 6,414E-03 |  |  | 6,923E-03 |  |  | 6,695E-03 |  |  | 6,760E-03 |  |  | 6,696E-03 |  |
| O-16 |  | 4,877E-03 |  |  |  |  |  | 2,572E-03 |  |  | 2,526E-03 |  |  | 2,516E-03 |  |  | 5,082E-03 |  |

Table13 Results of  CB1 calculations: reaction rates and ( averaged for CASE 8

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 3,899E-01 | 2,444E-01 | 2,434 | 3,831E-01 | 2,295E-01 | 2,421 | 3,903E-01 | 2,459E-01 | 2,439 | 3,883E-01 | 2,429E-01 | 2,434 | 3,876E-01 | 2,454E-01 | 2,436 | 3,899E-01 | 2,426E-01 | 2,434 |
| U-236 | 5,627E-04 | 8,406E-03 | 2,678 | 8,027E-04 | 8,881E-03 | 2,570 | 7,543E-04 | 9,474E-03 | 2,545 | 7,844E-04 | 8,937E-03 | 2,567 | 7,564E-04 | 6,769E-03 | 2,589 | 1,072E-03 | 8,720E-03 | 2,527 |
| U-238 | 6,753E-02 | 2,999E-01 | 2,826 | 7,385E-02 | 2,856E-01 | 2,803 | 6,853E-02 | 3,039E-01 | 2,794 | 6,887E-02 | 3,062E-01 | 2,792 | 7,167E-02 | 3,079E-01 | 2,790 | 6,863E-02 | 3,037E-01 | 2,832 |
| Pu-238 | 2,931E-04 | 1,865E-03 | 2,962 | 1,093E-04 | 1,829E-03 | 2,750 | 2,223E-04 | 1,865E-03 | 3,000 | 2,759E-04 | 1,904E-03 | 2,985 | 2,807E-04 | 1,910E-03 | 2,987 | 2,930E-04 | 2,031E-03 | 2,976 |
| Pu-239 | 4,494E-01 | 2,974E-01 | 2,864 | 4,500E-01 | 2,805E-01 | 2,865 | 4,488E-01 | 2,948E-01 | 2,873 | 4,493E-01 | 2,951E-01 | 2,872 | 4,474E-01 | 2,959E-01 | 2,873 | 4,482E-01 | 2,951E-01 | 2,864 |
| Pu-240 | 8,540E-04 | 7,010E-02 | 3,186 | 9,403E-04 | 6,682E-02 | 3,051 | 8,019E-04 | 6,854E-02 | 3,061 | 8,850E-04 | 6,954E-02 | 3,098 | 9,187E-04 | 6,945E-02 | 3,099 | 8,570E-04 | 7,093E-02 | 3,153 |
| Pu-241 | 9,081E-02 | 5,248E-02 | 2,923 | 9,064E-02 | 4,945E-02 | 2,918 | 8,984E-02 | 5,192E-02 | 2,934 | 9,087E-02 | 5,176E-02 | 2,947 | 9,070E-02 | 5,205E-02 | 2,947 | 9,051E-02 | 5,154E-02 | 2,939 |
| Pu-242 | 1,064E-04 | 3,073E-03 | 3,142 | 1,193E-04 | 3,011E-03 | 3,107 | 1,138E-04 | 3,024E-03 | 3,071 | 1,148E-04 | 3,417E-03 | 3,149 | 1,198E-04 | 2,707E-03 | 3,149 | 1,080E-04 | 3,161E-03 | 3,139 |
| Am-241 | 3,078E-04 | 1,135E-02 | 3,397 | 3,575E-04 | 1,096E-02 | 3,495 | 4,129E-04 | 1,169E-02 | 3,545 | 3,210E-04 | 1,130E-02 | 3,389 | 3,309E-04 | 1,141E-02 | 3,378 | 3,020E-04 | 1,105E-02 | 3,283 |
| Am-243 | 2,584E-05 | 1,107E-03 | 3,558 | 1,848E-05 | 1,001E-03 | 3,000 | 4,764E-05 | 1,113E-03 | 3,600 | 2,886E-05 | 1,125E-03 | 3,671 | 3,003E-05 | 1,146E-03 | 3,671 | 2,600E-05 | 1,068E-03 | 3,737 |
| Np-237 | 1,790E-04 | 5,010E-03 | 3,011 | 1,624E-04 | 5,078E-03 | 2,610 | 1,826E-04 | 5,411E-03 | 2,875 | 1,789E-04 | 5,403E-03 | 2,956 | 1,865E-04 | 5,431E-03 | 2,955 | 1,800E-04 | 4,963E-03 | 3,012 |
| O-16 |  | 4,907E-03 |  |  |  |  |  | 2,393E-03 |  |  | 2,517E-03 |  |  |  |  |  | 5,070E-03 |  |

Table14 Results of  CB1 calculations: reaction rates and ( averaged for CASE 9

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 2,892E-01 | 1,734E-01 | 2,434 | 2,839E-01 | 1,625E-01 | 2,421 | 2,880E-01 | 1,729E-01 | 2,439 | 2,878E-01 | 1,726E-01 | 2,434 | 2,879E-01 | 1,746E-01 | 2,436 | 2,892E-01 | 1,720E-01 | 2,434 |
| U-236 | 6,676E-04 | 9,440E-03 | 2,678 | 9,365E-04 | 9,817E-03 | 2,572 | 7,811E-04 | 1,026E-02 | 2,533 | 9,237E-04 | 9,891E-03 | 2,571 | 8,785E-04 | 7,504E-03 | 2,590 | 1,287E-03 | 9,720E-03 | 2,526 |
| U-238 | 7,024E-02 | 3,027E-01 | 2,826 | 7,603E-02 | 2,864E-01 | 2,805 | 7,095E-02 | 3,050E-01 | 2,792 | 7,195E-02 | 3,081E-01 | 2,795 | 7,326E-02 | 3,097E-01 | 2,792 | 7,169E-02 | 3,066E-01 | 2,832 |
| Pu-238 | 6,113E-04 | 3,824E-03 | 2,959 | 2,197E-04 | 3,718E-03 | 2,750 | 6,082E-04 | 3,685E-03 | 2,931 | 5,748E-04 | 3,910E-03 | 2,983 | 5,815E-04 | 3,930E-03 | 2,984 | 6,120E-04 | 4,154E-03 | 2,975 |
| Pu-239 | 5,097E-01 | 3,217E-01 | 2,865 | 5,097E-01 | 3,031E-01 | 2,865 | 5,102E-01 | 3,230E-01 | 2,873 | 5,093E-01 | 3,200E-01 | 2,873 | 5,079E-01 | 3,213E-01 | 2,873 | 5,082E-01 | 3,192E-01 | 2,865 |
| Pu-240 | 1,146E-03 | 8,315E-02 | 3,188 | 1,247E-03 | 7,923E-02 | 3,052 | 1,242E-03 | 8,117E-02 | 3,057 | 1,183E-03 | 8,166E-02 | 3,102 | 1,212E-03 | 8,251E-02 | 3,100 | 1,153E-03 | 8,394E-02 | 3,155 |
| Pu-241 | 1,274E-01 | 7,044E-02 | 2,923 | 1,270E-01 | 6,628E-02 | 2,918 | 1,271E-01 | 6,967E-02 | 2,934 | 1,272E-01 | 6,955E-02 | 2,946 | 1,273E-01 | 7,010E-02 | 2,947 | 1,269E-01 | 6,916E-02 | 2,939 |
| Pu-242 | 2,046E-04 | 5,306E-03 | 3,144 | 2,264E-04 | 5,291E-03 | 3,108 | 2,767E-04 | 5,108E-03 | 3,097 | 2,201E-04 | 5,936E-03 | 3,152 | 2,260E-04 | 4,378E-03 | 3,150 | 2,080E-04 | 5,564E-03 | 3,140 |
| Am-241 | 4,298E-04 | 1,529E-02 | 3,395 | 4,950E-04 | 1,475E-02 | 3,493 | 4,727E-04 | 1,607E-02 | 3,489 | 4,474E-04 | 1,526E-02 | 3,389 | 4,572E-04 | 1,543E-02 | 3,376 | 4,230E-04 | 1,487E-02 | 3,282 |
| Am-243 | 6,507E-05 | 2,657E-03 | 3,556 | 4,590E-05 | 2,412E-03 | 3,000 | 5,188E-05 | 2,809E-03 | 3,600 | 7,254E-05 | 2,715E-03 | 3,674 | 7,431E-05 | 2,748E-03 | 3,671 | 6,600E-05 | 2,542E-03 | 3,738 |
| Np-237 | 2,639E-04 | 7,177E-03 | 3,012 | 2,361E-04 | 7,256E-03 | 2,610 | 2,594E-04 | 7,799E-03 | 2,903 | 2,630E-04 | 7,723E-03 | 2,958 | 2,698E-04 | 7,799E-03 | 2,956 | 2,650E-04 | 7,099E-03 | 3,013 |
| O-16 |  | 4,930E-03 |  |  |  |  |  | 2,498E-03 |  |  | 2,600E-03 |  |  |  |  |  | 5,136E-03 |  |

Table15 Results of  CB1 calculations: reaction rates and ( averaged for CASE 10

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 3,832E-01 | 2,493E-01 | 2,434 | 3,758E-01 | 2,323E-01 | 2,421 | 3,826E-01 | 2,486E-01 | 2,439 | 3,815E-01 | 2,470E-01 | 2,434 | 3,804E-01 | 2,484E-01 | 2,436 | 3,830E-01 | 2,460E-01 | 2,434 |
| U-236 | 1,389E-04 | 2,732E-03 | 2,678 | 7,854E-04 | 8,920E-03 | 2,570 | 7,510E-04 | 9,430E-03 | 2,529 | 7,640E-04 | 9,140E-03 | 2,564 | 7,410E-04 | 6,812E-03 | 2,589 | 1,045E-03 | 8,749E-03 | 2,526 |
| U-238 | 6,517E-02 | 3,026E-01 | 2,826 | 7,240E-02 | 2,877E-01 | 2,803 | 6,504E-02 | 3,040E-01 | 2,793 | 6,674E-02 | 3,062E-01 | 2,790 | 7,030E-02 | 3,104E-01 | 2,790 | 6,657E-02 | 3,053E-01 | 2,832 |
| Pu-239 | 4,424E-01 | 3,040E-01 | 2,864 | 4,423E-01 | 2,846E-01 | 2,865 | 4,432E-01 | 3,024E-01 | 2,873 | 4,420E-01 | 3,006E-01 | 2,872 | 4,398E-01 | 3,002E-01 | 2,873 | 4,408E-01 | 2,996E-01 | 2,864 |
| Pu-240 | 8,242E-04 | 7,149E-02 | 3,187 |  |  |  | 9,179E-04 | 6,931E-02 | 3,066 | 8,552E-04 | 7,062E-02 | 3,098 | 9,006E-04 | 7,035E-02 | 3,099 | 8,310E-04 | 7,195E-02 | 3,153 |
| Pu-241 | 1,082E-01 | 6,496E-02 | 2,923 |  |  |  | 1,074E-01 | 6,389E-02 | 2,934 | 1,082E-01 | 6,382E-02 | 2,947 | 1,079E-01 | 6,390E-02 | 2,947 | 1,078E-01 | 6,338E-02 | 2,939 |
| O-16 |  | 4,918E-03 |  |  |  |  |  | 2,471E-03 |  |  | 2,517E-03 |  |  |  |  |  | 5,080E-03 |  |

Table16 Results of  CB1 calculations: reaction rates and ( averaged for CASE 11

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 3,911E-01 | 2,518E-01 | 2,434 | 3,840E-01 | 2,360E-01 | 2,421 | 3,920E-01 | 2,527E-01 | 2,439 | 3,896E-01 | 2,509E-01 | 2,434 | 3,886E-01 | 2,525E-01 | 2,436 | 3,912E-01 | 2,500E-01 | 2,434 |
| U-236 | 5,490E-04 | 8,464E-03 | 2,677 | 7,889E-04 | 8,945E-03 | 2,570 | 7,163E-04 | 9,772E-03 | 2,579 | 7,639E-04 | 8,827E-03 | 2,568 | 7,445E-04 | 6,837E-03 | 2,589 | 1,056E-03 | 8,777E-03 | 2,525 |
| U-238 | 6,582E-02 | 3,030E-01 | 2,826 | 7,262E-02 | 2,889E-01 | 2,803 | 6,602E-02 | 3,055E-01 | 2,792 | 6,756E-02 | 3,087E-01 | 2,791 | 7,057E-02 | 3,118E-01 | 2,790 | 6,690E-02 | 3,068E-01 | 2,832 |
| Pu-239 | 4,507E-01 | 3,063E-01 | 2,864 | 4,509E-01 | 2,885E-01 | 2,865 | 4,494E-01 | 3,060E-01 | 2,873 | 4,502E-01 | 3,045E-01 | 2,872 | 4,484E-01 | 3,045E-01 | 2,873 | 4,493E-01 | 3,038E-01 | 2,864 |
| Pu-240 | 8,331E-04 | 7,149E-02 | 3,187 |  |  |  | 9,058E-04 | 6,964E-02 | 3,088 | 8,645E-04 | 7,112E-02 | 3,098 | 9,048E-04 | 7,080E-02 | 3,099 | 8,360E-04 | 7,239E-02 | 3,153 |
| Pu-241 | 9,098E-02 | 5,404E-02 | 2,923 |  |  |  | 9,094E-02 | 5,383E-02 | 2,934 | 9,093E-02 | 5,338E-02 | 2,946 | 9,082E-02 | 5,355E-02 | 2,947 | 9,072E-02 | 5,309E-02 | 2,939 |
| O-16 |  | 4,916E-03 |  |  |  |  |  | 2,641E-03 |  |  | 2,537E-03 |  |  |  |  |  | 5,079E-03 |  |

Table17 Results of  CB1 calculations: mean values and standard deviations related to the reaction rates and ( averaged for CASE 1,2 and 3

|  | CASE 1 | CASE 2 | CASE 3 |
| --- | --- | --- | --- |
|  | mean value | standard deviation | mean value | standard deviation | mean value | standard deviation |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 9,397E-01 | 6,826E-01 | 2,433 | 0,0042 | 0,0189 | 0,006 | 3,734E-01 | 2,126E-01 | 2,433 | 3E-03 | 9E-04 | 0,006 | 2,729E-01 | 1,459E-01 | 2,433 | 2E-03 | 1E-03 | 0,006 |
| U-236 |  |  |  |  |  |  | 6,361E-04 | 5,908E-03 | 2,579 | 3E-04 | 3E-03 | 0,054 | 9,865E-04 | 8,789E-03 | 2,584 | 2E-04 | 1E-03 | 0,051 |
| U-238 | 6,027E-02 | 3,029E-01 | 2,801 | 0,0042 | 0,0060 | 0,019 | 7,568E-02 | 2,895E-01 | 2,806 | 2E-03 | 3E-03 | 0,019 | 8,001E-02 | 2,882E-01 | 2,808 | 1E-03 | 3E-03 | 0,017 |
| Pu-238 |  |  |  |  |  |  | 2,656E-04 | 1,701E-03 | 2,953 | 7E-05 | 7E-05 | 0,102 | 5,442E-04 | 3,265E-03 | 2,943 | 2E-04 | 2E-04 | 0,095 |
| Pu-239 |  |  |  |  |  |  | 4,415E-01 | 2,639E-01 | 2,868 | 1E-03 | 2E-03 | 0,005 | 4,953E-01 | 2,777E-01 | 2,869 | 2E-03 | 1E-03 | 0,004 |
| Pu-240 |  |  |  |  |  |  | 9,598E-04 | 6,470E-02 | 3,101 | 2E-05 | 1E-03 | 0,065 | 1,323E-03 | 7,513E-02 | 3,115 | 5E-05 | 1E-03 | 0,049 |
| Pu-241 |  |  |  |  |  |  | 1,072E-01 | 5,547E-02 | 2,935 | 5E-04 | 5E-04 | 0,012 | 1,482E-01 | 7,199E-02 | 2,935 | 5E-04 | 7E-04 | 0,012 |
| Pu-242 |  |  |  |  |  |  | 1,251E-04 | 3,037E-03 | 3,127 | 7E-06 | 3E-04 | 0,029 | 2,292E-04 | 5,062E-03 | 3,160 | 2E-05 | 6E-04 | 0,055 |
| Am-241 |  |  |  |  |  |  | 1,121E-04 | 3,271E-03 | 3,398 | 1E-05 | 8E-05 | 0,067 | 1,628E-04 | 4,480E-03 | 3,407 | 2E-05 | 5E-05 | 0,072 |
| Am-243 |  |  |  |  |  |  | 2,902E-05 | 1,051E-03 | 3,492 | 5E-06 | 2E-05 | 0,281 | 7,290E-05 | 2,486E-03 | 3,551 | 1E-05 | 8E-05 | 0,276 |
| Np-237 |  |  |  |  |  |  | 1,827E-04 | 4,839E-03 | 2,912 | 2E-05 | 2E-04 | 0,152 | 2,777E-04 | 6,779E-03 | 2,917 | 3E-05 | 3E-04 | 0,153 |
| Mo-95 |  |  |  |  |  |  |  | 2,175E-03 |  |  | 2E-04 |  |  | 2,696E-03 |  |  | 3E-04 |  |
| Tc-99 |  |  |  |  |  |  |  | 4,613E-03 |  |  | 3E-04 |  |  | 5,876E-03 |  |  | 4E-04 |  |
| Ru-101 |  |  |  |  |  |  |  | 1,719E-03 |  |  | 1E-04 |  |  | 2,200E-03 |  |  | 1E-04 |  |
| Rh-103 |  |  |  |  |  |  |  | 9,211E-03 |  |  | 6E-05 |  |  | 1,058E-02 |  |  | 1E-04 |  |
| Ag-109 |  |  |  |  |  |  |  | 1,594E-03 |  |  | 6E-05 |  |  | 2,111E-03 |  |  | 7E-05 |  |
| Cs-133 |  |  |  |  |  |  |  | 6,088E-03 |  |  | 8E-04 |  |  | 7,657E-03 |  |  | 9E-04 |  |
| Sm-147 |  |  |  |  |  |  |  | 2,672E-03 |  |  | 4E-03 |  |  | 3,221E-03 |  |  | 5E-03 |  |
| Sm-149 |  |  |  |  |  |  |  | 2,077E-02 |  |  | 1E-02 |  |  | 2,096E-02 |  |  | 1E-02 |  |
| Sm-150 |  |  |  |  |  |  |  | 1,915E-03 |  |  | 7E-04 |  |  | 2,556E-03 |  |  | 1E-03 |  |
| Sm-151 |  |  |  |  |  |  |  | 1,822E-02 |  |  | 4E-03 |  |  | 2,149E-02 |  |  | 2E-03 |  |
| Sm-152 |  |  |  |  |  |  |  | 2,885E-03 |  |  | 3E-04 |  |  | 3,543E-03 |  |  | 3E-04 |  |
| Nd-143 |  |  |  |  |  |  |  | 1,162E-02 |  |  | 3E-03 |  |  | 1,421E-02 |  |  | 4E-03 |  |
| Nd-145 |  |  |  |  |  |  |  | 2,747E-03 |  |  | 1E-04 |  |  | 3,429E-03 |  |  | 1E-04 |  |
| Eu-153 |  |  |  |  |  |  |  | 3,149E-03 |  |  | 7E-05 |  |  | 4,340E-03 |  |  | 1E-04 |  |
| Gd-155 |  |  |  |  |  |  |  | 1,132E-03 |  |  | 3E-06 |  |  | 1,883E-03 |  |  | 8E-06 |  |
| O-16 |  | 3,529E-03 |  |  | 0,0014 |  |  | 3,497E-03 |  |  | 1E-03 |  |  | 3,525E-03 |  |  | 1E-03 |  |

Table18 Results of  CB1 calculations: mean values and standard deviations related to the reaction rates and ( averaged for CASE 4,5 and 6

|  | CASE 4 | CASE 5 | CASE 6 |
| --- | --- | --- | --- |
|  | mean value | standard deviation | mean value | standard deviation | mean value | standard deviation |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 3,803E-01 | 2,400E-01 | 2,433 | 3E-03 | 7E-03 | 0,006 | 2,797E-01 | 1,693E-01 | 2,433 | 2E-03 | 5E-03 | 0,006 | 3,798E-01 | 2,119E-01 | 2,433 | 2E-03 | 1E-03 | 0,006 |
| U-236 | 5,651E-04 | 6,669E-03 | 2,582 | 3E-04 | 4E-03 | 0,053 | 9,182E-04 | 9,954E-03 | 2,576 | 2E-04 | 6E-04 | 0,057 | 8,578E-04 | 8,117E-03 | 2,580 | 2E-04 | 1E-03 | 0,053 |
| U-238 | 6,896E-02 | 2,995E-01 | 2,806 | 3E-03 | 8E-03 | 0,019 | 7,095E-02 | 3,009E-01 | 2,807 | 2E-03 | 8E-03 | 0,018 | 7,745E-02 | 2,885E-01 | 2,807 | 1E-03 | 3E-03 | 0,018 |
| Pu-238 | 2,478E-04 | 1,920E-03 | 2,938 | 7E-05 | 8E-05 | 0,093 | 5,556E-04 | 3,931E-03 | 2,937 | 2E-04 | 2E-04 | 0,092 | 2,710E-04 | 1,615E-03 | 2,947 | 8E-05 | 1E-04 | 0,097 |
| Pu-239 | 4,410E-01 | 2,928E-01 | 2,869 | 1E-03 | 8E-03 | 0,004 | 4,961E-01 | 3,155E-01 | 2,869 | 1E-03 | 8E-03 | 0,004 | 4,499E-01 | 2,635E-01 | 2,868 | 1E-03 | 9E-04 | 0,004 |
| Pu-240 | 8,915E-04 | 6,959E-02 | 3,110 | 5E-05 | 2E-03 | 0,051 | 1,185E-03 | 8,185E-02 | 3,108 | 6E-05 | 2E-03 | 0,055 | 9,993E-04 | 6,486E-02 | 3,121 | 5E-05 | 8E-04 | 0,048 |
| Pu-241 | 1,076E-01 | 6,214E-02 | 2,935 | 7E-04 | 2E-03 | 0,012 | 1,500E-01 | 8,315E-02 | 2,935 | 2E-04 | 2E-03 | 0,012 | 9,007E-02 | 4,564E-02 | 2,935 | 5E-04 | 5E-04 | 0,012 |
| Pu-242 | 1,144E-04 | 3,156E-03 | 3,136 | 8E-06 | 2E-04 | 0,017 | 2,079E-04 | 5,545E-03 | 3,123 | 2E-05 | 3E-04 | 0,041 | 1,393E-04 | 2,981E-03 | 3,124 | 3E-05 | 3E-04 | 0,038 |
| Am-241 | 9,859E-05 | 3,528E-03 | 3,407 | 8E-06 | 6E-05 | 0,081 | 1,539E-04 | 5,042E-03 | 3,386 | 2E-05 | 2E-04 | 0,067 | 3,430E-04 | 1,022E-02 | 3,403 | 2E-05 | 1E-04 | 0,069 |
| Am-243 | 2,552E-05 | 1,090E-03 | 3,495 | 4E-06 | 6E-05 | 0,281 | 6,122E-05 | 2,593E-03 | 3,540 | 1E-05 | 1E-04 | 0,272 | 2,990E-05 | 1,058E-03 | 3,499 | 6E-06 | 4E-05 | 0,283 |
| Np-237 | 1,658E-04 | 5,176E-03 | 2,905 | 2E-05 | 2E-04 | 0,152 | 2,515E-04 | 7,433E-03 | 2,898 | 1E-05 | 4E-04 | 0,154 | 1,944E-04 | 4,842E-03 | 2,906 | 1E-05 | 2E-04 | 0,152 |
| Mo-95 |  |  |  |  |  |  |  |  |  |  |  |  |  | 2,162E-03 |  |  | 2E-04 |  |
| Tc-99 |  |  |  |  |  |  |  |  |  |  |  |  |  | 4,525E-03 |  |  | 3E-04 |  |
| Ru-101 |  |  |  |  |  |  |  |  |  |  |  |  |  | 1,679E-03 |  |  | 1E-04 |  |
| Rh-103 |  |  |  |  |  |  |  |  |  |  |  |  |  | 9,183E-03 |  |  | 9E-05 |  |
| Ag-109 |  |  |  |  |  |  |  |  |  |  |  |  |  | 1,541E-03 |  |  | 7E-05 |  |
| Cs-133 |  |  |  |  |  |  |  |  |  |  |  |  |  | 6,126E-03 |  |  | 8E-04 |  |
| Sm-147 |  |  |  |  |  |  |  |  |  |  |  |  |  | 3,189E-03 |  |  | 4E-03 |  |
| Sm-149 |  |  |  |  |  |  |  |  |  |  |  |  |  | 2,083E-02 |  |  | 1E-02 |  |
| Sm-150 |  |  |  |  |  |  |  |  |  |  |  |  |  | 2,050E-03 |  |  | 5E-04 |  |
| Sm-151 |  |  |  |  |  |  |  |  |  |  |  |  |  | 1,781E-02 |  |  | 4E-03 |  |
| Sm-152 |  |  |  |  |  |  |  |  |  |  |  |  |  | 2,836E-03 |  |  | 3E-04 |  |
| Nd-143 |  |  |  |  |  |  |  |  |  |  |  |  |  | 1,153E-02 |  |  | 3E-03 |  |
| Nd-145 |  |  |  |  |  |  |  |  |  |  |  |  |  | 2,723E-03 |  |  | 1E-04 |  |
| Eu-153 |  |  |  |  |  |  |  |  |  |  |  |  |  | 3,105E-03 |  |  | 4E-05 |  |
| Gd-155 |  |  |  |  |  |  |  |  |  |  |  |  |  | 4,067E-03 |  |  | 3E-05 |  |
| O-16 |  | 3,755E-03 |  |  | 1E-03 |  |  | 3,808E-03 |  |  | 1E-03 |  |  | 3,487E-03 |  |  | 1E-03 |  |

Table19 Results of  CB1 calculations: mean values and standard deviations related to the reaction rates and ( averaged for CASE 7,8 and 9

|  | CASE 7 | CASE 8 | CASE 9 |
| --- | --- | --- | --- |
|  | mean value | standard deviation | mean value | standard deviation | mean value | standard deviation |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 2,802E-01 | 1,461E-01 | 2,433 | 2E-03 | 1E-03 | 0,006 | 3,882E-01 | 2,411E-01 | 2,433 | 3E-03 | 7E-03 | 0,006 | 2,877E-01 | 1,707E-01 | 2,433 | 2E-03 | 5E-03 | 0,006 |
| U-236 | 1,015E-03 | 8,923E-03 | 2,583 | 2E-04 | 1E-03 | 0,051 | 7,888E-04 | 8,883E-03 | 2,579 | 2E-04 | 4E-04 | 0,053 | 9,124E-04 | 9,826E-03 | 2,578 | 2E-04 | 3E-04 | 0,055 |
| U-238 | 8,203E-02 | 2,883E-01 | 2,807 | 1E-03 | 3E-03 | 0,018 | 6,984E-02 | 2,998E-01 | 2,806 | 2E-03 | 8E-03 | 0,018 | 7,235E-02 | 3,018E-01 | 2,807 | 2E-03 | 9E-03 | 0,018 |
| Pu-238 | 5,696E-04 | 3,268E-03 | 2,940 | 2E-04 | 1E-04 | 0,094 | 2,457E-04 | 1,899E-03 | 2,943 | 7E-05 | 8E-05 | 0,095 | 5,346E-04 | 3,858E-03 | 2,930 | 2E-04 | 2E-04 | 0,090 |
| Pu-239 | 5,080E-01 | 2,772E-01 | 2,869 | 2E-03 | 1E-03 | 0,004 | 4,488E-01 | 2,926E-01 | 2,869 | 9E-04 | 7E-03 | 0,004 | 5,092E-01 | 3,174E-01 | 2,869 | 9E-04 | 8E-03 | 0,004 |
| Pu-240 | 1,367E-03 | 7,509E-02 | 3,108 | 8E-05 | 1E-03 | 0,055 | 8,761E-04 | 6,919E-02 | 3,108 | 5E-05 | 2E-03 | 0,053 | 1,197E-03 | 8,183E-02 | 3,109 | 4E-05 | 2E-03 | 0,054 |
| Pu-241 | 1,257E-01 | 5,939E-02 | 2,935 | 6E-04 | 6E-04 | 0,012 | 9,056E-02 | 5,143E-02 | 2,935 | 4E-04 | 1E-03 | 0,012 | 1,272E-01 | 6,902E-02 | 2,935 | 2E-04 | 2E-03 | 0,012 |
| Pu-242 | 2,324E-04 | 5,062E-03 | 3,154 | 3E-05 | 6E-04 | 0,041 | 1,137E-04 | 3,137E-03 | 3,126 | 6E-06 | 2E-04 | 0,031 | 2,270E-04 | 5,441E-03 | 3,132 | 3E-05 | 3E-04 | 0,023 |
| Am-241 | 4,995E-04 | 1,353E-02 | 3,413 | 4E-05 | 3E-04 | 0,078 | 3,387E-04 | 1,127E-02 | 3,414 | 4E-05 | 3E-04 | 0,093 | 4,542E-04 | 1,525E-02 | 3,404 | 3E-05 | 5E-04 | 0,079 |
| Am-243 | 6,966E-05 | 2,466E-03 | 3,482 | 1E-05 | 7E-05 | 0,294 | 2,948E-05 | 1,083E-03 | 3,539 | 1E-05 | 5E-05 | 0,271 | 6,262E-05 | 2,627E-03 | 3,540 | 1E-05 | 2E-04 | 0,272 |
| Np-237 | 2,933E-04 | 6,714E-03 | 2,905 | 2E-05 | 3E-04 | 0,152 | 1,783E-04 | 5,173E-03 | 2,903 | 8E-06 | 2E-04 | 0,152 | 2,595E-04 | 7,411E-03 | 2,909 | 1E-05 | 3E-04 | 0,152 |
| Mo-95 |  | 2,722E-03 |  |  | 3E-04 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Tc-99 |  | 4,982E-03 |  |  | 8E-04 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ru-101 |  | 2,208E-03 |  |  | 1E-04 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Rh-103 |  | 1,042E-02 |  |  | 1E-04 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Ag-109 |  | 2,078E-03 |  |  | 9E-05 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cs-133 |  | 7,756E-03 |  |  | 1E-03 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sm-147 |  | 3,692E-03 |  |  | 5E-03 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sm-149 |  | 2,095E-02 |  |  | 1E-02 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sm-150 |  | 2,626E-03 |  |  | 8E-04 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sm-151 |  | 2,094E-02 |  |  | 2E-03 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Sm-152 |  | 3,516E-03 |  |  | 2E-04 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Nd-143 |  | 1,408E-02 |  |  | 4E-03 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Nd-145 |  | 3,353E-03 |  |  | 1E-04 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Eu-153 |  | 4,356E-03 |  |  | 7E-05 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Gd-155 |  | 6,756E-03 |  |  | 1E-04 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| O-16 |  | 3,514E-03 |  |  | 1E-03 |  |  | 3,722E-03 |  |  | 1E-03 |  |  | 3,791E-03 |  |  | 1E-03 |  |

Table 20 Results of  CB1 calculations: mean values and standard deviations related to the reaction rates and ( averaged for CASE 10 and 11

|  | CASE 10 | CASE 11 |  |
| --- | --- | --- | --- |
|  | mean value | standard deviation | mean value | standard deviation |  |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |  |
| U-235 | 3,821E-01 | 2,477E-01 | 2,435 | 3E-03 | 2E-03 | 0,002 | 3,905E-01 | 2,514E-01 | 2,435 | 3E-03 | 1E-03 | 0,002 |  |
| U-236 | 6,880E-04 | 7,513E-03 | 2,577 | 3E-04 | 3E-03 | 0,062 | 7,659E-04 | 8,960E-03 | 2,588 | 2E-04 | 6E-04 | 0,056 |  |
| U-238 | 6,677E-02 | 3,045E-01 | 2,806 | 3E-03 | 2E-03 | 0,021 | 6,738E-02 | 3,060E-01 | 2,806 | 3E-03 | 2E-03 | 0,021 |  |
| Pu-239 | 4,416E-01 | 3,016E-01 | 2,869 | 1E-03 | 2E-03 | 0,005 | 4,496E-01 | 3,052E-01 | 2,869 | 1E-03 | 1E-03 | 0,005 |  |
| Pu-240 | 8,658E-04 | 7,084E-02 | 3,120 | 4E-05 | 1E-03 | 0,048 | 8,688E-04 | 7,116E-02 | 3,125 | 4E-05 | 1E-03 | 0,043 |  |
| Pu-241 | 1,079E-01 | 6,401E-02 | 2,938 | 3E-04 | 7E-04 | 0,010 | 9,088E-02 | 5,359E-02 | 2,938 | 1E-04 | 4E-04 | 0,010 |  |
| O-16 |  | 3,746E-03 |  |  | 1E-03 |  |  | 3,793E-03 |  |  | 1E-03 |  |  |

Table 21 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%],   CASE  1

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,39 | 1,52 | 0,03 | -0,66 | -4,94 | -0,48 | 0,32 | 1,42 | 0,25 | 0,21 | 1,09 | 0,04 | -0,48 | 0,54 | 0,12 | 0,22 | 0,91 | 0,04 |
| U-238 | -6,14 | -0,14 | 0,69 | 10,34 | -3,38 | -0,09 | -4,95 | 0,80 | -0,39 | -3,24 | 1,56 | -0,55 | 7,47 | 3,57 | -0,62 | -3,47 | 1,15 | 0,96 |
| O-16 |  | 29,07 |  |  |  |  |  | -33,09 |  |  | -33,37 |  |  |  |  |  | 37,39 |  |

Table 22 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 2

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,32 | 0,31 | 0,04 | -1,24 | -4,31 | -0,48 | 0,70 | -0,01 | 0,24 | -0,05 | -0,45 | 0,04 | -0,07 | 0,55 | 0,12 | 0,34 | -0,40 | 0,04 |
| U-236 | -75,24 | -56,14 | 3,91 | 33,43 | 44,98 | -0,30 | 33,40 | 56,81 | -1,69 | 35,08 | 46,68 | -0,41 | 26,48 | 9,22 | 0,42 | -53,15 | -56,58 | -1,94 |
| U-238 | -1,99 | -1,31 | 0,72 | 3,45 | -5,81 | -0,05 | -2,17 | -0,56 | -0,53 | 0,25 | 0,88 | -0,53 | 0,80 | 0,55 | -0,52 | -0,34 | 0,44 | 0,91 |
| Pu-238 | 15,44 | -4,30 | 0,47 | -55,89 | -3,77 | -6,87 | 8,21 | 4,48 | 2,82 | 8,51 | -2,27 | 1,28 | 8,89 | -2,19 | 1,30 | 14,84 | 4,28 | 0,99 |
| Pu-239 | 0,20 | 0,84 | -0,15 | 0,47 | -3,40 | -0,12 | -0,49 | -0,75 | 0,16 | 0,00 | -0,27 | 0,14 | -0,13 | 0,08 | 0,14 | -0,05 | 0,10 | -0,16 |
| Pu-240 | -2,54 | 1,07 | 2,82 | 3,58 | -2,83 | -1,59 | -1,37 | -2,26 | -2,89 | 0,86 | -0,95 | -0,03 | 1,63 | -0,54 | -0,03 | -2,16 | 2,68 | 1,72 |
| Pu-241 | -0,09 | 0,90 | -0,37 | -0,11 | -3,45 | -0,56 | 0,88 | 1,15 | -0,02 | -0,21 | -0,88 | 0,41 | -0,02 | -0,19 | 0,41 | -0,43 | -0,98 | 0,14 |
| Pu-242 | -6,64 | -2,30 | 0,34 | 0,81 | -3,59 | -0,61 | 8,06 | 6,07 | -1,59 | 0,89 | 10,65 | 0,73 | 1,78 | -15,06 | 0,72 | -4,89 | 0,64 | 0,40 |
| Am-241 | -8,94 | -0,24 | 0,13 | 3,78 | -2,59 | 2,98 | 23,68 | 4,02 | 0,55 | -4,96 | -1,02 | -0,06 | -3,70 | -0,33 | -0,45 | -9,87 | -2,42 | -3,15 |
| Am-243 | -2,73 | -0,61 | 1,24 | -32,65 | -10,80 | -14,08 | 16,51 | 0,35 | -4,54 | 9,01 | 2,07 | 5,18 | 9,91 | 1,91 | 5,18 | -0,06 | -3,71 | 7,02 |
| Np-237 | 7,28 | -4,38 | 3,40 | -6,33 | -1,95 | -10,39 | -24,14 | 4,02 | 0,57 | 7,23 | 2,91 | 1,51 | 8,14 | 2,90 | 1,50 | 7,82 | -5,45 | 3,42 |
| Mo-95 |  | 8,57 |  |  |  |  |  | -3,52 |  |  | 0,88 |  |  | -15,41 |  |  | 9,48 |  |
| Tc-99 |  | 7,92 |  |  |  |  |  | 2,17 |  |  | -3,06 |  |  | -7,43 |  |  | 0,40 |  |
| Ru-101 |  | -3,11 |  |  |  |  |  | 9,57 |  |  | -7,81 |  |  | 6,43 |  |  | -5,09 |  |
| Rh-103 |  | 0,76 |  |  | -6,31 |  |  | -0,20 |  |  | 0,50 |  |  | -0,06 |  |  | -0,99 |  |
| Ag-109 |  | 0,64 |  |  | -4,74 |  |  | 4,50 |  |  | -0,50 |  |  | -6,28 |  |  | 1,64 |  |
| Cs-133 |  | 11,35 |  |  | -0,16 |  |  | 7,86 |  |  | -1,53 |  |  | -20,24 |  |  | 2,56 |  |
| Sm-147 |  | -70,91 |  |  | 244,41 |  |  | -71,82 |  |  | -70,76 |  |  | 284,05 |  |  | -70,56 |  |
| Sm-149 |  | 22,07 |  |  | -85,64 |  |  | 23,34 |  |  | 20,44 |  |  | -86,47 |  |  | 20,62 |  |
| Sm-150 |  | 47,56 |  |  | -68,93 |  |  | 2,98 |  |  | -6,06 |  |  | -59,38 |  |  | 14,89 |  |
| Sm-151 |  | -6,94 |  |  | 29,40 |  |  | -7,40 |  |  | -15,05 |  |  | 36,41 |  |  | -7,02 |  |
| Sm-152 |  | -3,78 |  |  | -18,26 |  |  | 13,28 |  |  | 7,69 |  |  | -16,43 |  |  | -0,77 |  |
| Nd-143 |  | -11,12 |  |  | 34,79 |  |  | -12,76 |  |  | -11,40 |  |  | 46,41 |  |  | -11,13 |  |
| Nd-145 |  | -5,35 |  |  | 12,42 |  |  | 4,22 |  |  | 0,60 |  |  | 2,77 |  |  | -2,25 |  |
| Eu-153 |  | -1,21 |  |  | 8,67 |  |  | 3,91 |  |  | -1,43 |  |  | 0,45 |  |  | -1,72 |  |
| Gd-155 |  | 0,13 |  |  | -5,27 |  |  | 0,30 |  |  | -0,36 |  |  | -0,21 |  |  | 0,14 |  |
| O-16 |  | 39,23 |  |  |  |  |  | -27,66 |  |  | -28,33 |  |  | -27,26 |  |  | 44,02 |  |

Table 23 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 3

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,24 | -0,17 | 0,04 | -1,27 | -3,83 | -0,48 | 0,80 | 0,02 | 0,24 | -0,10 | -0,11 | 0,04 | 0,11 | 1,20 | 0,12 | 0,21 | -0,94 | 0,04 |
| U-236 | -24,47 | 1,00 | 3,68 | 1,25 | 6,79 | -0,41 | -12,96 | 9,21 | -1,35 | 2,75 | 4,17 | -0,36 | -4,14 | -19,50 | 0,30 | 37,56 | 5,11 | -1,86 |
| U-238 | -1,61 | -1,59 | 0,64 | 1,77 | -6,05 | -0,07 | 0,21 | -0,18 | -0,36 | 0,32 | 1,10 | -0,55 | -1,16 | 0,41 | -0,53 | 0,47 | 0,25 | 0,87 |
| Pu-238 | 17,88 | -1,80 | 0,76 | -56,29 | -0,80 | -6,55 | 1,33 | -7,15 | 1,26 | 10,08 | 0,70 | 1,62 | 9,95 | 1,46 | 1,59 | 17,06 | 6,78 | 1,33 |
| Pu-239 | 0,18 | 0,30 | -0,15 | 0,48 | -2,96 | -0,13 | -0,60 | -0,38 | 0,16 | 0,02 | -0,03 | 0,14 | 0,05 | 0,61 | 0,14 | -0,15 | -0,50 | -0,15 |
| Pu-240 | -3,40 | 0,57 | 2,38 | 0,38 | -2,34 | -1,98 | 7,91 | -1,62 | -0,86 | -0,41 | -0,76 | -0,44 | -1,73 | -0,20 | -0,42 | -2,75 | 2,02 | 1,33 |
| Pu-241 | -0,07 | 0,54 | -0,37 | -0,03 | -2,77 | -0,56 | 0,47 | 0,71 | -0,02 | -0,15 | -0,46 | 0,41 | 0,24 | 0,59 | 0,41 | -0,45 | -1,38 | 0,14 |
| Pu-242 | 0,08 | -0,49 | -0,58 | 5,41 | 0,84 | -1,61 | -20,88 | 2,52 | 3,39 | 7,51 | 11,97 | -0,29 | 6,20 | -18,57 | -0,29 | 1,68 | 4,57 | -0,62 |
| Am-241 | -7,21 | 0,28 | -0,13 | 4,35 | -1,18 | 2,71 | 18,17 | 0,36 | 1,76 | -3,61 | 0,17 | -0,28 | -3,22 | 1,23 | -0,72 | -8,48 | -2,04 | -3,35 |
| Am-243 | -0,68 | -1,14 | 0,13 | -32,78 | -10,42 | -15,53 | 11,67 | 2,60 | 3,25 | 10,72 | 1,62 | 3,46 | 9,57 | 1,93 | 3,45 | 1,51 | -5,01 | 5,24 |
| Np-237 | 6,16 | -4,65 | 3,19 | -9,56 | -1,49 | -10,53 | -13,39 | 4,71 | 1,30 | 5,59 | 2,35 | 1,37 | 4,26 | 3,49 | 1,38 | 6,95 | -5,91 | 3,28 |
| Mo-95 |  | 10,86 |  |  |  |  |  | -6,10 |  |  | 0,30 |  |  | -15,87 |  |  | 10,81 |  |
| Tc-99 |  | 8,65 |  |  |  |  |  | 1,66 |  |  | -2,57 |  |  | -7,87 |  |  | 0,13 |  |
| Ru-101 |  | -0,07 |  |  |  |  |  | -1,23 |  |  | -5,93 |  |  | 9,51 |  |  | -2,28 |  |
| Rh-103 |  | -0,11 |  |  | -6,40 |  |  | 1,84 |  |  | -0,22 |  |  | -0,05 |  |  | -1,46 |  |
| Ag-109 |  | 1,95 |  |  | -2,20 |  |  | -1,50 |  |  | 2,53 |  |  | -4,88 |  |  | 1,90 |  |
| Cs-133 |  | 11,22 |  |  | 0,83 |  |  | 8,44 |  |  | -0,75 |  |  | -20,09 |  |  | 1,18 |  |
| Sm-147 |  | -72,90 |  |  | 248,71 |  |  | -70,67 |  |  | -72,67 |  |  | 288,82 |  |  | -72,58 |  |
| Sm-149 |  | 20,21 |  |  | -82,08 |  |  | 24,84 |  |  | 19,38 |  |  | -83,13 |  |  | 18,69 |  |
| Sm-150 |  | 47,94 |  |  | -73,76 |  |  | 6,89 |  |  | -4,28 |  |  | -65,65 |  |  | 15,09 |  |
| Sm-151 |  | -2,57 |  |  | 10,39 |  |  | -0,96 |  |  | -10,17 |  |  | 16,42 |  |  | -2,72 |  |
| Sm-152 |  | -4,46 |  |  | -10,48 |  |  | 8,79 |  |  | 6,21 |  |  | -8,48 |  |  | -2,06 |  |
| Nd-143 |  | -12,27 |  |  | 37,47 |  |  | -13,31 |  |  | -11,76 |  |  | 49,69 |  |  | -12,35 |  |
| Nd-145 |  | -5,05 |  |  | 11,34 |  |  | 3,80 |  |  | 1,58 |  |  | 1,75 |  |  | -2,07 |  |
| Eu-153 |  | 0,20 |  |  | 11,26 |  |  | -3,58 |  |  | 1,08 |  |  | 2,62 |  |  | -0,31 |  |
| Gd-155 |  | -0,33 |  |  | -4,55 |  |  | 0,14 |  |  | -0,04 |  |  | 0,63 |  |  | -0,41 |  |
| O-16 |  | 38,31 |  |  |  |  |  | -26,28 |  |  | -28,10 |  |  | -28,20 |  |  | 44,27 |  |

Table 24 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 4

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,51 | 1,91 | 0,04 | -1,37 | -4,96 | -0,48 | 0,46 | 1,26 | 0,24 | 0,02 | 0,60 | 0,04 | -0,18 | 1,60 | 0,12 | 0,55 | 1,19 | 0,04 |
| U-236 | -75,04 | -59,22 | 3,75 | 40,53 | 33,08 | -0,47 | 14,84 | 47,99 | -0,48 | 37,85 | 37,92 | -0,67 | 32,45 | 1,48 | 0,26 | -50,62 | -59,76 | -2,38 |
| U-238 | -3,94 | 0,33 | 0,73 | 6,13 | -4,69 | -0,08 | -1,36 | 0,99 | -0,52 | -1,46 | 1,70 | -0,51 | 2,94 | 2,74 | -0,54 | -2,31 | 1,67 | 0,92 |
| Pu-238 | 17,51 | -1,63 | 0,79 | -55,70 | -4,06 | -6,40 | -3,18 | -1,48 | 1,05 | 10,90 | 0,00 | 1,59 | 13,02 | 0,07 | 1,68 | 17,44 | 7,17 | 1,30 |
| Pu-239 | 0,16 | 1,90 | -0,15 | 0,16 | -4,50 | -0,13 | 0,11 | 0,97 | 0,15 | 0,07 | 0,50 | 0,13 | -0,41 | 0,68 | 0,14 | -0,10 | 1,13 | -0,15 |
| Pu-240 | -6,08 | 1,32 | 2,47 | 4,40 | -4,01 | -1,92 | 7,91 | -0,53 | -1,20 | -2,54 | 0,67 | -0,37 | 1,99 | -0,26 | -0,36 | -5,67 | 2,56 | 1,37 |
| Pu-241 | 0,49 | 2,58 | -0,38 | 0,13 | -4,04 | -0,56 | -1,37 | 0,29 | -0,02 | 0,35 | 0,40 | 0,41 | 0,21 | 0,96 | 0,41 | 0,20 | 0,76 | 0,13 |
| Pu-242 | -8,78 | -2,15 | 0,29 | 3,34 | -4,66 | -0,93 | 10,39 | -6,09 | -0,34 | -1,33 | 12,19 | 0,45 | 3,73 | -14,24 | 0,41 | -7,35 | 0,72 | 0,11 |
| Am-241 | -3,29 | 1,97 | -0,26 | 12,82 | -2,22 | 2,58 | -10,36 | -0,08 | 2,72 | 1,05 | 0,85 | -0,53 | 4,44 | 1,83 | -0,84 | -4,66 | -0,52 | -3,67 |
| Am-243 | -0,74 | 2,26 | 1,81 | -28,18 | -8,07 | -14,16 | -1,04 | 1,54 | -4,63 | 11,48 | 5,52 | 5,03 | 16,58 | 5,36 | 5,04 | 1,90 | -1,25 | 6,92 |
| Np-237 | 5,59 | -3,09 | 3,72 | -3,22 | -2,32 | -10,15 | -25,39 | 5,16 | -0,78 | 5,78 | 4,25 | 1,78 | 11,08 | 4,44 | 1,74 | 6,16 | -4,00 | 3,69 |
| O-16 |  | 30,78 |  |  |  |  |  | -32,76 |  |  | -33,30 |  |  |  |  |  | 35,28 |  |

Table 25 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 5

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,49 | 1,54 | 0,04 | -1,44 | -4,85 | -0,48 | 0,43 | 1,48 | 0,25 | 0,07 | 1,06 | 0,04 | -0,03 | 2,24 | 0,12 | 0,48 | 0,76 | 0,04 |
| U-236 | -28,79 | -5,38 | 3,95 | 0,47 | -1,46 | -0,14 | -1,96 | 9,60 | -2,21 | -0,89 | -0,25 | -0,24 | -5,74 | -24,62 | 0,57 | 36,90 | -2,51 | -1,93 |
| U-238 | -3,00 | 0,33 | 0,70 | 5,79 | -4,85 | -0,08 | -3,48 | 0,63 | -0,56 | -0,24 | 2,24 | -0,46 | 1,85 | 2,86 | -0,52 | -0,92 | 1,65 | 0,92 |
| Pu-238 | 8,85 | -2,30 | 0,78 | -60,42 | -4,91 | -6,36 | 36,38 | 1,03 | 1,06 | 2,52 | 0,03 | 1,59 | 3,79 | 0,35 | 1,63 | 8,88 | 6,16 | 1,30 |
| Pu-239 | 0,15 | 1,46 | -0,15 | 0,10 | -4,43 | -0,13 | 0,24 | 1,68 | 0,15 | -0,05 | 0,66 | 0,14 | -0,27 | 1,23 | 0,14 | -0,17 | 0,62 | -0,15 |
| Pu-240 | -5,44 | 1,37 | 2,58 | 3,58 | -3,38 | -1,79 | 7,95 | -0,61 | -1,83 | -1,93 | 0,26 | -0,22 | 0,64 | 0,57 | -0,24 | -4,80 | 2,36 | 1,51 |
| Pu-241 | 0,20 | 1,94 | -0,38 | -0,19 | -4,10 | -0,56 | -0,10 | 1,50 | -0,02 | 0,14 | 0,56 | 0,41 | 0,07 | 1,36 | 0,41 | -0,13 | 0,09 | 0,14 |
| Pu-242 | -3,63 | -4,45 | 0,64 | 7,47 | -4,63 | -0,48 | -13,43 | -0,91 | -2,49 | 4,21 | 9,75 | 0,91 | 7,26 | -21,09 | 0,86 | -1,88 | 0,24 | 0,56 |
| Am-241 | -9,30 | 0,41 | 0,17 | 4,83 | -3,24 | 3,20 | 24,02 | 5,03 | -0,14 | -5,44 | 0,00 | 0,10 | -3,16 | 1,26 | -0,26 | -10,95 | -2,20 | -3,07 |
| Am-243 | 4,15 | 2,59 | 0,45 | -25,92 | -6,81 | -15,24 | -20,98 | 0,13 | 1,71 | 16,84 | 5,95 | 3,75 | 19,74 | 6,28 | 3,73 | 6,18 | -1,85 | 5,60 |
| Np-237 | 2,47 | -3,97 | 3,91 | -7,60 | -2,87 | -9,93 | -5,97 | 8,32 | -2,03 | 2,60 | 3,57 | 2,07 | 5,52 | 4,35 | 2,01 | 2,98 | -5,05 | 3,97 |
| O-16 |  | 29,41 |  |  |  |  |  | -32,36 |  |  | -32,02 |  |  |  |  |  | 34,97 |  |

Table 26 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 6

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,46 | 0,08 | 0,04 | -0,97 | -3,88 | -0,48 | -0,13 | -0,18 | 0,24 | 0,01 | -0,23 | 0,04 | 0,20 | 0,99 | 0,12 | 0,43 | -0,68 | 0,04 |
| U-236 | -26,49 | -1,29 | 3,84 | 0,34 | 5,51 | -0,38 | -5,06 | 12,77 | -1,61 | 2,25 | 5,97 | -0,41 | -4,87 | -20,57 | 0,33 | 33,84 | 3,13 | -1,77 |
| U-238 | -1,98 | -1,31 | 0,70 | 2,34 | -5,60 | -0,06 | -0,45 | -0,75 | -0,45 | 0,67 | 0,91 | -0,54 | -0,20 | 0,76 | -0,53 | -0,39 | 0,39 | 0,89 |
| Pu-238 | 14,05 | -1,07 | 0,63 | -56,82 | 0,12 | -6,67 | 15,67 | -9,52 | 1,81 | 6,77 | 1,07 | 1,52 | 7,06 | 1,78 | 1,50 | 13,27 | 7,74 | 1,21 |
| Pu-239 | 0,05 | 0,25 | -0,15 | 0,45 | -3,30 | -0,12 | -0,06 | 0,30 | 0,13 | -0,06 | -0,24 | 0,14 | -0,15 | 0,18 | 0,14 | -0,24 | -0,49 | -0,15 |
| Pu-240 | -4,15 | 0,10 | 2,14 | 0,81 | -3,16 | -2,25 | 8,58 | -1,61 | 0,44 | -0,47 | 0,77 | -0,70 | -1,04 | -0,88 | -0,69 | -3,73 | 1,63 | 1,05 |
| Pu-241 | -0,20 | 0,48 | -0,37 | -0,03 | -3,15 | -0,56 | 1,14 | 1,66 | -0,02 | -0,38 | -0,85 | 0,41 | 0,06 | 0,14 | 0,41 | -0,58 | -1,43 | 0,14 |
| Pu-242 | -14,08 | -1,06 | 0,67 | -8,31 | -1,80 | -0,53 | 50,08 | 2,72 | -2,27 | -7,19 | 10,02 | 0,84 | -7,38 | -13,55 | 0,81 | -13,11 | 1,86 | 0,48 |
| Am-241 | -3,69 | 0,44 | 0,05 | 9,22 | -1,22 | 2,81 | -2,30 | 0,20 | 1,20 | 0,66 | 0,36 | -0,19 | 1,35 | 1,01 | -0,60 | -5,24 | -2,02 | -3,27 |
| Am-243 | -3,31 | -2,04 | 2,22 | -33,88 | -11,65 | -14,25 | 20,52 | 5,37 | -4,73 | 8,31 | 0,94 | 5,00 | 8,05 | 0,88 | 4,97 | 0,32 | -5,15 | 6,80 |
| Np-237 | 3,51 | -4,79 | 3,59 | -10,63 | -1,80 | -10,18 | -3,62 | 5,05 | -0,57 | 3,56 | 2,57 | 1,77 | 3,27 | 3,04 | 1,74 | 3,89 | -5,87 | 3,66 |
| Mo-95 |  | 9,10 |  |  |  |  |  | -6,59 |  |  | 2,07 |  |  | -14,69 |  |  | 10,11 |  |
| Tc-99 |  | 9,09 |  |  |  |  |  | -4,25 |  |  | -0,38 |  |  | -5,64 |  |  | 1,18 |  |
| Ru-101 |  | -1,05 |  |  |  |  |  | 2,08 |  |  | -6,77 |  |  | 8,82 |  |  | -3,09 |  |
| Rh-103 |  | 0,10 |  |  | -6,33 |  |  | 1,26 |  |  | 0,27 |  |  | -0,13 |  |  | -1,51 |  |
| Ag-109 |  | 3,14 |  |  | -1,38 |  |  | -6,02 |  |  | 2,20 |  |  | -3,09 |  |  | 3,77 |  |
| Cs-133 |  | 9,73 |  |  | -0,76 |  |  | 11,32 |  |  | -1,23 |  |  | -20,74 |  |  | 0,92 |  |
| Sm-147 |  | -56,12 |  |  | 188,84 |  |  | -54,31 |  |  | -55,91 |  |  | 222,00 |  |  | -55,66 |  |
| Sm-149 |  | 21,04 |  |  | -85,69 |  |  | 25,35 |  |  | 20,58 |  |  | -86,50 |  |  | 19,53 |  |
| Sm-150 |  | 37,23 |  |  | -47,55 |  |  | -0,48 |  |  | -12,06 |  |  | -31,47 |  |  | 6,78 |  |
| Sm-151 |  | -8,24 |  |  | 32,65 |  |  | -7,06 |  |  | -16,18 |  |  | 39,84 |  |  | -8,36 |  |
| Sm-152 |  | -3,07 |  |  | -16,87 |  |  | 8,52 |  |  | 9,91 |  |  | -15,01 |  |  | -0,36 |  |
| Nd-143 |  | -10,96 |  |  | 31,98 |  |  | -10,66 |  |  | -10,69 |  |  | 43,33 |  |  | -11,02 |  |
| Nd-145 |  | -5,16 |  |  | 13,47 |  |  | 0,61 |  |  | 2,81 |  |  | 3,68 |  |  | -1,93 |  |
| Eu-153 |  | -0,39 |  |  | 10,22 |  |  | -1,25 |  |  | 0,75 |  |  | 1,85 |  |  | -0,96 |  |
| Gd-155 |  | -0,36 |  |  | -4,97 |  |  | 1,40 |  |  | -0,70 |  |  | 0,08 |  |  | -0,42 |  |
| O-16 |  | 39,49 |  |  |  |  |  | -28,10 |  |  | -28,15 |  |  | -27,41 |  |  | 44,17 |  |

Table 27 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 7

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,26 | -0,16 | 0,04 | -1,19 | -3,96 | -0,48 | 0,63 | 0,50 | 0,24 | -0,07 | -0,43 | 0,04 | 0,17 | 1,04 | 0,12 | 0,20 | -0,96 | 0,04 |
| U-236 | -24,71 | -0,12 | 3,73 | 0,42 | 5,16 | -0,41 | -11,18 | 13,30 | -1,41 | 3,13 | 3,82 | -0,36 | -4,88 | -20,82 | 0,30 | 37,22 | 3,82 | -1,85 |
| U-238 | -1,56 | -1,50 | 0,68 | 1,09 | -6,32 | -0,02 | 1,04 | 0,02 | -0,57 | 0,62 | 1,07 | -0,51 | -1,67 | 0,12 | -0,48 | 0,47 | 0,29 | 0,90 |
| Pu-238 | 14,00 | -3,08 | 0,84 | -58,07 | -2,25 | -6,46 | 17,82 | -1,50 | 0,82 | 6,94 | -0,78 | 1,71 | 6,07 | -0,02 | 1,67 | 13,24 | 5,38 | 1,43 |
| Pu-239 | 0,20 | 0,47 | -0,15 | 0,56 | -2,92 | -0,13 | -0,77 | -0,62 | 0,15 | 0,00 | -0,18 | 0,14 | 0,13 | 0,65 | 0,14 | -0,12 | -0,31 | -0,15 |
| Pu-240 | -3,84 | 0,74 | 2,60 | -0,76 | -2,32 | -1,79 | 11,12 | -2,22 | -1,88 | -0,56 | -0,48 | -0,24 | -2,76 | -0,20 | -0,22 | -3,21 | 2,16 | 1,53 |
| Pu-241 | -0,16 | 0,66 | -0,37 | -0,05 | -2,80 | -0,56 | 0,90 | 0,79 | -0,02 | -0,32 | -0,74 | 0,41 | 0,20 | 0,58 | 0,41 | -0,57 | -1,29 | 0,14 |
| Pu-242 | 1,20 | -0,32 | -0,39 | 5,82 | 0,85 | -1,42 | -25,61 | 1,71 | 2,45 | 9,03 | 12,63 | -0,11 | 6,73 | -18,69 | -0,10 | 2,83 | 4,68 | -0,44 |
| Am-241 | -6,53 | -0,09 | -0,24 | 4,78 | -1,62 | 2,52 | 15,39 | 3,22 | 2,55 | -3,12 | -1,22 | -0,43 | -2,81 | 0,68 | -0,90 | -7,71 | -2,60 | -3,51 |
| Am-243 | 6,61 | -0,41 | 2,13 | -28,44 | -10,01 | -13,84 | -23,17 | 2,55 | -6,66 | 18,98 | -0,10 | 5,54 | 16,91 | 2,30 | 5,51 | 9,10 | -4,35 | 7,34 |
| Np-237 | 3,44 | -3,44 | 3,66 | -12,58 | -0,40 | -10,15 | 1,06 | -0,84 | -0,85 | 3,15 | 4,39 | 1,80 | 0,94 | 4,59 | 1,82 | 3,99 | -4,70 | 3,72 |
| Mo-95 |  | 10,17 |  |  |  |  |  | -2,36 |  |  | -1,39 |  |  | -16,57 |  |  | 10,14 |  |
| Tc-99 |  | -14,81 |  |  |  |  |  | 10,15 |  |  | 16,86 |  |  | 8,62 |  |  | -20,81 |  |
| Ru-101 |  | -0,41 |  |  |  |  |  | 0,93 |  |  | -6,77 |  |  | 8,86 |  |  | -2,61 |  |
| Rh-103 |  | 1,12 |  |  | -5,38 |  |  | -1,99 |  |  | -0,03 |  |  | 0,95 |  |  | -0,05 |  |
| Ag-109 |  | 4,05 |  |  | -0,61 |  |  | -5,11 |  |  | 0,27 |  |  | -3,47 |  |  | 4,26 |  |
| Cs-133 |  | 10,24 |  |  | -0,44 |  |  | 12,25 |  |  | -1,54 |  |  | -21,12 |  |  | 0,18 |  |
| Sm-147 |  | -59,78 |  |  | 204,27 |  |  | -60,18 |  |  | -59,85 |  |  | 239,16 |  |  | -59,35 |  |
| Sm-149 |  | 20,57 |  |  | -82,07 |  |  | 23,89 |  |  | 19,64 |  |  | -83,12 |  |  | 19,01 |  |
| Sm-150 |  | 44,12 |  |  | -56,64 |  |  | -5,13 |  |  | -7,90 |  |  | -43,28 |  |  | 12,19 |  |
| Sm-151 |  | -2,91 |  |  | 13,43 |  |  | -2,71 |  |  | -10,91 |  |  | 19,63 |  |  | -3,09 |  |
| Sm-152 |  | -3,23 |  |  | -9,86 |  |  | 4,24 |  |  | 8,07 |  |  | -7,86 |  |  | -1,22 |  |
| Nd-143 |  | -11,34 |  |  | 34,59 |  |  | -12,70 |  |  | -11,06 |  |  | 46,55 |  |  | -11,45 |  |
| Nd-145 |  | -2,71 |  |  | 13,91 |  |  | -4,24 |  |  | 2,58 |  |  | 4,03 |  |  | 0,35 |  |
| Eu-153 |  | -0,01 |  |  | 10,82 |  |  | -2,18 |  |  | 0,61 |  |  | 2,16 |  |  | -0,57 |  |
| Gd-155 |  | -0,77 |  |  | -5,06 |  |  | 2,48 |  |  | -0,89 |  |  | 0,07 |  |  | -0,88 |  |
| O-16 |  | 38,76 |  |  |  |  |  | -26,82 |  |  | -28,13 |  |  | -28,42 |  |  | 44,60 |  |

Table 28 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 8

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,44 | 1,40 | 0,04 | -1,32 | -4,81 | -0,48 | 0,55 | 2,01 | 0,25 | 0,04 | 0,75 | 0,04 | -0,14 | 1,79 | 0,12 | 0,43 | 0,65 | 0,04 |
| U-236 | -28,66 | -5,38 | 3,85 | 1,76 | -0,03 | -0,36 | -4,37 | 6,65 | -1,33 | -0,55 | 0,60 | -0,49 | -4,10 | -23,80 | 0,37 | 35,91 | -1,84 | -2,03 |
| U-238 | -3,32 | 0,02 | 0,71 | 5,74 | -4,77 | -0,10 | -1,88 | 1,35 | -0,43 | -1,40 | 2,11 | -0,52 | 2,61 | 2,67 | -0,56 | -1,75 | 1,29 | 0,90 |
| Pu-238 | 19,28 | -1,79 | 0,63 | -55,51 | -3,68 | -6,56 | -9,53 | -1,79 | 1,93 | 12,29 | 0,28 | 1,41 | 14,23 | 0,59 | 1,48 | 19,24 | 6,97 | 1,12 |
| Pu-239 | 0,13 | 1,64 | -0,15 | 0,25 | -4,11 | -0,13 | -0,01 | 0,76 | 0,15 | 0,11 | 0,85 | 0,13 | -0,32 | 1,13 | 0,14 | -0,15 | 0,87 | -0,15 |
| Pu-240 | -2,53 | 1,32 | 2,52 | 7,32 | -3,42 | -1,85 | -8,47 | -0,93 | -1,51 | 1,01 | 0,52 | -0,32 | 4,86 | 0,39 | -0,29 | -2,18 | 2,52 | 1,45 |
| Pu-241 | 0,27 | 2,05 | -0,38 | 0,09 | -3,85 | -0,56 | -0,80 | 0,95 | -0,02 | 0,34 | 0,64 | 0,41 | 0,15 | 1,20 | 0,41 | -0,06 | 0,21 | 0,13 |
| Pu-242 | -6,41 | -2,05 | 0,51 | 4,96 | -4,03 | -0,62 | 0,11 | -3,60 | -1,76 | 0,95 | 8,92 | 0,74 | 5,38 | -13,69 | 0,72 | -5,00 | 0,75 | 0,41 |
| Am-241 | -9,12 | 0,73 | -0,51 | 5,55 | -2,73 | 2,35 | 21,92 | 3,72 | 3,82 | -5,21 | 0,26 | -0,75 | -2,30 | 1,27 | -1,06 | -10,83 | -1,97 | -3,85 |
| Am-243 | -12,34 | 2,25 | 0,53 | -37,29 | -7,57 | -15,24 | 61,62 | 2,80 | 1,71 | -2,09 | 3,87 | 3,71 | 1,89 | 5,84 | 3,72 | -11,79 | -1,35 | 5,57 |
| Np-237 | 0,43 | -3,16 | 3,72 | -8,88 | -1,84 | -10,10 | 2,44 | 4,60 | -0,97 | 0,39 | 4,45 | 1,81 | 4,63 | 4,98 | 1,80 | 0,98 | -4,06 | 3,74 |
| O-16 |  | 31,84 |  |  |  |  |  | -35,70 |  |  | -32,36 |  |  |  |  |  | 36,22 |  |

Table 29 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 9

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,55 | 1,57 | 0,04 | -1,32 | -4,81 | -0,48 | 0,12 | 1,31 | 0,25 | 0,05 | 1,13 | 0,04 | 0,07 | 2,33 | 0,12 | 0,52 | 0,80 | 0,04 |
| U-236 | -26,83 | -3,92 | 3,86 | 2,64 | -0,09 | -0,25 | -14,39 | 4,42 | -1,75 | 1,24 | 0,66 | -0,30 | -3,71 | -23,63 | 0,47 | 41,06 | -1,07 | -2,04 |
| U-238 | -2,92 | 0,30 | 0,68 | 5,08 | -5,09 | -0,08 | -1,94 | 1,07 | -0,54 | -0,55 | 2,11 | -0,43 | 1,25 | 2,63 | -0,54 | -0,91 | 1,61 | 0,90 |
| Pu-238 | 14,36 | -0,89 | 0,98 | -58,91 | -3,63 | -6,15 | 13,77 | -4,49 | 0,03 | 7,52 | 1,34 | 1,80 | 8,77 | 1,87 | 1,83 | 14,48 | 7,67 | 1,52 |
| Pu-239 | 0,11 | 1,36 | -0,14 | 0,11 | -4,50 | -0,13 | 0,20 | 1,76 | 0,14 | 0,03 | 0,82 | 0,14 | -0,26 | 1,21 | 0,14 | -0,19 | 0,55 | -0,14 |
| Pu-240 | -4,25 | 1,61 | 2,54 | 4,14 | -3,17 | -1,83 | 3,74 | -0,81 | -1,67 | -1,18 | -0,21 | -0,23 | 1,23 | 0,84 | -0,28 | -3,69 | 2,58 | 1,47 |
| Pu-241 | 0,18 | 2,05 | -0,38 | -0,14 | -3,97 | -0,56 | -0,04 | 0,94 | -0,02 | 0,06 | 0,77 | 0,41 | 0,11 | 1,56 | 0,41 | -0,17 | 0,21 | 0,14 |
| Pu-242 | -9,86 | -2,47 | 0,39 | -0,27 | -2,76 | -0,77 | 21,91 | -6,12 | -1,11 | -3,02 | 9,09 | 0,65 | -0,41 | -19,54 | 0,57 | -8,35 | 2,26 | 0,26 |
| Am-241 | -5,36 | 0,29 | -0,26 | 8,98 | -3,29 | 2,62 | 4,07 | 5,39 | 2,49 | -1,49 | 0,11 | -0,44 | 0,67 | 1,18 | -0,82 | -6,87 | -2,50 | -3,59 |
| Am-243 | 3,92 | 1,16 | 0,45 | -26,70 | -8,19 | -15,25 | -17,14 | 6,93 | 1,70 | 15,84 | 3,34 | 3,79 | 18,68 | 4,59 | 3,72 | 5,41 | -3,23 | 5,59 |
| Np-237 | 1,68 | -3,16 | 3,55 | -9,05 | -2,09 | -10,27 | -0,05 | 5,24 | -0,20 | 1,34 | 4,22 | 1,71 | 3,97 | 5,23 | 1,63 | 2,11 | -4,21 | 3,57 |
| O-16 |  | 30,05 |  |  |  |  |  | -34,11 |  |  | -31,43 |  |  |  |  |  | 35,49 |  |

Table 30 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 10

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,28 | 0,64 | -0,06 | -1,66 | -6,24 | -0,58 | 0,13 | 0,35 | 0,15 | -0,16 | -0,27 | -0,06 | -0,46 | 0,27 | 0,02 | 0,22 | -0,72 | -0,06 |
| U-236 | -79,81 | -63,63 | 3,91 | 14,16 | 18,73 | -0,27 | 9,16 | 25,52 | -1,88 | 11,05 | 21,66 | -0,50 | 7,71 | -9,32 | 0,46 | 51,89 | 16,45 | -1,99 |
| U-238 | -2,38 | -0,63 | 0,71 | 8,43 | -5,52 | -0,11 | -2,59 | -0,17 | -0,47 | -0,03 | 0,56 | -0,58 | 5,29 | 1,91 | -0,56 | -0,29 | 0,24 | 0,90 |
| Pu-239 | 0,18 | 0,77 | -0,18 | 0,15 | -5,65 | -0,15 | 0,35 | 0,25 | 0,13 | 0,08 | -0,34 | 0,11 | -0,42 | -0,49 | 0,11 | -0,19 | -0,67 | -0,17 |
| Pu-240 | -4,80 | 0,91 | 2,12 |  |  |  | 6,02 | -2,16 | -1,74 | -1,22 | -0,31 | -0,73 | 4,02 | -0,70 | -0,69 | -4,02 | 1,56 | 1,03 |
| Pu-241 | 0,32 | 1,48 | -0,49 |  |  |  | -0,47 | -0,19 | -0,13 | 0,24 | -0,30 | 0,30 | 0,00 | -0,18 | 0,30 | -0,09 | -0,99 | 0,02 |
| O-16 |  | 31,26 |  |  |  |  |  | -34,04 |  |  | -32,81 |  |  |  |  |  | 35,59 |  |

Table 31 Results of  CB1 calculations: relative differences from mean values, (value/mean value - 1)*100 [%], CASE 11

|  | WIMS/ABBN | CASMO4 | MONK7B | MCNP4B (CZ) | HELIOS 1.4 | TWODANT |
| --- | --- | --- | --- | --- | --- | --- |
|  | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( | production | absorption | ( |
| U-235 | 0,16 | 0,17 | -0,06 | -1,67 | -6,12 | -0,58 | 0,38 | 0,53 | 0,15 | -0,23 | -0,17 | -0,06 | -0,49 | 0,46 | 0,02 | 0,18 | -0,54 | -0,06 |
| U-236 | -28,33 | -5,53 | 3,47 | 2,99 | -0,17 | -0,69 | -6,48 | 9,06 | -0,34 | -0,27 | -1,49 | -0,75 | -2,80 | -23,69 | 0,04 | 37,87 | -2,04 | -2,42 |
| U-238 | -2,30 | -0,99 | 0,71 | 7,78 | -5,59 | -0,11 | -2,01 | -0,17 | -0,51 | 0,28 | 0,88 | -0,54 | 4,74 | 1,89 | -0,57 | -0,71 | 0,27 | 0,90 |
| Pu-239 | 0,24 | 0,37 | -0,18 | 0,30 | -5,45 | -0,15 | -0,04 | 0,28 | 0,13 | 0,14 | -0,22 | 0,11 | -0,27 | -0,21 | 0,11 | -0,07 | -0,44 | -0,18 |
| Pu-240 | -4,11 | 0,46 | 1,98 |  |  |  | 4,25 | -2,14 | -1,18 | -0,50 | -0,06 | -0,85 | 4,14 | -0,51 | -0,84 | -3,78 | 1,73 | 0,88 |
| Pu-241 | 0,11 | 0,85 | -0,49 |  |  |  | 0,07 | 0,45 | -0,13 | 0,06 | -0,39 | 0,30 | -0,06 | -0,07 | 0,30 | -0,18 | -0,92 | 0,02 |
| O-16 |  | 29,60 |  |  |  |  |  | -30,38 |  |  | -33,12 |  |  |  |  |  | 33,90 |  |

Fig. 1 -  4

Fig. 5 - 8

Fig. 9 - 11

Fig. 12

Fig.13  Relative differences from the average absoption rates - CASE 7 (CASMO: not included into evaluation)

Fig.14  Relative differences from the average absoption rates - CASE 7 (continued)

Fig.15  Relative differences from the average production rates - CASE 7

Fig.16  Relative differences from the average numbers  of neutrons per fission  - CASE 7

# Supplement of CB1 :  case12 and case 13

Using the VVER fuel assembly and operating history descriptions made in specification of CB1 (/1/, /2/), the isotopic inventory for the specified spent fuel was calculated by SAS2 (SCALE) and the resulting number densities for the specified benchmark isotopes (according to Cases 1-11) were given to the participants as input data. To complete the CB1, two additional cases (12 and 13) were calculated by the SCALE, MCNP /4/ and HELIOS /3/ methodologies using all the inventory isotopes available in the libraries. The results of these calculations are shown Table 1, below. About 200 isotopes in the KENO VI library and about 150 isotopes in the HELIOS 1.5 library were available for the calculations but only 95 of them were found in the MCNP library (which is understandable as the code was not designed for the spent fuel calculations).

| Multiplication factor resulting from | library / number of groups | case12: 30 GWd/tU, one-year cooling time, ‘all’ isotopes in library | case13: 30 GWd/tU, five-year cooling time, ‘all’ isotopes in library |
| --- | --- | --- | --- |
| HELIOS 1.5 | 190 groups 90 groups 35 groups | 1.05055 1.04824 1.04853 | 1.03436 1.03233 1.03297 |
| KENO VI (under SCALE4.3) | 44groupndf5 | 1.0498(0.0010 | 1.0329(0.0009 |
| MCNP4B | DLC-189 | 1.05387(0.00098 | 1.03762(0.00096 |
| ‘reasonable’ average | only HELIOS 90g, 35g and KENO 44g | 1.0489 | 1.0327 |

Table 1. Multiplication factors resulting from the supplementary CB1 calculations using all inventory isotopes available in the selected code library

Based on the results written in the last row of Table 1, the following, Table 2, /2/, could be completed in the VVER columns with the ‘total’ (k  (resulting from cases 12-13) and the ratio [%] of (k resulting from cases 2-11, /2/, to the total (k. (Note:  (ki=kcase 1 - kcase i , where case 1 is the case of fresh fuel, see /2/).

The results above indicate that if using the BUC calculational methodology proposed for the VVER in CB1, the reactivity decrease resulting from the calculations seems to reach up to 92 -93 % of the ‘real’ (calculated) value for the given spent fuel system.

Table 2  Reactivity loss according to different sets of selected nuclides

|  | PWR | VVER-440 (as the result of CB1) |
| --- | --- | --- |
|  | 30 GWd/t,1 year | 30 GWd/t,5 year | 40/1 | 40/5 | 30/1 | 30/5 | 40/1 | 40/5 |
|  | (k | Ratio [%] | (k | ratio [%] | (k | (k | (k | ratio [%] | (k | ratio [%] | (k | (k |
| Major Actinides | 0.1746 | 53.2 | 0.1815 | 50.2 | not calculated | 0.1630 | 47.7 | 0.1706 | 47.7 | not calculated |
| Minor Actinides | 0.0176 | 5.3 | 0.0279 | 7.7 |  | 0.0207 | 6.1 | 0.0318 | 8.9 |  |
| All Actinides | 0.1922 | 58.5 | 0.2094 | 57.9 | 0.2492 | 0.2721 | 0.1837 | 53.8 | 0.2024 | 56.6 | 0.2324 | 0.2558 |
| Major Fission Products | 0.1054 | 32.0 | 0.1161 | 32.2 | 0.1248 | 0.1417 | 0.1303 | 38.1 | 0.1325 | 37.0 | 0.1462 | 0.1498 |
| All Actinides+MajorFPs | 0.2976 | 90.5 | 0.3255 | 90.1 | 0.3740 | 0.4138 | 0.3140 | 91.9 | 0.3349 | 93.6 | 0.3786 | 0.4056 |
| Minor Fission Products | 0.0314 | 9.5 | 0.0357 | 9.9 | not calculated | - | - | - | - | not calculated |
| Total | 0.3290 | 100.0 | 0.3612 | 100.0 |  | 0.3416 | 100.0 | 35.78 | 100.0 |  |

References

/1/ L.Markova: Calculational Burnup Credit Benchmark Proposal (Proceedings of 6th AER Symposium on VVER Reactor Physics and Reactor Safety, Kirkkonummi, Finland, Sept. 23-26, 1996)

/2/ L.Markova : Continuation of the VVER Burnup Credit Benchmark: Evaluation of  CB1   Results, Overview of CB2 Results to Date, and Specification of CB3 (8th AER Symposium on VVER Reactor Physics and Reactor Safety, Bystrice nad Pernstejnem, Czech Republic, September 21-25, 1998)

/3/ E. Tinkova - HELIOS1.5 calculations of the CB1 case12 and case13, CB2 results by HELIOS1.5 and 190-group library , personal communication, 1999

/4/ L.Markova : Report on the continuation of the VVER BUC benchmark (4th meeting of AER Working Group E on ‘The Physical Problems on Spent Fuel, Radwaste and Decommissioning of Nuclear Power Plant’, Rheinsberg , Germany, April 20 - 21, 1999)