ATOMIC ENERGY RESEARCH (AER)

AER BENCHMARK BOOK

BUDAPEST, 1999

The research work reported in the present publication was sponsored by the following institutions:

- VTT;

- VUJE;

- IVO;

- AEKI;

- PA Rt;

- ŠKODA;

- UJV;

- IAE.

The material for the present publication was prepared by the authors of the test problems. The test problems were collected and submitted for review by a Benchmark Committee including:

P. Dařilek		(VUJE)

L. Korpás		(PA Rt)

J. Kyncl		(UJV)

L. Maiorov		(KI)

M. Makai		(AEKI)	- head

P. Siltanen		(IVO)

The compilation is based on benchmark specifications and benchmark solutions prepared by the authors. The staff of Reviewers of the test cases and solutions included:

P. Dařilek (VUJE)

N. Kolev (IAE)

L. Korpás (PA Rt)

J. Kyncl (UJV)

M. Makai (AEKI)

I. Pós (PA Rt)

P. Siltanen (IVO)

J. Svarny (ŠKODA)

Abbreviations used for orghanizations:

AEKI		-KFKI Atomic Energy Research Institute, Budapest, Hungary

DNPP		-NPP Dukovany, Czech Republic

DSR		-DSR GmbH, Berlin, Germany

EGP		-Energoprojekt Praha, Czech Republic

FZR		-Research Centre Rossendorf Inc., Germany

IAE		-Institute for Nuclear Research and Nuclear Energy, Sofia, Bulgaria

IBJ		-Institute of Atomic Energy, Swierk, Poland

IPPE		-Institute Obninsk, Russia

IVO		-Fortum Engineering Ltd, (formerly IVO Power Engineering Ltd), Finland

KAB		-Kraftwerkanlagenbau GmbH, Berlin, Germany

KI	-Russian Scientific Centre "Kurchatov Institute", Institute of Nuclear Reactors, Moscow, Russia

KNPP		-NPP Kozloduy, Bulgaria

NIS		-NIS Rheinsberg GmbH Ingenieurservice, Rheinsberg, Germany

PARt		-Paks Nuclear Power Plant Co., Paks, Hungary

SE		-Slovenské Elektrárne, Slovakia

Škoda		-ŠKODA JS a.s., Czech Republic

TUB		-Technical University Budapest, Hungary

TÜV		-TÜV Süddeutschland, Germany

UJV		-Nuclear Research Institute Řež plc., Czech Republic

VNIA	-All-Russia Scientific and Research Institute for the Operation of Nuclear Power Plants, Moscow, Russia

VTT		-Technical Research Centre of Finland, Espoo, Finland

VUJE		-Nuclear Power Plants Research Institute, Trnva, Slovakia

ABSTRACT

A compilation of VVER related benchmarks is presented. The test cases serve testing the calculational models used in design and operation of VVER-440 and VVER-1000 reactors. The tests do not include experimental tests, which have been used elsewhere. Most test specifications provide all input data needed to calculate the test, along with the specification of the data to be calculated and compared. Some specifications refer to nuclear data available at the user working with the test. Some tests have a reference solution, others serve only to compare the calculated results.

COPYRIGHT AND DISCLAIMER

By accessing or using the information you accept the following conditions. The tests and the solutions provided in the present volume can be copied and distributed freely for any non-commercial purpose. You are not allowed to incorporate them, however, into any commercial product. If you copy parts of the book for somebody else you may ask for refund of your expenses. In any other case you should contact the AER Secretariat at the following address:

e-mail: vidov@sunserv.kfki.hu

Fax: 36-1-395-9293

Mail: Dr. Vidovszky István, KFKI AEKI, H-1525 Budapest 114, POB 49, Hungary

Phone: 36-1-395-9159.

The information is supplied "as is" with no warrantee express or implied or statutory of merchantability or fitness for any particular purpose. In no event shall Atomic Energy Research, or any of its member organizations be liable for any loss of profit or any other commercial damage, included but not limited to special, consequential or other damages.

## TABLE OF CONTENTS

- Introduction

- Terminology

- VVER-440

- VVER-1000

- Terminology used in connection with calculation

- Test Cases

- Test Specifications

- DYN001		(in separate file DYN001.doc)

- DYN002		(in separate file DYN002.doc)

- DYN003		(in separate file DYN003.doc)

- DYN004		(in separate file DYN004.doc)

- DYN005		(in separate file DYN005.doc)

- HOM101		(in separate file HOM101.doc)

- FCM001		(in separate file FCM001.doc)

- FCM002		(in separate file FCM002.doc)

- FCM101		(in separate file FCM101.doc)

- BCR001		(in separate file BCR001.doc)

- TRO001		(in separate file TRO001.doc)

- KAB001		(in separate file KAB001.doc)

- FCM102		(in separate file FCM102.doc)

## I. Introduction

The interest in VVER type is explained by the following facts. According to a report [1] issued in 1994, 26 units of VVER-440 and 21 units of VVER-1000 have been operating in seven countries. In 1990, institutions of countries operating VVERs established the Atomic Energy Research (AER) cooperation to promote research leading to safer and more economic operation of VVER type nuclear reactors.

In 1998, the Scientific Council of AER decided on compiling a volume of VVER related benchmarks, in order to facilitate the validation and verification (V&V) process of VVER calculation programs and codes. The AER Scientific Council established a Benchmark Committee, which issued a Call for Benchmark. In response to the call, test problems were specified and submitted for review. The submitted tests were reviewed and collected. The present volume intends to collect the submitted test cases into a unified framework. All submitted cases have been utilized in V&V of VVER codes.

Ours is not the first benchmark collection. One of the best known collections is perhaps the Argonne Benchmark Problem Book [2], its volumes appeared between 1972 and 1985. The volumes of Argonne Benchmark Problem Book involve experimental and mathematical tests. That benchmark collection focuses on the V&V of basic nuclear library data and calculation methods, and has only a few tests devoted to such complex problems as, for example, the coarse-mesh calculation of a HTGR reactor. Since the late 70's, complex reactor physical calculations have been organized into large codes. Elements of such large codes as well as the full code should be tested, this gives rise to a broader range of tests in a benchmark collection. Since then, the calculation models underwent a considerable development, and further benchmarks have been used to verify the entire model. The benchmarks used in the present book, are so called mathematical benchmarks (see dynamics), or, operational measurements on a power plant.

Detailed experiments have been performed to learn neutron physical characteristics of lattices occurring in VVER cores. Experiments [3] performed on the ZR-6 critical facility have revealed several details concerning the spectral and spatial behavior of typical VVER lattices. Cores composed of real VVER-440 and VVER-1000 assemblies have been investigated on the LR-0 facility [4]. Measurements on simple periodic structures allowed us to verify nuclear libraries and to estimate the accuracy of the asymptotic codes. Those results are available elsewhere, including comparisons with a number of calculated results [5].

The present volume does not include all the tests being used in practice. The Benchmark Committee issued a Call for Benchmarks, and only tests submitted before 31 July 1999 are included into the present volume. The tight deadline must hinder some authors to submit their tests in an electronic and reconsidered form. Later on the Benchmark Book will be enlarged.

The tests included in the present Benchmark Problem Book do not claim an official acknowledgement from any national regulatory body or authority. At the same time, the tests included in the present volume do essentially contribute to the reliable V&V process of VVER calculation tools. The users of the tests should remember the following:

- Good performance of a test does not guarantee good performance in practical applications. There are a number of other circumstances that the user should consider when selecting a code, e.g. its user friendly input and output, robustness, portability, speed.

- Like the equations of physics in general, the equations of reactor physics are frequently continuous functions of the parameters. Thus, one may expect to get more or less the same accuracy if the parameters have been changed slightly. One should always ponder if the parameter change may bridge a drastic change in the model, or, if a large number of parameter changes.

- The test set is not complete. It requires a considerable amount of work to document the performed measurement or calculation in such a manner that it is useful for others. There have been a number of tests to verify parts of the calculation models but the restricted resources have set a limit to the number of tests. At the same time if a test has been selected to be included it meets the requirements.

Throughout the book, we have been utilizing some naming conventions. From the point of view of the reference solution, tests have been classified as follows.

1, Benchmark. It is a problem to test a given algorithm. The input to the algorithm is provided. The required output of the algorithm is specified. There is a reference solution, its error is known. With a benchmark, we get a trustworthy estimation for the maximum error of the algorithm.  The error may be even larger in other cases unless the test case is shown to be overly conservative.

2, Standard exercise. It is a problem to test a given algorithm. The input to the algorithm is provided. The required output of the algorithm is specified. There is a reference solution. With a standard exercise, we get an impression of the error of the algorithm. The comparison alone is inappropriate because the reference may fail, we have to analyze the nature of the differences.

3, Intercomparison. It is a problem to test a given algorithm. The input to the algorithm is provided. The required output of the algorithm is specified. An intercomparison is suitable to estimate the maximal effect of diverse approximations made in different algorithms. It is often impossible to declare which result is better.

Concerning the origin of test input data, cases are classified as mathematical, experimental or operational tests.

- A mathematical test provides all input data to solve a given equation. A good example is the solution of the diffusion equation without feed back.

- An experimental test is where the reference solution comes from measurements and the input fixes the experiment’s situation. The recommended procedure is given in Ref. [6].

- An operational test describes the operational state of a working unit. The reference distribution is obtained from the plant measurements. The recommended procedure is given in [7].

In Section 2, we give a short description of VVER types in order to allow the possible user for judging if a given test is useful for him/her or not. This section provides the terminology utilized in the tests. The tests are enlisted in section 3.

Although the test cases and the present work have been prepared with much care they may contain errors. The reviewers have verified that the given test can be performed but the text may be corrupted during subsequent steps of editing. The readers are encouraged to report bugs, typographic or other errors to the authors or to the AER Secretariat.

Finally, we remark that the tests are available via Internet at location: http://www.kfki.hu/~aekihp/. Look up the Atomic Energy Research section there and follow the instructions.

## II. Basic Data on VVERs

The present section provides basic data of VVER-440 as well as VVER-1000 core and fuel assembly.  There are different designs, the data in Table I. refer to VVER-440 model V213 and VVER-1000 model V320. Since a part of the possible readership may be unfamiliar with basic VVER features, some generally used terminology, concerning the characteristics of the power distribution, is also given. Table I. is a summary of block data, partly after [8]. In both VVER types, low enriched UO2 fuel is used collected in hexagonal assemblies. Both types are controlled by boric acid and by control assemblies.

Table I. Main Features of VVER-440 and VVER-1000 Units

| Reactor | VVER-440 | VVER-1000 |
| --- | --- | --- |
| Thermal power | 1375 MW | 3000 MW |
| Number of loops, pumps and steam generators | 6 | 4 |
| Coolant pressure | 122.5 bar | 157 bar |
| Flow of coolant through the reactor | 31 000-35000 t/h | 63000 t/h |
| Average coolant temperature at in-let | 267 oC | 289.8 oC |
| Average coolant temperature increase | 28.9 oC | 30.3 oC |
| Fuel heat transmission area | 3050 m2 | 5175 m2 |
| Mass of Uranium | 42 t | 66 t |
| Number of fuel assemblies | 349 | 163 |
| Number of mechanical reactor control units | 37 pc | 61 pc |
| Vessel height (without upper plenum) | 11.8 m | 10.88 m |
| Vessel outer diameter | 3.84-4.27 m * | 4.57 m |
| Vessel mass | 200.8 t | 304 t |
| Outer diameter of main coolant pipeline | 500 mm | 850 mm |
| Steam generator |
| Steam production | 455 t/h | 1470 t/h |
| Steam pressure | 47 bar | 64 bar |
| Heat transmission area | 2500 m2 | 5040 m2 |
| Generator |
| Number of generators | 2 pc | 2 pc |
| Dry steam pressure before turbine | 44 bar | 60 bar |
| Output power | 220 MW | 500 MW |
| Unit |
| Electric power | 440 MW | 1000 MW |
| Efficiency (gross) | 32 % | 33.3 % |
| Efficiency (net) | 29.7 % | 31.5 % |

*3.84 m in the core region, 4.276 m at the vessel flange

### II.1. VVER-440 Reactor

VVER-440 is a water-cooled and water moderated thermal reactor.  The core consists of 349 hexagonal assemblies, see Figure 1.a. The fuel is low enriched UO2. Criticality is controlled by the boric acid concentration and by the position of control rod banks. Control rods are sorted into groups. The most frequently referred group is numbered as 6th and comprises 7 assemblies. Its elements are the central assembly, the other assemblies of the group are every 6th assemblies along the 6 different directions starting out from the central assembly stepping to the next neighboring assembly along a given direction.

In mathematical benchmarks, a simplified geometry is specified only: The core is composed of assemblies of identical geometry but with different material properties unless otherwise stated. Assemblies are considered as homogeneous, their composition is described by two-group cross-sections, in diffusion approximation. If the internal structure of the assembly is relevant, it is also specified in a simplified way. The cells making up the assembly are homogeneous hexagonal cells of identical size. This is only an approximation because the assembly wall is poorly described this manner.

In operational benchmarks, however, details of the actual geometry may be relevant. Therefore, such tests should specify all relevant information (geometry, material composition, and coolant flow rate, inlet temperature) in an appropriately detailed manner. Below, we present certain general information concerning geometry of VVER-440 and VVER-1000 cores including also the in-core instrumentation.

In a VVER-440, 210 assemblies are equipped with outlet temperature measurements, 36 assemblies with self powered neutron detectors (SPNDs). In most test cases, the core height is taken as the nominal value: 250 cm, unless indicated otherwise. The height of the active core, i.e. the height of the fuel pellet stack is given in Table II. The lowermost spacer is placed at elevations z=16,3 cm from the bottom of the fuel, further spacers are placed equidistantly at 24 cm distance Spacers are made of stainless steel or Zirconium Niobium. If a test accounts for the spacers, it indicates clearly the nuclide densities and the geometry.

Fig.1.a. In-Core Instrumentation in VVER-440 core

S-self powered neutron detector, T-Thermocouples, C-Control Assembly

The assembly geometry is shown in Figure 1.b. The assembly has a central tube and 126 fuel pins. The central tube houses the instrumentation in assemblies with self powered neutron detector (SPND) chains. Fuel pin data are given in Table II.

Table II. VVER-440 core component features

A, Standard and Follower Fuel Assemblies

Fuel pin:

Lattice pitch				1.22 cm

Fuel pin outer radius         		0.455 cm

Fuel pin cladding thickness		0.069 cm

Fuel pellet outer radius			0.38   cm

Fuel pellet central hole  radius		0.07 cm

Height of UO2 (cold)			242    cm

Height of UO2 (cold)			232    cm   (control fuel assembly)

Mass of  UO2 per fuel rod			1080 g  *)

Mass of  UO2 per fuel rod			1035 g  (control fuel assembly)  *)

Fuel pin clad composition (Zr110)		98.97 % Zr, 1% Nb, 0.03% Hf (in weight percent),

density  6.52 g/cm3

Instrumentation central tube:

Outer radius				0.515 cm

Thickness				0.075 cm

Material composition 			Zr110

Table II. VVER-440 core component features (continued)

Fuel assembly:

Fuel assembly pitch			14.7 cm

Shroud outer dimension			14.4 cm

Gap between assemblies			0.3 cm

Fuel assembly shroud thickness		0.2 cm (or 0.15 cm)

Fuel assembly shroud

composition (Zr125)			97.47 % Zr, 2.5% Nb, 0.03% Hf (in weight percent)

density  6.52 g/cm3

Spacer grids:

Spacer grid  material			stainless steel 12X18H10T of  7.86 g/cm3  (SS)

(or Zr110)

Spacer grid mass				SS 0.118 kg (or Zr110  0.092  kg)

Number of spacer grids in core

height					10

B, Absorber part of follower assembly:

Shroud:

Shroud outer dimension			14.4 cm

Shroud thickness				0.2 cm

Shroud material composition 		SS

Absorber (hexagonal tube made of boron steel):

Outer dimension 				13.7 cm,

Tube thickness 				0.7 cm

Material composition			boron steel containing 1.7(2.0 B,

its density is 7.51 g/cm3

Intermediate extension rod:

Cylindrical tubes (Inner/outer radii):	5.7 cm / 5.15 cm

2.0 cm / 1.0 cm

Fuel pin outer diameter: 	 0.91 cm

Pellet diameter:		 0.76 cm

Pellet density:			10.193 g/cm3

Fuel pin pitch:			1.22 cm

Clad composition: 		1% Nb, 98.97 % Zr, 0.03% Hf (weight percent)

Central tube:

Inner radius			0.440 cm

Outer radius			0.515 cm

Composition:			1% Nb, 98.97% Zr, 0.03 % Hf (weight percent)

Density:				6.6 g/cm3

*) Important mass of UO2 for core calculations

The clad material is Zirconium-Niobium with Hafnium. The control assemblies slightly differ in structure, their active height is smaller and its hydraulic resistance also has been changed. The control assembly has three major axial parts. The lower part is the follower, it resides in the core when the control rod is fully withdrawn. The upper part is the absorber followed by a structure joining the absorber part to the fuel part. The fuel part is called the control rod follower.

Fig. 1.b. Geometry of VVER-440 fuel assembly

Usually control assemblies are fully withdrawn except control group 6, which is kept in the upper one third of the core. The control assembly contains borated steel absorber, structural material and water. The radial structure of the control assembly is shown in Figure 1.c. The average fuel enrichment is 1.6, 2.4 or 3.6 w/w %.

A fuel cell has a fuel, a cladding and a moderator region. If an air gap is taken into account, it is indicated explicitly. Asymptotic codes (cell homogenization, generation of few group library, parametrization), such as burnup codes usually replace the hexagonal cell with a cylindrical cell of equal area.

Fig. 1.c. Radial structure of VVER-440 absorber of control assembly

In VVERs, the coolant and moderator is water. There are 6 loops in the primary circuit of VVER-440. The actual coolant flow rate through a given assembly depends on the flow rates of the individual loops. The assembly flow rates are not measured but estimated. The coolant entering temperature at a given assembly depends on the cold leg temperatures in the individual loops.

### II.2. VVER-1000 Reactor

VVER-1000 is a water-cooled and water moderated thermal reactor. The core consists of 163 hexagonal assemblies, see Figure 2.a. The fuel is low enriched UO2. Criticality is controlled by the boric acid concentration and by the position of control rod banks. Control rods are of cluster type and are sorted into 10 groups. The most frequently referred group is numbered as 10th and comprises 6 assemblies.

Fig. 2.a. VVER-1000 Core Geometry (30 deg Sector)

In mathematical benchmarks, a simplified geometry is specified only: The core is composed of assemblies of identical geometry but with different material properties unless otherwise stated. Assemblies are considered as homogeneous, their composition is described by two-group cross-sections, in diffusion approximation. If the internal structure of the assembly is relevant, it is also specified in a simplified way. The cells making up the assembly are homogeneous hexagonal cells of identical size.

In operational benchmarks, however, details of the actual geometry may be relevant. Therefore, such tests should specify all relevant information (geometry, material composition, and coolant flow rate, inlet temperature) in an appropriately detailed manner. Below, we present certain general information concerning geometry of VVER-1000 cores including also the in-core instrumentation.

The positions of the control assemblies are shown in Figure 2.b. In most test cases, the core height is taken as the nominal value: 350 cm, unless indicated otherwise. Spacers are made of stainless steel or Zirconium Niobium. If a test accounts for the spacers, it indicates clearly the nuclide densities and the geometry. The fuel assembly geometry [9] is shown in Figure 2.c. The VVER-1000 fuel assemblies are characterized by the following parameters [10,11]. The average enrichment of the assemblies is 2.0, 3.3, 3.6, 3.7, 4.0, 4.23, 4.3, 4.4 % (w/w). The structural and guide tube material is stainless steel or Zr alloy. In a VVER-1000, 95 assemblies are equipped with an outlet temperature measurement, 64 assemblies with self powered neutron detectors (SPNDs). The main features of VVER-1000 core components are shown in Table III. We remark only here that

- Type of burnable -poison rods (solid boron rods with natural boron concentration 0.036 g/cm3; Gd2O3 and UO2 mixture; no burnable poison at all)

- Number of burnable poison rods in an assembly (6 or 18)

- Pellet central hole diameter is given in Table III.

Fig. 2.b. Positions of Control Assemblies in VVER-1000

Table III. VVER-1000 Core Components Features

Fuel pin:

Lattice pitch				1.275 cm

Fuel pin outer radius         		0.455 cm

Fuel pin cladding thickness		0.069 cm

Fuel pellet outer radius			0.38   cm

Fuel pellet central hole  radius		0.14 cm  or 0.23 cm

Height of UO2 (cold)			353    cm

Mass of  UO2 per fuel rod 			1575 g*)  or 1460 g*)

Fuel pin clad composition (Zr110)		98.97 % Zr, 1% Nb, 0.03% Hf (in weight percent),

density  6.52 g/cm3

Instrumentation central tube:

Outer radius				0.56 cm

Thickness				0.08 cm

Material composition 			Zr110

Guide tubes for control rods:

Outer radius				0.63 cm

Thickness				0.08 cm

Material composition 			Stainless steel (SS)

Number in fuel assembly			18

Fuel assembly:

Fuel assembly pitch			23.6 cm

Spacer grid hoop outer dimension		23.4 cm

Fuel assembly shroud       			no

Spacer grids:

Spacer grid  material composition		stainless steel 12X18H10T of  7.86 g/cm3  (SS)

(or Zr110)

Spacer grid mass				SS 0.654 kg (or Zr110 0.560 kg)

Number of spacer grids in core

height					14

Control absorber rod :

Cladding outer radius			0.41 cm

Cladding thickness			0.06 cm

Cladding material			Zr110

Absorber material composition		B4C powder (natural boron), 1.8 g/cm3

Burnable absorber rod:

Cladding outer radius			0.455 cm

Cladding thickness			0.069 cm

Cladding material			Zr110

Absorber material composition		CrB2 + Al

natural boron in burnable absorber 0.036 g/cm3

*) Important mass of UO2 for core calculations

Fig. 2.c. VVER-1000 Assembly Geometry

### II.3. Terminology for Core Calculations

In the test cases, we compare characteristics of the computed flux or power distributions. Below, the terms are defined for VVER-440 core, with 349 fuel assemblies and 10 axial layers of equal volume in the calculation. In this context, the following terms will be used:

- Nuclear power release is defined as the instant rate of thermal energy released from nuclear fissions and decay. Most of this energy is deposited in the fuel, but a small fraction (app. 2,5 %) is deposited directly into the coolant via neutron slowing down and gamma radiation.

- Thermal power to coolant is defined as the instant rate of thermal energy input to the coolant in the core.  Most of this energy is transported to the coolant by heat transfer from the fuel, but a small fraction is deposited directly into the coolant via radiation.  Note that the thermal power to coolant can also be influenced by changes in coolant inlet temperature.  The difference between nuclear power release and thermal power to coolant results in a change of fuel temperature, including the cladding.

- The position of a control assembly is defined as the distance that the assembly is lifted from its fully inserted position.  It is usually measured in cm.  When fully withdrawn from the core, at position 250 cm, the bottom of the fuel pellet stack in the follower assembly is aligned with the rest of the core.

- Core energy production (sometimes referred to as core burnup) is defined as the total thermal energy production in the core since the beginning of an operating cycle.  It is often measured using a customized unit of energy called a full power day (FPD).  For VVER-440 reactors, full power (FP) is equivalent to 1375 MW and one FPD is hence equivalent to 1375 MWd of thermal energy.

- The boron concentration is defined as the mass fraction of natural boron in the coolant.  It is usually measured in ppm (parts per million = 10-6). Alternatively, the boric acid concentration is used. It is usually measured in g/kg (= 10-3). To a good approximation, 1 g/kg of boric acid is equivalent to 175 ppm of boron.

- A volume element is called node. There are 3490 nodes in the core when the above given discretization is utilized.

- Critical core state: The following parameters are subjected to possible change in a core: boron concentration, control assembly positions, core input coolant temperature and coolant flow rate, load pattern. A given core is called critical if these parameters are set so that the corresponding static eigenvalue keff=1. With the other parameters fixed, if one parameter (boron concentration or rod position) is set so that it makes the core critical then we speak of critical boron concentration or critical rod position.

- Multiplication factor: If the core is not a critical core state, the corresponding static eigenvalue keff that would make the core critical is called multiplication factor.

- Power level: the power released in the core is given either with absolute numbers (e.g. 343.75 MW) or in percent of the nominal power (1375 MW), e.g. 25%.

- Fuel burnup is defined as the release of thermal energy per unit mass of heavy metal (U, Pu) initially in the fuel.  It is usually measured in units of MWd/kgU.

- Power density: Wij  -the power produced in node j of assembly i divided by the node volume. Its average value for an assembly is

.

Its average value over the core is

.

- Assembly power: Wi -the power released in an assembly due to fission. The thermal power is the power conveyed by the coolant, the nuclear power is the power calculated directly from fission.

- Axial peaking factor (kz)

- Assemblywise peaking factor (kq) in assembly i:

.

- Nodal volume peaking factor (kv) in assembly i node j:

- Intra-assembly peaking factor (kk) in assembly i node j: Let wijm be the pin power in assembly i node j and pin m. Factor kk for assembly i and node j is given by

.

- Radial peaking factor (kr) kr=kq*kk

- Local peaking factor  (ko) ko=kr*kz

- Control group position (H6): position of the control assemblies in control group 6.

It may happen that not all of the above terms or features recurs in the first release of the Benchmark Book. If our endeavor is successful the scope of the benchmark activity will be gradually enlarged.

## References

1,World Nuclear Industry Handbook 1994, Nuclear Engineering International, 1994, pp. 22-49

2, Report ANL-7416, Supplement 1, (Revised 1972), Supplement 2. (Revised 1977), Suppl. 3 (Revised 1985)

3, Final Report of TIC, vol. 1 and 3, Experimental Investigations of the Physical Properties of WWER-Type Uranium-Water Lattices, Akadémiai Kiadó, Budapest, 1985-1991

4, At the end of 1999 no open publication is available to introduce the measurements on the LR-0 facility.

5, Final Report of TIC, vol. 2, Theoretical Investigations of the Physical Properties of WWER-Type Uranium-Water Lattices, Akadémiai Kiadó, Budapest, 1994

6. Requirements for Reference Reactor Physics Measurements, ANSI-ANS-19.5-1978 (reaffirmed 1984)

7. A Guide for Acquisition and Documentation of Reference Power Reactor Measurements for Nuclear Analysis Verification, ANS-194, ANSI N652-1976, (reaffirmed 1989)

8, F. Ya. Ovchinnikoff et al.: Operational Modes of Water Cooled, Water Moderated Power Reactors, Moscow, Atomizdat, 1977

9,J. Kyncl: Personal Communication, 1999

10,V. Pavlov and A. Pavlovichev: General Features of VVER-1000 Three- and Four Batch 12 Months Cycles with Improved Fuel Utilization, in Proc. of the fourth Symposium of AER, p. 575, Sozopol, BG, 1994

11, In-core fuel management code package validation for WWERs, IAEA-TECDOC-874, Vienna, November 1995

# III. Test Cases

This section is a short survey of the available tests. Each test has been assigned a mnemonic identification. The first invariable tag is AER. The second tag refers to the nature of the test. We used the following abbreviations:

DYN	-dynamics

FCM	-full core, mathematics

FCO	-full core, operational

HOM	-homogenization/dehomogenization

ASB	-asymptotic burnup

BCR	-burnup credit

KAB	-assembly burnup

TRO	-transient operational test.

The last tag is a three-digit number. Its first digit refers to the reactor type (0/1=VVER-440/VVER-1000), the last two digits make a sequential number.

The solutions to some test problems contain a large amount of numbers. Solutions to those test problems reside in separated files. The naming convention for solution files is as follows. We leave out AER in front of the test name and add the tag SXX, where XX is a serial number, S is a fixed character that refers to the word "solution".

| No. | Identification | Author | Company | Classification | Description | File |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Reference | Input |  |  |
| 1 | AER-DYN-001 | A. Kereszturi, M. Telbisz | AEKI | I | M | Neutronics | DYN001.doc |
| 2 | AER-DYN-002 | U. Grundmann | FZR | I | M | Neutronics +Doppler feedback | DYN002.doc |
| 3 | AER-DYN-003 | R. Kyrki-Rajamäki, E. Kaloinen | VTT | I | M | Neutronics +Thermal hydraulics | DYN003.doc |
| 4 | AER-DYN-004 | R. Kyrki-Rajamäki | VTT | I | M | Boron dilution | DYN004.doc |
| 5 | AER-DYN-005 | S. Kliem | FZR | I | M | Steam header break | DYN005.doc |
| 6 | AER-FCM-001 | Cs. Maráczy et al. | AEKI | B | M | 440 core, Seidel's test | FCM001.doc |
| 7 | AER-FCM-002 | Cs. Maráczy | AEKI | B | M | 180 deg 440 core | FCM002.doc |
| 8 | AER-FCM-101 | N. P. Kolev | IAE | B | M | Schultz test | FCM101.doc |
| 9 | AER-FCM-102 | Alekhova, Prodanova | KNPP-IAE | I | M | 1000 core | FCM102.doc |
| 10 | AER-BCR-001 | L. Markova | UJV | I | M | Burnup credit | BCR001.doc |
| 11 | AER-TRO-001 | D. Burket | DNPP | B | O | Load follow | TRO001.doc |
| 12 | AER-KAB-001 | P. Mikolaš | Škoda | I | M | Assembly burnup | KAB001.doc |
| 13 | AER-HOM-101 | M. Makai | AEKI | B | M | Assembly homogenization | HOM101.doc |

Table III.1. List of available tests

I-inter-comparison, B-benchmark

M-mathematical test; O-operational test

## IV. Test Specifications

The test specifications are available via internet at http://www.kfki.hu/~aekihp/ where you have to click on AER, there click on Benchmark Book.

# Comments

File names are tentative!