# AER Benchmark  Specification Sheet

- Test ID: AER-FCM-001

- Short Description:

Type: Mathematical Benchmark

Problem statement:

Seidel’s 3D benchmark1 models a VVER-440 core in 30 degree symmetry using two-group diffusion approximation and given cross-sections. The core is 250 cm high, covered with axial and radial reflectors and contains fuel elements of 3 different enrichments. The radial fuel assembly pitch is 14.7 cm. The control rods are large control elements with fuel followers. Rod Bank 6 is partially inserted, as shown in Figure 1. There are steep flux gradients between the inserted control rods and adjacent fuel elements. The applied boundary condition on the outer surface of reflectors is (I=2.13Di extrapolation length where Di is the diffusion constant of reflector material i. The extrapolation length corresponds to a diagonal albedo with elements 3.1477E-2 .The two-group diffusion parameters are given in Table 1. The task is to calculate the effective multiplication factor and the 3D power distribution. The power distribution should be normalized to core average power density of unity and presented for axial node size of 25 cm.

- Submitted by: Cs.Maráczy(KFKI), N.P.Kolev(INRNE), C.Magnaud,R.Lenain(CEA Saclay)

Date: 15.04.99

4. Reviewed by: I. Pós (PARt, Paks), M. Makai (AEKI)

Date: September 1999

5. Accepted by: I. Pós (PARt, Paks), M. Makai (AEKI)

Date: November 1999

- Objective: VVER-440 3-D core calculation test for homogenized nodes.

- Rationale for Test Setup: The benchmark was defined by Seidel in Ref.1 The reference solution was derived from solutions by the OSCAR2 finite-difference code using relatively coarse meshes because of limited computer resources. Two new recommended solutions3,5 are now available, derived by radial and axial extrapolation from finite-difference and finite-element calculations in fine triangular-z meshes.  Maraczy3 at KFKI used DIF3D-FD4 and Kolev, Magnaud and Lenain5 at CEA Saclay used CRONOS-FEM6,7. The extrapolation to zero mesh size has been done using Richardson’s method8 i.e. supposing the calculated values are functions of even powers of mesh size. The DIF3D recommended and CRONOS recommended solutions converge within 0.5 pcm in multiplication factor and 0.0017 in normalized 3D power distribution. The solutions of 1st-, 2nd- and 3rd-order, used for extrapolation enable a comparative convergence analysis of other approximations.

8. Input:

a, Geometry: Fig.1 shows the axial cut of the core,. Fig.2 shows the radial core map in 30 degree symmetry. The core is of height 250 cm, covered with axial and radial reflectors. The hexagonal lattice pitch in Fig.2 is 14.7 cm, the axial node size is 25 cm. The control rods are large control elements with fuel followers. Rod Bank 6 is half-inserted.

Fig.2. Radial core map

Table 1

Group Constants for Seidel’s 3-D Benchmark

| Parameter | Material type |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 |
| D1 [cm] | 1.3466 | 1.3377 | 1.3322 | 1.1953 | 1.4485 | 1.3413 |
| D2 [cm] | 0.37169 | 0.36918 | 0.36502 | 0.19313 | 0.25176 | 0.24871 |
| (a1+(12[cm-1] | 2.5255-2 | 2.4709-2 | 2.4350-2 | 2.5636-2 | 3.3184-2 | 2.9301-2 |
| ( a2 [cm-1] | 6.4277-2 | 7.9361-2 | 1.0010-1 | 1.3498-1 | 3.2839-2 | 6.4655-2 |
| (12 [cm-1] | 1.6893-2 | 1.5912-2 | 1.4888-2 | 2.2264-2 | 3.2262-2 | 2.7148-2 |
| (f1 [cm-1] | 2.21676-3 | 2.79212-3 | 3.59068-3 | 0.0 | 0.0 | 0.0 |
| (f2 [cm-1] | 3.94368-2 | 5.65720-2 | 8.00000-2 | 0.0 | 0.0 | 0.0 |
| (( f1 [cm-1] | 4.4488-3 | 5.5337-3 | 7.0391-3 | 0.0 | 0.0 | 0.0 |
| (( f2 [cm-1] | 7.3753-2 | 1.0581-1 | 1.4964-1 | 0.0 | 0.0 | 0.0 |

- Material Compositions: In Fig.2, the lower number in an assembly indicates the assembly type. Table 1 assigns the material types to assembly types and lists the cross-sections in two energy groups. Materials 1,2,3 are fuel, material 4 is control rod. The control rod followers are of material 2.  Materials 5,6 are reflectors.

c, Boundary conditions: At the external boundary of the core, the boundary condition is (I=2.13Di extrapolation length, where Di is the diffusion constant of reflector material i. This corresponds to a diagonal albedo with elements ( = 3.1477E-2 in partial current representation, or ( = 0.46948 in current-flux representation where ( = 0.5(1-()/(1+().

9. Hardware and Software Requirements: The test can be solved by nodal programs on a normal PC or low-end workstation. Fine-mesh calculations require a workstation with extended memory and may be time consuming depending on the mesh refinement.

- Output:

- Expected results: Keff; 3D and assembly-wise power distributions.

- Files, Format: none.

- References:

1. F.Seidel, "Diffusion Calculations for VVER-440 2D and 3D Test Problem", Proc. of the 14th Symp. of Temporary International Collective (TIC), Warsaw, Poland, 23-27 September, 1985, vol.1, p.216

2. K.Gartner,"OSCAR2", Kernenergie (DDR) no. 26, 1983, 402

3. C.Maraczy,”A Solution of Seidel’s 3D Benchmark for VVER-440 with the DIF3D-FD Code”, Proc. 5th Symp. of AER on VVER Reactor Physics and Safety, Dogoboko, Hungary, 1995

4. K.L.Derstine, "DIF3D: A Code to Solve One-,Two-, and Three- Dimensional Finite-Difference Diffusion Theory Problems', ANL-82-64, Argonne, Illinois, April 1984

5. N.P.Kolev,C.Fedon-Magnaud,R.Lenain “Solutions of Seidel’s 3D Benchmark for VVER-440 by CRONOS”, Proc. 7-th Symp. of AER on VVER Reactor Physics and Safety, Hoernitz, Germany, September 1997

6. J.J.Lautard,S.Loubiere and C.Fedon-Magnaud, "CRONOS: A Modular Computational System for Neutronic Core Calculations", IAEA Spec. Mtg. on Advanced Calculational Methods for Power Reactors, Cadarache, France, September 10-14, 1990

7. C.Fedon-Magnaud and J.J.Lautard, "Transport Calculation with the CRONOS Reactor Code” Seminar on 3D Deterministic Radiation Transport Codes, Dec. 2-3, OECD, Paris 1996

8. G.I.Marchuk,V.Shaidurov, “Difference Methods and Their Extrapolations”, Springer, 1983

- G.Schulz, "Solutions of a VVER-1000 Benchmark", Proc. 6th Symposium of AER, Kirkkonummi, 1996

- G.Schulz: FEM-3Di solution of Seidel’s benchmark, Private communication 1996

11.Y.A.Shatilla, Y.A.Chao, "Benchmark Problems for Two-Group Hexagonal Geometry Nodal Codes", Proc. Int. Conf. on Math. and Comp., Reactor Physics and Env. Analyses, Portland, Oregon,  1995, vol.2, p.1233

12. R. Becker, G. Schultz and S. Thomas: Accuracy assessment of the 3D nodal code TRAPEZ, in Proc. of the fourth Symposium of AER, pp. 103-115, Sozopol, Bulgaria, 1994

13. I. Pós, S. Patai Szabó and I. Nemes: C-PORCA 4.0 Version Description and Validation Procedure, in Proc. of the sixth Symposium of AER, pp. 565-594, Kirkkonummi, Finland, 1996

14. A.Kereszturi: KIKO3D solution of Seidel’s benchmark, Private communication 1997

- Recommended Solution: Two solutions of good quality are available which can be recommended as reference solutions.

- DIF3D recommended solution3

a, Method: Calculated with the DIF3D4 mesh-centered finite-difference code using fine triangular-z mesh. The spatial approximation is of 1st-order. The solution process uses Chebyshev acceleration for the outer iterations and LSOR for the inner iterations. Calculations have been made with 1.25, 2.50 and 2.50 cm axial and 2.829, 1.414 and 2.829 cm radial mesh sizes, respectively. The radial and axial extrapolation of the results to zero mesh size has been done using Richardson's method8 i.e. supposing the calculated values are functions of the even powers of mesh size.

b, Data, Estimated Error: The DIF3D recommended solution3 is given in Table 2. Fine-mesh solutions used for extrapolation are shown in Appendix 1. In the rest of the paper differences between distributions mean absolute differences rather than relative ones.

The differences of calculated parameters between the finest-mesh and extrapolated solutions characterize the accuracy of the recommended solution. The highest difference in the 3D power distribution is 0.0088; the difference in Keff is -0.00011 (see Table 3). The mesh is sufficiently fine to ensure extrapolation of good quality.

- CRONOS recommended solution5

CRONOS6,7 is a reactor code of CEA which uses finite elements and nodal methods for homogenized diffusion and transport calculations; the code has also 3D kinetics and pin-by-pin diffusion modules.

a, Method: The calculation was done by 2nd-order finite elements with Lagrange polynomials in fine triangular-z meshes. The approximation in the hexagonal plane used Gauss-Legendre numerical quadrature corresponding to super-convergent finite elements. The axial approximation used exact quadrature. The convergence rate is somewhat better than O(h2).

The solution process is one of inner, outer iteration. The outer iteration is the power method with Chebyshev parameters; the inner is the Conjugate Gradient method per plane.

The recommended solution was derived by Richardson's extrapolation8 from three finite-element solutions of 2nd-order with relative radial and axial mesh size as follows: (1,1/2); (1/2,1/4); (1/3,1/6). This corresponds to a basic mesh of 6,24,54 triangles per hexagon and Nz=24,48,72. The mesh-size for the finite-element interpolants is twice as small, the finest one being 1.4145 cm in radial direction. The high convergence rate permits generation of an accurate extrapolated solution without excessive mesh refinement.

b, Data, Estimated Error

The CRONOS recommended solution is given in Table 4.

Second-order solutions used for extrapolation are summarized in Table 7 and shown in Appendix 2, Tables A1-A7. The finest and extrapolated 3D solutions differ by maximum -0.0014; the difference in Keff is 3.2 pcm (see Table 5). The recommended solution is extrapolated from well converged solutions.

Third-order solutions are summarized in Table 7 and shown for comparison in Appendix 2, Tables A8-A15. The maximal difference of finest to extrapolated cubic solutions for node powers is -0.0011; the difference in Keff is 3.2 pcm (see Table A13).

Regarding the extrapolated solutions of 3rd- and 2nd-order, the multiplication factors are the same; the maximal difference in node powers of the cubic to 2nd-order solution is -0.0006 (see Table 7). The corresponding difference of the 3rd-order solution to DIF3D recommended solution is 0.5 pcm in Keff and maximum 0.002 in 3D distributions. However, the 2nd-order solution is recommended as reference from extrapolation accuracy viewpoint. It is derived by non-linear extrapolation from three different radial grids whereas that of 3rd-order is derived from two.

The maximal error of the CRONOS recommended solution is estimated to less than 0.001 in normalized 3D power distribution.

(3) Comparing the CRONOS recommended5 to DIF3D-FD recommended3 solution (see Tables 6,7), a very close agreement is observed. They differ by 0.5 pcm in Keff, respectively 0.0017 in normalized 3D power distribution. The relative 3D deviations are in the range of           -0.35% ( ( ( 0.36%. The error estimates for each solution are acceptable. It can be concluded that both solutions are reliable and can serve as reference solutions.

- Summary of Available Solutions

Table 7 summarizes fine-mesh and extrapolated Seidel’s benchmark solutions1,3,5,9,10.

CRONOS 1st-order solutions are included for methodological purposes only, as the radial mesh was not sufficiently fine.

A DIF3D-FD solution, radially extrapolated at Nz=120 is given in Ref.11.

Coarse-mesh solutions are given in Refs.3,5,12-14.

In Appendix 1, the following solutions are attached:

1, DIF3D solutions with HR=2.829 cm HZ=2.5 cm

2, DIF3D solutions with HR=1.4145 cm HZ=2.5 cm

3, DIF3D solutions with HR=0 cm HZ=2.5 cm

4, DIF3D solutions with HR=2.829 cm HZ=1.25 cm

5, DIF3D solutions with HR=2.829 cm HZ=0 cm

6, DIF3D solutions with HR=0 cm HZ=0 cm (recommended solution)

7, The OSCAR reference solution

In Appendix 2, Tables A1-A15, the following solutions are attached:

- CRONOS 2nd-order 19-point HXP19#P24 solution

- CRONOS 2nd-order  61-point HXP61#P48 solution

- CRONOS 2nd-order  61-point HXP61#P72 solution

- CRONOS 2nd-order 127-point HXP127#P72 solution

- CRONOS 2nd-order solution with hr=0 cm, hz=0 cm (recommended solution), F7.4

- CRONOS 3rd-order 37-point HXC37P24 solution

- CRONOS 3rd-order 37-point HXC37P36 solution

- CRONOS 3rd-order 37-point HXC37P24 solution

- CRONOS 3rd-order 127-point HXC127P72 solution

- CRONOS 3rd-order solution with hr=0 cm, hz=0 cm (extraolated solution), F7.4

- CRONOS 3rd-order solution with hr=0 cm, hz=0 cm (extraolated solution), F7.3

The available solutions3,5, attached in Appendices1;2 permit a comparative spatial convergence analysis of new approximations. Figures 3,4 illustrate the convergence rate and extrapolation of CRONOS and DIF3D solutions of 1st-order. The notations correspond to mesh-centered finite differences (DIF3D), super-convergent finite elements (CR-L#), classical finite elements (CR-L) and mesh-edged finite differences (CR-L$). In Fig.3, all solutions converge to nearly the same values when the radial mesh size hr  tends to zero. In Fig.4, the h2-extrapolated values of 3D peaking factors are in excellent agreement. The Summary Table 7 illustrates the convergence rate of 2nd- and 3rd-order finite-element solutions.

Table 2

CRONOS RECOMMENDED SOLUTION OF SEIDEL’S 3D BENCHMARK

hr=0.000000         hz=0.000000

Keff= 1.011325    Pmax = 2.456

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | Qmean |
| 01 | .520 | 1.075 | 1.456 | 1.586 | 1.344 | 0 | 0 | 0 | 0 | 0 | 1.1962 |
| 02 | .419 | .867 | 1.175 | 1.283 | 1.141 | .793 | .566 | .398 | .248 | .110 | .7009 |
| 03 | .545 | 1.126 | 1.527 | 1.672 | 1.536 | 1.207 | .895 | .631 | .394 | .174 | .9708 |
| 04 | .550 | 1.136 | 1.541 | 1.690 | 1.563 | 1.251 | .935 | .660 | .412 | .182 | .9920 |
| 05 | .439 | .908 | 1.232 | 1.354 | 1.265 | 1.035 | .782 | .554 | .346 | .153 | .8069 |
| 06 | .554 | 1.146 | 1.556 | 1.712 | 1.605 | 1.323 | 1.005 | .713 | .446 | .198 | 1.0257 |
| 07 | .563 | 1.164 | 1.579 | 1.735 | 1.620 | 1.326 | 1.002 | .709 | .444 | .196 | 1.0339 |
| 08 | .560 | 1.159 | 1.573 | 1.728 | 1.613 | 1.317 | .995 | .705 | .442 | .196 | 1.0287 |
| 09 | .433 | .897 | 1.219 | 1.341 | 1.253 | 1.025 | .777 | .552 | .347 | .154 | .7998 |
| 10 | .541 | 1.120 | 1.524 | 1.682 | 1.579 | 1.302 | .993 | .710 | .448 | .199 | 1.0097 |
| 11 | .449 | .929 | 1.262 | 1.384 | 1.277 | 1.014 | .756 | .535 | .335 | .148 | .8089 |
| 12 | .567 | 1.174 | 1.595 | 1.750 | 1.603 | 1.248 | .923 | .654 | .411 | .182 | 1.0107 |
| 13 | .440 | .912 | 1.240 | 1.366 | 1.266 | 1.013 | .762 | .543 | .342 | .152 | .80346 |
| 14 | .438 | .908 | 1.238 | 1.371 | 1.297 | 1.080 | .833 | .600 | .380 | .169 | .83141 |
| 15 | .571 | 1.186 | 1.620 | 1.806 | 1.736 | 1.484 | 1.167 | .849 | .540 | .241 | 1.1198 |
| 16 | .461 | .956 | 1.299 | 1.421 | 1.258 | .856 | .608 | .429 | .270 | .120 | .7677 |
| 17 | .589 | 1.221 | 1.660 | 1.820 | 1.617 | 1.109 | .793 | .563 | .355 | .158 | .9888 |
| 18 | .584 | 1.212 | 1.651 | 1.823 | 1.689 | 1.340 | 1.011 | .726 | .460 | .205 | 1.0701 |
| 19 | .461 | .957 | 1.308 | 1.455 | 1.390 | 1.175 | .918 | .667 | .424 | .189 | .8943 |
| 20 | .579 | 1.202 | 1.646 | 1.844 | 1.790 | 1.554 | 1.238 | .906 | .577 | .258 | 1.1593 |
| 21 | .511 | 1.063 | 1.457 | 1.637 | 1.602 | 1.407 | 1.131 | .831 | .531 | .237 | 1.0408 |
| 22 | .613 | 1.271 | 1.729 | 1.894 | 1.610 | 0 | 0 | 0 | 0 | 0 | 1.4234 |
| 23 | .491 | 1.020 | 1.390 | 1.529 | 1.372 | .965 | .702 | .504 | .319 | .142 | .8435 |
| 24 | .616 | 1.278 | 1.745 | 1.936 | 1.823 | 1.498 | 1.153 | .835 | .530 | .236 | 1.165 |
| 25 | .462 | .961 | 1.315 | 1.469 | 1.417 | 1.218 | .963 | .703 | .448 | .200 | .9156 |
| 26 | .614 | 1.274 | 1.746 | 1.961 | 1.915 | 1.675 | 1.343 | .987 | .630 | .282 | 1.2426 |
| 27 | .424 | .882 | 1.209 | 1.362 | 1.337 | 1.179 | .952 | .701 | .449 | .200 | .8695 |
| 28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 29 | .647 | 1.343 | 1.831 | 2.017 | 1.817 | 1.289 | .945 | .679 | .431 | .192 | 1.1191 |
| 30 | .509 | 1.059 | 1.445 | 1.601 | 1.495 | 1.204 | .919 | .664 | .422 | .188 | .9506 |
| 31 | .725 | 1.504 | 2.057 | 2.292 | 2.194 | 1.860 | 1.459 | 1.061 | .675 | .302 | 1.4129 |
| 32 | .581 | 1.206 | 1.652 | 1.850 | 1.796 | 1.558 | 1.241 | .908 | .579 | .259 | 1.1630 |
| 33 | .378 | .785 | 1.077 | 1.210 | 1.185 | 1.040 | .837 | .615 | .393 | .176 | .7695 |
| 34 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 35 | .782 | 1.622 | 2.215 | 2.456 | 2.312 | 1.897 | 1.459 | 1.056 | .671 | .299 | 1.4768 |
| 36 | .689 | 1.431 | 1.955 | 2.175 | 2.076 | 1.752 | 1.368 | .993 | .632 | .282 | 1.3353 |
| 37 | .517 | 1.074 | 1.469 | 1.641 | 1.583 | 1.362 | 1.077 | .786 | .500 | .223 | 1.0231 |
| 38 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 39 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 40 | .475 | .986 | 1.348 | 1.501 | 1.436 | 1.219 | .954 | .693 | .441 | .197 | .9250 |
| 41 | .410 | .852 | 1.164 | 1.299 | 1.250 | 1.071 | .844 | .614 | .391 | .174 | .8069 |

Table 3

DIFFERENCE OF THE CRONOS RECOMMENDED SOLUTION

TO DIF3D RECOMMENDED SOLUTION

(Keff = 0.5 pcm  (Pmax = 0.001

3D Distribution Differences*100

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .00 | -.02 | -.02 | -.04 | -.03 | .00 | .00 | .00 | .00 | .00 |
| 02 | .00 | -.09 | -.11 | -.11 | -.10 | -.12 | -.07 | -.02 | -.06 | -.01 |
| 03 | -.04 | .01 | -.04 | -.07 | -.10 | -.06 | -.07 | -.09 | -.06 | -.06 |
| 04 | -.05 | -.06 | -.01 | -.04 | -.14 | -.10 | -.11 | -.02 | -.06 | -.06 |
| 05 | -.03 | -.05 | -.05 | -.10 | -.04 | -.08 | -.06 | -.05 | -.07 | .00 |
| 06 | .00 | -.08 | -.10 | -.03 | -.04 | -.10 | -.03 | -.05 | -.06 | -.04 |
| 07 | -.05 | -.03 | -.10 | -.11 | -.08 | -.06 | -.06 | -.06 | -.01 | -.06 |
| 08 | -.01 | -.05 | -.04 | -.05 | -.11 | -.07 | -.10 | -.01 | -.04 | -.04 |
| 09 | .00 | -.08 | .00 | -.06 | -.05 | -.06 | -.04 | -.01 | -.04 | -.05 |
| 10 | -.02 | .01 | -.01 | -.05 | -.09 | -.02 | -.06 | .00 | -.04 | -.01 |
| 11 | -.05 | -.06 | -.03 | -.06 | -.13 | -.06 | -.11 | -.04 | .01 | .03 |
| 12 | .02 | -.06 | -.09 | -.08 | -.02 | -.02 | -.08 | -.02 | -.04 | .02 |
| 13 | -.03 | -.02 | -.08 | -.05 | -.04 | -.02 | -.04 | .01 | -.07 | .00 |
| 14 | -.04 | .02 | .01 | -.05 | .00 | -.01 | .00 | .00 | -.01 | -.01 |
| 15 | .02 | .07 | .03 | .01 | -.04 | -.04 | .02 | -.04 | -.04 | -.05 |
| 16 | .01 | .00 | -.03 | -.08 | -.02 | -.10 | -.05 | -.09 | -.04 | -.03 |
| 17 | .04 | .02 | -.05 | -.05 | -.06 | -.03 | -.07 | -.06 | .02 | .02 |
| 18 | .05 | -.01 | .02 | -.03 | -.01 | -.05 | .02 | .00 | -.04 | -.03 |
| 19 | -.03 | .04 | -.03 | .04 | .00 | .00 | -.07 | -.04 | -.03 | -.04 |
| 20 | .06 | .05 | .03 | .05 | -.01 | .05 | -.05 | -.03 | -.05 | -.04 |
| 21 | -.01 | .07 | -.01 | .04 | .04 | -.03 | -.02 | .05 | .02 | .01 |
| 22 | .04 | .04 | .04 | -.03 | -.03 | .00 | .00 | .00 | .00 | .00 |
| 23 | .04 | .04 | -.01 | -.05 | -.07 | -.05 | -.06 | -.05 | .00 | .01 |
| 24 | -.02 | .04 | .01 | -.01 | .04 | -.02 | .03 | -.04 | .02 | .03 |
| 25 | -.01 | .00 | -.02 | .00 | .03 | -.03 | .02 | .01 | .00 | -.04 |
| 26 | .06 | .12 | .14 | .08 | .06 | .03 | .03 | .06 | .01 | .05 |
| 27 | .00 | .05 | .14 | .15 | .10 | .13 | .08 | .04 | .06 | .04 |
| 28 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 29 | .03 | .03 | -.02 | .00 | -.04 | -.06 | -.02 | -.01 | -.03 | .01 |
| 30 | .04 | .00 | .03 | -.02 | .02 | -.07 | -.01 | -.01 | -.02 | -.02 |
| 31 | .00 | .04 | .05 | .06 | .07 | .04 | .07 | .02 | .05 | .05 |
| 32 | .07 | .12 | .17 | .08 | .07 | .09 | .10 | .05 | .05 | -.02 |
| 33 | .07 | .11 | .16 | .11 | .16 | .13 | .05 | .03 | .02 | .06 |
| 34 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 35 | .09 | .11 | .05 | .12 | .07 | -.01 | .01 | -.04 | -.02 | .03 |
| 36 | .04 | .06 | .08 | .04 | .08 | .08 | .00 | .04 | -.01 | .00 |
| 37 | .09 | .06 | .17 | .15 | .11 | .05 | .09 | .06 | .04 | .03 |
| 38 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 39 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 40 | .05 | .03 | .09 | .09 | .02 | -.02 | .05 | .04 | .01 | .05 |
| 41 | .10 | .05 | .13 | .18 | .09 | .07 | .09 | .04 | .01 | .04 |

DEVIATION RANGE: -0.0014( ( ( 0.0017

Table 4

DIFFERENCE OF THE CRONOS RECOMMENDED SOLUTION

TO DIF3D RECOMMENDED SOLUTION

(Keff = 0.5 pcm           (Pmax =  0.001

Relative Differences  %

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .01 | -.01 | -.02 | -.02 | -.02 | .00 | .00 | .00 | .00 | .00 |
| 02 | -.01 | -.10 | -.10 | -.09 | -.09 | -.16 | -.12 | -.04 | -.23 | -.12 |
| 03 | -.07 | .01 | -.03 | -.04 | -.06 | -.05 | -.08 | -.14 | -.16 | -.34 |
| 04 | -.09 | -.06 | -.01 | -.02 | -.09 | -.08 | -.12 | -.04 | -.15 | -.35 |
| 05 | -.07 | -.06 | -.04 | -.07 | -.04 | -.08 | -.08 | -.09 | -.21 | -.01 |
| 06 | .00 | -.07 | -.06 | -.02 | -.02 | -.08 | -.03 | -.07 | -.13 | -.19 |
| 07 | -.09 | -.03 | -.06 | -.07 | -.05 | -.04 | -.06 | -.09 | -.01 | -.30 |
| 08 | -.02 | -.04 | -.02 | -.03 | -.07 | -.05 | -.10 | -.02 | -.08 | -.23 |
| 09 | -.01 | -.09 | .00 | -.04 | -.04 | -.06 | -.05 | -.02 | -.11 | -.31 |
| 10 | -.04 | .01 | -.01 | -.03 | -.06 | -.02 | -.06 | .00 | -.08 | -.06 |
| 11 | -.11 | -.07 | -.03 | -.04 | -.10 | -.06 | -.14 | -.07 | .03 | .21 |
| 12 | .04 | -.05 | -.05 | -.05 | -.01 | -.02 | -.09 | -.03 | -.11 | .09 |
| 13 | -.07 | -.02 | -.06 | -.04 | -.03 | -.02 | -.06 | .01 | -.20 | -.02 |
| 14 | -.10 | .02 | .01 | -.04 | .00 | -.01 | -.01 | -.01 | -.03 | -.04 |
| 15 | .04 | .06 | .02 | .01 | -.02 | -.03 | .02 | -.04 | -.08 | -.20 |
| 16 | .02 | .01 | -.02 | -.06 | -.02 | -.12 | -.08 | -.20 | -.14 | -.23 |
| 17 | .07 | .01 | -.03 | -.03 | -.04 | -.02 | -.09 | -.11 | .05 | .10 |
| 18 | .08 | -.01 | .01 | -.01 | -.01 | -.04 | .02 | .00 | -.08 | -.14 |
| 19 | -.08 | .04 | -.02 | .02 | .00 | .00 | -.07 | -.06 | -.07 | -.19 |
| 20 | .10 | .04 | .02 | .03 | .00 | .03 | -.04 | -.04 | -.09 | -.16 |
| 21 | -.01 | .06 | -.01 | .02 | .02 | -.02 | -.02 | .06 | .05 | .04 |
| 22 | .06 | .03 | .02 | -.02 | -.02 | .00 | .00 | .00 | .00 | .00 |
| 23 | .07 | .04 | -.01 | -.03 | -.05 | -.05 | -.08 | -.10 | .00 | .09 |
| 24 | -.04 | .03 | .01 | .00 | .02 | -.01 | .03 | -.05 | .04 | .14 |
| 25 | -.02 | .00 | -.02 | .00 | .02 | -.02 | .03 | .02 | .00 | -.22 |
| 26 | .09 | .10 | .08 | .04 | .03 | .02 | .03 | .06 | .01 | .19 |
| 27 | .01 | .06 | .12 | .11 | .08 | .11 | .08 | .05 | .13 | .22 |
| 28 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 29 | .05 | .02 | -.01 | .00 | -.02 | -.05 | -.02 | -.02 | -.08 | .07 |
| 30 | .07 | .00 | .02 | -.01 | .02 | -.06 | -.01 | -.01 | -.06 | -.13 |
| 31 | .00 | .02 | .02 | .03 | .03 | .02 | .05 | .02 | .07 | .17 |
| 32 | .13 | .10 | .10 | .04 | .04 | .06 | .08 | .05 | .09 | -.10 |
| 33 | .18 | .15 | .14 | .09 | .13 | .12 | .07 | .05 | .06 | .36 |
| 34 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 35 | .12 | .07 | .02 | .05 | .03 | -.01 | .01 | -.04 | -.04 | .10 |
| 36 | .06 | .04 | .04 | .02 | .04 | .05 | .00 | .04 | -.02 | .00 |
| 37 | .18 | .05 | .11 | .09 | .07 | .04 | .08 | .07 | .09 | .13 |
| 38 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 39 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 40 | .11 | .03 | .07 | .06 | .02 | -.02 | .05 | .06 | .02 | .26 |
| 41 | .24 | .06 | .11 | .14 | .07 | .07 | .11 | .07 | .02 | .24 |

DEVIATION RANGE: -0.35 % ( ( ( 0.36 %

Table 5

Summary of Seidel’s Benchmark Results

| Code & Approx. | Radial | Axial | Mesh | Keff | Peaking Factor | ((P)max to CRONOS recom. | ((P)max to DIF3D recom. |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | L7# | L120 | 1,1/10 | 1.010853 | 2.442 | -0.0390 |  |
| CRONOS | L19# | L120 | 1/2,1/10 | 1.011406 | 2.460 | 0.0156 |  |
| 1.order FEM | L37# | L120 | 1/3,1/10 | 1.011396 | 2.4586 | 0.0083 |  |
| with G-L | L37# | L144 | 1/3,1/12 | 1.011396 | 2.4587 |  |  |
| Quadrature | L37# | L180 | 1,1/15 | 1.011397 | 2.4588 |  | 0.0102 |
|  | ( | L120 | 0,1/10 | 1.011329 | 2.4562 |  |  |
|  | ( | ( | 0,0 | 1.011330 | 2.4564 |  | -0.0033 |
|  | P19# | P24 | 1,1/2 | 1.011415 | 2.4542 | -0.0102 |  |
| CRONOS | P19# | P72 | 1,1/6 | 1.011405 | 2.4546 |  |  |
| 2.order FEM | P61# | P48 | 1/2,1/4 | 1.011376 | 2.4568 | -0.0048 |  |
| with G-L | P61# | P72 | 1/2,1/6 | 1.011373 | 2.4571 | -0.0032 |  |
| Quadrature | P127# | P72 | 1/3,1/6 | 1.011357 | 2.4565 | -0.0014 |  |
|  | ( | ( | 0,0 | 1.011325 | 2.4562 | 0.0 | 0.0017 |
| CRONOS | C37 | P36 | 1,1/3 | 1.011392 | 2.4571 |  |  |
| 3.order | C127 | P72 | 1/2,1/6 | 1.011342 | 2.4566 | -0.0013 |  |
| Classical FEM | ( | ( | 0,0 | 1.011325 | 2.4564 | -0.0006 | 0.0020 |
| DIF3D-FD | L37 | L120 | 1/3,1/10 | 1.010864 | 2.439 |  | -0.0281 |
| 1.order, | L37 | L240 | 1/3,1/20 | 1.010857 | 2.439 |  | -0.0283 |
| Mesh- | L127 | L120 | 1/6,1/10 | 1.011214 | 2.452 |  | 0.0088 |
| Centered FD | ( | L120 | 0,1/10 | 1.011330 | 2.456 |  | 0.0052 |
|  | ( | ( | 0,0 | 1.011320 | 2.455 | -0.0017 | 0.0 |
| FEM-3Di | P | P12 | 1,1 |  |  |  |  |
| 2.order | P | P24 | 1,1/2 |  |  |  |  |
| Classical FEM | P | P24 | 1/2,1/2 |  |  |  |  |
|  | ( | ( | 0,0 | 1.011316 | 2.453 |  | 0.0060 |
| OSCAR2 | ( | ( | 0,0 | 1.011470 | 2.460 | -0.0182 | -0.0185 |

Table 6

CRONOS HXP19#-P24 SIX-TRIANGLE-PER-HEXAGON SOLUTION

Keff = 1.011415              Pmax = 2.454

3D Power Distribution Difference*100

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .521 | 1.071 | 1.449 | 1.578 | 1.333 | .000 | .000 | .000 | .000 | .000 |
| 02 | .420 | .865 | 1.171 | 1.278 | 1.136 | .790 | .565 | .397 | .248 | .110 |
| 03 | .546 | 1.123 | 1.521 | 1.665 | 1.529 | 1.202 | .892 | .629 | .394 | .175 |
| 04 | .552 | 1.134 | 1.536 | 1.683 | 1.556 | 1.246 | .932 | .658 | .412 | .183 |
| 05 | .440 | .907 | 1.229 | 1.349 | 1.260 | 1.031 | .780 | .552 | .346 | .154 |
| 06 | .556 | 1.144 | 1.551 | 1.705 | 1.598 | 1.318 | 1.001 | .711 | .446 | .198 |
| 07 | .565 | 1.161 | 1.574 | 1.728 | 1.614 | 1.321 | .999 | .707 | .443 | .197 |
| 08 | .562 | 1.157 | 1.568 | 1.723 | 1.607 | 1.313 | .992 | .703 | .441 | .196 |
| 09 | .435 | .896 | 1.216 | 1.338 | 1.250 | 1.022 | .775 | .551 | .346 | .154 |
| 10 | .543 | 1.119 | 1.520 | 1.676 | 1.574 | 1.298 | .991 | .709 | .447 | .200 |
| 11 | .450 | .928 | 1.259 | 1.380 | 1.272 | 1.011 | .754 | .533 | .335 | .149 |
| 12 | .570 | 1.173 | 1.591 | 1.745 | 1.597 | 1.244 | .921 | .652 | .410 | .183 |
| 13 | .442 | .911 | 1.238 | 1.362 | 1.262 | 1.010 | .760 | .542 | .342 | .153 |
| 14 | .440 | .908 | 1.236 | 1.369 | 1.294 | 1.078 | .832 | .600 | .380 | .170 |
| 15 | .575 | 1.186 | 1.619 | 1.803 | 1.733 | 1.481 | 1.166 | .848 | .540 | .242 |
| 16 | .463 | .955 | 1.296 | 1.418 | 1.254 | .853 | .606 | .429 | .270 | .120 |
| 17 | .593 | 1.221 | 1.658 | 1.816 | 1.613 | 1.106 | .792 | .563 | .356 | .159 |
| 18 | .588 | 1.212 | 1.649 | 1.819 | 1.685 | 1.338 | 1.010 | .726 | .460 | .206 |
| 19 | .463 | .958 | 1.307 | 1.453 | 1.388 | 1.173 | .917 | .666 | .424 | .190 |
| 20 | .583 | 1.204 | 1.646 | 1.842 | 1.788 | 1.552 | 1.237 | .906 | .578 | .260 |
| 21 | .516 | 1.065 | 1.459 | 1.638 | 1.603 | 1.407 | 1.132 | .833 | .533 | .240 |
| 22 | .617 | 1.271 | 1.727 | 1.890 | 1.602 | .000 | .000 | .000 | .000 | .000 |
| 23 | .494 | 1.021 | 1.388 | 1.527 | 1.369 | .963 | .702 | .503 | .319 | .143 |
| 24 | .620 | 1.279 | 1.744 | 1.933 | 1.820 | 1.496 | 1.152 | .834 | .531 | .238 |
| 25 | .466 | .962 | 1.315 | 1.468 | 1.416 | 1.217 | .963 | .704 | .449 | .201 |
| 26 | .621 | 1.278 | 1.749 | 1.962 | 1.915 | 1.676 | 1.345 | .988 | .632 | .285 |
| 27 | .429 | .885 | 1.212 | 1.364 | 1.339 | 1.181 | .954 | .703 | .451 | .203 |
| 28 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 |
| 29 | .652 | 1.344 | 1.829 | 2.014 | 1.813 | 1.288 | .944 | .679 | .431 | .194 |
| 30 | .513 | 1.060 | 1.445 | 1.599 | 1.494 | 1.203 | .919 | .664 | .423 | .189 |
| 31 | .733 | 1.507 | 2.058 | 2.291 | 2.193 | 1.860 | 1.459 | 1.063 | .677 | .305 |
| 32 | .588 | 1.210 | 1.654 | 1.851 | 1.797 | 1.559 | 1.243 | .910 | .582 | .262 |
| 33 | .382 | .788 | 1.079 | 1.213 | 1.187 | 1.042 | .839 | .617 | .395 | .178 |
| 34 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 |
| 35 | .790 | 1.624 | 2.214 | 2.454 | 2.310 | 1.896 | 1.459 | 1.056 | .672 | .303 |
| 36 | .698 | 1.434 | 1.957 | 2.177 | 2.077 | 1.753 | 1.370 | .995 | .634 | .286 |
| 37 | .523 | 1.077 | 1.472 | 1.643 | 1.585 | 1.364 | 1.079 | .788 | .503 | .226 |
| 38 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 |
| 39 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 |
| 40 | .480 | .989 | 1.350 | 1.502 | 1.438 | 1.220 | .956 | .695 | .443 | .199 |
| 41 | .415 | .854 | 1.166 | 1.300 | 1.251 | 1.072 | .845 | .616 | .393 | .177 |

Table 7

DIFFERENCE OF HXP19#-P24 RESULTS TO CRONOS RECOMMENDED SOLUTION

Keff = 1.011415          Pmax =  2.454

(Keff = 9.0 pcm         (Pmax = -0.002

3D Power Distribution Difference*100

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .13 | -.35 | -.63 | -.79 | -1.02 | .00 | .00 | .00 | .00 | .00 |
| 02 | .11 | -.21 | -.42 | -.53 | -.52 | -.29 | -.15 | -.08 | -.02 | .04 |
| 03 | .18 | -.30 | -.58 | -.73 | -.71 | -.52 | -.33 | -.19 | -.07 | .07 |
| 04 | .21 | -.25 | -.52 | -.67 | -.66 | -.50 | -.33 | -.19 | -.07 | .08 |
| 05 | .15 | -.18 | -.38 | -.50 | -.49 | -.39 | -.26 | -.15 | -.05 | .05 |
| 06 | .22 | -.23 | -.50 | -.64 | -.64 | -.51 | -.35 | -.20 | -.07 | .08 |
| 07 | .23 | -.24 | -.51 | -.66 | -.65 | -.52 | -.35 | -.20 | -.08 | .08 |
| 08 | .25 | -.19 | -.43 | -.57 | -.58 | -.46 | -.31 | -.17 | -.06 | .09 |
| 09 | .17 | -.11 | -.29 | -.39 | -.40 | -.31 | -.20 | -.11 | -.03 | .07 |
| 10 | .24 | -.15 | -.38 | -.52 | -.52 | -.41 | -.27 | -.14 | -.03 | .10 |
| 11 | .18 | -.12 | -.32 | -.43 | -.43 | -.33 | -.21 | -.11 | -.03 | .06 |
| 12 | .27 | -.16 | -.41 | -.55 | -.56 | -.41 | -.25 | -.13 | -.03 | .09 |
| 13 | .21 | -.05 | -.21 | -.31 | -.32 | -.25 | -.14 | -.06 | .00 | .08 |
| 14 | .22 | -.01 | -.17 | -.26 | -.28 | -.21 | -.12 | -.04 | .02 | .10 |
| 15 | .38 | .04 | -.15 | -.27 | -.29 | -.22 | -.12 | -.03 | .05 | .17 |
| 16 | .22 | -.07 | -.25 | -.36 | -.39 | -.25 | -.12 | -.05 | .00 | .06 |
| 17 | .34 | -.05 | -.27 | -.41 | -.45 | -.23 | -.08 | -.02 | .03 | .11 |
| 18 | .36 | -.01 | -.22 | -.36 | -.37 | -.26 | -.13 | -.04 | .04 | .14 |
| 19 | .28 | .04 | -.11 | -.20 | -.22 | -.17 | -.09 | -.02 | .05 | .13 |
| 20 | .47 | .13 | -.05 | -.16 | -.18 | -.13 | -.06 | .02 | .09 | .22 |
| 21 | .53 | .28 | .17 | .10 | .07 | .08 | .11 | .14 | .16 | .25 |
| 22 | .38 | -.02 | -.25 | -.40 | -.74 | .00 | .00 | .00 | .00 | .00 |
| 23 | .29 | .03 | -.14 | -.25 | -.29 | -.17 | -.06 | .00 | .04 | .10 |
| 24 | .45 | .06 | -.15 | -.28 | -.30 | -.21 | -.10 | -.01 | .07 | .19 |
| 25 | .36 | .13 | .00 | -.08 | -.10 | -.07 | -.01 | .04 | .09 | .17 |
| 26 | .70 | .34 | .21 | .13 | .09 | .11 | .14 | .17 | .20 | .33 |
| 27 | .53 | .34 | .29 | .25 | .22 | .21 | .20 | .20 | .19 | .25 |
| 28 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 29 | .46 | .04 | -.19 | -.34 | -.38 | -.18 | -.04 | .03 | .08 | .16 |
| 30 | .39 | .12 | -.04 | -.13 | -.15 | -.08 | .00 | .05 | .09 | .16 |
| 31 | .77 | .30 | .11 | -.01 | -.04 | .00 | .08 | .14 | .19 | .34 |
| 32 | .68 | .36 | .25 | .17 | .14 | .14 | .17 | .19 | .21 | .31 |
| 33 | .47 | .32 | .27 | .24 | .21 | .20 | .20 | .19 | .18 | .22 |
| 34 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 35 | .78 | .22 | -.02 | -.17 | -.20 | -.12 | -.01 | .08 | .15 | .32 |
| 36 | .81 | .39 | .24 | .15 | .11 | .13 | .17 | .20 | .22 | .35 |
| 37 | .64 | .38 | .31 | .25 | .21 | .21 | .21 | .21 | .21 | .28 |
| 38 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 39 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 40 | .52 | .31 | .22 | .16 | .13 | .13 | .15 | .16 | .17 | .23 |
| 41 | .48 | .28 | .21 | .16 | .14 | .14 | .15 | .16 | .16 | .21 |

DEVIATION RANGE:           -0.0102 ( (  ( 0.0081

REL.DEVIATION RANGE:   -0.76 % ( (’ ( 1.27%

Table 8

CRONOS HXP61#_P48 SOLUTION

hr=4.2435cm, hz=6.25cm

Keff  =  1.011376     Pmax  =  2.457

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .5202 | 1.0737 | 1.4538 | 1.5832 | 1.3406 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 02 | .4189 | .8660 | 1.1730 | 1.2806 | 1.1387 | .7911 | .5651 | .3971 | .2480 | .1098 |
| 03 | .5448 | 1.1250 | 1.5246 | 1.6699 | 1.5336 | 1.2054 | .8938 | .6301 | .3938 | .1744 |
| 04 | .5498 | 1.1353 | 1.5389 | 1.6871 | 1.5601 | 1.2489 | .9333 | .6588 | .4118 | .1824 |
| 05 | .4387 | .9075 | 1.2307 | 1.3518 | 1.2624 | 1.0333 | .7810 | .5526 | .3458 | .1529 |
| 06 | .5544 | 1.1454 | 1.5545 | 1.7097 | 1.6026 | 1.3212 | 1.0034 | .7116 | .4460 | .1977 |
| 07 | .5629 | 1.1628 | 1.5772 | 1.7326 | 1.6179 | 1.3244 | 1.0009 | .7084 | .4434 | .1965 |
| 08 | .5603 | 1.1577 | 1.5711 | 1.7265 | 1.6108 | 1.3155 | .9937 | .7040 | .4412 | .1956 |
| 09 | .4332 | .8966 | 1.2177 | 1.3399 | 1.2519 | 1.0240 | .7756 | .5512 | .3463 | .1536 |
| 10 | .5415 | 1.1199 | 1.5232 | 1.6804 | 1.5779 | 1.3008 | .9927 | .7096 | .4475 | .1991 |
| 11 | .4487 | .9286 | 1.2602 | 1.3826 | 1.2749 | 1.0129 | .7548 | .5339 | .3347 | .1483 |
| 12 | .5678 | 1.1739 | 1.5940 | 1.7487 | 1.6012 | 1.2464 | .9222 | .6532 | .4103 | .1823 |
| 13 | .4400 | .9114 | 1.2393 | 1.3643 | 1.2643 | 1.0117 | .7608 | .5426 | .3421 | .1521 |
| 14 | .4380 | .9080 | 1.2375 | 1.3706 | 1.2961 | 1.0792 | .8324 | .5997 | .3798 | .1691 |
| 15 | .5722 | 1.1860 | 1.6202 | 1.8058 | 1.7352 | 1.4832 | 1.1670 | .8487 | .5398 | .2410 |
| 16 | .4614 | .9555 | 1.2976 | 1.4197 | 1.2562 | .8547 | .6067 | .4286 | .2694 | .1198 |
| 17 | .5902 | 1.2210 | 1.6598 | 1.8194 | 1.6161 | 1.1078 | .7927 | .5631 | .3551 | .1583 |
| 18 | .5854 | 1.2120 | 1.6508 | 1.8221 | 1.6881 | 1.3398 | 1.0108 | .7258 | .4597 | .2050 |
| 19 | .4613 | .9574 | 1.3074 | 1.4548 | 1.3894 | 1.1745 | .9180 | .6665 | .4238 | .1889 |
| 20 | .5798 | 1.2030 | 1.6465 | 1.8435 | 1.7898 | 1.5535 | 1.2376 | .9058 | .5778 | .2581 |
| 21 | .5121 | 1.0632 | 1.4571 | 1.6374 | 1.6024 | 1.4067 | 1.1309 | .8317 | .5316 | .2377 |
| 22 | .6143 | 1.2714 | 1.7289 | 1.8928 | 1.6078 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 23 | .4920 | 1.0203 | 1.3894 | 1.5287 | 1.3714 | .9638 | .7020 | .5033 | .3190 | .1423 |
| 24 | .6170 | 1.2788 | 1.7452 | 1.9358 | 1.8231 | 1.4977 | 1.1533 | .8347 | .5305 | .2368 |
| 25 | .4627 | .9612 | 1.3146 | 1.4686 | 1.4169 | 1.2174 | .9631 | .7031 | .4482 | .1999 |
| 26 | .6153 | 1.2753 | 1.7473 | 1.9615 | 1.9152 | 1.6759 | 1.3440 | .9872 | .6307 | .2824 |
| 27 | .4255 | .8828 | 1.2108 | 1.3629 | 1.3383 | 1.1804 | .9528 | .7022 | .4493 | .2011 |
| 28 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 29 | .6485 | 1.3437 | 1.8308 | 2.0166 | 1.8161 | 1.2890 | .9448 | .6790 | .4309 | .1925 |
| 30 | .5102 | 1.0591 | 1.4450 | 1.6002 | 1.4946 | 1.2038 | .9187 | .6639 | .4219 | .1881 |
| 31 | .7270 | 1.5055 | 2.0574 | 2.2923 | 2.1943 | 1.8610 | 1.4593 | 1.0618 | .6761 | .3024 |
| 32 | .5826 | 1.2076 | 1.6530 | 1.8510 | 1.7968 | 1.5590 | 1.2419 | .9093 | .5802 | .2596 |
| 33 | .3791 | .7865 | 1.0781 | 1.2117 | 1.1860 | 1.0416 | .8377 | .6162 | .3940 | .1763 |
| 34 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 35 | .7841 | 1.6233 | 2.2154 | 2.4568 | 2.3122 | 1.8974 | 1.4597 | 1.0562 | .6714 | .3002 |
| 36 | .6914 | 1.4317 | 1.9557 | 2.1761 | 2.0764 | 1.7524 | 1.3687 | .9941 | .6325 | .2829 |
| 37 | .5187 | 1.0751 | 1.4702 | 1.6420 | 1.5845 | 1.3628 | 1.0780 | .7865 | .5012 | .2241 |
| 38 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 39 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 40 | .4758 | .9871 | 1.3485 | 1.5014 | 1.4366 | 1.2192 | .9549 | .6938 | .4415 | .1971 |
| 41 | .4115 | .8530 | 1.1659 | 1.3004 | 1.2514 | 1.0721 | .8451 | .6154 | .3918 | .1751 |

Table 9

CRONOS HXP61#_P72 SOLUTION

hr=4.2435cm, hz=4.1666667cm

Keff  =  1.011373     Pmax  =  2.457

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .5197 | 1.0736 | 1.4539 | 1.5834 | 1.3414 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 02 | .4186 | .8659 | 1.1730 | 1.2808 | 1.1390 | .7913 | .5653 | .3971 | .2480 | .1097 |
| 03 | .5443 | 1.1248 | 1.5247 | 1.6701 | 1.5339 | 1.2057 | .8940 | .6303 | .3939 | .1743 |
| 04 | .5493 | 1.1351 | 1.5389 | 1.6874 | 1.5605 | 1.2492 | .9335 | .6589 | .4119 | .1822 |
| 05 | .4384 | .9073 | 1.2307 | 1.3520 | 1.2626 | 1.0335 | .7812 | .5527 | .3458 | .1529 |
| 06 | .5539 | 1.1453 | 1.5545 | 1.7099 | 1.6029 | 1.3215 | 1.0036 | .7118 | .4460 | .1976 |
| 07 | .5623 | 1.1626 | 1.5773 | 1.7328 | 1.6182 | 1.3247 | 1.0012 | .7085 | .4435 | .1963 |
| 08 | .5598 | 1.1576 | 1.5711 | 1.7267 | 1.6112 | 1.3158 | .9939 | .7041 | .4412 | .1955 |
| 09 | .4328 | .8964 | 1.2178 | 1.3400 | 1.2521 | 1.0243 | .7758 | .5513 | .3463 | .1535 |
| 10 | .5410 | 1.1197 | 1.5232 | 1.6806 | 1.5782 | 1.3011 | .9929 | .7097 | .4475 | .1989 |
| 11 | .4483 | .9285 | 1.2603 | 1.3828 | 1.2751 | 1.0131 | .7549 | .5340 | .3347 | .1482 |
| 12 | .5673 | 1.1737 | 1.5940 | 1.7489 | 1.6015 | 1.2467 | .9224 | .6533 | .4103 | .1822 |
| 13 | .4397 | .9112 | 1.2393 | 1.3644 | 1.2646 | 1.0119 | .7610 | .5427 | .3421 | .1520 |
| 14 | .4376 | .9079 | 1.2375 | 1.3708 | 1.2963 | 1.0794 | .8326 | .5998 | .3798 | .1690 |
| 15 | .5716 | 1.1858 | 1.6202 | 1.8060 | 1.7355 | 1.4835 | 1.1672 | .8488 | .5398 | .2408 |
| 16 | .4610 | .9554 | 1.2977 | 1.4199 | 1.2565 | .8549 | .6068 | .4287 | .2694 | .1197 |
| 17 | .5896 | 1.2208 | 1.6598 | 1.8196 | 1.6164 | 1.1081 | .7929 | .5631 | .3551 | .1582 |
| 18 | .5848 | 1.2118 | 1.6508 | 1.8223 | 1.6884 | 1.3401 | 1.0110 | .7259 | .4597 | .2049 |
| 19 | .4609 | .9573 | 1.3074 | 1.4549 | 1.3896 | 1.1747 | .9182 | .6666 | .4238 | .1888 |
| 20 | .5791 | 1.2028 | 1.6465 | 1.8437 | 1.7901 | 1.5537 | 1.2378 | .9059 | .5778 | .2579 |
| 21 | .5115 | 1.0630 | 1.4571 | 1.6376 | 1.6026 | 1.4069 | 1.1311 | .8318 | .5315 | .2374 |
| 22 | .6137 | 1.2712 | 1.7289 | 1.8930 | 1.6087 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 23 | .4915 | 1.0201 | 1.3894 | 1.5288 | 1.3716 | .9640 | .7022 | .5034 | .3190 | .1422 |
| 24 | .6163 | 1.2786 | 1.7452 | 1.9360 | 1.8234 | 1.4979 | 1.1535 | .8348 | .5304 | .2366 |
| 25 | .4622 | .9610 | 1.3146 | 1.4688 | 1.4171 | 1.2176 | .9632 | .7032 | .4481 | .1997 |
| 26 | .6145 | 1.2751 | 1.7473 | 1.9617 | 1.9155 | 1.6762 | 1.3442 | .9873 | .6306 | .2820 |
| 27 | .4249 | .8826 | 1.2108 | 1.3630 | 1.3384 | 1.1806 | .9529 | .7023 | .4492 | .2009 |
| 28 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 29 | .6478 | 1.3435 | 1.8308 | 2.0169 | 1.8165 | 1.2894 | .9449 | .6790 | .4308 | .1924 |
| 30 | .5097 | 1.0589 | 1.4450 | 1.6004 | 1.4949 | 1.2041 | .9189 | .6640 | .4219 | .1879 |
| 31 | .7260 | 1.5052 | 2.0574 | 2.2925 | 2.1946 | 1.8613 | 1.4595 | 1.0619 | .6761 | .3020 |
| 32 | .5818 | 1.2074 | 1.6530 | 1.8512 | 1.7971 | 1.5593 | 1.2421 | .9094 | .5802 | .2593 |
| 33 | .3786 | .7864 | 1.0781 | 1.2118 | 1.1862 | 1.0418 | .8378 | .6163 | .3939 | .1761 |
| 34 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 35 | .7830 | 1.6230 | 2.2155 | 2.4571 | 2.3126 | 1.8978 | 1.4600 | 1.0563 | .6713 | .2998 |
| 36 | .6905 | 1.4314 | 1.9557 | 2.1763 | 2.0768 | 1.7527 | 1.3689 | .9942 | .6325 | .2825 |
| 37 | .5180 | 1.0749 | 1.4702 | 1.6422 | 1.5847 | 1.3630 | 1.0781 | .7866 | .5012 | .2238 |
| 38 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 39 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 40 | .4752 | .9869 | 1.3485 | 1.5015 | 1.4369 | 1.2194 | .9551 | .6939 | .4415 | .1968 |
| 41 | .4109 | .8528 | 1.1659 | 1.3005 | 1.2516 | 1.0723 | .8452 | .6154 | .3918 | .1749 |

Table 10

DIFFERENCE OF HXP61#_P72 SOLUTION TO DIF3D RECOMMENDED SOLUTION

Keff  =  1.011373      Pmax   =  2.457

(Keff =  5.3 pcm      ( Pmax  =  0.002

3D Power Distribution Difference*100

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | -.03 | -.14 | -.21 | -.26 | -.26 | .00 | .00 | .00 | .00 | .00 |
| 02 | -.04 | -.21 | -.30 | -.32 | -.30 | -.27 | -.17 | -.09 | -.10 | -.03 |
| 03 | -.07 | -.12 | -.23 | -.29 | -.31 | -.23 | -.20 | -.17 | -.11 | -.07 |
| 04 | -.07 | -.19 | -.21 | -.26 | -.35 | -.28 | -.25 | -.11 | -.11 | -.08 |
| 05 | -.06 | -.17 | -.23 | -.30 | -.24 | -.25 | -.18 | -.13 | -.12 | -.01 |
| 06 | -.01 | -.17 | -.25 | -.21 | -.21 | -.25 | -.14 | -.12 | -.10 | -.04 |
| 07 | -.07 | -.14 | -.27 | -.32 | -.28 | -.23 | -.18 | -.15 | -.05 | -.07 |
| 08 | -.02 | -.14 | -.19 | -.23 | -.28 | -.22 | -.21 | -.09 | -.08 | -.05 |
| 09 | -.02 | -.16 | -.12 | -.20 | -.19 | -.17 | -.12 | -.07 | -.07 | -.05 |
| 10 | .00 | -.03 | -.08 | -.14 | -.18 | -.09 | -.11 | -.03 | -.05 | -.01 |
| 11 | -.07 | -.15 | -.17 | -.22 | -.29 | -.19 | -.21 | -.10 | -.03 | .02 |
| 12 | .03 | -.13 | -.20 | -.21 | -.15 | -.13 | -.16 | -.07 | -.07 | .02 |
| 13 | -.03 | -.08 | -.17 | -.16 | -.14 | -.11 | -.10 | -.03 | -.09 | .00 |
| 14 | -.04 | -.01 | -.05 | -.12 | -.07 | -.06 | -.04 | -.02 | -.02 | .00 |
| 15 | .06 | .08 | .02 | .00 | -.05 | -.05 | .02 | -.02 | -.02 | -.02 |
| 16 | .00 | -.06 | -.13 | -.21 | -.15 | -.21 | -.12 | -.13 | -.06 | -.03 |
| 17 | .06 | -.02 | -.12 | -.14 | -.16 | -.09 | -.11 | -.09 | .01 | .02 |
| 18 | .08 | -.02 | -.02 | -.07 | -.06 | -.09 | .00 | -.01 | -.03 | -.01 |
| 19 | -.01 | .03 | -.06 | -.01 | -.04 | -.03 | -.08 | -.04 | -.02 | -.02 |
| 20 | .11 | .08 | .05 | .07 | .01 | .07 | -.02 | -.01 | -.02 | -.01 |
| 21 | .05 | .10 | .01 | .06 | .06 | -.01 | .01 | .08 | .05 | .04 |
| 22 | .07 | .02 | -.01 | -.10 | -.13 | .00 | .00 | .00 | .00 | .00 |
| 23 | .05 | .01 | -.06 | -.12 | -.14 | -.10 | -.08 | -.06 | .00 | .02 |
| 24 | .03 | .06 | .02 | .00 | .04 | -.01 | .05 | -.02 | .04 | .06 |
| 25 | .02 | .00 | -.04 | -.02 | .01 | -.04 | .02 | .02 | .01 | -.03 |
| 26 | .15 | .21 | .23 | .17 | .15 | .12 | .12 | .13 | .06 | .10 |
| 27 | .09 | .16 | .28 | .30 | .24 | .26 | .19 | .13 | .12 | .09 |
| 28 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 29 | .08 | .05 | -.02 | -.01 | -.05 | -.06 | -.01 | .00 | -.02 | .04 |
| 30 | .07 | -.01 | .00 | -.06 | -.01 | -.09 | -.01 | .00 | -.01 | -.01 |
| 31 | .10 | .12 | .14 | .15 | .16 | .13 | .15 | .09 | .11 | .10 |
| 32 | .18 | .24 | .30 | .22 | .21 | .23 | .21 | .14 | .12 | .03 |
| 33 | .16 | .24 | .31 | .28 | .32 | .28 | .18 | .13 | .09 | .11 |
| 34 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 35 | .20 | .20 | .15 | .21 | .16 | .08 | .10 | .03 | .03 | .08 |
| 36 | .15 | .14 | .17 | .13 | .18 | .17 | .09 | .12 | .05 | .05 |
| 37 | .20 | .19 | .32 | .32 | .27 | .20 | .21 | .16 | .12 | .08 |
| 38 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 39 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 40 | .12 | .09 | .15 | .15 | .09 | .04 | .11 | .09 | .05 | .08 |
| 41 | .19 | .18 | .29 | .35 | .26 | .23 | .22 | .14 | .08 | .09 |

DEVIATION RANGE:         -0.0032 ( ( ( 0.0032

REL.DEVIATION RANGE: -0.42%  ( (’ (  0.62%

Table 11

CRONOS FINEST HXP127#_P72 SOLUTION

hr=2.829cm,    hz=4.1666667cm

Keff= 1.011357   Pmax = 2.4565

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .5201 | 1.0743 | 1.4549 | 1.5845 | 1.3423 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 02 | .4189 | .8666 | 1.1740 | 1.2818 | 1.1399 | .7919 | .5657 | .3974 | .2482 | .1098 |
| 03 | .5447 | 1.1256 | 1.5257 | 1.6712 | 1.5349 | 1.2064 | .8946 | .6306 | .3941 | .1744 |
| 04 | .5496 | 1.1358 | 1.5399 | 1.6885 | 1.5615 | 1.2500 | .9341 | .6593 | .4121 | .1823 |
| 05 | .4387 | .9080 | 1.2316 | 1.3530 | 1.2635 | 1.0343 | .7817 | .5531 | .3460 | .1530 |
| 06 | .5542 | 1.1459 | 1.5553 | 1.7107 | 1.6037 | 1.3222 | 1.0041 | .7121 | .4462 | .1977 |
| 07 | .5627 | 1.1633 | 1.5782 | 1.7338 | 1.6191 | 1.3255 | 1.0017 | .7089 | .4437 | .1964 |
| 08 | .5601 | 1.1582 | 1.5719 | 1.7275 | 1.6119 | 1.3165 | .9944 | .7045 | .4414 | .1956 |
| 09 | .4330 | .8969 | 1.2184 | 1.3407 | 1.2527 | 1.0248 | .7761 | .5515 | .3464 | .1535 |
| 10 | .5411 | 1.1200 | 1.5236 | 1.6811 | 1.5786 | 1.3014 | .9931 | .7099 | .4476 | .1990 |
| 11 | .4486 | .9290 | 1.2610 | 1.3835 | 1.2758 | 1.0137 | .7554 | .5343 | .3349 | .1483 |
| 12 | .5675 | 1.1741 | 1.5946 | 1.7495 | 1.6020 | 1.2472 | .9227 | .6535 | .4104 | .1822 |
| 13 | .4398 | .9116 | 1.2398 | 1.3649 | 1.2650 | 1.0123 | .7612 | .5428 | .3422 | .1520 |
| 14 | .4378 | .9081 | 1.2378 | 1.3711 | 1.2966 | 1.0796 | .8327 | .5998 | .3799 | .1690 |
| 15 | .5717 | 1.1859 | 1.6203 | 1.8060 | 1.7355 | 1.4834 | 1.1671 | .8487 | .5397 | .2407 |
| 16 | .4612 | .9558 | 1.2982 | 1.4205 | 1.2570 | .8553 | .6071 | .4289 | .2695 | .1197 |
| 17 | .5897 | 1.2211 | 1.6602 | 1.8200 | 1.6168 | 1.1083 | .7930 | .5632 | .3551 | .1582 |
| 18 | .5849 | 1.2119 | 1.6510 | 1.8225 | 1.6885 | 1.3402 | 1.0110 | .7259 | .4597 | .2048 |
| 19 | .4609 | .9574 | 1.3076 | 1.4551 | 1.3897 | 1.1747 | .9182 | .6666 | .4237 | .1888 |
| 20 | .5791 | 1.2027 | 1.6464 | 1.8435 | 1.7899 | 1.5535 | 1.2375 | .9057 | .5776 | .2578 |
| 21 | .5114 | 1.0629 | 1.4570 | 1.6374 | 1.6024 | 1.4067 | 1.1308 | .8316 | .5314 | .2373 |
| 22 | .6138 | 1.2714 | 1.7292 | 1.8933 | 1.6089 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 23 | .4916 | 1.0203 | 1.3897 | 1.5291 | 1.3719 | .9642 | .7022 | .5034 | .3190 | .1422 |
| 24 | .6163 | 1.2786 | 1.7452 | 1.9359 | 1.8233 | 1.4978 | 1.1533 | .8346 | .5303 | .2365 |
| 25 | .4622 | .9611 | 1.3147 | 1.4688 | 1.4171 | 1.2175 | .9632 | .7031 | .4481 | .1997 |
| 26 | .6144 | 1.2747 | 1.7468 | 1.9611 | 1.9149 | 1.6756 | 1.3436 | .9869 | .6303 | .2819 |
| 27 | .4247 | .8821 | 1.2101 | 1.3622 | 1.3376 | 1.1798 | .9522 | .7018 | .4489 | .2008 |
| 28 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 29 | .6479 | 1.3435 | 1.8308 | 2.0169 | 1.8164 | 1.2892 | .9448 | .6789 | .4307 | .1923 |
| 30 | .5097 | 1.0591 | 1.4451 | 1.6005 | 1.4950 | 1.2040 | .9188 | .6639 | .4218 | .1879 |
| 31 | .7259 | 1.5049 | 2.0570 | 2.2920 | 2.1940 | 1.8607 | 1.4590 | 1.0615 | .6758 | .3019 |
| 32 | .5816 | 1.2069 | 1.6523 | 1.8504 | 1.7962 | 1.5585 | 1.2414 | .9089 | .5798 | .2591 |
| 33 | .3783 | .7858 | 1.0773 | 1.2109 | 1.1853 | 1.0409 | .8371 | .6158 | .3936 | .1759 |
| 34 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 35 | .7829 | 1.6227 | 2.2150 | 2.4565 | 2.3120 | 1.8972 | 1.4594 | 1.0559 | .6711 | .2997 |
| 36 | .6903 | 1.4311 | 1.9552 | 2.1758 | 2.0761 | 1.7521 | 1.3683 | .9937 | .6322 | .2824 |
| 37 | .5177 | 1.0743 | 1.4694 | 1.6413 | 1.5838 | 1.3622 | 1.0774 | .7860 | .5008 | .2236 |
| 38 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 39 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 40 | .4751 | .9867 | 1.3482 | 1.5011 | 1.4364 | 1.2190 | .9547 | .6936 | .4413 | .1968 |
| 41 | .4107 | .8522 | 1.1651 | 1.2996 | 1.2506 | 1.0714 | .8445 | .6149 | .3914 | .1747 |

Table 12

DIFFERENCE OF THE CRONOS FINEST TO CRONOS RECOMMENDED

SOLUTION

Keff = 1.011357          Pmax = 2.4565

(Keff = 3.2 pcm          (Pmax = 0.0003

3D Power Distribution Difference*100

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .01 | -.05 | -.09 | -.11 | -.14 | .00 | .00 | .00 | .00 | .00 |
| 02 | .00 | -.05 | -.09 | -.11 | -.11 | -.08 | -.06 | -.04 | -.02 | .00 |
| 03 | .01 | -.05 | -.09 | -.12 | -.12 | -.10 | -.07 | -.05 | -.03 | .00 |
| 04 | .01 | -.05 | -.09 | -.12 | -.12 | -.10 | -.07 | -.05 | -.03 | .00 |
| 05 | .00 | -.05 | -.09 | -.10 | -.10 | -.09 | -.07 | -.05 | -.02 | .00 |
| 06 | .02 | -.04 | -.07 | -.09 | -.09 | -.08 | -.06 | -.04 | -.02 | .00 |
| 07 | .01 | -.05 | -.08 | -.10 | -.11 | -.09 | -.07 | -.05 | -.02 | .00 |
| 08 | .02 | -.04 | -.07 | -.09 | -.10 | -.08 | -.06 | -.04 | -.02 | .00 |
| 09 | .01 | -.03 | -.06 | -.07 | -.08 | -.07 | -.05 | -.03 | -.02 | .00 |
| 10 | .03 | -.01 | -.03 | -.05 | -.05 | -.04 | -.03 | -.02 | -.01 | .01 |
| 11 | .01 | -.04 | -.07 | -.09 | -.09 | -.07 | -.06 | -.04 | -.02 | .00 |
| 12 | .03 | -.02 | -.05 | -.07 | -.07 | -.06 | -.05 | -.03 | -.01 | .01 |
| 13 | .01 | -.02 | -.04 | -.06 | -.06 | -.05 | -.04 | -.02 | -.01 | .00 |
| 14 | .02 | -.01 | -.03 | -.04 | -.04 | -.04 | -.02 | -.01 | .00 | .01 |
| 15 | .05 | .02 | .00 | -.01 | -.02 | -.01 | -.01 | .00 | .01 | .02 |
| 16 | .01 | -.03 | -.05 | -.07 | -.07 | -.06 | -.04 | -.03 | -.01 | .00 |
| 17 | .03 | -.01 | -.03 | -.05 | -.06 | -.05 | -.03 | -.02 | -.01 | .01 |
| 18 | .04 | .01 | -.01 | -.03 | -.03 | -.03 | -.02 | -.01 | .00 | .01 |
| 19 | .03 | .00 | -.01 | -.03 | -.03 | -.02 | -.01 | -.01 | .00 | .01 |
| 20 | .05 | .02 | .01 | .00 | .00 | .00 | .00 | .01 | .01 | .02 |
| 21 | .05 | .02 | .01 | .00 | .00 | .00 | .00 | .01 | .01 | .02 |
| 22 | .04 | .00 | -.02 | -.04 | -.08 | .00 | .00 | .00 | .00 | .00 |
| 23 | .03 | .00 | -.03 | -.04 | -.04 | -.04 | -.02 | -.01 | .00 | .01 |
| 24 | .05 | .02 | .01 | .00 | -.01 | -.01 | .00 | .01 | .01 | .02 |
| 25 | .03 | .01 | -.01 | -.02 | -.02 | -.02 | -.01 | .00 | .01 | .02 |
| 26 | .08 | .05 | .04 | .04 | .03 | .03 | .03 | .03 | .03 | .04 |
| 27 | .07 | .06 | .06 | .06 | .06 | .06 | .05 | .04 | .03 | .03 |
| 28 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 29 | .06 | .02 | .00 | -.01 | -.02 | -.01 | .00 | .00 | .01 | .02 |
| 30 | .04 | .00 | -.02 | -.03 | -.03 | -.02 | -.01 | .00 | .00 | .01 |
| 31 | .09 | .06 | .05 | .04 | .03 | .03 | .03 | .03 | .03 | .04 |
| 32 | .08 | .07 | .07 | .06 | .06 | .05 | .05 | .04 | .04 | .04 |
| 33 | .06 | .07 | .07 | .08 | .07 | .06 | .06 | .05 | .04 | .03 |
| 34 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 35 | .10 | .06 | .05 | .04 | .03 | .03 | .03 | .03 | .03 | .04 |
| 36 | .09 | .05 | .04 | .03 | .03 | .03 | .03 | .03 | .03 | .04 |
| 37 | .08 | .07 | .07 | .07 | .07 | .06 | .05 | .05 | .04 | .04 |
| 38 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 39 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 40 | .05 | .03 | .03 | .02 | .02 | .02 | .02 | .02 | .02 | .02 |
| 41 | .07 | .07 | .08 | .08 | .08 | .07 | .06 | .05 | .04 | .03 |

DEVIATION RANGE:  -0.0014 ( ( ( 0.0010

Table 13

EXTRAPOLATED CRONOS 2nd-ORDER SOLUTION

hr=0.000000  hz=0.000000

Keff= 1.011325   Pmax = 2.4562

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .5200 | 1.0748 | 1.4558 | 1.5856 | 1.3437 | 0 | 0 | 0 | 0 | 0 |
| 02 | .4190 | .8671 | 1.1749 | 1.2829 | 1.1410 | .7928 | .5663 | .3978 | .2484 | .1099 |
| 03 | .5446 | 1.1261 | 1.5266 | 1.6723 | 1.5360 | 1.2074 | .8953 | .6311 | .3944 | .1744 |
| 04 | .5495 | 1.1364 | 1.5409 | 1.6896 | 1.5626 | 1.2510 | .9349 | .6598 | .4124 | .1824 |
| 05 | .4387 | .9085 | 1.2325 | 1.3540 | 1.2646 | 1.0352 | .7824 | .5535 | .3463 | .1530 |
| 06 | .5540 | 1.1462 | 1.5560 | 1.7117 | 1.6046 | 1.3230 | 1.0047 | .7125 | .4464 | .1976 |
| 07 | .5625 | 1.1637 | 1.5790 | 1.7349 | 1.6202 | 1.3264 | 1.0024 | .7094 | .4439 | .1964 |
| 08 | .5599 | 1.1585 | 1.5726 | 1.7285 | 1.6129 | 1.3173 | .9950 | .7049 | .4416 | .1956 |
| 09 | .4330 | .8972 | 1.2190 | 1.3414 | 1.2535 | 1.0254 | .7766 | .5519 | .3466 | .1535 |
| 10 | .5408 | 1.1201 | 1.5239 | 1.6815 | 1.5791 | 1.3018 | .9934 | .7100 | .4476 | .1989 |
| 11 | .4485 | .9294 | 1.2617 | 1.3844 | 1.2767 | 1.0144 | .7559 | .5346 | .3351 | .1483 |
| 12 | .5672 | 1.1744 | 1.5951 | 1.7502 | 1.6028 | 1.2478 | .9232 | .6538 | .4106 | .1822 |
| 13 | .4397 | .9118 | 1.2402 | 1.3655 | 1.2656 | 1.0128 | .7616 | .5431 | .3423 | .1520 |
| 14 | .4376 | .9082 | 1.2381 | 1.3715 | 1.2970 | 1.0799 | .8330 | .6000 | .3799 | .1689 |
| 15 | .5712 | 1.1857 | 1.6203 | 1.8061 | 1.7356 | 1.4836 | 1.1672 | .8486 | .5396 | .2405 |
| 16 | .4611 | .9560 | 1.2987 | 1.4212 | 1.2578 | .8560 | .6075 | .4291 | .2696 | .1197 |
| 17 | .5894 | 1.2212 | 1.6605 | 1.8205 | 1.6174 | 1.1087 | .7933 | .5634 | .3552 | .1582 |
| 18 | .5845 | 1.2119 | 1.6512 | 1.8227 | 1.6889 | 1.3405 | 1.0112 | .7260 | .4596 | .2047 |
| 19 | .4607 | .9574 | 1.3077 | 1.4554 | 1.3900 | 1.1750 | .9183 | .6666 | .4237 | .1886 |
| 20 | .5786 | 1.2025 | 1.6463 | 1.8435 | 1.7899 | 1.5535 | 1.2375 | .9057 | .5775 | .2576 |
| 21 | .5109 | 1.0627 | 1.4569 | 1.6374 | 1.6024 | 1.4067 | 1.1308 | .8315 | .5312 | .2371 |
| 22 | .6134 | 1.2714 | 1.7294 | 1.8937 | 1.6097 | 0 | 0 | 0 | 0 | 0 |
| 23 | .4914 | 1.0204 | 1.3899 | 1.5295 | 1.3723 | .9645 | .7024 | .5035 | .3190 | .1421 |
| 24 | .6158 | 1.2784 | 1.7451 | 1.9359 | 1.8234 | 1.4978 | 1.1533 | .8346 | .5302 | .2363 |
| 25 | .4619 | .9610 | 1.3148 | 1.4690 | 1.4173 | 1.2177 | .9632 | .7031 | .4480 | .1996 |
| 26 | .6136 | 1.2742 | 1.7464 | 1.9608 | 1.9146 | 1.6753 | 1.3433 | .9866 | .6301 | .2815 |
| 27 | .4240 | .8815 | 1.2094 | 1.3615 | 1.3370 | 1.1793 | .9518 | .7014 | .4486 | .2004 |
| 28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 29 | .6473 | 1.3433 | 1.8308 | 2.0170 | 1.8166 | 1.2894 | .9448 | .6789 | .4307 | .1921 |
| 30 | .5094 | 1.0590 | 1.4453 | 1.6008 | 1.4952 | 1.2043 | .9189 | .6639 | .4218 | .1878 |
| 31 | .7250 | 1.5044 | 2.0565 | 2.2916 | 2.1937 | 1.8604 | 1.4587 | 1.0612 | .6755 | .3015 |
| 32 | .5807 | 1.2062 | 1.6517 | 1.8498 | 1.7957 | 1.5579 | 1.2410 | .9085 | .5795 | .2588 |
| 33 | .3777 | .7851 | 1.0766 | 1.2101 | 1.1846 | 1.0403 | .8365 | .6153 | .3932 | .1756 |
| 34 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 35 | .7819 | 1.6221 | 2.2145 | 2.4562 | 2.3117 | 1.8969 | 1.4591 | 1.0556 | .6708 | .2993 |
| 36 | .6894 | 1.4306 | 1.9548 | 2.1754 | 2.0758 | 1.7518 | 1.3680 | .9934 | .6319 | .2820 |
| 37 | .5169 | 1.0736 | 1.4687 | 1.6405 | 1.5831 | 1.3615 | 1.0769 | .7856 | .5004 | .2233 |
| 38 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 39 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 40 | .4745 | .9863 | 1.3479 | 1.5009 | 1.4362 | 1.2188 | .9545 | .6934 | .4411 | .1965 |
| 41 | .4100 | .8515 | 1.1643 | 1.2988 | 1.2499 | 1.0707 | .8439 | .6144 | .3911 | .1744 |

Table 14

CRONOS C37_P24 SOLUTION

hr=2.829 cm ,   hz=12.5 cm

Keff = 1.011401  Pmax = 2.456

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .523 | 1.074 | 1.453 | 1.581 | 1.336 | .000 | .000 | .000 | .000 | .000 |
| 02 | .421 | .866 | 1.172 | 1.279 | 1.137 | .789 | .564 | .396 | .248 | .110 |
| 03 | .548 | 1.126 | 1.524 | 1.668 | 1.531 | 1.203 | .892 | .629 | .393 | .175 |
| 04 | .553 | 1.136 | 1.538 | 1.685 | 1.558 | 1.247 | .932 | .658 | .411 | .183 |
| 05 | .441 | .908 | 1.230 | 1.350 | 1.260 | 1.031 | .780 | .552 | .345 | .153 |
| 06 | .557 | 1.146 | 1.554 | 1.708 | 1.600 | 1.319 | 1.002 | .711 | .446 | .198 |
| 07 | .566 | 1.163 | 1.577 | 1.731 | 1.616 | 1.322 | .999 | .707 | .443 | .197 |
| 08 | .563 | 1.158 | 1.571 | 1.725 | 1.609 | 1.313 | .992 | .703 | .441 | .196 |
| 09 | .435 | .897 | 1.217 | 1.339 | 1.250 | 1.022 | .774 | .550 | .346 | .154 |
| 10 | .544 | 1.121 | 1.523 | 1.679 | 1.576 | 1.299 | .991 | .709 | .447 | .200 |
| 11 | .451 | .929 | 1.260 | 1.381 | 1.273 | 1.011 | .753 | .533 | .334 | .149 |
| 12 | .571 | 1.175 | 1.594 | 1.747 | 1.599 | 1.244 | .921 | .652 | .410 | .183 |
| 13 | .442 | .912 | 1.239 | 1.363 | 1.263 | 1.010 | .760 | .542 | .342 | .153 |
| 14 | .440 | .909 | 1.237 | 1.370 | 1.295 | 1.078 | .831 | .599 | .380 | .170 |
| 15 | .576 | 1.187 | 1.620 | 1.805 | 1.734 | 1.482 | 1.166 | .848 | .540 | .242 |
| 16 | .464 | .956 | 1.297 | 1.418 | 1.254 | .853 | .606 | .428 | .269 | .120 |
| 17 | .594 | 1.222 | 1.660 | 1.818 | 1.614 | 1.106 | .792 | .562 | .355 | .159 |
| 18 | .589 | 1.213 | 1.651 | 1.821 | 1.686 | 1.338 | 1.010 | .725 | .460 | .206 |
| 19 | .464 | .958 | 1.307 | 1.454 | 1.388 | 1.173 | .917 | .666 | .424 | .190 |
| 20 | .584 | 1.205 | 1.647 | 1.843 | 1.788 | 1.552 | 1.236 | .905 | .578 | .260 |
| 21 | .516 | 1.065 | 1.457 | 1.637 | 1.601 | 1.405 | 1.130 | .831 | .532 | .239 |
| 22 | .618 | 1.273 | 1.729 | 1.891 | 1.603 | .000 | .000 | .000 | .000 | .000 |
| 23 | .495 | 1.021 | 1.389 | 1.528 | 1.370 | .962 | .701 | .503 | .319 | .143 |
| 24 | .621 | 1.280 | 1.745 | 1.935 | 1.822 | 1.496 | 1.152 | .834 | .531 | .238 |
| 25 | .466 | .962 | 1.315 | 1.468 | 1.415 | 1.216 | .962 | .703 | .448 | .201 |
| 26 | .620 | 1.277 | 1.748 | 1.961 | 1.914 | 1.675 | 1.343 | .987 | .631 | .284 |
| 27 | .429 | .884 | 1.211 | 1.363 | 1.338 | 1.180 | .952 | .702 | .450 | .203 |
| 28 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 |
| 29 | .653 | 1.345 | 1.831 | 2.016 | 1.814 | 1.287 | .944 | .678 | .431 | .194 |
| 30 | .513 | 1.060 | 1.445 | 1.599 | 1.493 | 1.202 | .918 | .663 | .422 | .189 |
| 31 | .733 | 1.508 | 2.058 | 2.292 | 2.193 | 1.859 | 1.458 | 1.061 | .676 | .304 |
| 32 | .588 | 1.210 | 1.654 | 1.851 | 1.796 | 1.558 | 1.241 | .909 | .581 | .261 |
| 33 | .382 | .788 | 1.079 | 1.212 | 1.186 | 1.041 | .837 | .616 | .394 | .178 |
| 34 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 |
| 35 | .791 | 1.626 | 2.216 | 2.456 | 2.311 | 1.896 | 1.459 | 1.056 | .672 | .302 |
| 36 | .697 | 1.434 | 1.956 | 2.175 | 2.075 | 1.751 | 1.367 | .994 | .633 | .285 |
| 37 | .523 | 1.077 | 1.471 | 1.642 | 1.584 | 1.362 | 1.077 | .786 | .502 | .226 |
| 38 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 |
| 39 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 | .000 |
| 40 | .479 | .989 | 1.349 | 1.501 | 1.435 | 1.218 | .954 | .693 | .442 | .198 |
| 41 | .415 | .855 | 1.167 | 1.301 | 1.251 | 1.072 | .845 | .615 | .392 | .176 |

Table 15

DIFFERENCE OF HXC37-P24 RESULTS TO CRONOS RECOMMENDED SOLUTION

Keff = 1.011401       Pmax = 2.456

(Keff = 7.6 pcm      (Pmax = 0.000

3D Power Distribution Difference*100 DEVIATION RANGE: -0.0077( ( ( 0.0086

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .27 | -.06 | -.26 | -.42 | -.77 | .00 | .00 | .00 | .00 | .00 |
| 02 | .18 | -.09 | -.26 | -.39 | -.44 | -.35 | -.23 | -.15 | -.07 | .02 |
| 03 | .30 | -.06 | -.27 | -.42 | -.48 | -.42 | -.30 | -.19 | -.09 | .06 |
| 04 | .31 | -.06 | -.27 | -.42 | -.48 | -.43 | -.32 | -.20 | -.09 | .06 |
| 05 | .20 | -.07 | -.25 | -.37 | -.42 | -.37 | -.28 | -.18 | -.08 | .04 |
| 06 | .33 | -.01 | -.21 | -.35 | -.42 | -.38 | -.29 | -.18 | -.07 | .08 |
| 07 | .33 | -.03 | -.24 | -.39 | -.45 | -.41 | -.31 | -.20 | -.09 | .08 |
| 08 | .34 | -.01 | -.21 | -.36 | -.42 | -.39 | -.29 | -.18 | -.08 | .08 |
| 09 | .22 | -.01 | -.17 | -.29 | -.34 | -.30 | -.23 | -.14 | -.06 | .05 |
| 10 | .36 | .08 | -.09 | -.22 | -.29 | -.27 | -.20 | -.12 | -.03 | .10 |
| 11 | .23 | -.03 | -.20 | -.33 | -.37 | -.34 | -.25 | -.16 | -.07 | .04 |
| 12 | .37 | .04 | -.15 | -.30 | -.37 | -.33 | -.24 | -.14 | -.05 | .08 |
| 13 | .24 | .02 | -.13 | -.24 | -.30 | -.26 | -.19 | -.11 | -.04 | .06 |
| 14 | .26 | .06 | -.08 | -.19 | -.24 | -.22 | -.16 | -.09 | -.02 | .08 |
| 15 | .45 | .17 | .01 | -.12 | -.19 | -.19 | -.14 | -.06 | .02 | .16 |
| 16 | .26 | .01 | -.16 | -.29 | -.36 | -.30 | -.19 | -.12 | -.05 | .04 |
| 17 | .42 | .09 | -.09 | -.25 | -.35 | -.29 | -.17 | -.10 | -.03 | .08 |
| 18 | .44 | .14 | -.04 | -.18 | -.26 | -.24 | -.16 | -.08 | .00 | .12 |
| 19 | .31 | .11 | -.03 | -.15 | -.20 | -.19 | -.14 | -.07 | .00 | .10 |
| 20 | .51 | .21 | .05 | -.08 | -.16 | -.16 | -.12 | -.04 | .04 | .19 |
| 21 | .49 | .19 | .04 | -.08 | -.14 | -.14 | -.10 | -.04 | .04 | .20 |
| 22 | .46 | .13 | -.06 | -.23 | -.67 | .00 | .00 | .00 | .00 | .00 |
| 23 | .33 | .09 | -.07 | -.20 | -.28 | -.24 | -.14 | -.08 | -.01 | .07 |
| 24 | .52 | .21 | .03 | -.11 | -.19 | -.18 | -.12 | -.05 | .03 | .17 |
| 25 | .36 | .13 | -.02 | -.13 | -.18 | -.17 | -.13 | -.06 | .02 | .13 |
| 26 | .69 | .30 | .15 | .02 | -.05 | -.07 | -.05 | .01 | .09 | .28 |
| 27 | .51 | .29 | .20 | .13 | .07 | .05 | .05 | .07 | .10 | .21 |
| 28 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 29 | .54 | .21 | .02 | -.14 | -.25 | -.21 | -.10 | -.04 | .03 | .14 |
| 30 | .39 | .13 | -.04 | -.16 | -.23 | -.20 | -.13 | -.06 | .01 | .12 |
| 31 | .80 | .34 | .16 | .00 | -.09 | -.11 | -.06 | .01 | .09 | .29 |
| 32 | .68 | .34 | .21 | .09 | .02 | -.01 | .01 | .05 | .11 | .26 |
| 33 | .46 | .29 | .23 | .17 | .12 | .09 | .08 | .08 | .10 | .19 |
| 34 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 35 | .86 | .37 | .16 | .00 | -.11 | -.12 | -.06 | .01 | .09 | .29 |
| 36 | .79 | .33 | .15 | .00 | -.09 | -.10 | -.06 | .01 | .09 | .29 |
| 37 | .62 | .34 | .23 | .13 | .07 | .04 | .04 | .07 | .11 | .24 |
| 38 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 39 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 40 | .49 | .22 | .09 | -.02 | -.08 | -.08 | -.05 | .00 | .06 | .18 |
| 41 | .50 | .32 | .25 | .18 | .12 | .09 | .08 | .09 | .11 | .19 |

Table 16

CRONOS HXC37_P36 3rd-ORDER SOLUTION

hr=8.487cm, hz=8.3333333cm

Keff  =  1.011392     Pmax  =  2.4571

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .5208 | 1.0736 | 1.4533 | 1.5823 | 1.3390 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 02 | .4193 | .8657 | 1.1723 | 1.2796 | 1.1376 | .7901 | .5645 | .3966 | .2477 | .1098 |
| 03 | .5455 | 1.1249 | 1.5240 | 1.6689 | 1.5324 | 1.2043 | .8930 | .6296 | .3936 | .1745 |
| 04 | .5504 | 1.1351 | 1.5382 | 1.6862 | 1.5590 | 1.2478 | .9325 | .6582 | .4116 | .1825 |
| 05 | .4391 | .9072 | 1.2301 | 1.3509 | 1.2613 | 1.0323 | .7802 | .5521 | .3455 | .1530 |
| 06 | .5551 | 1.1454 | 1.5540 | 1.7089 | 1.6016 | 1.3203 | 1.0027 | .7111 | .4458 | .1978 |
| 07 | .5636 | 1.1627 | 1.5767 | 1.7317 | 1.6168 | 1.3234 | 1.0001 | .7078 | .4432 | .1966 |
| 08 | .5611 | 1.1577 | 1.5706 | 1.7256 | 1.6098 | 1.3146 | .9929 | .7035 | .4410 | .1958 |
| 09 | .4336 | .8965 | 1.2173 | 1.3391 | 1.2510 | 1.0232 | .7750 | .5508 | .3461 | .1536 |
| 10 | .5422 | 1.1201 | 1.5231 | 1.6800 | 1.5773 | 1.3002 | .9922 | .7093 | .4474 | .1993 |
| 11 | .4492 | .9285 | 1.2597 | 1.3818 | 1.2739 | 1.0120 | .7541 | .5334 | .3345 | .1484 |
| 12 | .5686 | 1.1740 | 1.5937 | 1.7480 | 1.6003 | 1.2456 | .9216 | .6528 | .4101 | .1824 |
| 13 | .4405 | .9114 | 1.2390 | 1.3637 | 1.2636 | 1.0110 | .7603 | .5423 | .3420 | .1522 |
| 14 | .4386 | .9082 | 1.2373 | 1.3702 | 1.2955 | 1.0786 | .8320 | .5994 | .3797 | .1692 |
| 15 | .5732 | 1.1865 | 1.6203 | 1.8056 | 1.7349 | 1.4828 | 1.1667 | .8485 | .5398 | .2413 |
| 16 | .4620 | .9555 | 1.2972 | 1.4190 | 1.2553 | .8539 | .6061 | .4282 | .2692 | .1198 |
| 17 | .5911 | 1.2212 | 1.6596 | 1.8188 | 1.6153 | 1.1071 | .7922 | .5628 | .3549 | .1585 |
| 18 | .5863 | 1.2123 | 1.6508 | 1.8217 | 1.6876 | 1.3393 | 1.0104 | .7256 | .4596 | .2053 |
| 19 | .4620 | .9577 | 1.3074 | 1.4545 | 1.3889 | 1.1740 | .9177 | .6663 | .4237 | .1891 |
| 20 | .5809 | 1.2036 | 1.6467 | 1.8434 | 1.7895 | 1.5531 | 1.2373 | .9057 | .5779 | .2585 |
| 21 | .5131 | 1.0636 | 1.4572 | 1.6372 | 1.6020 | 1.4063 | 1.1306 | .8315 | .5316 | .2380 |
| 22 | .6153 | 1.2717 | 1.7288 | 1.8923 | 1.6064 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 23 | .4927 | 1.0205 | 1.3892 | 1.5282 | 1.3707 | .9631 | .7016 | .5030 | .3189 | .1424 |
| 24 | .6181 | 1.2794 | 1.7454 | 1.9356 | 1.8228 | 1.4973 | 1.1531 | .8346 | .5305 | .2372 |
| 25 | .4634 | .9615 | 1.3146 | 1.4683 | 1.4164 | 1.2169 | .9627 | .7029 | .4481 | .2002 |
| 26 | .6169 | 1.2761 | 1.7478 | 1.9617 | 1.9152 | 1.6758 | 1.3439 | .9872 | .6309 | .2830 |
| 27 | .4267 | .8835 | 1.2114 | 1.3633 | 1.3386 | 1.1806 | .9529 | .7024 | .4495 | .2016 |
| 28 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 29 | .6497 | 1.3443 | 1.8309 | 2.0165 | 1.8157 | 1.2886 | .9445 | .6788 | .4309 | .1928 |
| 30 | .5110 | 1.0594 | 1.4449 | 1.5998 | 1.4941 | 1.2033 | .9183 | .6637 | .4218 | .1883 |
| 31 | .7288 | 1.5064 | 2.0580 | 2.2925 | 2.1942 | 1.8609 | 1.4592 | 1.0619 | .6763 | .3030 |
| 32 | .5841 | 1.2085 | 1.6537 | 1.8514 | 1.7970 | 1.5591 | 1.2420 | .9095 | .5805 | .2602 |
| 33 | .3802 | .7873 | 1.0788 | 1.2122 | 1.1865 | 1.0419 | .8380 | .6165 | .3942 | .1767 |
| 34 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 35 | .7860 | 1.6243 | 2.2161 | 2.4571 | 2.3122 | 1.8973 | 1.4597 | 1.0563 | .6716 | .3008 |
| 36 | .6932 | 1.4326 | 1.9562 | 2.1763 | 2.0764 | 1.7522 | 1.3686 | .9941 | .6327 | .2835 |
| 37 | .5201 | 1.0760 | 1.4709 | 1.6425 | 1.5848 | 1.3630 | 1.0781 | .7867 | .5015 | .2246 |
| 38 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 39 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 40 | .4768 | .9876 | 1.3487 | 1.5013 | 1.4364 | 1.2190 | .9548 | .6938 | .4416 | .1974 |
| 41 | .4126 | .8539 | 1.1667 | 1.3010 | 1.2519 | 1.0725 | .8454 | .6157 | .3921 | .1755 |

Table 17

DIFFERENCE OF HXC37#_P36 SOLUTION TO THE EXTRAPOLATED

3rd-ORDER SOLUTION

Keff = 1.011392     Pmax = 2.4571

(Keff = 6.7 pcm    (Pmax = 0.0007

3D Power Distribution Difference*100

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .10 | -.09 | -.20 | -.27 | -.42 | .00 | .00 | .00 | .00 | .00 |
| 02 | .05 | -.11 | -.21 | -.28 | -.29 | -.23 | -.16 | -.11 | -.06 | .00 |
| 03 | .11 | -.09 | -.21 | -.28 | -.30 | -.26 | -.19 | -.13 | -.06 | .02 |
| 04 | .11 | -.09 | -.21 | -.29 | -.31 | -.27 | -.20 | -.13 | -.07 | .02 |
| 05 | .06 | -.10 | -.21 | -.27 | -.28 | -.25 | -.19 | -.13 | -.06 | .01 |
| 06 | .13 | -.05 | -.16 | -.23 | -.26 | -.23 | -.18 | -.12 | -.05 | .03 |
| 07 | .13 | -.07 | -.19 | -.27 | -.29 | -.26 | -.20 | -.13 | -.06 | .02 |
| 08 | .13 | -.05 | -.17 | -.24 | -.27 | -.24 | -.18 | -.12 | -.06 | .03 |
| 09 | .08 | -.05 | -.15 | -.21 | -.22 | -.20 | -.15 | -.10 | -.05 | .01 |
| 10 | .15 | .02 | -.07 | -.13 | -.16 | -.15 | -.11 | -.07 | -.02 | .04 |
| 11 | .08 | -.07 | -.17 | -.23 | -.25 | -.22 | -.17 | -.11 | -.05 | .01 |
| 12 | .15 | -.01 | -.11 | -.19 | -.22 | -.20 | -.14 | -.09 | -.04 | .03 |
| 13 | .09 | -.03 | -.11 | -.17 | -.19 | -.17 | -.12 | -.08 | -.03 | .02 |
| 14 | .11 | .00 | -.07 | -.12 | -.15 | -.13 | -.10 | -.06 | -.02 | .03 |
| 15 | .21 | .08 | .01 | -.05 | -.08 | -.08 | -.06 | -.02 | .01 | .07 |
| 16 | .10 | -.04 | -.13 | -.20 | -.23 | -.20 | -.13 | -.09 | -.04 | .01 |
| 17 | .18 | .02 | -.07 | -.15 | -.19 | -.16 | -.10 | -.06 | -.02 | .03 |
| 18 | .20 | .06 | -.03 | -.10 | -.13 | -.12 | -.08 | -.04 | .00 | .06 |
| 19 | .14 | .03 | -.04 | -.09 | -.12 | -.11 | -.08 | -.04 | .00 | .05 |
| 20 | .24 | .11 | .03 | -.03 | -.06 | -.06 | -.04 | -.01 | .03 | .09 |
| 21 | .23 | .09 | .02 | -.03 | -.06 | -.06 | -.04 | -.01 | .02 | .09 |
| 22 | .20 | .04 | -.05 | -.13 | -.32 | .00 | .00 | .00 | .00 | .00 |
| 23 | .14 | .02 | -.07 | -.13 | -.16 | -.15 | -.09 | -.05 | -.02 | .03 |
| 24 | .24 | .10 | .02 | -.04 | -.08 | -.08 | -.05 | -.01 | .02 | .08 |
| 25 | .16 | .04 | -.03 | -.08 | -.11 | -.10 | -.07 | -.04 | .00 | .06 |
| 26 | .34 | .18 | .13 | .08 | .04 | .02 | .03 | .04 | .06 | .14 |
| 27 | .26 | .20 | .19 | .16 | .13 | .11 | .10 | .09 | .08 | .11 |
| 28 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 29 | .25 | .10 | .01 | -.06 | -.11 | -.09 | -.05 | -.02 | .01 | .06 |
| 30 | .17 | .03 | -.05 | -.11 | -.14 | -.12 | -.08 | -.04 | .00 | .05 |
| 31 | .39 | .20 | .13 | .07 | .02 | .01 | .02 | .04 | .06 | .14 |
| 32 | .34 | .22 | .18 | .14 | .10 | .08 | .07 | .08 | .08 | .14 |
| 33 | .25 | .21 | .21 | .20 | .17 | .14 | .12 | .10 | .09 | .10 |
| 34 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 35 | .41 | .21 | .14 | .07 | .01 | .00 | .02 | .04 | .07 | .14 |
| 36 | .38 | .19 | .12 | .06 | .01 | .00 | .02 | .04 | .06 | .14 |
| 37 | .32 | .23 | .21 | .17 | .14 | .11 | .10 | .09 | .09 | .13 |
| 38 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 39 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 40 | .23 | .12 | .07 | .02 | -.01 | -.01 | .00 | .02 | .04 | .09 |
| 41 | .27 | .23 | .23 | .21 | .18 | .15 | .12 | .10 | .09 | .10 |

DEVIATION RANGE: -0.0042 ( ( ( 0.0027

Table 18

CRONOS 3rd-ORDER HXC127#_P72 SOLUTION

hr=4.2435cm, hz=4.16666667cm

Keff  =  1.011342   Pmax  =  2.4566

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .5201 | 1.0743 | 1.4548 | 1.5844 | 1.3421 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 02 | .4189 | .8666 | 1.1739 | 1.2817 | 1.1398 | .7918 | .5657 | .3974 | .2482 | .1098 |
| 03 | .5447 | 1.1255 | 1.5256 | 1.6710 | 1.5347 | 1.2063 | .8945 | .6306 | .3940 | .1744 |
| 04 | .5496 | 1.1358 | 1.5398 | 1.6883 | 1.5613 | 1.2498 | .9340 | .6592 | .4121 | .1823 |
| 05 | .4387 | .9080 | 1.2316 | 1.3529 | 1.2634 | 1.0342 | .7816 | .5530 | .3460 | .1529 |
| 06 | .5541 | 1.1458 | 1.5552 | 1.7106 | 1.6036 | 1.3221 | 1.0040 | .7120 | .4462 | .1976 |
| 07 | .5626 | 1.1632 | 1.5781 | 1.7337 | 1.6190 | 1.3253 | 1.0016 | .7088 | .4436 | .1964 |
| 08 | .5601 | 1.1581 | 1.5718 | 1.7274 | 1.6118 | 1.3164 | .9943 | .7044 | .4414 | .1956 |
| 09 | .4330 | .8969 | 1.2184 | 1.3407 | 1.2527 | 1.0247 | .7761 | .5515 | .3464 | .1535 |
| 10 | .5411 | 1.1200 | 1.5236 | 1.6810 | 1.5785 | 1.3013 | .9931 | .7098 | .4475 | .1990 |
| 11 | .4486 | .9290 | 1.2610 | 1.3835 | 1.2758 | 1.0136 | .7553 | .5342 | .3349 | .1483 |
| 12 | .5675 | 1.1741 | 1.5946 | 1.7494 | 1.6020 | 1.2471 | .9227 | .6535 | .4104 | .1822 |
| 13 | .4398 | .9116 | 1.2398 | 1.3649 | 1.2650 | 1.0123 | .7612 | .5428 | .3422 | .1520 |
| 14 | .4378 | .9081 | 1.2378 | 1.3711 | 1.2966 | 1.0796 | .8327 | .5998 | .3799 | .1690 |
| 15 | .5717 | 1.1859 | 1.6202 | 1.8060 | 1.7355 | 1.4834 | 1.1671 | .8487 | .5397 | .2407 |
| 16 | .4612 | .9558 | 1.2982 | 1.4205 | 1.2570 | .8554 | .6071 | .4289 | .2695 | .1197 |
| 17 | .5897 | 1.2210 | 1.6601 | 1.8200 | 1.6168 | 1.1083 | .7930 | .5632 | .3551 | .1582 |
| 18 | .5849 | 1.2119 | 1.6510 | 1.8224 | 1.6885 | 1.3402 | 1.0110 | .7259 | .4597 | .2049 |
| 19 | .4609 | .9574 | 1.3076 | 1.4552 | 1.3898 | 1.1748 | .9183 | .6666 | .4238 | .1888 |
| 20 | .5791 | 1.2028 | 1.6464 | 1.8436 | 1.7900 | 1.5536 | 1.2376 | .9058 | .5777 | .2578 |
| 21 | .5115 | 1.0629 | 1.4571 | 1.6374 | 1.6025 | 1.4068 | 1.1309 | .8316 | .5314 | .2374 |
| 22 | .6138 | 1.2714 | 1.7292 | 1.8933 | 1.6089 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 23 | .4917 | 1.0204 | 1.3897 | 1.5292 | 1.3719 | .9642 | .7023 | .5034 | .3190 | .1422 |
| 24 | .6163 | 1.2786 | 1.7452 | 1.9360 | 1.8234 | 1.4979 | 1.1534 | .8347 | .5304 | .2366 |
| 25 | .4623 | .9611 | 1.3148 | 1.4689 | 1.4172 | 1.2177 | .9633 | .7032 | .4481 | .1997 |
| 26 | .6144 | 1.2747 | 1.7468 | 1.9612 | 1.9149 | 1.6756 | 1.3437 | .9869 | .6304 | .2819 |
| 27 | .4247 | .8821 | 1.2100 | 1.3621 | 1.3376 | 1.1798 | .9522 | .7018 | .4489 | .2007 |
| 28 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 29 | .6479 | 1.3435 | 1.8308 | 2.0169 | 1.8165 | 1.2893 | .9449 | .6790 | .4308 | .1923 |
| 30 | .5098 | 1.0592 | 1.4453 | 1.6007 | 1.4951 | 1.2042 | .9189 | .6640 | .4219 | .1879 |
| 31 | .7259 | 1.5049 | 2.0570 | 2.2920 | 2.1941 | 1.8608 | 1.4590 | 1.0616 | .6758 | .3019 |
| 32 | .5816 | 1.2068 | 1.6523 | 1.8503 | 1.7962 | 1.5585 | 1.2414 | .9089 | .5799 | .2591 |
| 33 | .3783 | .7857 | 1.0772 | 1.2108 | 1.1852 | 1.0408 | .8371 | .6157 | .3935 | .1759 |
| 34 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 35 | .7829 | 1.6227 | 2.2151 | 2.4566 | 2.3121 | 1.8973 | 1.4595 | 1.0560 | .6711 | .2997 |
| 36 | .6903 | 1.4311 | 1.9553 | 2.1759 | 2.0763 | 1.7522 | 1.3684 | .9938 | .6322 | .2824 |
| 37 | .5177 | 1.0742 | 1.4694 | 1.6412 | 1.5838 | 1.3622 | 1.0774 | .7860 | .5008 | .2236 |
| 38 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 39 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 | .0000 |
| 40 | .4751 | .9867 | 1.3483 | 1.5012 | 1.4365 | 1.2190 | .9548 | .6937 | .4413 | .1968 |
| 41 | .4106 | .8522 | 1.1650 | 1.2995 | 1.2506 | 1.0714 | .8445 | .6149 | .3914 | .1747 |

Table 19

DIFFERENCE OF THE FINEST 3rd-ORDER HXC127#_P72 SOLUTION

TO THE EXTRAPOLATED 3rd-ORDER SOLUTION

Keff  =  1.011357     Pmax  =  2.4566

(Keff =  3.2 pcm  (Pmax =  0.0002

3D Power Distribution Difference*100

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .02 | -.02 | -.05 | -.07 | -.11 | .00 | .00 | .00 | .00 | .00 |
| 02 | .01 | -.03 | -.05 | -.07 | -.07 | -.06 | -.04 | -.03 | -.01 | .00 |
| 03 | .03 | -.02 | -.05 | -.07 | -.08 | -.06 | -.05 | -.03 | -.02 | .00 |
| 04 | .03 | -.02 | -.05 | -.07 | -.08 | -.07 | -.05 | -.03 | -.02 | .00 |
| 05 | .02 | -.02 | -.05 | -.07 | -.07 | -.06 | -.05 | -.03 | -.02 | .00 |
| 06 | .03 | -.01 | -.04 | -.06 | -.06 | -.06 | -.04 | -.03 | -.01 | .01 |
| 07 | .03 | -.02 | -.05 | -.07 | -.07 | -.06 | -.05 | -.03 | -.02 | .01 |
| 08 | .03 | -.01 | -.04 | -.06 | -.07 | -.06 | -.05 | -.03 | -.01 | .01 |
| 09 | .02 | -.01 | -.04 | -.05 | -.06 | -.05 | -.04 | -.02 | -.01 | .00 |
| 10 | .04 | .00 | -.02 | -.03 | -.04 | -.04 | -.03 | -.02 | -.01 | .01 |
| 11 | .02 | -.02 | -.04 | -.06 | -.06 | -.06 | -.04 | -.03 | -.01 | .00 |
| 12 | .04 | .00 | -.03 | -.05 | -.05 | -.05 | -.04 | -.02 | -.01 | .01 |
| 13 | .02 | -.01 | -.03 | -.04 | -.05 | -.04 | -.03 | -.02 | -.01 | .01 |
| 14 | .03 | .00 | -.02 | -.03 | -.04 | -.03 | -.02 | -.01 | .00 | .01 |
| 15 | .05 | .02 | .00 | -.01 | -.02 | -.02 | -.01 | -.01 | .00 | .02 |
| 16 | .02 | -.01 | -.03 | -.05 | -.06 | -.05 | -.03 | -.02 | -.01 | .00 |
| 17 | .05 | .01 | -.02 | -.04 | -.05 | -.04 | -.03 | -.02 | -.01 | .01 |
| 18 | .05 | .01 | -.01 | -.02 | -.03 | -.03 | -.02 | -.01 | .00 | .01 |
| 19 | .03 | .01 | -.01 | -.02 | -.03 | -.03 | -.02 | -.01 | .00 | .01 |
| 20 | .06 | .03 | .01 | -.01 | -.01 | -.02 | -.01 | .00 | .01 | .02 |
| 21 | .06 | .02 | .01 | -.01 | -.02 | -.02 | -.01 | .00 | .01 | .02 |
| 22 | .05 | .01 | -.01 | -.03 | -.08 | .00 | .00 | .00 | .00 | .00 |
| 23 | .03 | .00 | -.02 | -.03 | -.04 | -.04 | -.02 | -.01 | .00 | .01 |
| 24 | .06 | .03 | .01 | -.01 | -.02 | -.02 | -.01 | .00 | .01 | .02 |
| 25 | .04 | .01 | -.01 | -.02 | -.03 | -.02 | -.02 | -.01 | .00 | .01 |
| 26 | .08 | .05 | .03 | .02 | .01 | .01 | .01 | .01 | .02 | .03 |
| 27 | .07 | .05 | .05 | .04 | .03 | .03 | .02 | .02 | .02 | .03 |
| 28 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 29 | .06 | .02 | .00 | -.02 | -.03 | -.02 | -.01 | .00 | .00 | .02 |
| 30 | .04 | .01 | -.01 | -.03 | -.04 | -.03 | -.02 | -.01 | .00 | .01 |
| 31 | .10 | .05 | .03 | .02 | .01 | .00 | .00 | .01 | .02 | .04 |
| 32 | .08 | .05 | .05 | .04 | .03 | .02 | .02 | .02 | .02 | .03 |
| 33 | .06 | .05 | .05 | .05 | .04 | .04 | .03 | .03 | .02 | .03 |
| 34 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 35 | .10 | .05 | .03 | .02 | .00 | .00 | .00 | .01 | .02 | .04 |
| 36 | .09 | .05 | .03 | .01 | .00 | .00 | .00 | .01 | .02 | .04 |
| 37 | .08 | .06 | .05 | .04 | .03 | .03 | .02 | .02 | .02 | .03 |
| 38 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 39 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 | .00 |
| 40 | .06 | .03 | .02 | .01 | .00 | .00 | .00 | .00 | .01 | .02 |
| 41 | .07 | .06 | .06 | .05 | .04 | .04 | .03 | .03 | .02 | .03 |

DEVIATION RANGE: -0.0011 ( ( ( 0.0010

Table 20a

EXTRAPOLATED CRONOS 3rd-ORDER SOLUTION

hr = 0.000000       hz = 0.000000

Keff = 1.011325    Pmax = 2.4564

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 01 | .5198 | 1.0745 | 1.4553 | 1.5850 | 1.3432 | 0 | 0 | 0 | 0 | 0 |
| 02 | .4188 | .8668 | 1.1745 | 1.2824 | 1.1405 | .7924 | .5661 | .3977 | .2483 | .1098 |
| 03 | .5444 | 1.1257 | 1.5261 | 1.6718 | 1.5354 | 1.2069 | .8949 | .6309 | .3942 | .1743 |
| 04 | .5493 | 1.1360 | 1.5404 | 1.6891 | 1.5620 | 1.2505 | .9345 | .6595 | .4122 | .1823 |
| 05 | .4385 | .9082 | 1.2321 | 1.3536 | 1.2641 | 1.0348 | .7821 | .5533 | .3462 | .1529 |
| 06 | .5538 | 1.1459 | 1.5556 | 1.7112 | 1.6042 | 1.3226 | 1.0045 | .7123 | .4463 | .1976 |
| 07 | .5623 | 1.1634 | 1.5786 | 1.7344 | 1.6197 | 1.3260 | 1.0021 | .7091 | .4438 | .1963 |
| 08 | .5597 | 1.1582 | 1.5723 | 1.7280 | 1.6125 | 1.3169 | .9948 | .7047 | .4415 | .1955 |
| 09 | .4328 | .8970 | 1.2187 | 1.3412 | 1.2533 | 1.0252 | .7765 | .5518 | .3466 | .1535 |
| 10 | .5407 | 1.1199 | 1.5237 | 1.6813 | 1.5789 | 1.3017 | .9934 | .7100 | .4476 | .1989 |
| 11 | .4484 | .9292 | 1.2614 | 1.3841 | 1.2764 | 1.0142 | .7557 | .5345 | .3350 | .1483 |
| 12 | .5671 | 1.1741 | 1.5949 | 1.7499 | 1.6025 | 1.2476 | .9230 | .6537 | .4105 | .1821 |
| 13 | .4396 | .9117 | 1.2401 | 1.3654 | 1.2655 | 1.0127 | .7615 | .5430 | .3423 | .1520 |
| 14 | .4375 | .9081 | 1.2380 | 1.3714 | 1.2970 | 1.0799 | .8330 | .6000 | .3799 | .1689 |
| 15 | .5712 | 1.1857 | 1.6202 | 1.8061 | 1.7357 | 1.4837 | 1.1673 | .8487 | .5397 | .2405 |
| 16 | .4610 | .9559 | 1.2986 | 1.4210 | 1.2576 | .8558 | .6075 | .4291 | .2696 | .1197 |
| 17 | .5893 | 1.2210 | 1.6603 | 1.8203 | 1.6172 | 1.1087 | .7933 | .5634 | .3552 | .1581 |
| 18 | .5844 | 1.2118 | 1.6511 | 1.8227 | 1.6889 | 1.3405 | 1.0112 | .7260 | .4597 | .2047 |
| 19 | .4606 | .9573 | 1.3077 | 1.4554 | 1.3901 | 1.1751 | .9184 | .6667 | .4238 | .1887 |
| 20 | .5785 | 1.2025 | 1.6463 | 1.8436 | 1.7901 | 1.5538 | 1.2377 | .9058 | .5776 | .2576 |
| 21 | .5109 | 1.0627 | 1.4570 | 1.6375 | 1.6026 | 1.4069 | 1.1310 | .8316 | .5314 | .2371 |
| 22 | .6133 | 1.2713 | 1.7293 | 1.8936 | 1.6097 | 0 | 0 | 0 | 0 | 0 |
| 23 | .4913 | 1.0203 | 1.3899 | 1.5295 | 1.3723 | .9646 | .7025 | .5036 | .3190 | .1421 |
| 24 | .6157 | 1.2784 | 1.7451 | 1.9361 | 1.8236 | 1.4980 | 1.1535 | .8347 | .5303 | .2364 |
| 25 | .4619 | .9610 | 1.3148 | 1.4692 | 1.4175 | 1.2179 | .9634 | .7033 | .4481 | .1996 |
| 26 | .6135 | 1.2743 | 1.7465 | 1.9610 | 1.9148 | 1.6756 | 1.3436 | .9868 | .6302 | .2816 |
| 27 | .4240 | .8816 | 1.2095 | 1.3617 | 1.3372 | 1.1795 | .9520 | .7015 | .4487 | .2005 |
| 28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 29 | .6473 | 1.3433 | 1.8308 | 2.0171 | 1.8168 | 1.2895 | .9450 | .6790 | .4307 | .1922 |
| 30 | .5094 | 1.0591 | 1.4454 | 1.6010 | 1.4955 | 1.2045 | .9191 | .6641 | .4219 | .1878 |
| 31 | .7249 | 1.5044 | 2.0567 | 2.2919 | 2.1940 | 1.8608 | 1.4590 | 1.0615 | .6756 | .3016 |
| 32 | .5807 | 1.2063 | 1.6518 | 1.8500 | 1.7960 | 1.5583 | 1.2413 | .9087 | .5796 | .2588 |
| 33 | .3777 | .7852 | 1.0767 | 1.2103 | 1.1848 | 1.0405 | .8368 | .6155 | .3933 | .1757 |
| 34 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 35 | .7819 | 1.6222 | 2.2147 | 2.4564 | 2.3120 | 1.8973 | 1.4595 | 1.0559 | .6709 | .2993 |
| 36 | .6894 | 1.4307 | 1.9550 | 2.1757 | 2.0762 | 1.7522 | 1.3684 | .9937 | .6321 | .2821 |
| 37 | .5169 | 1.0737 | 1.4689 | 1.6408 | 1.5834 | 1.3619 | 1.0772 | .7858 | .5006 | .2233 |
| 38 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 39 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 40 | .4745 | .9864 | 1.3481 | 1.5011 | 1.4365 | 1.2191 | .9548 | .6936 | .4412 | .1966 |
| 41 | .4100 | .8516 | 1.1644 | 1.2990 | 1.2501 | 1.0710 | .8442 | .6146 | .3912 | .1745 |

Table 20b

EXTRAPOLATED CRONOS 3rd-ORDER SOLUTION

hr=00000   hz=00000

Keff= 1.011325             Pmax = 2.456

3D Power Distribution

| Layer |
| --- |
| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | Qmean |
| 01 | .520 | 1.074 | 1.455 | 1.585 | 1.343 | 0 | 0 | 0 | 0 | 0 | 1.1956 |
| 02 | .419 | .867 | 1.174 | 1.282 | 1.141 | .792 | .566 | .398 | .248 | .110 | .6997 |
| 03 | .544 | 1.126 | 1.526 | 1.672 | 1.535 | 1.207 | .895 | .631 | .394 | .174 | .9705 |
| 04 | .549 | 1.136 | 1.540 | 1.689 | 1.562 | 1.250 | .935 | .660 | .412 | .182 | .9916 |
| 05 | .439 | .908 | 1.232 | 1.354 | 1.264 | 1.035 | .782 | .553 | .346 | .153 | .8066 |
| 06 | .554 | 1.146 | 1.556 | 1.711 | 1.604 | 1.323 | 1.004 | .712 | .446 | .198 | 1.0255 |
| 07 | .562 | 1.163 | 1.579 | 1.734 | 1.620 | 1.326 | 1.002 | .709 | .444 | .196 | 1.0336 |
| 08 | .560 | 1.158 | 1.572 | 1.728 | 1.612 | 1.317 | .995 | .705 | .442 | .195 | 1.0284 |
| 09 | .433 | .897 | 1.219 | 1.341 | 1.253 | 1.025 | .776 | .552 | .347 | .153 | .7997 |
| 10 | .541 | 1.120 | 1.524 | 1.681 | 1.579 | 1.302 | .993 | .710 | .448 | .199 | 1.0096 |
| 11 | .448 | .929 | 1.261 | 1.384 | 1.276 | 1.014 | .756 | .535 | .335 | .148 | .8087 |
| 12 | .567 | 1.174 | 1.595 | 1.750 | 1.603 | 1.248 | .923 | .654 | .410 | .182 | 1.0105 |
| 13 | .440 | .912 | 1.240 | 1.365 | 1.265 | 1.013 | .762 | .543 | .342 | .152 | .8034 |
| 14 | .437 | .908 | 1.238 | 1.371 | 1.297 | 1.080 | .833 | .600 | .380 | .169 | .8314 |
| 15 | .571 | 1.186 | 1.620 | 1.806 | 1.736 | 1.484 | 1.167 | .849 | .540 | .241 | 1.1199 |
| 16 | .461 | .956 | 1.299 | 1.421 | 1.258 | .856 | .607 | .429 | .270 | .120 | .7676 |
| 17 | .589 | 1.221 | 1.660 | 1.820 | 1.617 | 1.109 | .793 | .563 | .355 | .158 | .9887 |
| 18 | .584 | 1.212 | 1.651 | 1.823 | 1.689 | 1.340 | 1.011 | .726 | .460 | .205 | 1.0701 |
| 19 | .461 | .957 | 1.308 | 1.455 | 1.390 | 1.175 | .918 | .667 | .424 | .189 | .8944 |
| 20 | .579 | 1.202 | 1.646 | 1.844 | 1.790 | 1.554 | 1.238 | .906 | .578 | .258 | 1.1594 |
| 21 | .511 | 1.063 | 1.457 | 1.638 | 1.603 | 1.407 | 1.131 | .832 | .531 | .237 | 1.0409 |
| 22 | .613 | 1.271 | 1.729 | 1.894 | 1.610 | 0 | 0 | 0 | 0 | 0 | 1.7234 |
| 23 | .491 | 1.020 | 1.390 | 1.530 | 1.372 | .965 | .703 | .504 | .319 | .142 | .8435 |
| 24 | .616 | 1.278 | 1.745 | 1.936 | 1.824 | 1.498 | 1.154 | .835 | .530 | .236 | 1.1652 |
| 25 | .462 | .961 | 1.315 | 1.469 | 1.417 | 1.218 | .963 | .703 | .448 | .200 | .9157 |
| 26 | .614 | 1.274 | 1.746 | 1.961 | 1.915 | 1.676 | 1.344 | .987 | .630 | .282 | 1.2428 |
| 27 | .424 | .882 | 1.210 | 1.362 | 1.337 | 1.180 | .952 | .702 | .449 | .200 | .8696 |
| 28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 29 | .647 | 1.343 | 1.831 | 2.017 | 1.817 | 1.290 | .945 | .679 | .431 | .192 | 1.1192 |
| 30 | .509 | 1.059 | 1.445 | 1.601 | 1.495 | 1.204 | .919 | .664 | .422 | .188 | .9508 |
| 31 | .725 | 1.504 | 2.057 | 2.292 | 2.194 | 1.861 | 1.459 | 1.061 | .676 | .302 | 1.4130 |
| 32 | .581 | 1.206 | 1.652 | 1.850 | 1.796 | 1.558 | 1.241 | .909 | .580 | .259 | 1.1632 |
| 33 | .378 | .785 | 1.077 | 1.210 | 1.185 | 1.040 | .837 | .615 | .393 | .176 | .7697 |
| 34 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 35 | .782 | 1.622 | 2.215 | 2.456 | 2.312 | 1.897 | 1.459 | 1.056 | .671 | .299 | 1.4770 |
| 36 | .689 | 1.431 | 1.955 | 2.176 | 2.076 | 1.752 | 1.368 | .994 | .632 | .282 | 1.3356 |
| 37 | .517 | 1.074 | 1.469 | 1.641 | 1.583 | 1.362 | 1.077 | .786 | .501 | .223 | 1.0233 |
| 38 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 39 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 40 | .475 | .986 | 1.348 | 1.501 | 1.437 | 1.219 | .955 | .694 | .441 | .197 | .9252 |
| 41 | .410 | .852 | 1.164 | 1.299 | 1.250 | 1.071 | .844 | .615 | .391 | .174 | .8071 |

Table 21. DIF3D Power Distribution with HR=2.829016 HZ=2.500000

KEFF= 1.01086415040

| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.525 | 1.087 | 1.472 | 1.605 | 1.366 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 2 | 0.426 | 0.882 | 1.195 | 1.306 | 1.164 | 0.813 | 0.582 | 0.409 | 0.256 | 0.113 |
| 3 | 0.550 | 1.139 | 1.545 | 1.694 | 1.558 | 1.227 | 0.912 | 0.644 | 0.403 | 0.178 |
| 4 | 0.555 | 1.150 | 1.560 | 1.712 | 1.586 | 1.272 | 0.952 | 0.673 | 0.421 | 0.186 |
| 5 | 0.445 | 0.923 | 1.252 | 1.377 | 1.287 | 1.056 | 0.799 | 0.566 | 0.354 | 0.157 |
| 6 | 0.558 | 1.156 | 1.570 | 1.728 | 1.622 | 1.340 | 1.019 | 0.724 | 0.454 | 0.201 |
| 7 | 0.567 | 1.176 | 1.596 | 1.755 | 1.641 | 1.346 | 1.019 | 0.722 | 0.452 | 0.200 |
| 8 | 0.564 | 1.169 | 1.587 | 1.746 | 1.631 | 1.335 | 1.010 | 0.716 | 0.449 | 0.199 |
| 9 | 0.437 | 0.907 | 1.233 | 1.357 | 1.270 | 1.041 | 0.789 | 0.561 | 0.353 | 0.156 |
| 10 | 0.541 | 1.123 | 1.528 | 1.687 | 1.586 | 1.309 | 1.000 | 0.715 | 0.451 | 0.200 |
| 11 | 0.454 | 0.941 | 1.278 | 1.403 | 1.296 | 1.032 | 0.771 | 0.546 | 0.342 | 0.151 |
| 12 | 0.570 | 1.181 | 1.605 | 1.762 | 1.616 | 1.261 | 0.935 | 0.663 | 0.416 | 0.185 |
| 13 | 0.443 | 0.919 | 1.250 | 1.378 | 1.278 | 1.025 | 0.771 | 0.550 | 0.347 | 0.154 |
| 14 | 0.439 | 0.912 | 1.244 | 1.379 | 1.305 | 1.087 | 0.839 | 0.605 | 0.383 | 0.170 |
| 15 | 0.569 | 1.183 | 1.617 | 1.803 | 1.733 | 1.482 | 1.167 | 0.849 | 0.540 | 0.240 |
| 16 | 0.465 | 0.965 | 1.311 | 1.436 | 1.274 | 0.871 | 0.620 | 0.438 | 0.275 | 0.122 |
| 17 | 0.590 | 1.225 | 1.666 | 1.828 | 1.627 | 1.120 | 0.803 | 0.570 | 0.360 | 0.160 |
| 18 | 0.584 | 1.212 | 1.651 | 1.824 | 1.692 | 1.344 | 1.015 | 0.729 | 0.462 | 0.205 |
| 19 | 0.461 | 0.959 | 1.310 | 1.459 | 1.394 | 1.179 | 0.922 | 0.669 | 0.426 | 0.189 |
| 20 | 0.576 | 1.198 | 1.641 | 1.838 | 1.785 | 1.550 | 1.235 | 0.904 | 0.577 | 0.257 |
| 21 | 0.508 | 1.060 | 1.453 | 1.634 | 1.599 | 1.404 | 1.129 | 0.830 | 0.531 | 0.236 |
| 22 | 0.613 | 1.273 | 1.732 | 1.898 | 1.619 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 23 | 0.493 | 1.024 | 1.395 | 1.536 | 1.381 | 0.973 | 0.709 | 0.509 | 0.322 | 0.143 |
| 24 | 0.613 | 1.274 | 1.740 | 1.931 | 1.820 | 1.496 | 1.153 | 0.834 | 0.530 | 0.236 |
| 25 | 0.462 | 0.962 | 1.316 | 1.471 | 1.420 | 1.220 | 0.966 | 0.705 | 0.449 | 0.200 |
| 26 | 0.606 | 1.263 | 1.731 | 1.944 | 1.899 | 1.662 | 1.333 | 0.979 | 0.625 | 0.279 |
| 27 | 0.415 | 0.865 | 1.188 | 1.337 | 1.313 | 1.159 | 0.935 | 0.689 | 0.441 | 0.197 |
| 28 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 29 | 0.645 | 1.340 | 1.827 | 2.014 | 1.816 | 1.292 | 0.947 | 0.681 | 0.432 | 0.192 |
| 30 | 0.510 | 1.062 | 1.449 | 1.606 | 1.501 | 1.210 | 0.923 | 0.667 | 0.424 | 0.189 |
| 31 | 0.717 | 1.493 | 2.041 | 2.275 | 2.179 | 1.848 | 1.450 | 1.055 | 0.672 | 0.299 |
| 32 | 0.571 | 1.190 | 1.630 | 1.826 | 1.773 | 1.539 | 1.226 | 0.898 | 0.573 | 0.255 |
| 33 | 0.368 | 0.767 | 1.051 | 1.182 | 1.158 | 1.017 | 0.818 | 0.602 | 0.385 | 0.171 |
| 34 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 35 | 0.774 | 1.610 | 2.199 | 2.439 | 2.297 | 1.886 | 1.451 | 1.050 | 0.667 | 0.297 |
| 36 | 0.682 | 1.420 | 1.941 | 2.161 | 2.063 | 1.741 | 1.360 | 0.988 | 0.629 | 0.280 |
| 37 | 0.507 | 1.055 | 1.444 | 1.614 | 1.557 | 1.340 | 1.060 | 0.773 | 0.493 | 0.219 |
| 38 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 39 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 40 | 0.470 | 0.979 | 1.339 | 1.491 | 1.427 | 1.212 | 0.949 | 0.690 | 0.439 | 0.195 |
| 41 | 0.400 | 0.832 | 1.138 | 1.269 | 1.222 | 1.047 | 0.825 | 0.601 | 0.383 | 0.170 |

Table 22.  DIF3D Power DIstribution with HR=1.414508 HZ=2.500000

KEFF= 1.01121378948

| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.521 | 1.078 | 1.461 | 1.592 | 1.353 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 2 | 0.421 | 0.871 | 1.181 | 1.290 | 1.148 | 0.799 | 0.571 | 0.401 | 0.251 | 0.111 |
| 3 | 0.546 | 1.130 | 1.532 | 1.679 | 1.543 | 1.213 | 0.900 | 0.635 | 0.397 | 0.175 |
| 4 | 0.551 | 1.140 | 1.546 | 1.696 | 1.570 | 1.257 | 0.940 | 0.664 | 0.415 | 0.183 |
| 5 | 0.440 | 0.913 | 1.238 | 1.361 | 1.271 | 1.041 | 0.787 | 0.557 | 0.349 | 0.154 |
| 6 | 0.555 | 1.149 | 1.560 | 1.717 | 1.610 | 1.328 | 1.009 | 0.716 | 0.449 | 0.198 |
| 7 | 0.563 | 1.167 | 1.584 | 1.741 | 1.627 | 1.332 | 1.007 | 0.713 | 0.446 | 0.197 |
| 8 | 0.561 | 1.162 | 1.577 | 1.734 | 1.619 | 1.323 | 0.999 | 0.708 | 0.444 | 0.196 |
| 9 | 0.434 | 0.900 | 1.223 | 1.346 | 1.259 | 1.030 | 0.780 | 0.555 | 0.348 | 0.154 |
| 10 | 0.541 | 1.121 | 1.525 | 1.683 | 1.581 | 1.304 | 0.995 | 0.712 | 0.449 | 0.199 |
| 11 | 0.450 | 0.933 | 1.266 | 1.390 | 1.283 | 1.020 | 0.760 | 0.538 | 0.337 | 0.149 |
| 12 | 0.567 | 1.176 | 1.598 | 1.754 | 1.607 | 1.252 | 0.927 | 0.656 | 0.412 | 0.183 |
| 13 | 0.440 | 0.914 | 1.243 | 1.369 | 1.270 | 1.016 | 0.764 | 0.545 | 0.344 | 0.152 |
| 14 | 0.438 | 0.909 | 1.240 | 1.374 | 1.300 | 1.082 | 0.835 | 0.601 | 0.381 | 0.169 |
| 15 | 0.570 | 1.185 | 1.619 | 1.805 | 1.735 | 1.483 | 1.167 | 0.849 | 0.540 | 0.240 |
| 16 | 0.462 | 0.959 | 1.302 | 1.426 | 1.263 | 0.860 | 0.611 | 0.432 | 0.271 | 0.120 |
| 17 | 0.589 | 1.222 | 1.662 | 1.823 | 1.621 | 1.112 | 0.796 | 0.565 | 0.357 | 0.159 |
| 18 | 0.584 | 1.212 | 1.651 | 1.823 | 1.690 | 1.342 | 1.012 | 0.727 | 0.460 | 0.205 |
| 19 | 0.460 | 0.958 | 1.308 | 1.456 | 1.391 | 1.176 | 0.919 | 0.667 | 0.424 | 0.189 |
| 20 | 0.577 | 1.201 | 1.645 | 1.842 | 1.789 | 1.553 | 1.237 | 0.905 | 0.577 | 0.257 |
| 21 | 0.509 | 1.062 | 1.456 | 1.636 | 1.601 | 1.406 | 1.130 | 0.831 | 0.531 | 0.237 |
| 22 | 0.613 | 1.272 | 1.730 | 1.895 | 1.616 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 23 | 0.491 | 1.021 | 1.392 | 1.532 | 1.376 | 0.967 | 0.704 | 0.505 | 0.320 | 0.142 |
| 24 | 0.614 | 1.277 | 1.744 | 1.935 | 1.823 | 1.498 | 1.153 | 0.834 | 0.530 | 0.236 |
| 25 | 0.461 | 0.961 | 1.315 | 1.470 | 1.418 | 1.219 | 0.964 | 0.704 | 0.448 | 0.199 |
| 26 | 0.610 | 1.271 | 1.742 | 1.956 | 1.910 | 1.672 | 1.340 | 0.984 | 0.629 | 0.280 |
| 27 | 0.421 | 0.877 | 1.203 | 1.355 | 1.330 | 1.173 | 0.947 | 0.698 | 0.446 | 0.199 |
| 28 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 29 | 0.646 | 1.342 | 1.830 | 2.016 | 1.818 | 1.290 | 0.946 | 0.679 | 0.431 | 0.192 |
| 30 | 0.509 | 1.060 | 1.446 | 1.602 | 1.497 | 1.206 | 0.920 | 0.665 | 0.422 | 0.188 |
| 31 | 0.721 | 1.501 | 2.052 | 2.287 | 2.190 | 1.857 | 1.456 | 1.059 | 0.674 | 0.300 |
| 32 | 0.577 | 1.201 | 1.645 | 1.843 | 1.789 | 1.553 | 1.237 | 0.905 | 0.577 | 0.257 |
| 33 | 0.374 | 0.780 | 1.069 | 1.202 | 1.177 | 1.034 | 0.831 | 0.611 | 0.391 | 0.174 |
| 34 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 35 | 0.778 | 1.618 | 2.210 | 2.452 | 2.308 | 1.894 | 1.457 | 1.054 | 0.670 | 0.298 |
| 36 | 0.686 | 1.427 | 1.951 | 2.171 | 2.072 | 1.749 | 1.366 | 0.992 | 0.631 | 0.281 |
| 37 | 0.513 | 1.068 | 1.462 | 1.633 | 1.576 | 1.355 | 1.072 | 0.782 | 0.498 | 0.222 |
| 38 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 39 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 40 | 0.472 | 0.984 | 1.345 | 1.498 | 1.434 | 1.217 | 0.953 | 0.692 | 0.440 | 0.196 |
| 41 | 0.406 | 0.846 | 1.157 | 1.291 | 1.242 | 1.064 | 0.839 | 0.611 | 0.389 | 0.173 |

Table 23.  DIF3D Power Distribution with HR=0.000000 HZ=2.500000

KEFF= 1.01133033584

| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.520 | 1.076 | 1.457 | 1.587 | 1.349 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 2 | 0.419 | 0.868 | 1.176 | 1.284 | 1.143 | 0.794 | 0.567 | 0.398 | 0.249 | 0.110 |
| 3 | 0.544 | 1.127 | 1.528 | 1.674 | 1.538 | 1.209 | 0.896 | 0.632 | 0.395 | 0.174 |
| 4 | 0.549 | 1.137 | 1.542 | 1.691 | 1.564 | 1.252 | 0.936 | 0.660 | 0.413 | 0.182 |
| 5 | 0.439 | 0.909 | 1.233 | 1.355 | 1.266 | 1.036 | 0.783 | 0.554 | 0.347 | 0.153 |
| 6 | 0.554 | 1.147 | 1.557 | 1.713 | 1.606 | 1.324 | 1.006 | 0.713 | 0.447 | 0.198 |
| 7 | 0.562 | 1.164 | 1.580 | 1.736 | 1.622 | 1.328 | 1.003 | 0.710 | 0.444 | 0.196 |
| 8 | 0.559 | 1.159 | 1.574 | 1.730 | 1.614 | 1.318 | 0.996 | 0.705 | 0.442 | 0.196 |
| 9 | 0.433 | 0.898 | 1.220 | 1.343 | 1.255 | 1.026 | 0.777 | 0.552 | 0.347 | 0.154 |
| 10 | 0.540 | 1.120 | 1.524 | 1.682 | 1.580 | 1.303 | 0.994 | 0.710 | 0.448 | 0.199 |
| 11 | 0.448 | 0.930 | 1.263 | 1.386 | 1.278 | 1.015 | 0.757 | 0.535 | 0.335 | 0.148 |
| 12 | 0.567 | 1.175 | 1.596 | 1.751 | 1.604 | 1.249 | 0.924 | 0.654 | 0.411 | 0.182 |
| 13 | 0.440 | 0.912 | 1.241 | 1.366 | 1.267 | 1.081 | 0.833 | 0.600 | 0.380 | 0.169 |
| 15 | 0.570 | 1.186 | 1.620 | 1.806 | 1.736 | 1.484 | 1.167 | 0.849 | 0.540 | 0.240 |
| 16 | 0.461 | 0.957 | 1.299 | 1.422 | 1.260 | 0.857 | 0.608 | 0.430 | 0.270 | 0.120 |
| 17 | 0.589 | 1.221 | 1.661 | 1.821 | 1.620 | 1.109 | 0.794 | 0.564 | 0.355 | 0.158 |
| 18 | 0.584 | 1.212 | 1.651 | 1.823 | 1.690 | 1.341 | 1.011 | 0.726 | 0.460 | 0.205 |
| 19 | 0.460 | 0.957 | 1.308 | 1.456 | 1.391 | 1.175 | 0.919 | 0.667 | 0.424 | 0.189 |
| 20 | 0.577 | 1.202 | 1.646 | 1.843 | 1.790 | 1.554 | 1.237 | 0.906 | 0.577 | 0.257 |
| 21 | 0.510 | 1.062 | 1.457 | 1.637 | 1.602 | 1.407 | 1.131 | 0.831 | 0.531 | 0.237 |
| 22 | 0.613 | 1.271 | 1.730 | 1.895 | 1.615 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 23 | 0.491 | 1.020 | 1.390 | 1.530 | 1.374 | 0.965 | 0.703 | 0.504 | 0.319 | 0.142 |
| 24 | 0.615 | 1.278 | 1.745 | 1.936 | 1.824 | 1.498 | 1.153 | 0.835 | 0.530 | 0.236 |
| 25 | 0.461 | 0.961 | 1.315 | 1.469 | 1.418 | 1.218 | 0.963 | 0.703 | 0.448 | 0.199 |
| 26 | 0.611 | 1.273 | 1.745 | 1.960 | 1.914 | 1.675 | 1.343 | 0.986 | 0.630 | 0.281 |
| 27 | 0.422 | 0.881 | 1.208 | 1.360 | 1.336 | 1.178 | 0.951 | 0.701 | 0.448 | 0.200 |
| 28 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 29 | 0.646 | 1.343 | 1.831 | 2.017 | 1.818 | 1.290 | 0.945 | 0.679 | 0.431 | 0.192 |
| 30 | 0.509 | 1.059 | 1.445 | 1.601 | 1.496 | 1.205 | 0.919 | 0.664 | 0.422 | 0.188 |
| 31 | 0.723 | .503 | 2.056 | 2.291 | 2.193 | 1.860 | 1.458 | 1.061 | 0.675 | 0.301 |
| 32 | 0.579 | 1.205 | 1.651 | 1.849 | 1.795 | 1.557 | 1.240 | 0.908 | 0.579 | 0.258 |
| 33 | 0.376 | 0.784 | 1.075 | 1.209 | 1.183 | 1.039 | 0.836 | 0.615 | 0.393 | 0.175 |
| 34 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 35 | 0.779 | 1.621 | 2.214 | 2.456 | 2.312 | 1.897 | 1.459 | 1.055 | 0.671 | 0.298 |
| 36 | 0.687 | 1.430 | 1.954 | 2.175 | 2.076 | 1.752 | 1.368 | 0.993 | 0.632 | 0.281 |
| 37 | 0.515 | 1.072 | 1.467 | 1.639 | 1.582 | 1.361 | 1.076 | 0.785 | 0.500 | 0.223 |
| 38 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 39 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 40 | 0.473 | 0.986 | 1.347 | 1.501 | 1.436 | 1.219 | 0.954 | 0.693 | 0.441 | 0.196 |
| 41 | 0.408 | 0.850 | 1.163 | 1.298 | 1.249 | 1.070 | 0.843 | 0.614 | 0.391 | 0.174 |

Table 24, DIF3D Power Distribution with HR=2.829016 HZ=1.250000

KEFF= 1.01085651417

| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.525 | 1.086 | 1.472 | 1.604 | 1.362 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 2 | 0.426 | 0.881 | 1.195 | 1.306 | 1.163 | 0.813 | 0.582 | 0.409 | 0.256 | 0.113 |
| 3 | 0.550 | 1.139 | 1.544 | 1.693 | 1.557 | 1.227 | 0.912 | 0.644 | 0.403 | 0.178 |
| 4 | 0.556 | 1.150 | 1.559 | 1.711 | 1.585 | 1.271 | 0.952 | 0.673 | 0.421 | 0.186 |
| 5 | 0.445 | 0.922 | 1.252 | 1.376 | 1.287 | 1.055 | 0.799 | 0.566 | 0.354 | 0.157 |
| 6 | 0.558 | 1.156 | 1.570 | 1.728 | 1.622 | 1.340 | 1.019 | 0.724 | 0.454 | 0.201 |
| 7 | 0.568 | 1.175 | 1.596 | 1.754 | 1.641 | 1.346 | 1.019 | 0.722 | 0.452 | 0.200 |
| 8 | 0.565 | 1.169 | 1.587 | 1.746 | 1.631 | 1.335 | 1.010 | 0.716 | 0.449 | 0.199 |
| 9 | 0.437 | 0.907 | 1.232 | 1.357 | 1.270 | 1.040 | 0.789 | 0.561 | 0.353 | 0.156 |
| 10 | 0.542 | 1.122 | 1.528 | 1.687 | 1.585 | 1.309 | 1.000 | 0.715 | 0.451 | 0.200 |
| 11 | 0.454 | 0.941 | 1.278 | 1.403 | 1.296 | 1.032 | 0.770 | 0.546 | 0.342 | 0.151 |
| 12 | 0.570 | 1.181 | 1.604 | 1.761 | 1.615 | 1.261 | 0.935 | 0.663 | 0.416 | 0.185 |
| 13 | 0.443 | 0.919 | 1.250 | 1.377 | 1.278 | 1.024 | 0.771 | 0.551 | 0.347 | 0.154 |
| 14 | 0.439 | 0.912 | 1.244 | 1.378 | 1.304 | 1.087 | 0.839 | 0.605 | 0.383 | 0.170 |
| 15 | 0.570 | 1.183 | 1.617 | 1.803 | 1.733 | 1.482 | 1.167 | 0.849 | 0.540 | 0.241 |
| 16 | 0.465 | 0.965 | 1.311 | 1.436 | 1.273 | 0.871 | 0.620 | 0.438 | 0.275 | 0.122 |
| 17 | 0.591 | 1.225 | 1.666 | 1.827 | 1.626 | 1.120 | 0.803 | 0.570 | 0.360 | 0.160 |
| 18 | 0.584 | 1.212 | 1.651 | 1.824 | 1.691 | 1.344 | 1.015 | 0.729 | 0.462 | 0.206 |
| 19 | 0.461 | 0.959 | 1.310 | 1.458 | 1.394 | 1.179 | 0.922 | 0.669 | 0.426 | 0.189 |
| 20 | 0.576 | 1.198 | 1.641 | 1.838 | 1.785 | 1.550 | 1.235 | 0.904 | 0.577 | 0.257 |
| 21 | 0.509 | 1.060 | 1.453 | 1.633 | 1.599 | 1.404 | 1.129 | 0.831 | 0.531 | 0.237 |
| 22 | 0.614 | 1.273 | 1.732 | 1.898 | 1.615 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 23 | 0.493 | 1.024 | 1.395 | 1.536 | 1.380 | 0.973 | 0.709 | 0.509 | 0.322 | 0.144 |
| 24 | 0.614 | 1.274 | 1.740 | 1.931 | 1.820 | 1.496 | 1.153 | 0.834 | 0.530 | 0.236 |
| 25 | 0.462 | 0.962 | 1.316 | 1.471 | 1.420 | 1.220 | 0.966 | 0.705 | 0.449 | 0.200 |
| 26 | 0.608 | 1.263 | 1.731 | 1.944 | 1.899 | 1.662 | 1.333 | 0.979 | 0.626 | 0.279 |
| 27 | 0.416 | 0.865 | 1.188 | 1.337 | 1.313 | 1.159 | 0.935 | 0.690 | 0.441 | 0.197 |
| 28 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 29 | 0.645 | 1.340 | 1.827 | 2.013 | 1.815 | 1.292 | 0.947 | 0.681 | 0.432 | 0.193 |
| 30 | 0.510 | 1.062 | 1.449 | 1.605 | 1.500 | 1.209 | 0.923 | 0.667 | 0.424 | 0.189 |
| 31 | 0.719 | 1.493 | 2.041 | 2.275 | 2.178 | 1.848 | 1.450 | 1.055 | 0.672 | 0.300 |
| 32 | 0.573 | 1.190 | 1.630 | 1.826 | 1.773 | 1.539 | 1.226 | 0.898 | 0.573 | 0.256 |
| 33 | 0.369 | 0.767 | 1.051 | 1.182 | 1.158 | 1.017 | 0.818 | 0.602 | 0.385 | 0.172 |
| 34 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 35 | 0.776 | 1.610 | 2.198 | 2.439 | 2.297 | 1.886 | 1.451 | 1.050 | 0.667 | 0.298 |
| 36 | 0.684 | 1.420 | 1.941 | 2.161 | 2.062 | 1.741 | 1.360 | 0.988 | 0.629 | 0.280 |
| 37 | 0.508 | 1.055 | 1.444 | 1.613 | 1.557 | 1.340 | 1.060 | 0.773 | 0.493 | 0.220 |
| 38 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 39 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 40 | 0.471 | 0.979 | 1.339 | 1.491 | 1.427 | 1.212 | 0.949 | 0.690 | 0.439 | 0.195 |
| 41 | 0.400 | 0.832 | 1.137 | 1.269 | 1.222 | 1.047 | 0.825 | 0.601 | 0.383 | 0.171 |

Table 25, DIF3D Power Distribution with HR=2.829016 HZ=0.000000

KEFF= 1.01085396876

| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.525 | 1.086 | 1.472 | 1.604 | 1.361 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 2 | 0.426 | 0.881 | 1.195 | 1.305 | 1.163 | 0.812 | 0.582 | 0.409 | 0.256 | 0.113 |
| 3 | 0.551 | 1.139 | 1.544 | 1.693 | 1.557 | 1.227 | 0.912 | 0.644 | 0.403 | 0.178 |
| 4 | 0.556 | 1.150 | 1.559 | 1.711 | 1.585 | 1.271 | 0.952 | 0.673 | 0.421 | 0.186 |
| 5 | 0.445 | 0.922 | 1.252 | 1.376 | 1.287 | 1.055 | 0.799 | 0.566 | 0.354 | 0.157 |
| 6 | 0.559 | 1.156 | 1.570 | 1.728 | 1.622 | 1.339 | 1.019 | 0.724 | 0.454 | 0.201 |
| 7 | 0.568 | 1.175 | 1.595 | 1.754 | 1.640 | 1.345 | 1.019 | 0.722 | 0.452 | 0.200 |
| 8 | 0.565 | 1.169 | 1.587 | 1.745 | 1.631 | 1.334 | 1.010 | 0.716 | 0.449 | 0.199 |
| 9 | 0.437 | 0.907 | 1.232 | 1.357 | 1.270 | 1.040 | 0.789 | 0.561 | 0.353 | 0.156 |
| 10 | 0.542 | 1.122 | 1.528 | 1.686 | 1.585 | 1.309 | 1.000 | 0.715 | 0.451 | 0.201 |
| 11 | 0.454 | 0.941 | 1.278 | 1.403 | 1.295 | 1.032 | 0.770 | 0.546 | 0.342 | 0.152 |
| 12 | 0.570 | 1.181 | 1.604 | 1.761 | 1.615 | 1.261 | 0.934 | 0.663 | 0.416 | 0.185 |
| 13 | 0.443 | 0.919 | 1.250 | 1.377 | 1.278 | 1.024 | 0.771 | 0.551 | 0.347 | 0.154 |
| 14 | 0.439 | 0.912 | 1.244 | 1.378 | 1.304 | 1. 087 | 0.839 | 0.605 | 0.383 | 0.170 |
| 15 | 0.570 | 1.183 | 1.616 | 1.802 | 1.733 | 1.482 | 1.167 | 0.849 | 0.540 | 0.241 |
| 16 | 0.465 | 0.965 | 1.311 | 1.436 | 1.273 | 0.871 | 0.620 | 0.438 | 0.275 | 0.122 |
| 17 | 0.591 | 1.225 | 1.666 | 1.827 | 1.625 | 1.119 | 0.803 | 0.570 | 0.360 | 0.160 |
| 18 | 0.584 | 1.212 | 1.651 | 1.824 | 1.691 | 1.344 | 1.015 | 0.729 | 0.462 | 0.206 |
| 19 | 0.461 | 0.959 | 1.310 | 1.458 | 1.394 | 1.179 | 0.922 | 0.669 | 0.426 | 0.190 |
| 20 | 0.576 | 1.198 | 1.641 | 1.838 | 1.785 | 1.550 | 1.235 | 0.904 | 0.577 | 0.257 |
| 21 | 0.509 | 1.060 | 1.453 | 1.633 | 1.599 | 1.404 | 1.129 | 0.831 | 0.531 | 0.237 |
| 22 | 0.614 | 1.273 | 1.732 | 1.897 | 1.614 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 23 | 0.493 | 1.024 | 1.395 | 1.536 | 1.379 | 0.973 | 0.709 | 0.509 | 0.322 | 0.144 |
| 24 | 0.614 | 1.274 | 1.740 | 1.931 | 1.820 | 1.496 | 1.153 | 0.834 | 0.530 | 0.236 |
| 25 | 0.462 | 0.962 | 1.316 | 1.471 | 1.420 | 1.220 | 0.966 | 0.705 | 0.449 | 0.200 |
| 26 | 0.608 | 1.263 | 1.731 | 1.944 | 1.899 | 1.662 | 1.333 | 0.979 | 0.626 | 0.280 |
| 27 | 0.416 | 0.865 | 1.188 | 1.337 | 1.313 | 1.159 | 0.936 | 0.690 | 0.441 | 0.197 |
| 28 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 29 | 0.646 | 1.340 | 1.827 | 2.013 | 1.814 | 1.292 | 0.947 | 0.681 | 0.432 | 0.193 |
| 30 | 0.511 | 1.062 | 1.449 | 1.605 | 1.500 | 1.209 | 0.923 | 0.667 | 0.424 | 0.189 |
| 31 | 0.719 | 1.493 | 2.041 | 2.275 | 2.178 | 1.848 | 1.450 | 1.055 | 0.672 | 0.300 |
| 32 | 0.573 | 1.190 | 1.630 | 1.826 | 1.773 | 1.539 | 1.226 | 0.898 | 0.573 | 0.256 |
| 33 | 0.369 | 0.767 | 1.051 | 1.182 | 1.158 | 1.017 | 0.818 | 0.602 | 0.385 | 0.172 |
| 34 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 35 | 0.776 | 1.610 | 2.198 | 2.439 | 2.296 | 1.886 | 1.451 | 1. 050 | 0.668 | 0.298 |
| 36 | 0.684 | 1.420 | 1.941 | 2.161 | 2.062 | 1.741 | 1.360 | 0.988 | 0.629 | 0.281 |
| 37 | 0.508 | 1.055 | 1.444 | 1.613 | 1.557 | 1.340 | 1.060 | 0.773 | 0.493 | 0.220 |
| 38 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 39 | 0.000 | 0.000 | 0. 000 | 0.000 | 0.000 | 0. 000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 40 | 0.471 | 0.979 | 1.339 | 1.491 | 1.427 | 1.212 | 0.949 | 0.690 | 0.439 | 0.196 |
| 41 | 0.401 | 0.832 | 1.137 | 1.269 | 1.222 | 1.047 | 0.825 | 0.601 | 0.383 | 0.171 |

Table 30. Recommended Solution (by DIF3D)

The recommended solution was obtained by a two dimensional Richardson extrapolation to HZ=HR=0 from the DIF3D solutions.

KEFF= 1.01132015420 HR=0.000000 HZ=0.000000

| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | Qmean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.520 | 1.075 | 1.456 | 1.586 | 1.344 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 1.197 |
| 2 | 0.419 | 0.868 | 1.176 | 1.284 | 1.142 | 0.794 | 0.567 | 0.398 | 0.249 | 0.110 | 0.701 |
| 3 | 0.545 | 1.126 | 1.527 | 1.673 | 1.537 | 1.208 | 0.896 | 0.632 | 0.395 | 0.175 | 0.971 |
| 4 | 0.550 | 1.137 | 1.541 | 1.690 | 1.564 | 1.252 | 0.936 | 0.660 | 0.413 | 0.183 | 0.993 |
| 5 | 0.439 | 0.909 | 1.233 | 1.355 | 1.265 | 1.036 | 0.783 | 0.554 | 0.347 | 0.153 | 0.807 |
| 6 | 0.554 | 1.147 | 1.557 | 1.712 | 1.605 | 1.324 | 1.005 | 0.713 | 0.447 | 0.198 | 1.026 |
| 7 | 0.563 | 1.164 | 1.580 | 1.736 | 1.621 | 1.327 | 1.003 | 0.710 | 0.444 | 0.197 | 1.034 |
| 8 | 0.560 | 1.159 | 1.573 | 1.729 | 1.614 | 1.318 | 0.996 | 0.705 | 0.442 | 0.196 | 1.029 |
| 9 | 0.433 | 0.898 | 1.219 | 1.342 | 1.254 | 1.026 | 0.777 | 0.552 | 0.347 | 0.154 | 0.800 |
| 10 | 0.541 | 1.120 | 1.524 | 1.682 | 1.580 | 1.302 | 0.994 | 0.710 | 0.448 | 0.199 | 1.010 |
| 11 | 0.449 | 0.930 | 1.262 | 1.385 | 1.278 | 1.015 | 0.757 | 0.535 | 0.335 | 0.148 | 0.809 |
| 12 | 0.567 | 1.175 | 1.596 | 1.751 | 1.603 | 1.248 | 0.924 | 0.654 | 0.411 | 0.182 | 1.011 |
| 13 | 0.440 | 0.912 | 1.241 | 1.366 | 1.266 | 1.013 | 0.762 | 0.543 | 0.343 | 0.152 | 0.804 |
| 14 | 0.438 | 0.908 | 1.238 | 1.372 | 1.297 | 1.080 | 0.833 | 0.600 | 0.380 | 0.169 | 0.832 |
| 15 | 0.571 | 1.185 | 1.620 | 1.806 | 1.736 | 1.484 | 1.167 | 0.849 | 0.540 | 0.241 | 1.120 |
| 16 | 0.461 | 0.956 | 1.299 | 1.422 | 1.258 | 0.857 | 0.608 | 0.430 | 0.270 | 0.120 | 0.768 |
| 17 | 0.589 | 1.221 | 1.661 | 1.821 | 1.618 | 1.109 | 0.794 | 0.564 | 0.355 | 0.158 | 0.989 |
| 18 | 0.584 | 1.212 | 1.651 | 1.823 | 1.689 | 1.341 | 1.011 | 0.726 | 0.460 | 0.205 | 1.070 |
| 19 | 0.461 | 0.957 | 1.308 | 1.455 | 1.390 | 1.175 | 0.919 | 0.667 | 0.424 | 0.189 | 0.894 |
| 20 | 0.578 | 1.202 | 1.646 | 1.843 | 1.790 | 1.553 | 1.238 | 0.906 | 0.578 | 0.258 | 1.159 |
| 21 | 0.511 | 1.062 | 1.457 | 1.637 | 1.602 | 1.407 | 1.131 | 0.831 | 0.531 | 0.237 | 1.041 |
| 22 | 0.613 | 1.271 | 1.729 | 1.894 | 1.610 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 1.424 |
| 23 | 0.491 | 1.020 | 1.390 | 1.530 | 1.373 | 0.965 | 0.703 | 0.504 | 0.319 | 0.142 | 0.844 |
| 24 | 0.616 | 1.278 | 1.745 | 1.936 | 1.823 | 1.498 | 1.153 | 0.835 | 0.530 | 0.236 | 1.165 |
| 25 | 0.462 | 0.961 | 1.315 | 1.469 | 1.417 | 1.218 | 0.963 | 0.703 | 0.448 | 0.200 | 0.916 |
| 26 | 0.613 | 1.273 | 1.745 | 1.960 | 1.914 | 1.675 | 1.343 | 0.986 | 0.630 | 0.281 | 1.242 |
| 27 | 0.424 | 0.881 | 1.208 | 1.360 | 1.336 | 1.178 | 0.951 | 0.701 | 0.448 | 0.200 | 0.869 |
| 28 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 29 | 0.647 | 1.343 | 1.831 | 2.017 | 1.817 | 1.290 | 0.945 | 0.679 | 0.431 | 0.192 | 1.119 |
| 30 | 0.509 | 1.059 | 1.445 | 1.601 | 1.495 | 1.205 | 0.919 | 0.664 | 0.422 | 0.188 | 0.951 |
| 31 | 0.725 | 1.504 | 2.056 | 2.291 | 2.193 | 1.860 | 1.458 | 1.061 | 0.675 | 0.301 | 1.412 |
| 32 | 0.580 | 1.205 | 1.650 | 1.849 | 1.795 | 1.557 | 1.240 | 0.908 | 0.579 | 0.259 | 1.162 |
| 33 | 0.377 | 0.784 | 1.075 | 1.209 | 1.183 | 1.039 | 0.836 | 0.615 | 0.393 | 0.175 | 0.769 |
| 34 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 35 | 0.781 | 1.621 | 2.214 | 2.455 | 2.311 | 1.897 | 1.459 | 1.056 | 0.671 | 0.299 | 1.476 |
| 36 | 0.689 | 1.430 | 1.954 | 2.175 | 2.075 | 1.751 | 1.368 | 0.993 | 0.632 | 0.282 | 1.335 |
| 37 | 0.516 | 1.073 | 1.467 | 1.639 | 1.582 | 1.361 | 1.076 | 0.785 | 0.500 | 0.223 | 1.022 |
| 38 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 39 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 40 | 0.474 | 0.986 | 1.347 | 1.500 | 1.436 | 1.219 | 0.954 | 0.693 | 0.441 | 0.196 | 0.925 |
| 41 | 0.409 | 0.851 | 1.163 | 1.297 | 1.249 | 1.070 | 0.843 | 0.614 | 0.391 | 0.174 | 0.806 |

Table 31.  OSCAR reference power distribution (from Ref.[])

KEFF= 1.01147000000

| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.521 | 1.072 | 1.451 | 1.577 | 1.339 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 2 | 0.412 | 0.849 | 1.149 | 1.252 | 1.104 | 0.740 | 0.521 | 0.364 | 0.227 | 0.101 |
| 3 | 0.538 | 1.108 | 1.500 | 1.638 | 1.496 | 1.161 | 0.853 | 0.599 | 0.374 | 0.166 |
| 4 | 0.543 | 1.117 | 1.513 | 1.657 | 1.524 | 1.208 | 0.896 | 0.630 | 0.393 | 0.175 |
| 5 | 0.434 | 0.895 | 1.212 | 1.329 | 1.238 | 1.007 | 0.757 | 0.534 | 0.334 | 0.148 |
| 6 | 0.549 | 1.131 | 1.533 | 1.684 | 1.575 | 1.294 | 0.980 | 0.694 | 0.435 | 0.193 |
| 7 | 0.556 | 1.147 | 1.554 | 1.705 | 1.587 | 1.294 | 0.973 | 0.687 | 0.430 | 0.191 |
| 8 | 0.555 | 1.143 | 1.551 | 1.702 | 1.585 | 1.290 | 0.971 | 0.687 | 0.430 | 0.191 |
| 9 | 0.430 | 0.887 | 1.204 | 1.325 | 1.236 | 1.009 | 0.763 | 0.542 | 0.341 | 0.151 |
| 10 | 0.538 | 1.111 | 1.510 | 1.666 | 1.564 | 1.289 | 0.983 | 0.702 | 0.443 | 0.198 |
| 11 | 0.445 | 0.919 | 1.247 | 1.365 | 1.257 | 0.996 | 0.740 | 0.523 | 0.328 | 0.146 |
| 12 | 0.564 | 1.163 | 1.579 | 1.731 | 1.583 | 1.230 | 0.909 | 0.643 | 0.404 | 0.180 |
| 13 | 0.438 | 0.905 | 1.231 | 1.354 | 1.255 | 1.004 | 0.754 | 0.538 | 0.339 | 0.151 |
| 14 | 0.437 | 0.904 | 1.232 | 1.363 | 1.290 | 1.075 | 0.829 | 0.598 | 0.379 | 0.169 |
| 15 | 0.571 | 1.181 | 1.614 | 1.798 | 1.729 | 1.479 | 1.166 | 0.848 | 0.540 | 0.242 |
| 16 | 0.459 | 0.948 | 1.288 | 1.409 | 1.245 | 0.846 | 0.600 | 0.423 | 0.266 | 0.119 |
| 17 | 0.588 | 1.214 | 1.650 | 1.809 | 1.607 | 1.101 | 0.788 | 0.560 | 0.353 | 0.158 |
| 18 | 0.585 | 1.208 | 1.645 | 1.816 | 1.684 | 1.337 | 1.010 | 0.725 | 0.460 | 0.206 |
| 19 | 0.461 | 0.956 | 1.304 | 1.453 | 1.388 | 1.174 | 0.919 | 0.668 | 0.425 | 0.190 |
| 20 | 0.579 | 1.199 | 1.640 | 1.839 | 1.786 | 1.551 | 1.238 | 0.907 | 0.579 | 0.259 |
| 21 | 0.510 | 1.056 | 1.448 | 1.627 | 1.594 | 1.401 | 1.127 | 0.830 | 0.531 | 0.238 |
| 22 | 0.614 | 1.268 | 1.724 | 1.888 | 1.604 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 23 | 0.493 | 1.020 | 1.390 | 1.530 | 1.374 | 0.967 | 0.706 | 0.507 | 0.321 | 0.144 |
| 24 | 0.620 | 1.281 | 1.748 | 1.940 | 1.829 | 1.504 | 1.161 | 0.841 | 0.535 | 0.240 |
| 25 | 0.465 | 0.963 | 1.317 | 1.472 | 1.421 | 1.223 | 0.968 | 0.708 | 0.452 | 0.202 |
| 26 | 0.615 | 1.271 | 1.742 | 1.956 | 1.912 | 1.674 | 1.344 | 0.989 | 0.632 | 0.284 |
| 27 | 0.418 | 0.866 | 1.187 | 1.337 | 1.313 | 1.160 | 0.937 | 0.691 | 0.443 | 0.199 |
| 28 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 29 | 0.652 | 1.349 | 1.837 | 2.025 | 1.827 | 1.300 | 0.956 | 0.688 | 0.437 | 0.196 |
| 30 | 0.515 | 1.067 | 1.455 | 1.614 | 1.509 | 1.217 | 0.931 | 0.674 | 0.429 | 0.192 |
| 31 | 0.735 | 1.518 | 2.074 | 2.313 | 2.216 | 1.883 | 1.479 | 1.078 | 0.687 | 0.309 |
| 32 | 0.589 | 1.217 | 1.667 | 1.868 | 1.815 | 1.577 | 1.258 | 0.923 | 0.589 | 0.265 |
| 33 | 0.379 | 0.785 | 1.076 | 1.210 | 1.186 | 1.042 | 0.839 | 0.618 | 0.395 | 0.178 |
| 34 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 35 | 0.795 | 1.640 | 2.239 | 2.485 | 2.342 | 1.927 | 1.486 | 1.078 | 0.686 | 0.308 |
| 36 | 0.704 | 1.453 | 1.987 | 2.211 | 2.113 | 1.787 | 1.399 | 1.018 | 0.649 | 0.291 |
| 37 | 0.534 | 1.103 | 1.508 | 1.685 | 1.629 | 1.404 | 1.112 | 0.813 | 0.519 | 0.233 |
| 38 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 39 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 |
| 40 | 0.489 | 1.011 | 1.381 | 1.540 | 1.476 | 1.255 | 0.986 | 0.718 | 0.457 | 0.205 |
| 41 | 0.431 | 0.890 | 1.216 | 1.359 | 1.310 | 1.125 | 0.889 | 0.649 | 0.414 | 0.186 |

Table 32. OSCAR DIFFERENCE from recommended [%]:

| Hex | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | -0.2 | 0.3 | 0.4 | 0.6 | 0.4 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| 2 | 1.7 | 2.2 | 2.3 | 2.5 | 3.4 | 7.2 | 8.8 | 9.4 | 9.6 | 8.9 |
| 3 | 1.3 | 1.7 | 1.8 | 2.1 | 2.7 | 4.1 | 5.0 | 5.5 | 5.6 | 5.2 |
| 4 | 1.2 | 1.8 | 1.9 | 2.0 | 2.6 | 3.6 | 4.4 | 4.8 | 5.0 | 4.3 |
| 5 | 1.1 | 1.6 | 1.7 | 1.9 | 2.2 | 2.9 | 3.5 | 3.8 | 3.8 | 3.5 |
| 6 | 0.9 | 1.4 | 1.5 | 1.7 | 1.9 | 2.3 | 2.6 | 2.8 | 2.7 | 2.5 |
| 7 | 1.2 | 1.5 | 1.6 | 1.8 | 2.1 | 2.6 | 3.1 | 3.3 | 3.3 | 2.9 |
| 8 | 0.9 | 1.4 | 1.4 | 1.6 | 1.8 | 2.2 | 2.5 | 2.7 | 2.8 | 2.5 |
| 9 | 0.7 | 1.2 | 1.3 | 1.3 | 1.5 | 1.7 | 1.9 | 1.9 | 1.7 | 1.8 |
| 10 | 0.5 | 0.8 | 0.9 | 1.0 | 1.0 | 1.0 | 1.1 | 1.2 | 1.1 | 0.5 |
| 11 | 0.8 | 1.2 | 1.2 | 1.5 | 1.6 | 1.9 | 2.2 | 2.3 | 2.3 | 1.7 |
| 12 | 0.6 | 1.0 | 1.0 | 1.1 | 1.3 | 1.5 | 1.6 | 1.8 | 1.7 | 1.3 |
| 13 | 0.4 | 0.8 | 0.8 | 0.9 | 0.9 | 0.9 | 1.1 | 1.0 | 1.1 | 0.7 |
| 14 | 0.1 | 0.5 | 0.5 | 0.6 | 0.6 | 0.5 | 0.5 | 0.4 | 0.3 | 0.0 |
| 15 | 0.0 | 0.4 | 0.4 | 0.4 | 0.4 | 0.3 | 0.1 | 0.1 | -0.1 | -0.6 |
| 16 | 0.5 | 0.9 | 0.9 | 0.9 | 1.1 | 1.3 | 1.4 | 1.6 | 1.5 | 0.7 |
| 17 | 0.2 | 0.6 | 0.6 | 0.7 | 0.7 | 0.8 | 0.7 | 0.7 | 0.7 | 0.2 |
| 18 | -0.1 | 0.3 | 0.4 | 0.4 | 0.3 | 0.3 | 0.1 | 0.2 | 0.0 | -0.6 |
| 19 | -0.1 | 0.1 | 0.3 | 0.2 | 0.2 | 0.1 | 0.0 | -0.2 | -0.3 | -0.7 |
| 20 | -0.1 | 0.3 | 0.4 | 0.2 | 0.2 | 0.2 | 0.0 | -0.1 | -0.2 | -0.5 |
| 21 | 0.1 | 0.6 | 0.6 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | -0.4 |
| 22 | -0.1 | 0.3 | 0.3 | 0.3 | 0.4 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| 23 | -0.3 | 0.0 | 0.0 | 0.0 | -0.1 | -0.2 | -0.4 | -0.6 | -0.6 | -1.2 |
| 24 | -0.7 | -0.2 | -0.2 | -0.2 | -0.3 | -0.4 | -0.6 | -0.7 | -0.9 | -1.5 |
| 25 | -0.7 | -0.2 | -0.2 | -0.2 | -0.3 | -0.4 | -0.5 | -0.7 | -0.9 | -1.2 |
| 26 | -0.3 | 0.2 | 0.2 | 0.2 | 0.1 | 0.0 | -0.1 | -0.3 | -0.3 | -0.9 |
| 27 | 1.3 | 1.7 | 1.8 | 1.7 | 1.7 | 1.6 | 1.5 | 1.4 | 1.2 | 0.7 |
| 28 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| 29 | -0.7 | -0.4 | -0.4 | -0.4 | -0.6 | -0.8 | -1.1 | -1.3 | -1.4 | -1.9 |
| 30 | -1.1 | -0.7 | -0.7 | -0.8 | -0.9 | -1.0 | -1.3 | -1.5 | -1.6 | -2.2 |
| 31 | -1.4 | -0.9 | -0.9 | -1.0 | -1.0 | -1.2 | -1.4 | -1.6 | -1.7 | -2.4 |
| 32 | -1.5 | -1.0 | -1.0 | -1.0 | -1.1 | -1.3 | -1.4 | -1.6 | -1.6 | -2.4 |
| 33 | -0.5 | -0.1 | -0.1 | -0.1 | -0.2 | -0.3 | -0.4 | -0.5 | -0.5 | -1.4 |
| 34 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| 35 | -1.7 | -1.1 | -1.1 | -1.2 | -1.3 | -1.6 | -1.8 | -2.1 | -2.2 | -2.8 |
| 36 | -2.1 | -1.6 | -1.7 | -1.6 | -1.8 | -2.0 | -2.2 | -2.4 | -2.6 | -3.1 |
| 37 | -3.3 | -2.8 | -2.7 | -2.7 | -2.9 | -3.1 | -3.2 | -3.4 | -3.6 | -4.2 |
| 38 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| 39 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| 40 | -3.0 | -2.5 | -2.4 | -2.6 | -2.7 | -2.9 | -3.2 | -3.4 | -3.5 | -4.1 |
| 41 | -5.0 | -4.4 | -4.4 | -4.5 | -4.7 | -4.9 | -5.2 | -5.4 | -5.6 | -6.3 |

Table 33.  kq values by OSCAR and their deviation from DIF3D Recommended Solution

| NODE | KQ | Dev (%) |
| --- | --- | --- |
| 1 | 1.192 | 0.4 |
| 2 | 0.672 | 4.3 |
| 3 | 0.943 | 3.0 |
| 4 | 0.966 | 2.8 |
| 5 | 0.789 | 2.4 |
| 6 | 1.007 | 1.9 |
| 7 | 1.012 | 2.2 |
| 8 | 1.010 | 1.9 |
| 9 | 0.789 | 1.5 |
| 10 | 1.000 | 1.0 |
| 11 | 0.797 | 1.6 |
| 12 | 0.999 | 1.3 |
| 13 | 0.797 | 0.9 |
| 14 | 0.828 | 0.5 |
| 15 | 1.117 | 0.3 |
| 16 | 0.760 | 1.0 |
| 17 | 0.983 | 0.6 |
| 18 | 1.068 | 0.2 |
| 19 | 0.894 | 0.1 |
| 20 | 1.158 | 0.1 |
| 21 | 1.036 | 0.4 |
| 22 | 1.420 | 0.3 |
| 23 | 0.845 | -0.2 |
| 24 | 1.170 | -0.4 |
| 25 | 0.919 | -0.4 |
| 26 | 1.242 | 0.0 |
| 27 | 0.855 | 1.6 |
| 28 | 0.000 | 0.0 |
| 29 | 1.127 | -0.7 |
| 30 | 0.960 | -1.0 |
| 31 | 1.429 | -1.2 |
| 32 | 1.177 | -1.2 |
| 33 | 0.771 | -0.3 |
| 34 | 0.000 | 0.0 |
| 35 | 1.499 | -1.5 |
| 36 | 1.361 | -1.9 |
| 37 | 1.054 | -3.0 |
| 38 | 0.000 | 0.0 |
| 39 | 0.000 | 0.0 |
| 40 | 0.952 | -2.8 |
| 41 | 0.847 | -4.8 |