# AER Benchmark Specification Sheet

1. Test ID:	VVER-440 FA Burn-up Comparison

2. Short Description:	    Burn-up  processes  of   four   different   FA   of   VVER-440   type   are

- solved.  Basic  parameters,  like  kinf,  pin  power  distributions, cross  sections  and nuclear densities of selected nuclides are to be determined for  comparison

3. Submitted by: : P. Mikolaš (ŠKODA)

Date:	20.6.1999 (1. announcement Sept. 1996), Revision 1., 4.2.2000

4. Reviewed by L. Korpás (PARt), M. Makai (AEKI)

Date: September 1999

5. Accepted by: L. Korpás (PARt), M. Makai (AEKI)

Date: November 1999

6. Objective: To study the effect of burnup on reactivity, power distribution and cross-sections.

7. Rationale for Test Setup:  Although  VVER-440  FA  of Russian design  is  relatively simple,

- there are some features like radial  profiling  and  FA  gap.  This implies the necessity  of   calculation   by   the  whole  FA  when   preparing  few-group diffusion data   library   for   whole   core   calculations.   Therefore,   this benchmark  is  proposed. Benchmark   was   proposed   on  the sixth   Symposium of  AER,   Kirkkonummi,  Finland,  1996. Some  results  from  comparison  were presented  on the   seventh  and  on  the eight Symposium of    AER, where also solution   by  some authors presented Comprehensive comparison of kinf was presented  on the eight  Symposium   of   AER   (1998).   Comparison of  others  parameter   is expected to be provided if related data are available.

8. Input:

a, Geometry												b, Material Composition	(Geometry and material composition is given in

the Appendix

c, Other			  Calculated states are provided in Table I.

9. Hardware and Software Requirements: memory, files, app. comp. time

- There  are  no special  requirements on  Hardware  and  Software, both depend on code  used  (usually  Workstation  or  PC (Pentium)),  time depends  on the code and  computer type used (typically  tens of minutes or maybe due hour for show on older computer)

10. Output:

a, Expected Results (primary, secondary)

- Primary results are kinf, and  pin power distribution, the others (concentrations, cross sections (micro- and macroscopic are supposed  as secondary), Expected results are described in the from Tables II.-V.

b, Files, Format

MS-WORD format is not necessary, only ASCI format is requested

11. References

[1]	In-core fuel management code package validation for WWER’s, IAEA  - TEC DOC-847,

Vienna, Austria, 1995

[2]	P.Mikoláš:      Proposal   on    benchmark   for    VVER-440   FA    burn-up   comparison,

In:   Proceedings  of   the  sixth   Symposium  of   AER. Kirkkonummi,  23-26  Sept.1996,	Finland

[3]	P.Mikoláš:    Some  results  of  VVER-440  FA  burn-up  comparison, In:  Proceedings  of

the  seventh  Symposium of AER, Hörnitz near Zittau, Germany, 23-26 Sept. 1997

[4]	P.Daøílek:    Benchmark   for  VVER-440   FA  burn-up  comparison,  In:  Proceedings  of

the  seventh  Symposium of AER, Hörnitz near Zittau, Germany, 23-26 Sept. 1997

[5]	Cs.Maráczy:  Results  of  the  VVER-440  fuel   assembly  benchmark  calculated with the 	multicell  module  of  the   KARATE-440 code system,  In:  Proceedings  of  the  seventh  	Symposium of AER, Hörnitz near Zittau, Germany, 23-26 Sept. 1997

[6]	R.Becker, W.R.Blank:   NESSEL-4  Benchmark results  for a FA of type VVER-440, In:  	Proceedings  of  the  seventh  Symposium of AER, Hörnitz near Zittau, Germany,	 23-26 	Sept. 1997

[7]	P.Mikoláš: Benchmark  for VVER-440 FA  burnup  comparison, In  Proceedings  of  the  	eight   Symposium   of   AER,  Bystrice nad Pernštejnem,  Czech Republic,  21-25  Sept. 	1998

[8]	E.Tinková: Unpublished information

12. Recommended Solution:

a, Method

- There is  not  reference  solution   Results  of   Solution   calculated  by  author are

- summarized  in   Tables II-V.  Other  results  are given in References Benchmark is 		designed  for intercomparison of selection.

b, Data, Estimated Error

13. Summary of Available Solutions

Solution of participants  are given in Refs. [2,4,5,6,8].

Analyses and intercomparison of result are summarized in Refs. [3,7].

A p p e n d i x

INPUT DATA

Input data were taken from [1]. Part of this report is reprinted here.

(Some data are not relevant to this benchmark)

Fuel assembly data

The following information is valid for each type of fuel assembly (FA):

General:

Fuel assembly pitch							14.7 cm

Gap between assemblies						0.3 cm

Shell material								Zirconium alloy

(Z125-2.5%Nb)

Shell thickness								0.2 cm

Fuel type:

Enrichment

Geometry (including all supporting elements and enrichments

of particular fuel rods)							Fig.2.1.1.3

Number of fuel rods							126

Total mass of UO2 per FA						136 kg

(119.75 kg U metal)

Lattice pitch								1.22 cm

Spacer grid:

Material								12X18H10T

stainless-steel

Density								7.86 g/cm3

Number, location, axial dimensions, mass or volume fraction

of materials in one spacer grid						Fig.2.1.1.4

Mass of one spacer grid						0.118 kg

Instrumentation tubes:

Material								Z110 - 1%Nb

Zirconium alloy

Density								6.52 g/cm3

Outer radius								0.515 cm

Thickness								0.075 cm

Location in core							in the center of FA

Fuel rod

Cladding:

Material								Z110 - 1%Nb

Zirconium alloy

Density								6.52 g/cm3

Outer radius								0.455 cm

Inner radius								0.386 cm

Pellet:

Material								UO2

Percent of theoretical density x density				0.95 x 10.2 g/cm3

Outer Radius								0.3800(0.0025 cm

Average mass of pellet						13.17 g UO2

(11.59 g metal)

Height									3 cm

Number in fuel rod							82

Height of UO2 (HFP)							246 cm

Initial He pressure, if any						(0.15 MPa

Mass of UO2 per fuel rod in a fuel assembly				1080 g

Mass of UO2 per fuel rod in a control assembly			1035 g

Control assembly

Geometry:

in radial plane (cross section of control absorber)			Fig.2.1.1.5

in axial plane								Fig.2.1.1.6

Absorber							Boron steel

Density							7.51 g/cm3

Compositions of steel and boron steel

Material	Weight per cent			Nominal density

Fe	Ni	Cr	Mn	B	g/cm3

Steel		70.5	10	18	1.5	-	7.86

Boron steel	69.2	9.8	17.7	1.5	1.9	7.51

Compositions of zirconium alloy

Material	Weight per cent

Zr	Nb	Hf

Z110		98.97	1.0	0.03

Z125		97.47	2.5	0.03

Remarks: (important!)

1) Suppose  that  mass of  UO2  per fuel rod (pin)  in  each  FA is 1080 g for  nuclei  concentration

determination.

- Height of UO2 is 246 cm for all cases

- Density  of  UO2  is  calculated  from  pin  height  (246 cm), its  outer radius (0.38) cm and its

mass (1080 g).

2) For  classical design, steel grids  are supposed, for  advanced fuel Zr girds   (mass of one spacer

grid  is  0.092 kg, density of Zr alloy is 6.52 g/cm3, composition is supposed  the same as for Zr

110 alloy) are designed;  the positions of grids are the same as for steel grids.

3) FA shell thickness is 0.2 cm for classical fuel, 0.15 cm for advanced one!

4) Enrichment  of  individual  pins  for   advanced  fuel is given on Fig.1. also  with  numeration of

individual pins (also used in results concerning pin-power distribution)

5) Total  fuel  loading in the core is supposed 42 000 kg U (this value  does  not correspond to the

individual pin mass, but this value is used in burn-up process).

6) For  zero  burn-up  step,  concentrations of Xe135 and Sm149 are zero.  For  the others steps, Xe

and Sm are real (it means calculated by an adequate process).

7) Figs mentioned in „Fuel assembly data“ above are irrelevant.

There  is  not  given  any  prescription, how to model FA,  or  any other recommendations.

If  burn-up  process  is  followed,  steps  are  requested  at   least by step 5 [MWd/kgU], but some

data can be presented only by step 15 [MWd/kgU].

Table 1	Calculated states

| State | Burn-up [Mwd /kgU] | Tr [K] | Tc [K] | Tm [K] | [g/kg] | Xe135 | Sm149 | Void |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.0 | 935.15 | 558.15 | 558.15 | 0.0 | none | none | 1 |
| 2 | 0.0 | 373.15 | 373.15 | 73.15 | 3.0 | none | none | 1 |
| 3 | 0.0 | 935.15 | 473.15 | 473.15 | 3.0 | none | none | 1 |
| 4 | 0.0 | 935.15 | 543.15 | 543.15 | 3.0 | none | none | 1 |
| 5 | 0.0 | 658.15 | 558.15 | 558.15 | 3.0 | none | none | 1 |
| 6 | 0.0 | 1223.15 | 558.15 | 558.15 | 3.0 | none | none | 1 |
| 7 | 0.0 | 935.15 | 558.15 | 558.15 | 3.0 | none | none | 1.035027 |
| 8 | 0.0 | 935.15 | 558.15 | 558.15 | 3.0 | none | none | 0.959583 |
| 9 | 0.0 | 935.15 | 573.15 | 573.15 | 3.0 | none | none | 1 |
| 10 | 0.0 | 293.15 | 293.15 | 293.15 | 6.0 | none | none | 1 |
| 11 | 0.0 | 373.15 | 373.15 | 373.15 | 6.0 | none | none | 1 |
| 12 | 0.0 | 463.15 | 463.15 | 463.15 | 6.0 | none | none | 1 |
| 13 | 0.0 | 533.15 | 533.15 | 533.15 | 6.0 | none | none | 1 |
| 14 | 0.0 | 935.15 | 558.15 | 558.15 | 6.0 | none | none | 1 |
| 15 | 0.0 | 473.15 | 473.15 | 473.15 | 8.0 | none | none | 1 |
| 16 | 0.0 | 533.15 | 533.15 | 533.15 | 8.0 | none | none | 0.95 |
| 17 | 0.0 | 533.15 | 533.15 | 533.15 | 8.0 | none | none | 0.9 |
| 18 | 0.0 | 533.15 | 533.15 | 533.15 | 8.0 | none | none | 1 |
| 19 | 0.0 | 373.15 | 373.15 | 373.15 | 9.0 | none | none | 1 |
| 20 | 0.0 | 935.15 | 558.15 | 558.15 | 9.0 | none | none | 1 |
| 21 | 0.0 | 293.15 | 293.15 | 293.15 | 12.0 | none | none | 1 |
| 22 | 0.0 | 935.15 | 558.15 | 558.15 | 3.0 | none | none | 1 |
| 23 | 0.2 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 24 | 1.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 25 | 2.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 26 | 3.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 27 | 4.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 28 | 5.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 29 | 7.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 30 | 10.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 31 | 12.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 32 | 15.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 33 | 17.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 34 | 20.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 35 | 22.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 36 | 25.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 37 | 27.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 38 | 30.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 39 | 32.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 40 | 35.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 41 | 37.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 42 | 40.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 43 | 42.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 44 | 45.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 45 | 47.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 46 | 50.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 47 | 52.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 48 | 55.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 49 | 57.5 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |
| 50 | 60.0 | 935.15 | 558.15 | 558.15 | 3.0 | calc | calc | 1 |

Table II	     Kinf  values

| enrich: | 1.6 w/o | 2.4 w/o | 3.6 w/o | 4.0 w/o (p) |
| --- | --- | --- | --- | --- |
| state | Kinf |
| 1 | 1.12400 | 1.23784 | 1.32876 | 1.34439 |
| 2 | 1.05356 | 1.19277 | 1.30997 | 1.32808 |
| 3 | 1.03778 | 1.17116 | 1.28291 | 1.30048 |
| 4 | 1.03681 | 1.16506 | 1.27187 | 1.28897 |
| 5 | 1.04459 | 1.17221 | 1.27828 | 1.29534 |
| 6 | 1.02783 | 1.15363 | 1.25838 | 1.27523 |
| 7 | 1.03658 | 1.16491 | 1.27178 | 1.28889 |
| 8 | 1.03469 | 1.15939 | 1.26298 | 1.27974 |
| 9 | 1.03447 | 1.15924 | 1.26289 | 1.27966 |
| 10 | 0.95982 | 1.10826 | 1.23895 | 1.25825 |
| 11 | 0.96090 | 1.10821 | 1.23738 | 1.25661 |
| 12 | 0.96595 | 1.10980 | 1.23506 | 1.25398 |
| 13 | 0.97131 | 1.11031 | 1.23035 | 1.24878 |
| 14 | 0.96197 | 1.09695 | 1.21321 | 1.23120 |
| 15 | 0.91787 | 1.06458 | 1.19512 | 1.21457 |
| 16 | 0.93047 | 1.07082 | 1.19411 | 1.21285 |
| 17 | 0.93454 | 1.07236 | 1.19295 | 1.21140 |
| 18 | 0.92739 | 1.06854 | 1.19441 | 1.21342 |
| 19 | 0.88465 | 1.03601 | 1.17338 | 1.19341 |
| 20 | 0.89904 | 1.03923 | 1.16368 | 1.18250 |
| 21 | 0.81594 | 0.96936 | 1.11344 | 1.13413 |
| 22 | 1.03590 | 1.16259 | 1.26795 | 1.28489 |
| 23 | 0.99936 | 1.12036 | 1.22425 | 1.24110 |
| 24 | 0.99938 | 1.11196 | 1.21230 | 1.22881 |
| 25 | 0.99601 | 1.10332 | 1.20232 | 1.21873 |
| 26 | 0.98899 | 1.09284 | 1.19150 | 1.20796 |
| 27 | 0.98061 | 1.08165 | 1.18021 | 1.19674 |
| 28 | 0.97186 | 1.07037 | 1.16881 | 1.18542 |
| 29 | 0.95083 | 1.04346 | 1.14116 | 1.15788 |
| 30 | 0.93168 | 1.01908 | 1.11559 | 1.13356 |
| 31 | 0.91420 | 0.99688 | 1.09197 | 1.10881 |
| 32 | 0.89814 | 0.97641 | 1.07001 | 1.08676 |
| 33 | 0.88329 | 0.95734 | 1.04938 | 1.06604 |
| 34 | 0.86956 | 0.93945 | 1.02984 | 1.04641 |
| 35 | 0.85686 | 0.92260 | 1.01122 | 1.02770 |
| 36 | 0.84514 | 0.90671 | 0.99339 | 1.00980 |
| 37 | 0.83499 | 0.89174 | 0.97630 | 0.99259 |
| 38 | 0.82512 | 0.87764 | 0.95984 | 0.97599 |
| 39 | 0.00000 | 0.86440 | 0.94398 | 0.95995 |
| 40 | 0.00000 | 0.85201 | 0.92870 | 0.94446 |
| 41 | 0.00000 | 0.84044 | 0.91401 | 0.92950 |
| 42 | 0.00000 | 0.82967 | 0.89990 | 0.91508 |
| 43 | 0.00000 | 0.81968 | 0.88637 | 0.90121 |
| 44 | 0.00000 | 0.81044 | 0.87344 | 0.88788 |
| 45 | 0.00000 | 0.00000 | 0.86111 | 0.87511 |
| 46 | 0.00000 | 0.00000 | 0.84940 | 0.86292 |
| 47 | 0.00000 | 0.00000 | 0.83831 | 0.85130 |
| 48 | 0.00000 | 0.00000 | 0.82783 | 0.84027 |
| 49 | 0.00000 | 0.00000 | 0.81798 | 0.82984 |
| 50 | 0.00000 | 0.00000 | 0.80875 | 0.82000 |

Table III	Relative pin power distribution

| fuel enrichment = 1.6 w/o |
| --- |
| State Pin No. | 22 | 32 | 38 |
| 1 | 0.97224 | 0.97573 | 1.01101 |
| 2 | 0.96011 | 0.95647 | 0.98670 |
| 3 | 0.96070 | 0.95682 | 0.98867 |
| 4 | 0.96350 | 0.96426 | 0.98545 |
| 5 | 0.95973 | 0.95838 | 0.98326 |
| 6 | 0.95973 | 0.95838 | 0.98326 |
| 7 | 0.98482 | 0.98401 | 0.98702 |
| 8 | 0.97403 | 0.96896 | 0.97767 |
| 9 | 0.97118 | 0.96453 | 0.97518 |
| 10 | 0.97403 | 0.96897 | 0.97768 |
| 11 | 1.01986 | 1.01773 | 0.99987 |
| 12 | 1.00352 | 0.99635 | 0.98529 |
| 13 | 0.99739 | 0.98729 | 0.98014 |
| 14 | 0.99739 | 0.98730 | 0.98015 |
| 15 | 1.00352 | 0.99636 | 0.98530 |
| 16 | 1.07446 | 1.07587 | 1.03888 |
| 17 | 1.05054 | 1.06508 | 1.03980 |
| 18 | 1.04122 | 1.05137 | 1.03143 |
| 19 | 1.04027 | 1.04969 | 1.03201 |
| 20 | 1.04122 | 1.05138 | 1.03143 |
| 21 | 1.05054 | 1.06508 | 1.03980 |

| fuel enrichment = 2.4 w/o |
| --- |
| State Pin No. | 22 | 32 | 38 | 44 |
| 1 | 0.96715 | 0.97157 | 0.97961 | 0.98381 |
| 2 | 0.95083 | 0.95191 | 0.95988 | 0.96330 |
| 3 | 0.95159 | 0.95248 | 0.96019 | 0.96348 |
| 4 | 0.95494 | 0.95988 | 0.97040 | 0.97525 |
| 5 | 0.95044 | 0.95360 | 0.96300 | 0.96722 |
| 6 | 0.95044 | 0.95360 | 0.96300 | 0.96722 |
| 7 | 0.98027 | 0.98313 | 0.98878 | 0.99069 |
| 8 | 0.96761 | 0.96688 | 0.97067 | 0.97155 |
| 9 | 0.96761 | 0.96206 | 0.96528 | 0.96587 |
| 10 | 0.97762 | 0.96689 | 0.97068 | 0.97156 |
| 11 | 1.02264 | 1.02173 | 1.02037 | 1.01916 |
| 12 | 1.00306 | 0.99808 | 0.99496 | 0.99278 |
| 13 | 0.99550 | 0.98812 | 0.98407 | 0.98142 |
| 14 | 0.99550 | 0.98813 | 0.98408 | 0.98143 |
| 15 | 1.00306 | 0.99809 | 0.99497 | 0.99279 |
| 16 | 1.09388 | 1.08443 | 1.06656 | 1.06078 |
| 17 | 1.06355 | 1.06939 | 1.06295 | 1.06099 |
| 18 | 1.05185 | 1.05417 | 1.04657 | 1.04398 |
| 19 | 1.05057 | 1.05230 | 1.04446 | 1.04175 |
| 20 | 1.05186 | 1.05418 | 1.04657 | 1.04399 |
| 21 | 1.06356 | 1.06940 | 1.06296 | 1.06099 |

Tab. III - cont.

| fuel enrichment = 3.6 w/o |
| --- |
| State Pin No. | 22 | 32 | 38 | 44 | 50 |
| 1 | 0.96138 | 0.96623 | 0.97410 | 0.98166 | 0.98588 |
| 2 | 0.94019 | 0.94411 | 0.95423 | 0.96295 | 0.96667 |
| 3 | 0.94116 | 0.94511 | 0.95493 | 0.96334 | 0.96687 |
| 4 | 0.94507 | 0.95167 | 0.96468 | 0.97566 | 0.98062 |
| 5 | 0.93978 | 0.94512 | 0.95689 | 0.96696 | 0.97145 |
| 6 | 0.93978 | 0.94512 | 0.95689 | 0.96696 | 0.97145 |
| 7 | 0.97479 | 0.97953 | 0.98798 | 0.99384 | 0.99542 |
| 8 | 0.96008 | 0.96197 | 0.96840 | 0.97299 | 0.97396 |
| 9 | 0.95582 | 0.95673 | 0.96256 | 0.96680 | 0.96761 |
| 10 | 0.96009 | 0.96198 | 0.96842 | 0.97301 | 0.97398 |
| 11 | 1.02536 | 1.02569 | 1.02574 | 1.02415 | 1.02206 |
| 12 | 1.00215 | 0.99923 | 0.99744 | 0.99502 | 0.99265 |
| 13 | 0.99301 | 0.98822 | 0.98547 | 0.98257 | 0.98001 |
| 14 | 0.99302 | 0.98824 | 0.98548 | 0.98258 | 0.98002 |
| 15 | 1.00216 | 0.99924 | 0.99745 | 0.99503 | 0.99267 |
| 16 | 1.11698 | 1.10166 | 1.07574 | 1.05767 | 1.05266 |
| 17 | 1.07878 | 1.07871 | 1.06812 | 1.05943 | 1.05698 |
| 18 | 1.06438 | 1.06156 | 1.04987 | 1.04079 | 1.03818 |
| 19 | 1.06284 | 1.05958 | 1.04760 | 1.03836 | 1.03567 |
| 20 | 1.06439 | 1.06157 | 1.04988 | 1.04080 | 1.03819 |
| 21 | 1.07879 | 1.07871 | 1.06813 | 1.05944 | 1.05699 |

| fuel enrichment = 4.0; 3.6; 3.3 w/o |
| --- |
| State Pin No. | 22 | 32 | 38 | 44 | 50 |
| 1 | 0.98132 | 0.97768 | 0.98533 | 0.99045 | 0.99222 |
| 2 | 0.96072 | 0.95734 | 0.96496 | 0.97130 | 0.97282 |
| 3 | 0.96091 | 0.95783 | 0.96523 | 0.97133 | 0.97272 |
| 4 | 0.97091 | 0.96848 | 0.97855 | 0.98668 | 0.98899 |
| 5 | 0.96295 | 0.96011 | 0.96920 | 0.97668 | 0.97876 |
| 6 | 0.96295 | 0.96011 | 0.96921 | 0.97668 | 0.97876 |
| 7 | 1.01241 | 1.00355 | 1.00581 | 1.00645 | 1.00368 |
| 8 | 0.99133 | 0.98167 | 0.98269 | 0.98275 | 0.98004 |
| 9 | 0.98523 | 0.97521 | 0.97586 | 0.97578 | 0.97308 |
| 10 | 0.99134 | 0.98168 | 0.98270 | 0.98277 | 0.98005 |
| 11 | 0.99477 | 1.00070 | 0.99658 | 0.99419 | 0.99592 |
| 12 | 1.04992 | 1.03042 | 1.02029 | 1.01142 | 1.00399 |
| 13 | 1.03448 | 1.01516 | 1.00489 | 0.99623 | 0.98921 |
| 14 | 1.03449 | 1.01518 | 1.00490 | 0.99624 | 0.98922 |
| 15 | 1.04993 | 1.03043 | 1.02030 | 1.01144 | 1.00401 |
| 16 | 1.01813 | 1.05037 | 1.05070 | 1.05175 | 1.05904 |
| 17 | 0.97767 | 1.00623 | 1.00614 | 1.00763 | 1.01524 |
| 18 | 1.02912 | 1.04127 | 1.03815 | 1.03548 | 1.03689 |
| 19 | 1.02461 | 1.03722 | 1.03417 | 1.03162 | 1.03321 |
| 20 | 1.02913 | 1.04127 | 1.03816 | 1.03549 | 1.03690 |
| 21 | 0.97768 | 1.00624 | 1.00615 | 1.00764 | 1.01525 |

Table IV	Concentrations of selected nuclides

| State | U235 Pu242 | U238 Am241 | Np239 Am242m | Pu239 Am243 | Pu240 Xe135 | Pu241 Sm149 |
| --- | --- | --- | --- | --- | --- | --- |
| fuel enrichment = 1.6 w/o |
| 22 | 0.10683E-03 0.30544E-19 | 0.64868E-02 0.30543E-19 | 0.30543E-19 0.30543E-19 | 0.30544E-20 0.30544E-19 | 0.30543E-19 0.30543E-19 | 0.30544E-19 0.30544E-19 |
| 32 | 0.41269E-04 0.11627E-05 | 0.63898E-02 0.80520E-07 | 0.67607E-06 0.87012E-09 | 0.31245E-04 0.12305E-06 | 0.95314E-05 0.15892E-08 | 0.51744E-05 0.16059E-07 |
| 38 | 0.16747E-04 0.46846E-05 | 0.62864E-02 0.25112E-06 | 0.71314E-06 0.30789E-08 | 0.36775E-04 0.10256E-05 | 0.16399E-04 0.16305E-08 | 0.98789E-05 0.18846E-07 |
| fuel enrichment = 2.4 w/o |
| 22 | 0.16023E-03 0.30544E-19 | 0.64340E-02 0.30543E-19 | 0.30543E-19 0.30543E-19 | 0.30544E-20 0.30543E-19 | 0.30544E-19 0.30544E-19 | 0.30543E-19 0.30543E-19 |
| 32 | 0.79484E-04 0.68064E-06 | 0.63514E-02 0.66322E-07 | 0.58420E-06 0.71617E-09 | 0.32016E-04 0.60462E-07 | 0.77360E-05 0.19977E-08 | 0.42433E-05 0.20229E-07 |
| 38 | 0.38509E-04 0.34169E-05 | 0.62597E-02 0.25332E-06 | 0.64234E-06 0.32014E-08 | 0.39102E-04 0.65279E-06 | 0.14971E-04 0.19227E-08 | 0.94566E-05 0.22413E-07 |
| 44 | 0.17789E-04 0.69751E-05 | 0.61604E-02 0.39723E-06 | 0.68492E-06 0.52335E-08 | 0.41088E-04 0.19698E-05 | 0.19328E-04 0.18581E-08 | 0.12352E-04 0.22926E-07 |
| fuel enrichment =3.6 w/o |
| 22 | 0.24035E-03 0.30543E-19 | 0.63546E-02 0.30543E-19 | 0.30543E-19 0.30543E-19 | 0.30544E-20 0.30543E-19 | 0.30544E-19 0.30544E-19 | 0.30543E-19 0.30543E-19 |
| 32 | 0.14642E-03 0.35169E-06 | 0.62846E-02 0.50589E-07 | 0.49260E-06 0.53677E-09 | 0.32486E-04 0.25986E-07 | 0.59419E-05 0.26448E-08 | 0.32268E-05 0.27600E-07 |
| 38 | 0.85942E-04 0.21716E-05 | 0.62061E-02 0.24568E-06 | 0.54913E-06 0.32380E-08 | 0.42556E-04 0.35183E-06 | 0.12888E-04 0.24782E-08 | 0.86430E-05 0.29507E-07 |
| 44 | 0.47414E-04 0.51131E-05 | 0.61196E-02 0.44125E-06 | 0.60307E-06 0.61286E-08 | 0.45280E-04 0.12610E-05 | 0.18048E-04 0.22853E-08 | 0.12376E-04 0.28785E-07 |
| 50 | 0.24573E-04 0.83353E-05 | 0.60258E-02 0.55442E-06 | 0.64771E-06 0.77937E-08 | 0.45691E-04 0.26758E-05 | 0.21307E-04 0.21377E-08 | 0.14406E-04 0.27788E-07 |
| fuel enrichment =4.0; 3.6; 3.3 w/o |
| 22 | 0.25529E-03 0.30544E-19 | 0.63399E-02 0.30544E-19 | 0.30544E-19 0.30544E-19 | 0.30544E-20 0.30544E-19 | 0.30544E-19 0.30543E-19 | 0.30544E-19 0.30543E-19 |
| 32 | 0.15969E-03 0.31769E-06 | 0.62716E-02 0.48233E-07 | 0.47968E-06 0.50820E-09 | 0.32425E-04 0.22820E-07 | 0.56989E-05 0.27582E-08 | 0.30752E-05 0.29023E-07 |
| 38 | 0.96367E-04 0.20140E-05 | 0.61952E-02 0.24212E-06 | 0.53461E-06 0.32037E-08 | 0.42968E-04 0.31771E-06 | 0.12545E-04 0.25815E-08 | 0.84530E-05 0.30901E-07 |
| 44 | 0.54767E-04 0.48337E-05 | 0.61108E-02 0.44539E-06 | 0.58813E-06 0.62325E-08 | 0.45926E-04 0.11643E-05 | 0.17778E-04 0.23717E-08 | 0.12298E-04 0.29998E-07 |
| 50 | 0.29205E-04 0.80092E-05 | 0.60190E-02 0.56725E-06 | 0.63460E-06 0.80330E-08 | 0.46304E-04 0.25205E-05 | 0.21179E-04 0.22010E-08 | 0.14439E-04 0.28707E-07 |

Table V		Microscopic cross sections of selected nuclides

| State cross section | U235 Pu242 | U238 Am241 | Np239 Am242m | Pu239 Am243 | Pu240 Xe135 | Pu241 Sm149 |
| --- | --- | --- | --- | --- | --- | --- |
| fuel enrichment = 1.6 w/o |
| 22 (a1 | 0.13221E+02 0.34882E+02 | 0.98451E+00 0.32292E+02 | 0.15011E+02 0.50655E+02 | 0.15383E+02 0.58802E+02 | 0.26904E+03 0.13815E+03 | 0.23614E+02 0.11037E+03 |
| 22 (a2 | 0.33755E+03 0.10527E+02 | 0.14711E+01 0.62306E+03 | 0.19790E+02 0.60901E+04 | 0.11202E+04 0.44577E+02 | 0.18699E+03 0.16528E+07 | 0.10163E+04 0.51249E+05 |
| 22 (f1 | 0.90359E+01 0.49761E+00 | 0.11068E+00 0.74560E+00 | 0.65489E+00 0.44154E+02 | 0.96134E+01 0.47230E+00 | 0.70477E+00 0.00000E+00 | 0.18375E+02 0.00000E+00 |
| 22 (f2 | 0.28792E+03 0.81577E-02 | 0.63396E-05 0.40910E+01 | 0.00000E+00 0.49168E+04 | 0.72533E+03 0.28984E-01 | 0.42431E-01 0.00000E+00 | 0.75836E+03 0.00000E+00 |
| 32 (a1 | 0.13132E+02 0.34935E+02 | 0.99830E+00 0.31262E+02 | 0.15128E+02 0.47629E+02 | 0.15057E+02 0.57990E+02 | 0.12883E+03 0.12137E+03 | 0.23572E+02 0.10085E+03 |
| 32 (a2 | 0.32475E+03 0.10299E+02 | 0.14260E+01 0.61136E+03 | 0.19215E+02 0.58735E+04 | 0.10527E+04 0.44142E+02 | 0.18461E+03 0.15886E+07 | 0.96574E+03 0.49161E+05 |
| 32 (f1 | 0.88930E+01 0.49190E+00 | 0.10918E+00 0.73029E+00 | 0.64815E+00 0.41476E+02 | 0.93868E+01 0.46576E+00 | 0.67190E+00 0.00000E+00 | 0.18330E+02 0.00000E+00 |
| 32 (f2 | 0.27712E+03 0.79773E-02 | 0.61434E-05 0.39776E+01 | 0.00000E+00 0.47418E+04 | 0.68366E+03 0.28709E-01 | 0.41784E-01 0.00000E+00 | 0.72097E+03 0.00000E+00 |
| 38 (a1 | 0.13090E+02 0.33753E+02 | 0.10074E+01 0.30219E+02 | 0.15150E+02 0.46089E+02 | 0.14972E+02 0.56164E+02 | 0.96798E+02 0.11406E+03 | 0.23464E+02 0.96475E+02 |
| 38 (a2 | 0.32278E+03 0.10238E+02 | 0.14205E+01 0.61139E+03 | 0.19123E+02 0.58290E+04 | 0.10439E+04 0.43993E+02 | 0.18425E+03 0.15802E+07 | 0.95599E+03 0.48898E+05 |
| 38 (f1 | 0.88357E+01 0.48829E+00 | 0.10836E+00 0.71879E+00 | 0.64484E+00 0.40122E+02 | 0.93146E+01 0.46154E+00 | 0.66270E+00 0.00000E+00 | 0.18239E+02 0.00000E+00 |
| 38 (f2 | 0.27546E+03 0.79290E-02 | 0.61196E-05 0.39735E+01 | 0.00000E+00 0.47058E+04 | 0.67827E+03 0.28614E-01 | 0.41679E-01 0.00000E+00 | 0.71370E+03 0.00000E+00 |
| fuel enrichment = 2.4 w/o |
| 22 (a1 | 0.12657E+02 0.33251E+02 | 0.96726E+00 0.30779E+02 | 0.14529E+02 0.48178E+02 | 0.14861E+02 0.55982E+02 | 0.25207E+03 0.12965E+03 | 0.22738E+02 0.10452E+03 |
| 22 (a2 | 0.32015E+03 0.10086E+02 | 0.14019E+01 0.64664E+03 | 0.18835E+02 0.58311E+04 | 0.11329E+04 0.43176E+02 | 0.18238E+03 0.15433E+07 | 0.98841E+03 0.48363E+05 |
| 22 (f1 | 0.86714E+01 0.50603E+00 | 0.11312E+00 0.74610E+00 | 0.66741E+00 0.42002E+02 | 0.92942E+01 0.47979E+00 | 0.71160E+00 0.00000E+00 | 0.17702E+02 0.00000E+00 |
| 22 (f2 | 0.27301E+03 0.78083E-02 | 0.60380E-05 0.42999E+01 | 0.00000E+00 0.47114E+04 | 0.72924E+03 0.28075E-01 | 0.41231E-01 0.00000E+00 | 0.73623E+03 0.00000E+00 |
| 32 (a1 | 0.12773E+02 0.33956E+02 | 0.98582E+00 0.30430E+02 | 0.14779E+02 0.46447E+02 | 0.14722E+02 0.56258E+02 | 0.13606E+03 0.11827E+03 | 0.22965E+02 0.98461E+02 |
| 32 (a2 | 0.31231E+03 0.10002E+02 | 0.13764E+01 0.62541E+03 | 0.18537E+02 0.56951E+04 | 0.10560E+04 0.43222E+02 | 0.18142E+03 0.15112E+07 | 0.94511E+03 0.47112E+05 |
| 32 (f1 | 0.86746E+01 0.49760E+00 | 0.11082E+00 0.73207E+00 | 0.65656E+00 0.40456E+02 | 0.91890E+01 0.47089E+00 | 0.68017E+00 0.00000E+00 | 0.17866E+02 0.00000E+00 |
| 32 (f2 | 0.26647E+03 0.77419E-02 | 0.59275E-05 0.41022E+01 | 0.00000E+00 0.46003E+04 | 0.68302E+03 0.28112E-01 | 0.40954E-01 0.00000E+00 | 0.70481E+03 0.00000E+00 |
| Table V - cont. |
| 38 (a1 | 0.12844E+02 0.33405E+02 | 0.99825E+00 0.29735E+02 | 0.14900E+02 0.45327E+02 | 0.14721E+02 0.55260E+02 | 0.99175E+02 0.11210E+03 | 0.23032E+02 0.94897E+02 |
| 38 (a2 | 0.31169E+03 0.10011E+02 | 0.13792E+01 0.61621E+03 | 0.18587E+02 0.56658E+04 | 0.10359E+04 0.43280E+02 | 0.18121E+03 0.15172E+07 | 0.93533E+03 0.47155E+05 |
| 38 (f1 | 0.86865E+01 0.49239E+00 | 0.10947E+00 0.72050E+00 | 0.65049E+00 0.39464E+02 | 0.91686E+01 0.46526E+00 | 0.66773E+00 0.00000E+00 | 0.17910E+02 0.00000E+00 |
| 38 (f2 | 0.26598E+03 0.77497E-02 | 0.59401E-05 0.40240E+01 | 0.00000E+00 0.45757E+04 | 0.67140E+03 0.28151E-01 | 0.40916E-01 0.00000E+00 | 0.69783E+03 0.00000E+00 |
| 44 (a1 | 0.12877E+02 0.32405E+02 | 0.10081E+01 0.29090E+02 | 0.14960E+02 0.44521E+02 | 0.14734E+02 0.53792E+02 | 0.85737E+02 0.10830E+03 | 0.23032E+02 0.92760E+02 |
| 44 (a2 | 0.31031E+03 0.10001E+02 | 0.13797E+01 0.61186E+03 | 0.18599E+02 0.56410E+04 | 0.10288E+04 0.43240E+02 | 0.18085E+03 0.15185E+07 | 0.93061E+03 0.47139E+05 |
| 44 (f1 | 0.86895E+01 0.48846E+00 | 0.10852E+00 0.71145E+00 | 0.64640E+00 0.38756E+02 | 0.91617E+01 0.46093E+00 | 0.66157E+00 0.00000E+00 | 0.17903E+02 0.00000E+00 |
| 44 (f2 | 0.26482E+03 0.77421E-02 | 0.59424E-05 0.39901E+01 | 0.00000E+00 0.45554E+04 | 0.66724E+03 0.28126E-01 | 0.40838E-01 0.00000E+00 | 0.69440E+03 0.00000E+00 |
| fuel enrichment = 3.6 w/o |
| 22 (a1 | 0.12038E+02 0.31522E+02 | 0.95073E+00 0.29155E+02 | 0.14017E+02 0.45515E+02 | 0.14305E+02 0.52992E+02 | 0.23343E+03 0.12042E+03 | 0.21803E+02 0.98209E+02 |
| 22 (a2 | 0.29893E+03 0.95440E+01 | 0.13173E+01 0.67395E+03 | 0.17667E+02 0.55060E+04 | 0.11434E+04 0.41462E+02 | 0.17667E+03 0.14091E+07 | 0.95168E+03 0.44737E+05 |
| 22 (f1 | 0.82728E+01 0.51404E+00 | 0.11547E+00 0.74539E+00 | 0.67956E+00 0.39689E+02 | 0.89539E+01 0.48682E+00 | 0.71773E+00 0.00000E+00 | 0.16984E+02 0.00000E+00 |
| 22 (f2 | 0.25484E+03 0.73795E-02 | 0.56689E-05 0.45407E+01 | 0.00000E+00 0.44532E+04 | 0.73113E+03 0.26962E-01 | 0.39752E-01 0.00000E+00 | 0.70726E+03 0.00000E+00 |
| 32 (a1 | 0.12257E+02 0.32494E+02 | 0.96998E+00 0.29195E+02 | 0.14305E+02 0.44666E+02 | 0.14261E+02 0.53771E+02 | 0.14280E+03 0.11319E+03 | 0.22133E+02 0.94666E+02 |
| 32 (a2 | 0.29390E+03 0.95582E+01 | 0.13029E+01 0.64616E+03 | 0.17530E+02 0.54265E+04 | 0.10596E+04 0.41845E+02 | 0.17663E+03 0.13965E+07 | 0.91360E+03 0.44003E+05 |
| 32 (f1 | 0.83582E+01 0.50485E+00 | 0.11294E+00 0.73316E+00 | 0.66747E+00 0.38917E+02 | 0.89143E+01 0.47735E+00 | 0.69030E+00 0.00000E+00 | 0.17229E+02 0.00000E+00 |
| 32 (f2 | 0.25071E+03 0.73905E-02 | 0.56069E-05 0.42853E+01 | 0.00000E+00 0.43871E+04 | 0.68140E+03 0.27219E-01 | 0.39710E-01 0.00000E+00 | 0.68013E+03 0.00000E+00 |
| 38 (a1 | 0.12411E+02 0.32497E+02 | 0.98392E+00 0.28807E+02 | 0.14484E+02 0.443911+02 | 0.14300E+02 0.53428E+02 | 0.10242E+03 0.10820E+03 | 0.22310E+02 0.91935E+02 |
| 38 (a2 | 0.29623E+03 0.96411E+01 | 0.13171E+01 0.63079E+03 | 0.17739E+02 0.54351E+04 | 0.10318E+04 0.42146E+02 | 0.17718E+03 0.14213E+07 | 0.90613E+03 0.44553E+05 |
| 38 (f1 | 0.84216E+01 0.49900E+00 | 0.11134E+00 0.72262E+00 | 0.66007E+00 0.38241E+02 | 0.89215E+01 0.47116E+00 | 0.67618E+00 0.00000E+00 | 0.17357E+02 0.00000E+00 |
| 38 (f2 | 0.25276E+03 0.74570E-02 | 0.56695E-05 0.41528E+01 | 0.00000E+00 0.43924E+04 | 0.66579E+03 0.27416E-01 | 0.39870E-01 0.00000E+00 | 0.67520E+03 0.00000E+00 |
| 44 (a1 | 0.12551E+02 0.32000E+02 | 0.99673E+00 0.28436E+02 | 0.14633E+02 0.43471E+02 | 0.14392E+02 0.52681E+02 | 0.86301E+02 0.10537E+03 | 0.22467E+02 0.90458E+02 |
| 44 (a2 | 0.29853E+03 0.97215E+01 | 0.13320E+01 0.62150E+03 | 0.17951E+02 0.54586E+04 | 0.10218E+04 0.42397E+02 | 0.17773E+03 0.14445E+07 | 0.90649E+03 0.45119E+05 |
| 44 (f1 | 0.84899E+01 0.49378E+00 | 0.10999E+00 0.71359E+00 | 0.65387E+00 0.38749E+02 | 0.89625E+01 0.46568E+00 | 0.66775E+00 0.00000E+00 | 0.17471E+02 0.00000E+00 |
| 44 (f2 | 0.25475E+03 0.75211E-02 | 0.57347E-05 0.40758E+01 | 0.00000E+00 0.44103E+04 | 0.66061E+03 0.27580E-01 | 0.40029E-01 0.00000E+00 | 0.67582E+03 0.00000E+00 |
| Table V - cont. |
| 50 (a1 | 0.12639E+02 0.31282E+02 | 0.10076E+01 0.28064E+02 | 0.14731E+02 0.43083E+02 | 0.14468E+02 0.51632E+02 | 0.78608E+02 0.10332E+03 | 0.22556E+02 0.89444E+02 |
| 50 (a2 | 0.29944E+03 0.97675E+01 | 0.13420E+01 0.61589E+03 | 0.18091E+02 0.54729E+04 | 0.10183E+04 0.42520E+02 | 0.17800E+03 0.14600E+07 | 0.90785E+03 0.45509E+05 |
| 50 (f1 | 0.85327E+01 0.48963E+00 | 0.10894E+00 0.70615E+00 | 0.64921E+00 0.37504E+02 | 0.89966E+01 0.46126E+00 | 0.66229E+00 0.00000E+00 | 0.17534E+02 0.00000E+00 |
| 50 (f2 | 0.25554E+03 0.75580E-02 | 0.57781E-05 0.40311E+01 | 0.00000E+00 0.44212E+04 | 0.65909E+03 0.27660E-01 | 0.40115E-01 0.00000E+00 | 0.67702E+03 0.00000E+00 |
| fuel enrichment = 4.0; 3.6; 3.3 w/o |
| 22 (a1 | 0.11922E+02 0.31226E+02 | 0.94807E+00 0.28882E+02 | 0.13929E+02 0.45069E+02 | 0.14210E+02 0.52490E+02 | 0.23030E+03 0.11890E+03 | 0.21643E+02 0.97155E+02 |
| 22 (a2 | 0.29336E+03 0.94433E+01 | 0.13024E+01 0.67514E+03 | 0.17459E+02 0.54458E+04 | 0.11406E+04 0.41108E+02 | 0.17537E+03 0.13872E+07 | 0.94364E+03 0.44121E+05 |
| 22 (f1 | 0.81986E+01 0.51578E+00 | 0.11600E+00 0.74578E+00 | 0.68211E+00 0.39301E+02 | 0.88963E+01 0.48843E+00 | 0.71925E+00 0.00000E+00 | 0.16861E+02 0.00000E+00 |
| 22 (f2 | 0.25008E+03 0.73003E-02 | 0.56044E-05 0.45555E+01 | 0.00000E+00 0.44050E+04 | 0.72871E+03 0.26733E-01 | 0.39434E-01 0.00000E+00 | 0.70107E+03 0.00000E+00 |
| 32 (a1 | 0.12148E+02 0.32233E+02 | 0.96721E+00 0.28971E+02 | 0.14220E+02 0.44340E+02 | 0.14177E+02 0.53348E+02 | 0.14348E+03 0.11210E+03 | 0.21985E+02 0.93847E+02 |
| 32 (a2 | 0.28835E+03 0.95168E+01 | 0.12900E+01 0.64857E+03 | 0.17370E+02 0.53896E+04 | 0.10577E+04 0.41764E+02 | 0.17581E+03 0.13707E+07 | 0.90882E+03 0.43232E+05 |
| 32 (f1 | 0.82911E+01 0.50626E+00 | 0.11344E+00 0.73368E+00 | 0.66978E+00 0.38636E+02 | 0.88643E+01 0.47863E+00 | 0.69231E+00 0.00000E+00 | 0.17116E+02 0.00000E+00 |
| 32 (f2 | 0.24597E+03 0.73575E-02 | 0.55512E-05 0.43072E+01 | 0.00000E+00 0.43577E+04 | 0.67961E+03 0.27166E-01 | 0.39503E-01 0.00000E+00 | 0.67641E+03 0.00000E+00 |
| 38 (a1 | 0.12310E+02 0.32297E+02 | 0.98122E+00 0.28616E+02 | 0.14404E+02 0.436191+02 | 0.14219E+02 0.53076E+02 | 0.10287E+03 0.10732E+03 | 0.22170E+02 0.91259E+02 |
| 38 (a2 | 0.29074E+03 0.95999E+01 | 0.13059E+01 0.63194E+03 | 0.17597E+02 0.53899E+04 | 0.10288E+04 0.42054E+02 | 0.17645E+03 0.13989E+07 | 0.90074E+03 0.43892E+05 |
| 38 (f1 | 0.83594E+01 0.50042E+00 | 0.11182E+00 0.72337E+00 | 0.66224E+00 0.37989E+02 | 0.88735E+01 0.47247E+00 | 0.67808E+00 0.00000E+00 | 0.17250E+02 0.00000E+00 |
| 38 (f2 | 0.24807E+03 0.74241E-02 | 0.56208E-05 0.41653E+01 | 0.00000E+00 0.43563E+04 | 0.66340E+03 0.27357E-01 | 0.39684E-01 0.00000E+00 | 0.67105E+03 0.00000E+00 |
| 44 (a1 | 0.12462E+02 0.31871E+02 | 0.99427E+00 0.28281E+02 | 0.14563E+02 0.43224E+02 | 0.14318E+02 0.52420E+02 | 0.86391E+02 0.10465E+03 | 0.22343E+02 0.89891E+02 |
| 44 (a2 | 0.29344E+03 0.96832E+01 | 0.13230E+01 0.62191E+03 | 0.17836E+02 0.54163E+04 | 0.10186E+04 0.42306E+02 | 0.17706E+03 0.14264E+07 | 0.90139E+03 0.44587E+05 |
| 44 (f1 | 0.84354E+01 0.49514E+00 | 0.11042E+00 0.71443E+00 | 0.65581E+00 0.37635E+02 | 0.89193E+01 0.46696E+00 | 0.66941E+00 0.00000E+00 | 0.17377E+02 0.00000E+00 |
| 44 (f2 | 0.25040E+03 0.74907E-02 | 0.56953E-05 0.40822E+01 | 0.00000E+00 0.43764E+04 | 0.65822E+03 0.27521E-01 | 0.39863E-01 0.00000E+00 | 0.67192E+03 0.00000E+00 |
| 50 (a1 | 0.12569E+02 0.31212E+02 | 0.10057E+01 0.27948E+02 | 0.14676E+02 0.42891E+02 | 0.14409E+02 0.51469E+02 | 0.78481E+02 0.10277E+03 | 0.22458E+02 0.88998E+02 |
| 50 (a2 | 0.29503E+03 0.97381E+01 | 0.13355E+01 0.61573E+03 | 0.18009E+02 0.54389E+04 | 0.10156E+04 0.42449E+02 | 0.17747E+03 0.14472E+07 | 0.90375E+03 0.45125E+05 |
| 50 (f1 | 0.84891E+01 0.49080E+00 | 0.10930E+00 0.70692E+00 | 0.65078E+00 0.37339E+02 | 0.89622E+01 0.46238E+00 | 0.66360E+00 0.00000E+00 | 0.17459E+02 0.00000E+00 |
| 50 (f2 | 0.25178E+03 0.75347E-02 | 0.57502E-05 0.40325E+01 | 0.00000E+00 0.43939E+04 | 0.65706E+03 0.27614E-01 | 0.39985E-01 0.00000E+00 | 0.67389E+03 0.00000E+00 |

Table VI    Macroscopic cross sections

| State |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| fuel enrichment = 1.6 w/o |
| 22 | 0.14286E+01 0.38730E+00 | 0.81958E-02 0.57882E-01 | 0.43632E-02 0.74997E-01 | 0.17211E-02 0.31449E-01 | 0.15883E-01 |
| 32 | 0.14167E+01 0.38039E+00 | 0.99939E-02 0.81284E-01 | 0.40041E-02 0.10012E+00 | 0.15386E-02 0.38379E-01 | 0.14894E-01 |
| 38 | 0.14092E+01 0.37869E+00 | 0.10975E-01 0.87404E-01 | 0.38480E-02 0.10361E+00 | 0.14538E-02 0.38770E-01 | 0.14400E-01 |
| fuel enrichment = 2.4 w/o |
| 22 | 0.14396E+01 0.38750E+00 | 0.86548E-02 0.72605E-01 | 0.54294E-02 0.10667E+00 | 0.21646E-02 0.44725E-01 | 0.15037E-01 |
| 32 | 0.14244E+01 0.37997E+00 | 0.10119E-01 0.92555E-01 | 0.47556E-02 0.12315E+00 | 0.18533E-02 0.48083E-01 | 0.14479E-01 |
| 38 | 0.14145E+01 0.37800E+00 | 0.11016E-01 0.95421E-01 | 0.43284E-02 0.11973E+00 | 0.16534E-02 0.45424E-01 | 0.14139E-01 |
| 44 | 0.14070E+01 0.37718E+00 | 0.11691E-01 0.96583E-01 | 0.40797E-02 0.11563E+00 | 0.15376E-02 0.43167E-01 | 0.13887E-01 |
| fuel enrichment = 3.6 w/o |
| 22 | 0.14499E+01 0.38626E+00 | 0.93448E-02 0.92548E-01 | 0.69133E-02 0.14936E+00 | 0.27827E-02 0.62617E-01 | 0.14134E-01 |
| 32 | 0.14340E+01 0.37853E+00 | 0.10467E-01 0.11035E+00 | 0.60060E-02 0.15944E+00 | 0.23769E-02 0.63369E-01 | 0.13860E-01 |
| 38 | 0.14230E+01 0.37637E+00 | 0.11220E-01 0.11127E+00 | 0.52999E-02 0.15142E+00 | 0.20583E-02 0.58533E-01 | 0.13647E-01 |
| 44 | 0.14136E+01 0.37569E+00 | 0.11803E-01 0.10918E+00 | 0.47677E-02 0.14002E+00 | 0.18216E-02 0.53085E-01 | 0.13525E-01 |
| 50 | 0.14059E+01 0.37544E+00 | 0.12298E-01 0.10731E+00 | 0.44087E-02 0.13090E+00 | 0.16630E-02 0.48938E-01 | 0.13411E-01 |
| fuel enrichment = 4.0; 3.6; 3.3 w/o |
| 22 | 0.14540E+01 0.38671E+00 | 0.94562E-02 0.95106E-01 | 0.71748E-02 0.15568E+00 | 0.28915E-02 0.65266E-01 | 0.13990E-01 |
| 32 | 0.14381E+01 0.37902E+00 | 0.10530E-01 0.11267E+00 | 0.62412E-02 0.16508E+00 | 0.24753E-02 0.65762E-01 | 0.13750E-01 |
| 38 | 0.14271E+01 0.37685E+00 | 0.11258E-01 0.11347E+00 | 0.54972E-02 0.15675E+00 | 0.21409E-02 0.60766E-01 | 0.13552E-01 |
| 44 | 0.14175E+01 0.37619E+00 | 0.11822E-01 0.11106E+00 | 0.49213E-02 0.14460E+00 | 0.18855E-02 0.54978E-01 | 0.13447E-01 |
| 50 | 0.14095E+01 0.37599E+00 | 0.12305E-01 0.10868E+00 | 0.45157E-02 0.13430E+00 | 0.17072E-02 0.50328E-01 | 0.13353E-01 |