# AER Benchmark Solution Sheet

1. Test ID: AER-DYN-001 kinetic benchmark [1]

2. a, Solution Submitted by: J. Krell, KAB AG

Date: 05.21.2000

b, Reviewed by: A. Keresztúri

Date:

c, Accepted by: A. Keresztúri

Date:

3. Code or Program Applied: DYN3D [2]

4. Short Description of Code:

See other DYN3D solutions given in the Specification Sheet.

5. Known approximations

A very simple homogenization model was applied for the mixed nodes containing both absorber and fuel. The fuel assemblies had to be subdivided into 12 nodes (+2 axial reflector nodes)  as a consequence of this simple approximation. See Specification Sheet and [2].

6. Mathematical Model:

See  [2]

7. Features of Techniques Used:

See [2]

8. Computer, Operational System:

See [2]

9. References:

[1] A. Keresztúri, M. Telbisz: A Three-Dimensional Hexagonal Kinetic Benchmark Problem, 2nd AER Symposium , Paks Hungary, 1992

[2] U. Grundmann, U. Rohde: DYN3D/M2 a Code for Calculation of Reactivity Transients in Cores with Hexagonal Geometry, Report ZfK-690, Rossendorf, 1989

[3] M. Telbisz, A. Keresztúri: Results of a Three-Dimensional Hexagonal Kinetic Benchmark Problem, 3rd AER Symposium , Piestany, Slovakia, 1993

[4] A.Keresztúri, M.Telbisz, I.Vidovszky, U.Grundmann, J.Krell: Results of a Three-Dimensional Hexagonal Kinetic Benchmark Problem, ENS Meeting, Portoroz 1993

10. Results

The benchmark has two versions - 1A and 1B - according to the Specification Sheet. This solution sheet contains the results of version 1A.  Analysis of the results can be found in [3,4] and in the Specification Sheet.

The results of benchmark 1A (power vs. time and 3-dimensional dynamic power distributions according to the specification) are given in the dyn001_solkab.txt file.

11. Comparison to Recommended Solution:

See [3,4] and Specification Sheet.